## Slide 1
COM-405: Mobile Networks
Lecture 14.0: Multipath TCP
Haitham Hassanieh
Laboratory of SEnsing
& Networking Systems
slides shamelessly stolen from Prof. JP Hubaux & others

## Slide 2: Reminder: Transmission Control Protocol (TCP)
Reliable, in-order data delivery service
Single path
  tied to the source and destination addresses of the endpoints
Flow control
Congestion avoidance and control
End-to-end semantics

## Slide 3: TCP Connection Setup
Three-way handshake

## Slide 4: TCP Data Transmission
Browser: Send 3KB of data
HTTP Server: Read Request
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server

## Slide 5: TCP Data Transmission
Data: 0-1000
Browser: Send 3KB of data
HTTP Server: Read Request
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server

## Slide 6: TCP Data Transmission
Data: 1000-2000
Data: 0-1000
Browser: Send 3KB of data
HTTP Server: Read Request
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server

## Slide 7: TCP Data Transmission
Data: 1001-2000
Data: 1-1000
Data: 2001-3000
Browser: Send 3KB of data
HTTP Server: Read Request
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server

## Slide 8: TCP: Lost Packets
Data: 1-1000
Data:
2001-3000
Browser: Send 3KB of data
HTTP Server: Read Request
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server
  How do the browser and the server know that a packet is lost?

## Slide 9: TCP: Sequence #s and ACKs
Data: 1001-2000
Data: 1-1000
Data: 2001-3000
Browser: Send 3KB of data
HTTP Server: Read Request
SEQ
1
SEQ 1001
SEQ 2001
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server
    How do the browser and the server know that a packet is lost?
      Based on the sequence numbers and ACKs

## Slide 10: TCP: Sequence #s and ACKs
Data: 1001-2000
Data: 2001-3000
Browser: Send 3KB of data
HTTP Server: Read Request
SEQ 1001
SEQ 2001
ACK 1001
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server
    How do the browser and the server know that a packet is lost?
      Based on the sequence numbers and ACKs

## Slide 11: TCP: Sequence #s and ACKs
Data: 2001-3000
Browser: Send 3KB of data
HTTP Server: Read Request
SEQ 2001
ACK 2001
ACK 1001
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server
    How do the browser and the server know that a packet is lost?
      Based on the sequence numbers and ACKs

## Slide 12: TCP: Sequence #s and ACKs
Browser: Send 3KB of data
HTTP Server: Read Request
ACK 2001
ACK 1001
ACK 3001
Assuming a browser wants to send 3KB of data in 3 TCP segments to an HTTP Server
    How do the browser and the server know that a packet is lost?
      Based on the sequence numbers and ACKs

## Slide 13: TCP for Wireless and Mobile Networks
Imagine a phone with cellular network and WiFi, moving around a campus
  Would like to use the cellular network as semi-reliable baseline service, supplemented by WiFi when available, and switching between WiFi APs as they come and go
cell tower

## Slide 14: TCP for Wireless and Mobile Networks
cell tower
Imagine a phone with cellular network and WiFi, moving around a campus
  Would like to use the cellular network as semi-reliable baseline service, supplemented by WiFi when available, and switching between WiFi APs as they come and go

## Slide 15: TCP for Wireless and Mobile Networks
Imagine a phone with cellular network and WiFi, moving around a campus
  Would like to use cellular network as semi-reliable baseline service, supplemented by WiFi when available, and switching between WiFi APs as they come and go
cell tower

## Slide 16: TCP for Wireless and Mobile Networks
Offload to WiFi
Imagine a phone with cellular network and WiFi, moving around a campus
  Would like to use cellular network as semi-reliable baseline service, supplemented by WiFi when available, and switching between WiFi APs as they come and go
cell tower

## Slide 17: TCP for Wireless and Mobile Networks
All ongoing TCP connections die
Imagine a phone with cellular network and WiFi, moving around a campus
  Would like to use the cellular network as semi-reliable baseline service, supplemented by WiFi when available, and switching between WiFi APs as they come and go
  Conventional TCP is not designed around such agile network connectivity
cell tower

## Slide 18
  MPTCP is a modification of TCP that presents a regular TCP interface to applications, while spreading data across several subflows
  Specified in RFC 6824, obsoleted by RFC 8684 (March 2020)
  Not a new idea; originally proposed more than 15 years ago
  MPTCP goes further to solve issues of fairness when competing with regular TCP and deployment issues
  An MPTCP connection is composed of one or more regular TCP subflows that are combined
  Each host maintains states that glue the TCP subflows of a MPTCP connection together
  Each TCP subflow is sent over a single path and appears like a regular TCP connection along this path
Benefits
  Higher throughput
  Failover from one path to another
  Seamless mobility
Bringing Multipath TCP to the End Host

## Slide 19: MPTCP Architecture
Physical
Datalink
Network
Transport
Application
Multipath TCP
TCP1
socket
TCP2
TCPn
...
Application

## Slide 20: How to set up an MPTCP session?
  Establish the initial subflow
    Three-way TCP handshake with MP_CAPABLE option
  Then additional subflows can be established
    Three-way TCP handshake with MP_JOIN option
  Each subflow looks similar to a regular TCP connection
Which subflows can be associated to a MPTCP connection?
  At least one of the elements of the four-tuple needs to differ between two subflows
    Local IP address
    Remote IP address
    Local port
    Remote port

## Slide 21: MPTCP Operation – Setting up the Initial Subflow
SYN
MP_CAP ABLE X

## Slide 22: MPTCP Operation – Setting up the Initial Subflow
SYN/ACK
MP_CAPABLE Y

## Slide 23: MPTCP Operation – Setting up the Initial Subflow
STATE 1 CWND Snd.SEQNO Rcv.SEQNO

## Slide 24: MPTCP Operation – Adding an Additional Subflow
STATE 1 CWND Snd.SEQNO Rcv.SEQNO
SYN
JOIN Y

## Slide 25: MPTCP Operation – Adding an Additional Subflow
STATE 1 CWND Snd.SEQNO Rcv.SEQNO
SYN/ACK
JOIN X

## Slide 26: MPTCP Operation – Adding an Additional Subflow
STATE 1 CWND Snd.SEQNO Rcv.SEQNO
STATE 2 CWND Snd.SEQNO Rcv.SEQNO

## Slide 27: How to Transfer Data?
seq=123,"a"
seq=124,"b"
seq=125,"c"
ack=124
ack=126
ack=125
Gap in sequence numbering space. Some network middleboxes will not allow this!
Assuming a MPTCP connection with 2 subflows and data for the connection can then be sent over any of the active subflows that has the capacity to take it

## Slide 28: MPTCP Data Transfer
To solve the problem of gaps in the sequence numbering space, MPTCP uses two levels of sequence numbers
Multipath TCP
TCP1
socket
TCP2
Multipath TCP
TCP1
socket
TCP2
ABCDEF
Data sequence #
TCP1 sequence #
TCP2 sequence #

## Slide 29: MPTCP Data Transfer
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=2, seq=124,"c"
DAck=1,ack=124
DAck=3, ack=125
DAck=2,ack=457
Dseq is the data sequence number (SQN)
seq is the additional SQN carried inside the TCP option
  ensures that the segments sent on any given subflow have consecutive SQNs (to not upset the middleboxes)
*seq* is the sequence for a flow
*dseq* is for the MPTCP connection

## Slide 30: What Happens When a TCP Subflow Fails ?
Dseq=0,seq=123,"a"
DSeq=1, seq=456,"b"
DSeq=0,ack=457
Dseq=0,seq=457,"a"
DAck=2,ack=458

## Slide 31: Retransmission Heuristics
Heuristics used by current Linux implementation
  Fast retransmit is performed on the same subflow as the original transmission
  Upon timeout expiration, re-evaluate whether the packet could be retransmitted over another subflow
  Upon loss of a subflow, all the unacknowledged data are retransmitted on other subflows

## Slide 32: An Important Question
How does the congestion control algorithm work?

## Slide 33: An Important Question
How does the congestion control algorithm work?

## Slide 34: MPTCP Congestion Control
Each path runs its own congestion control, to detect and respond to the congestion it sees.
But link the congestion control parameters, so as to move trafﬁc away from the more congested paths.
be more aggressive
be less aggressive

## Slide 35: Design Goals for MPTCP
Goal 1: Be fair to regular TCP
Goal 2: Use efficient (meaning uncongested) paths
Goal 3: Perform as well as TCP
We detail them one by one in the next slides

## Slide 36: Design Goal 1: Be Fair to Regular TCP
To be fair, MPTCP should take as much capacity as TCP at a bottleneck link, no matter how many paths it is using
Regular TCP
MPTCP

## Slide 37: Design Goal 2: MPTCP Should Use Efﬁcient Paths
12Mb/s
12Mb/s
12Mb/s
Assume there are 3 MPTCP connections with the same data rates of X Mb/s, each consisting of 2 subflows
  Each connection has a choice of a 1-hop and a 2-hop path
  How should each connection split its traffic between its 1-hop and 2-hop subflows?
X Mb/s
X Mb/s
X Mb/s

## Slide 38: Design Goal 2: MPTCP Should Use Efﬁcient Paths
Assume there are 3 MPTCP connections with the same data rates of X Mb/s, each consisting of 2 subflows
  If each connection splits its traffic between its 1-hop and 2-hop subflows with ratio 1:1
X/2 + X/2 + X/2 = 12  X = 8Mb/s
12Mb/s
12Mb/s
12Mb/s
X Mb/s
X Mb/s
X Mb/s

## Slide 39: Design Goal 2: MPTCP Should Use Efﬁcient Paths
Assume there are 3 MPTCP connections with the same data rates of X Mb/s, each consisting of 2 subflows
  If each connection splits its traffic between its 1-hop and 2-hop subflows with ratio 2:1
2X/3 + X/3 + X/3 = 12  X = 9Mb/s
12Mb/s
12Mb/s
12Mb/s
X Mb/s
X Mb/s
X Mb/s

## Slide 40: Design Goal 2: MPTCP Should Use Efﬁcient Paths
Assume there are 3 MPTCP connections with the same data rates of X Mb/s, each consisting of 2 subflows
  If each connection splits its traffic between its 1-hop and 2-hop subflows with ratio 4:1
4X/5 + X/5 + X/5 = 12  X = 10 Mb/s
12Mb/s
12Mb/s
12Mb/s
X Mb/s
X Mb/s
X Mb/s

## Slide 41: Design Goal 2: MPTCP Should Use Efﬁcient Paths
Assume there are 3 MPTCP connections with the same data rates of X Mb/s, each consisting of 2 subflows
  If each connection splits its traffic between its 1-hop and 2-hop subflows with ratio ∞ :1
12Mb/s
12Mb/s
12Mb/s
X Mb/s
X Mb/s
X Mb/s
All data is sent through the 1-hop subflow  X = 12 Mb/s

## Slide 42: Design Goal 2: MPTCP Should Use Efﬁcient Paths
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
Theoretical solution (Kelly + Voice 2005)
  MPTCP should send all its trafﬁc on its least-congested paths.
  Theorem: This will lead to the most efficient allocation possible, given a network topology and a set of available paths.
F. Kelly and T. Voice: Stability of end-to-end algorithms for joint routing and rate control, ACM SIGCOMM Communication Review, 2005
Assume there are 3 MPTCP connections, each consisting of 2 subflows

## Slide 43: Design Goal 3: Perform as well as TCP
Goal 3a.
  A Multipath TCP user should get at least as much throughput as a single-path TCP would on the best of the available paths
Goal 3b.
  A Multipath TCP flow should take no more capacity on any link than a single-path TCP would
  This is actually Design Goal 1
wifi path: high loss, small RTT
3G path: low loss, high RTT
WiFi path: small RTT
cellular path: high RTT
RTT = Round-Trip Time

## Slide 44: MPTCP Congestion Control Algorithm
Needs to satisfy design goals 2 and 3
The authors do not claim that:
  The algorithm is optimal
  It is an exhaustive survey of the design space
  The design space was signposted by examples, analyzed by calculations and experiments

## Slide 45: MPTCP Congestion Control Algorithm
A connection consists of set of subflows R
Each subflow r ∈ R maintains a congestion window wr
Denote RTTr the round trip time measured by subflow r
Denote S the subset of R s.t. subflows in S share a bottleneck with r
Example:
S0
Assume R consists of 4 subflows in red and this is r,
then the bottlenecks for r are S1 and S2 as shown in the figure.
S1
S2

## Slide 46: MPTCP Congestion Control Algorithm
For each ACK on path r, increase wr by:
For each drop on path r, decrease wr by wr /2
Reminder: TCP sender maintains a congestion window, which governs the number of packets that the sender can send without
waiting for an acknowledgment. The congestion window is updated dynamically, growing linearly when there is no congestion
and halved when packet loss occurs. TCP congestion control ensures fairness: when multiple connections utilize the same congested link,
each of them will independently converge to the same average value of the congestion window.
Reminder – Algorithm for regular TCP
- For each ACK, increase the congestion window w by 1/w, resulting in an increase of one packet per RTT.1
- For each loss, decrease w by w/2.

## Slide 47: MPTCP Congestion Control Algorithm
For each ACK on path r, increase wr by:
For each drop on path r, decrease wr by wr /2
Design goal 3: At any potential bottleneck S that path r might be in, look at the best that a single-path TCP could get, and compare to what I’m getting.
Intuition:
Numerator -> the best that regular TCP could get
Denominator -> what MPTCP gets
Min -> least congested or used part

## Slide 48: MPTCP Congestion Control Algorithm
For each ACK on path r, increase wr by
For each drop on path r, decrease wr by wr /2
Design goal 2: We want to shift traffic away from congestion.
To achieve this, we
increase windows in
proportion to their size.

## Slide 49: References
RFC 8684 (March 2020): https://www.rfc-editor.org/rfc/rfc8684.txt
Q. Peng, A. Walid, J. Hwang and S. H. Low, "Multipath TCP: Analysis, Design, and Implementation," in IEEE/ACM Transactions on Networking, vol. 24, no. 1, pp. 596-609, Feb. 2016.
O. Bonaventure, M. Handley, and C. Raiciu, An Overview of Multipath TCP, ;login:, Oct. 2012: http://inl.info.ucl.ac.be/system/files/bonaventure_0.pdf