## Slide 1
Constructive Computer Architecture
Networks-on-Chip
Part I: Flow Control & Router Microarch
Thomas Bourgeat – EPFL
Slides from Jianming Tong and Tushar Krishna (Georgia Tech)

## Slide 2: Recap: Symmetric Multiprocessors
All memory is equally accessible to all processors
Any processor can do any I/O operation
Memory
Processor-Memory Interconnect
bridge
Processor
+ cache
I/O controller
Graphics
output
I/O controller
I/O controller
I/O Interconnect
Networks
Processor
+ cache
Notes: Shared Memory Abstraction
Case 1: same cores
Case 2: multiple cores.

## Slide 3: Early commercial Multicore Chips 2006 - 2011
IBM Power 7 8 Cores
AMD MagnyCours 12 Cores
Tilera Tile64 64 Cores
Intel Teraflops 80 Cores
Sun UltraSpac T2
8 Cores
IBM Cell
8 Cores

## Slide 4: Accelerator Chips – ~2015
NVIDIA Pascal
64 CUDA cores (per SM)
60 SMs
ShiDianNao
64 PEs
MIT Eyeriss
168 PEs
Google TPU
256x256 MACs
IBM TrueNorth
4096 cores
Deep Learning Accelerators

## Slide 5: Today: everything together
Source: twitter.com/highyieldYT

## Slide 6: Recap: Symmetric Multiprocessors
All memory is (equally?) accessible to all processors
Any processor can do any I/O operation
Memory
Processor-Memory Interconnect
bridge
Processor
+ cache
I/O controller
Graphics
output
I/O controller
I/O controller
I/O Interconnect
Networks
Processor
+ cache
Notes: Shared Memory Abstraction
Case 1: same cores
Case 2: multiple cores.

## Slide 7: Network-on-Chip (NoC)
Core + L1$
Core + L1$
Core + L1$
Core + L1$
Core + L1$
Core + L1$
L2$
L2$
L2$
L2$
L2$
L2$
Network-on-Chip

## Slide 8: What traffic goes on the NoC?
Upgrade Req
c2m
m2c
interconnect
c2m
m2c
Dngrade Resp
Upgrade Resp
Dngrade Req
  Two FIFOs guarantee that an upgrade request cannot block a response message
  A downgrade request always completes and therefore it can share the same FIFO as for response messages
child
parent
Cache Coherence!

## Slide 9: Modern NoCs
Network Interface
Router
“Tile”
Core will not be shown explicitly in the rest of the slides. Only the routers will be.
L3$/Directory
L2$
L1
D$
Core
L1
I$
“Tile”
Mesh
Ring

## Slide 10: NoC Metrics
Performance
  Latency
    Delay to deliver a message
  Throughput
    How many messages are delivered per cycle
Power
  Links
  Routers
Area
  Links
  Routers

## Slide 11: An analogy

## Slide 12: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)

## Slide 13: How are messages sent?
Route
Seq#
Type
VCID
Packet
Flit
Head, Body, Tail, Head & Tail
Header
Payload
Head Flit
Body Flit
Tail Flit
Message
x40
x10
Lausanne Gare
Classroom
Message
Packet
Flit

## Slide 14: Packet Switching
Messages composed of one or more packets
  If message size is <= maximum packet size only one packet created
Packets composed of one or more flits
  Flit size same as link width
Link segments allocated at packet/flit granularity
x40
x10
Lausanne Gare
Classroom
Message
Packet
Flit

## Slide 15: Typical NoC Packets
Route
Cache line
Type
VCid
Addr
Head Flit
Bytes 0-15
Bytes 16-31
Bytes 32-47
Bytes 48-63
Body Flits
Tail Flit
Cache Line Request
Head_Tail Flit
Route
Type
VCid
Addr
Cmd
64B Cache Line
128-bit flits (i.e., link width)
1 control flit (cache line req)
5 data flits (cache line data)
Packet contains destination/route information
  Flits may not  all flits of a packet must take same route

## Slide 16: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)
Today’s class

## Slide 17: Designing a NoC
…
Core
Core
Core
Core
Core
Core
Core
Core
Suppose the cores are connected in a ring

## Slide 18: Designing the Ring Stop
Output to Core
Input from Core
?
Ring
1. Who should use output link?
2. What to do with the other flit (from ring/core)
Have you seen this same situation in real life on a road network?
…

## Slide 19: Real life example
Traffic already on ring has priority
Wait
1. Who should use output link?
2. What to do with the other flit (from ring/core)

## Slide 20: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)

## Slide 21: Need for Flow Control
Contention!
  Two packets trying to use the same link at the same time
    Why?
      Multiple packets sharing same links
    Why not all to all connectivity?
      Not scalable (next lecture)

## Slide 22: Handling Contention
Output to Core
Input from Core
?
Ring
1. Who should use output link?
2. What to do with the other flit (from ring/core)
…
Traffic already on ring has priority
Wait
Note: opposite policy also possible.

## Slide 23: Implementing Flow Control
Traffic already on ring has priority
3. What should a flit do if its output is blocked?
This is known as “arbitration”
Output to Core
Input from Core
Output to Core
Input from Core
Full
New Flit
The control structure is called an “arbiter”
1. Who should use output link?
2. What to do with the other flit (from ring/core)
Wait

## Slide 24: Flow Control: Buffer Management
Option 1: Drop!
  Send a NACK back for dropped packet or have a timeout
    Source retransmits
    Implicit congestion control
  Flow control protocol on the Internet
  Advantage: can be bufferless!
  Challenges?
    Latency and energy overhead of re-transmitting more than that of buffering so not preferred on-chip
What should a flit do if its output is blocked?

## Slide 25: Flow Control: Buffer Management
Option 2: Misroute!
  As long as N input ports and N output ports, can send flit out of some other output port
    called “bouncing” on a ring
  Advantage: can be bufferless!
  Challenges?
    Energy
      Routes become non-minimal – more energy consumption at router latches and on links
    Performance
      Non-minimal routes – can lead to longer delays
    Correctness
      Livelock! – cannot guarantee forward progress
        Need to restrict number of misroutes of same packet
What should a flit do if its output is blocked?

## Slide 26: Flow Control: Buffer Management
Option 3: Wait!
  Signal to previous router to not send any more flits till the input at this router can be drained
    Backpressure techniques
      On/Off : one bit to signal if next router can receive or not
        Challenge: Delay of on/off signal
      Credit-based : A count of how many flits can be sent to the next node?
        When should credit be decremented?
        When should credit be incremented?
Whenever a flit is sent to the next router
Whenever a flit leaves the next router
What should a flit do if its output is blocked?
Note: In NoC lab you will use On/Off

## Slide 27: Flow Control: Link and Buffer Allocation
Store and Forward Virtual Cut Through | Wormhole
X | Virtual Channel
Per Packet
Per Flit
Per Packet
Per Flit
Buffers
Links
wait for entire packet to arrive before forwarding
start forwarding as soon as flit arrives
Buffer can be smaller than entire packet
Interleave flits of different packets on link
May block channel mid-packet
Complex Router

## Slide 28: Wormhole Flow Control
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until red proceeds
Dest for Red
Dest for Blue
6 flit buffers/input port
“Head-of-Line Blocking”
Notes: Imagine being stuck behind a car that wants to turn but you want to go straight

## Slide 29: Virtual Channels
When a message blocks, instead of holding on to physical links so others can’t use them, hold on to virtual links (i.e., buffers)
  Analogous to lanes on the highway
    “Right-only” lane so that traffic going straight does not block
Disadvantages?
  More complex router (multiple sets of queues)
  Arbitration between VCs required

## Slide 30: Virtual Channel Flow Control
Buffer full: blue cannot proceed
Blocked by other packets
Dest for Red
Dest for Blue
6 flit buffers/input port
3 flit buffers/VC

## Slide 31: Flow Control Protocols
Bufferless
  Circuit switching
  Dropping
  Misrouting
Buffered
  Store-and-forward
  Virtual cut-through
  Wormhole
  Virtual-channel
Complexity
&
Efficiency

## Slide 32: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)

## Slide 33: What does a router look like?
Crossbar Switch
Input Buffers
VC 1
VC 2
VC n
VA: VC Allocation
Input VCs arbitrate for “output” VCs (Input VCs at next router)
SA: Switch Allocation
Input ports arbitrate for output ports
Input Buffers
VC 0
VC 1
VC n
BW
VA
ST
LT
VC Allocator
SW Allocator
BW: Buffer Write
ST: Switch Traversal
LT: Link Traversal
RC: Route Compute
RC
Route
Compute
SA
BR
BR: Buffer Read
VN0
VN
1
FLIT
…
Input Ports
Output Ports

## Slide 34: Router Microarchitecture
Components
  Virtual Channel Buffers
  Routing Logic
  Allocation
    Switch Allocation
    VC Allocation
  Crossbar Switch
  Link
Pipeline
Crossbar Switch
Input Buffers
VC 1
VC 2
VC n
Input Buffers
VC 0
VC 1
VC n
VC Allocator
SW Allocator
Route
Compute
VN0
VN
1

## Slide 35: Virtual Channel Buffers
Why are VCs used?
  Correctness: Avoid Cache Coherence Deadlock
  Performance: Avoid “Head-of-line Blocking”
How are VCs implemented?
  “Separate” queues at each input port
    Implementation Choices:
      Physically separate set of queues
      Logically separate and share a common pool of buffers
  Each packet arrives with a VCid
    Selects a VC at the previous router
      Previous router needs to know how many VCs empty
      This information is conveyed via “credits” or On/Off
  Question: Many shallow VCs or few deep VCs?

## Slide 36: VC and Switch Allocation
“Allocator” matches N requests to M resources
“Arbiter” matches N requests to 1 resource
VC Allocation
  Requests: Input VCs
  Resources: Output VCs (i.e., VCs at next router)
Switch Allocation
  Requests: Input VCs/Input ports
  Resources: Output ports of the router
Allocator that delivers the highest matching translates to higher network throughput
  Must also be fast and/or able to be pipelined
More discussion in recitation!

## Slide 37: Switch (Crossbar)
Mux-based Crossbar
Mux
Pass-gate switch
Input-driver
Matrix Crossbar
+ Synthesizable from RTL
- Typically More Area and Power
+ Lower area and power
- Requires careful custom design

## Slide 38: Crossbar Scalability
Key Challenges
  Area and power scale at O((pw)2)
    p: number of ports (function of topology)
    w: port width in bits (determines phit/flit size and impacts packet energy and delay)
  Arbitration in a large crossbar is challenging
Crossbar Optimizations
  Dimension-Slicing
    2x2 crossbar for X-dimension
      Local, X
    3x3 crossbar for Y-dimension
      Local, Y, X (i.e., turning)
  Bit-Interleaving / Double-pumping (e.g., Intel SCC)
    Send alternate bits on positive and negative phase of clock

## Slide 39: Router Pipeline vs Processor Pipelining
Logical Stages
  BW
  RC
  VA
  SA
  BR
  ST
  LT
Flits go through all/some stages
  Multiple kinds of flits
There can be multiple implementations for each stage
Logical Stages
  IF
  ID
  EX
  MA
  WB
Instructions go through all/some stages
  Multiple kinds of instructions
There can be multiple implementations for each stage
Today: most NoC routers have 1-2 pipeline stages
Router
Processor

## Slide 40: Router for Lab
Three logical Stages. One Cycle

## Slide 41: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)
Next class

## Slide 42: Backup

## Slide 43: Circuit Switching
Form a circuit from source to dest
Probe to set up path through network
Reserve all links
Send data through links
  Bufferless
Tear down circuit once transmission complete
SA
DC
DA
DB
SB
SC

## Slide 44: Circuit Switching Example
Significant latency overhead prior to data transfer
  Data transfer does not pay per-hop overhead for routing and allocation
Acknowledgement
Configuration Probe
Data
Circuit
0
5

## Slide 45: When does circuit switching make sense?
When sending large chunks of data
How large is the data being sent across the chip in shared memory NoCs?
  Cache Line – 64B
  Suppose
    Link Width – 128b
      64x8/128 = 4 chunks of data
    1-cycle per hop
      Setup Time: 3 cycles
      ACK Time: 3 cycles
      Data Transfer Time: 3 (for first chunk) + 3 (remaining chunks) cycles = 6 cycles
      Total Time = 12 cycles
        Half of the time went in circuit setup!

## Slide 46: How is contention handled?
When there is contention
  Significant wait time
  Message from 1  2 must wait
Acknowledgement
Configuration Probe
Data
Circuit
0
5
1
2
Wait till Data transmission from 0 complete!

## Slide 47: Arbiter Example
1
0
1
1
1
0
0
0
4:1 Arbiter
REQS
GRANT

## Slide 48: Allocator Example
12:3 Allocator
Suppose 4 requestors (A, B, C, D) and 3 resources (X, Y, Z)
1
1
1
1
0
1
0
0
1
1
0
1
1
0
0
0
0
0
0
0
0
0
0
1
Request A:
X, Y, Z
Request B:
X, Z
Request C:
Z
Request D:
X, Z
Grant X:
A
Grant Y:
0
Grant Z:
D

## Slide 49: Possible Implementation: Separable Allocator
12:3 Allocator
Suppose 4 requestors (A, B, C, D) and 3 resources (X, Y, Z)
3:1 arbiter
3:1 arbiter
3:1 arbiter
3:1 arbiter
4:1 arbiter
4:1 arbiter
4:1 arbiter
1
1
1
1
0
1
0
0
1
1
0
1
1
0
0
0
0
0
0
0
0
0
0
1
Request A:
X, Y, Z
Request B:
X, Z
Request C:
Z
Request D:
X, Z
Grant X:
A
Grant Y:
0
Grant Z:
D
Easier to implement in HW but not very efficient

## Slide 50: Separable Switch Allocator
Intel SCC (48-core, 45nm) in 2012
N input ports, v VCs per input port
N x v : N Allocator
  Stage 1: At every input port, choose one VC
    N v:1 allocators
  Stage 2: At every output port, choose one input port