## Slide 1
Constructive Computer Architecture
Networks-on-Chip
Part II: Topology and Routing
Thomas Bourgeat (EPFL)
From slides from Tushar Krishna (Georgia Tech)

## Slide 2: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)

## Slide 3: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)
Today’s class

## Slide 4: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)

## Slide 5: Topology Overview
Often the first step in network design
Significant impact on network cost-performance
  Determines implementation complexity, i.e., cost
    number of routers and links
    router degree (i.e., ports)
    ease of layout
  Determines application performance
    number of hops  latency and energy consumption
    maximum throughput
Notes: What does topology impact?

## Slide 6: How to select a topology?
A
B
C
D
Application’s
Task Communication Graph
Vertices - tasks
Edges - communication
E
A
B
C
D
E
Best topology?
Vertices - cores
Edges - links
Problems?
Cannot change algorithm
Cannot change mapping
Cannot adapt to data-dependent load imbalance in application
Layout/packaging issue with long wires and high-node degree
Topology is fixed at design-time.
Benefits to being regular and flexible
F
F
Network Topology Graph

## Slide 7: Design-time metrics
Degree – number of ports at a node
  Proxy for area/energy cost
Bisection Bandwidth - bandwidth crossing a minimal cut that divides the network in half
  (Min # channels crossing two halves) * (BW of each channel)
  Proxy for peak bandwidth
    Can be misleading as it does not account for routing and flow control efficiency
    At this stage, we assume ideal routing (perfect load balancing) and ideal flow control (no idle cycles on any channel)
Diameter – maximum routing distance (number of links in shortest route)
  Proxy for latency

## Slide 8: Regular topologies
Application’s
Task Communication Graph
Vertices - tasks
Edges - communication
Can you suggest a regular topology (each router with same degree) with smallest possible diameter?
Trick question :p
One node. Degree = 0, Diameter = 0.
A
B
C
D
E
F

## Slide 9: Regular topologies
Application’s
Task Communication Graph
Vertices - tasks
Edges - communication
Can you suggest a regular topology (each router with same degree) with diameter = 1?
A
B
C
D
E
F
Bisection Cut
Bisection BW = ?
Degree = ?
5
9
Challenge?
Not scalable!! Cannot layout more than 4-6 cores in this manner for area and power reasons
Fully Connected

## Slide 10: Bus
Pros
  Cost-effective for small number of nodes
  Easy to implement snoopy coherence
  Most multicores with 4-6 cores use Buses
Cons
  Bandwidth!  Not scalable
Bisection BW = ?
Degree = ?
1
1
Diameter = ?
1
…

## Slide 11: Popular Bus Protocols
ARM AMBA Bus
  AHB
  AXI
  ACE
  CHI
IBM Core Connect
ST Microelectronics STBus
How to increase bus bandwidth?
  Hierarchical Buses
  Split-buses

## Slide 12: Crossbar
Pros
  Every node connected to all others (non-blocking)
  Low latency and high bandwidth
  Used by GPUs
Cons
  Area and Power goes up quadratically (O(N2) cost)
  Expensive to layout
  Difficult to arbitrate
S
S
S
S
D
D
D
…
…
D
Switch
Bisection BW = ?
Degree = ?
Diameter = ?
1
N
1

## Slide 13: Ring
Pros
  Cheap: O(N) cost
  Used in most multicores today
Cons
  High latency
  Difficult to scale – bisection bandwidth remains constant
  No path diversity
    1 shortest path from A to B
A
B
…
Diameter?
Bisection BW?
Degree?
N/2
N/4
Avg Distance?
2
2

## Slide 14: Torus
Pros
  O(N) cost
  Exploit locality for near-neighbor traffic
  High path diversity
    6 shortest paths from A to B
  Edge symmetric
    good for load balancing
    Same router degree
Cons
  Unequal link lengths
  Harder to layout
B
A
Diameter?
Bisection BW?
Degree?
√N
2√N
4

## Slide 15: Mesh
Pros
  O(N) cost
  Easy to layout on-chip: regular and equal-length links
  Path diversity
    3 shortest paths from A to B
Cons
  Not symmetric on edges
    Performance sensitive to placement on edge vs. middle
    Different degrees for edge vs. middle routers
  Blocking, i.e., certain paths can block others (unlike crossbar)
Diameter?
Bisection BW?
Degree?
2(√N-1)
√N
4

## Slide 16: Hierarchical Topologies
Hierarchical Rings
64 cores connected by a 4x4 Mesh
Concentrated Mesh
Pros
Lower degree
Fewer Wires
Cons
Data Layout
Bandwidth at access points

## Slide 17: Other Topologies
Tree
Fat Tree
Butterfly
3D Mesh
Mostly used in off-chip multi-processors

## Slide 18: Run-time metrics
Hop count (or routing distance)
  Number of hops between a communicating pair
  Depends on application and mapping
  Average hop count or Average distance: average hops across all valid routes
Channel load
  Number of flows passing through a particular link
  Depends on application and mapping
  Maximum channel load determines throughput
Path diversity
  Number of shortest paths between a communicating pair
    Can be exploited by routing algorithm
    Provides fault tolerance

## Slide 19: Network Latency
TN = (tr+tl)×H + Tc
TN | Network Latency
tr | Router Latency
tl | Link Latency
H | Hops
Tc | Contention Latency
Ts | Serialization Latency (for multi-flit packets)
tr
tl
Router
Link
Tc
Contention
Hops
H
+ Ts
Which of these is dynamic (traffic-dependent)?
Which of these is static?
H
Tc
Ts
tr
tl
Ts = Serialization latency: time for packet with Length L to cross channel with bandwidth b (L/b)

## Slide 20: Latency Example
What is the average hop count for any message from A?
  (Sum hops from Ai, for all i) / Num (i)
  (1 + 1 + 2 + 2 + 3 + 3 + 4) / 7 = 16/7 = 2.28
Latency?
  2.28 x (router_delay + link_delay)
A
C
D
B
E
G
H
F

## Slide 21: Throughput
Estimate the maximum bandwidth the network can support
  Ideally this should be same as Bisection Bandwidth
  In reality, depends on traffic pattern, congestion, and efficiency of routing and flow-control
Maximum Channel Load
  Determine most congested link for a traffic pattern
  Will limit overall network bandwidth
Network Saturation
  network is operating at its peak and cannot accept any more packets

## Slide 22: Maximum Throughput Example
Suppose uniform random traffic
  Every node has equal probability of sending to every node
Identify bottleneck channel
Suppose each node generates p messages per cycle
  4p messages per cycle in left ring
  2p message per cycle will cross to other ring  Maximum Channel Load
  Link can handle one message per cycle
  So maximum injection rate (i.e., throughput) of p = ½
A
C
D
B
E
G
H
F
Similar calculation can be done for any {Topology,Traffic}

## Slide 23: Path Diversity
Multiple shortest paths between source/destination pair (R)
  Routing algorithm can exploit path diversity
Better load balancing
Fault tolerance
B
A
B
A
A
B
…
RAB = 1
RAB = 3
RAB = 6

## Slide 24: Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)

## Slide 25: Routing
Once topology is fixed, routing determines exact path from source to destination
Analogous to the series of road segments from source to destination

## Slide 26: Routing Algorithms
Minimal or Non-Minimal
  Minimal: only select shortest paths
  Non Minimal: need not select shortest paths
Oblivious or Adaptive
  Oblivious: routing decisions do not depend on network state/traffic
    Deterministic is a subset where same route is always chosen
  Adaptive: uses different routes depending on traffic
Implementation
  Table based or combination circuit

## Slide 27: Dimension Ordered Routing
XY: Always go X first, then Y
SA
DC
DA
DB
SB
SC
Cons of this approach?
And yet … This is the most common approach!
Eliminates any path diversity provided by topology
Poor load balancing
No deadlock under inf source, inf sink hypothesis
Minimal and Deterministic

## Slide 28: XY vs YX
XY
SA
DC
DA
DB
SB
SC
SB
SA
DB
DC
DA
SC
What happens if you use both simultaneously?
Suppose we toss a coin and send either XY or YX
YX
Minimal and Oblivious

## Slide 29: Challenge with Oblivious XY + YX
Deadlock!

## Slide 30: Routing Deadlock
  Packet A holds buffer u (in 1) and wants buffer v (in 2)
  Packet B holds buffer v (in 2) and wants buffer w (in 3)
  Packet C holds buffer w (in 3) and wants buffer x (in 0)
  Packet D holds buffer x (in 0) and wants buffer u (in 1)
0
1
2
3
A
B
C
D
u
v
w
x
Deadlock: A condition in which a set of agents wait indefinitely trying to acquire a set of resources
Agents: Packets
Resources: Buffers

## Slide 31: Classic Example: Dining Philosopher’s Problem
Agents: Philosophers
Resources: Forks
Deadlock: A condition in which a set of agents wait indefinitely trying to acquire a set of resources

## Slide 32: Deadlock Condition
Agents hold and do not release a resource while waiting for access to another
A cycle exists between waiting agents such that there exists a set of agents A0, .. An-1, where agent Ai holds resource Ri, while waiting on resource R(i+i mod n), for i = 0, …, n-1
To avoid deadlock – resource dependence graph should not have any cycles

## Slide 33: Turn Model (Glass & Ni 1994)
One way of looking at whether a routing algorithm is deadlock free is to look at the turns allowed.
Deadlocks may occur if turns can form a cycle
  Removing some turns can make algorithm deadlock free
XY Model
YX Model

## Slide 34: Deadlock-free Routing Algorithms
West-First Turn Model
North-Last Turn Model
Negative-First Turn Model

## Slide 35: Can we eliminate any two turns?
Six turn model
Deadlock!

## Slide 36: Path Diversity vs Deadlock
Path diversity required for higher throughput
Path restrictions because of deadlock-free routing requirement
Can we allow all turns and still get deadlock freedom ?

## Slide 37: Why do deadlocks occur?
Resource conflicts!
Add more buffers and partition!
  Packet A holds buffer u (in 1) and wants buffer v (in 2)
  Packet B holds buffer v (in 2) and wants buffer w (in 3)
  Packet C holds buffer w (in 3) and wants buffer x (in 0)
  Packet D holds buffer x (in 0) and wants buffer u (in 1)
0
1
2
3
A
B
C
D
u
v
w
x

## Slide 38: Virtual Channels
Same physical link/channel between routers
  additional buffers in each router to avoid deadlocks – called “virtual” channels
F
A
B
E
D
C
VC0
VC1

## Slide 39: Escape Virtual Channels
F
A
B
E
D
C
VC0
VC1
Allow any turns across all VCs except one
  “Escape” VC  deadlock-free route
If there is a deadlock, can jump into escape VC which is guaranteed to drain
VC0
VC1
Escape VC

## Slide 40: Another kind of deadlock: Protocol Deadlock
Cache 0
Directory
req
req
req
req
req
req
req
resp
resp
req
req
out
out
in
in
req
Cache / Directory can process a request only if there is space in its output queue to send a response
Need separate Virtual Channels for requests and responses
(called Virtual Networks (VN))
for full coherence protocol, need three VNs
(see Cache Coherence Lecture)
Deadlock, even though network is deadlock-free!

## Slide 41: Summary of Network Architecture
Topology
  How to connect the nodes
  ~Road Network
Routing
  Which path should a message take
  ~Series of road segments from source to destination
Flow Control
  When does the message have to stop/proceed
  ~Traffic signals at end of each road segment
Router Microarchitecture
  How to build the routers
  ~Design of traffic intersection (number of lanes, algorithm for turning red/green)

## Slide 42: Evaluating NoCs
Latency
Offered Traffic (bits/sec)
Min latency given by topology
Min latency given by routing algorithm
Zero load latency
(topology+routing+flow control)
Throughput given by topology
Throughput given by routing
Throughput given by flow control