## Slide 1
Constructive Computer Architecture
Sequential Circuits:
Circuits with state
Thomas – EPFL
Slides adapted from 6.1920 with Arvind
(Spring 23, MIT)
Notes: (Andy) Changed course website to correct website

## Slide 2: Outline
Logistic stuff
Simplest sequential module
Simple sequential module
Guarded Atomic Actions

## Slide 3: Github classroom lab 1
https://classroom.github.com/a/ZA44tux2

## Slide 4: Modulo-4 counter
Prev State | NextState | 
q1q0 | inc = 0 | inc = 1
00 | 00 | 01
01 | 01 | 10
10 | 10 | 11
11 | 11 | 00
reg[1:0] q1q0;
if (inct == 0)
  q1q0(t+1) = q1q0t
else
  q1q0(t+1) = q1q0t + 1;
00
01
10
11
inc=1
inc=1
inc=1
inc=1
inc=0
inc=0
inc=0
inc=0
Finite State Machine (FSM) representation
Notes: State diagram – replace Cnt by inc

## Slide 5: Modulo-4 counter in BSV
interface Counter;
method Action inc;
method Bit#(2) read;
endinterface
module moduloCounter(Counter);
Reg#(Bit#(2)) cnt <- mkReg(0);
method Action inc;
cnt <= cnt+1;
endmethod
method Bit#(2) read;
return cnt;
endmethod
endmodule
Modulo-4
counter
inc
read
2
An action to specify how the value of the cnt is to be set
State specification
Initial value

## Slide 6: Modules
A module in BSV is like a class definition in Java or C++
  It has internal state
  The internal state can only be read and manipulated by the (interface) methods
  An action specifies which state elements are to be modified
  Actions are atomic -- either all the specified state elements are modified or none of them are modified (no partially modified state is visible)
interface Counter;
method Action inc;
method Bit#(2) read;
endinterface

## Slide 7: Inside the Modulo-4 counter
inc
module moduloCounter(Counter);
Reg#(Bit#(2)) cnt <- mkReg(0);
method Action inc;
cnt <= cnt+1;
endmethod
method Bit#(2) read;
return cnt;
endmethod
endmodule
read
1
0
+1
cnt
If the user calls read and inc together, what value will read get?
The old value of cnt.

## Slide 8: Another example: GCD
When the machine keeps going on its own

## Slide 9: A hardware module for computing GCD
Euclid’s algorithm for computing the Greatest Common Divisor (GCD):
15 6
9 6 subtract
3 6 subtract
6 3 swap
3 3 subtract
0 3 subtract
answer
gcd (a,b) = if a==0 then b \\ stop
else if a>=b then gcd(a-b,b) \\ subtract
else gcd (b,a) \\ swap
Number of steps to compute the answer are input dependent

## Slide 10: GCD module
start
GCD
busy
getResult
ready
en
en
interface GCD;
method Action start (Bit#(32) a,
Bit#(32) b);
method ActionValue#(Bit#(32))
getResult;
method Bool busy;
method Bool ready;
endinterface
GCD can be started if the module is not busy; Results can be read when ready
data
result

## Slide 11: GCD in BSV
module mkGCD (GCD);
Reg#(Bit#(32)) x <- mkReg(0);
Reg#(Bit#(32)) y <- mkReg(0);
Reg#(Bool) busy_flag <- mkReg(False);
rule gcd;
if (x >= y) begin x <= x – y; end //subtract
else if (x != 0) begin x <= y; y <= x; end //swap
endrule
method Action start(Bit#(32) a, Bit#(32) b);
x <= a; y <= b; busy_flag <= True;
endmethod
method ActionValue#(Bit#(32)) getResult;
busy_flag <= False; return y;
endmethod
method busy = busy_flag;
method ready = x==0;
endmodule
Assume b /= 0
start should be called only if the module is not busy;
getResult should be called only when ready is true.

## Slide 12: Rule
rule gcd;
if (x >= y) begin x <= x – y; end //subtract
else if (x != 0) begin x <= y; y <= x; end //swap
endrule
parallel composition of actions
A rule is a collection of actions, which invoke methods
All actions in a rule execute in parallel
A rule can execute any time and when it executes all of its actions must execute
atomicity
A module may contain rules

## Slide 13: Parallel Composition of Actions & Double-Writes
Parallel composition, and consequently a rule containing it, is illegal if a double-write possibility exists
The BSV compiler rejects a program with potential multiple writes to a register, unless it can prove that there are never multiple writes
rule one;
y <= 3; x <= 5; x <= 7; endrule
Double write
Possibility of a double write
No double write
rule two;
y <= 3; if (b) x <= 7; else x <= 5; endrule
rule three;
y <= 3; x <= 5; if (b) x <= 7; endrule

## Slide 14: Calling the GCD module
start
gcd
busy
getResult
ready
GCD can be started if the module is not busy
invoke
getResult
GCD gcd <- mkGCD;
rule invoke;
if (!gcd.busy) gcd.start(10, 20);
endrule
rule getResult;
if (gcd.ready) begin
let x <- gcd.getResult; $display(x);
end
endrule
Results can be read when ready

## Slide 15: Guarded interfaces
Make the life of the programmers easier: Include some checks (busy, ready, ...) in the method definition itself, so that the user does not have to test the applicability of the method from outside
Guarded Interface:
  Every method has a guard (rdy wire)
  The value returned by a method is meaningful only if its guard is true
  Every action method has an enable signal (en wire) and it can be invoked (en can be set to true) only if its guard is true
not busy
ready
n
n
rdy
en
en
rdy
start
getResult
GCD
notice, en and rdy wires are implicit
n
interface GCD;
method Action start (Bit#(32) a, Bit#(32) b);
method ActionValue#(Bit#(32)) getResult;
endinterface

## Slide 16: GCD with and without guards
start
GCD
busy
getResult
ready
start
GCD
getResult
ready
busy
en
en
en
Interface without guards
Interface with guards
en
interface GCD;
method Action start (Bit#(32) a, Bit#(32) b);
method ActionValue#(Bit#(32)) getResult;
method Bool busy;
method Bool ready;
endinterface

## Slide 17: GCD with guarded interfaces implementation
module mkGCD (GCD);
Reg#(Bit#(32)) x <- mkReg(0);
Reg#(Bit#(32)) y <- mkReg(0);
Reg#(Bool) busy <- mkReg(False);
rule gcd;
if (x >= y) begin x <= x – y; end //subtract
else if (x != 0) begin x <= y; y <= x; end //swap
endrule
method Action start(Bit#(32) a, Bit#(32) b)
x <= a; y <= b; busy <= True;
endmethod
method ActionValue (Bit#(32)) getResult
busy <= False; return y;
endmethod
endmodule
Assume b /= 0
interface GCD;
method Action start
(Bit#(32) a,Bit#(32) b);
method ActionValue(Bit#(32))
getResult;
endinterface
if (!busy);
if (x==0);

## Slide 18: Code available:
https://github.com/VCA-EPFL/Feb21_sp2024

## Slide 19: Defining FIFOs and it’s uses

## Slide 20: FIFO Module Interface with Guards
not full
not empty
not empty
n
n
rdy
en
rdy
en
rdy
enq
deq
first
FIFO
interface Fifo#(numeric type size,
type t);
method Action enq(t x);
method Action deq;
method t first;
endinterface

## Slide 21: One-Element FIFO Implementation with guards
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x)
v <= True; d <= x;
endmethod
method Action deq
v <= False;
endmethod
method t first
return d;
endmethod
endmodule
not full
not empty
not empty
n
n
rdy
en
rdy
en
rdy
enq
deq
first
FIFO
if (!v);
if (v);
if (v);
Notice, no semicolon turns the if into a guard

## Slide 22: Guards vs Ifs
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action enq(t x);
if (!v) begin v <= True; d <= x; end
endmethod
versus
guard is !v; enq can be applied only if v is false
guard is True, i.e., the method is always applicable.
if v is true then x would get lost;
bad

## Slide 23: Rules with guards
Like a method, a rule can also have a guard
A rule can execute only if it’s guard is true, i.e., if the guard is false the rule has no effect
True guards can be omitted
rule foo if (p);
x1 <= e1; x2 <= e2;
endrule
guard

## Slide 24: Streaming the GCD module with guarded interfaces
outQ
inQ
rule invokeGCD;
gcd.start(inQ.first); inQ.deq;
endrule;
invoke
GCD
get
result
rule getResult;
let x <- gcd.getResult; outQ.enq(x);
endrule;
start
GCD
getResult
A rule can be executed only if guards of all of its actions are true
The guard of a rule is a conjunction of explicit guard and implicit guards. In the invoke rule, the explicit guard is true and implicit guards come out of gcd.start, inQ.deq and inQ.first

## Slide 25: Design Alternatives
f1
f2
f3
f1
f2
f3
fi
Combinational (C)
Pipeline (P)
Folded (F)
Reuse a block,
multicycle
Clock?
Area?
Throughput?
Clock: C < P ~ F
Area: F < C < P
Throughput: F < C < P
Multiple tokens in the pipeline

## Slide 26: Pipelined circuit
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1;
fifo1.enq(f1(inQ.first));
inQ.deq(); endrule
rule stage2;
fifo2.enq(f2(fifo1.first));
fifo1.deq; endrule
rule stage3;
outQ.enq(f3(fifo2.first));
fifo2.deq; endrule
When can stage1 rule fire?
Can tokens be left in the pipeline?
Can these rules execute concurrently?
- inQ has an element
- fifo1 has space
No
Depends upon the design of the queue. Later …

## Slide 27: Duplicate modules to increase throughput
outQ
inQ
invoke
GCD
get
result
start
GCD
getResult
start
GCD
getResult
Bookeeping queue to remember which unit token were sent to

## Slide 28: Duplicate modules to increase throughput
module mkGCD2(GCD);
GCD gcd1 <- mkGCD(); GCD gcd2 <- mkGCD();
Reg#(Bool) turn <- mkReg(True); FIFO#(Bool) bk<-mkFIFO;
method Action start(Bit#(32) a, Bit#(32) b);
turn <= ! turn; bk.enq(turn);
if (turn) gcd1.start(a,b);
else gcd2.start(a,b);
endmethod
method ActionValue#(Bit#(32)) getResult();
let turn = bk.first(); bk.deq();
if (turn) begin
let v <- gcd1.getResult(); return v; end
else begin
let v <- gcd2.getResult(); return v; end
endmethod
endmodule

## Slide 29
Folded “Combinational” circuits
Notes: (Andy) Changed course website to correct website

## Slide 30: Expressing a loop using registers
int s = s0;
while (p(s)) { s = f(s); } return s; C-code
sel = start
en = start | notDone
s
p
notDone
s0
f
sel
en
Such a loop cannot be implemented by elaborating/unfolding because the number of iterations is input-data dependent
A register is needed to hold s from one iteration to the next
s has to be initialized when the computation starts, and updated every cycle until the computation terminates

## Slide 31: Expressing a “loop computation” in BSV
sel = start
en = start | notDone
Reg#(t) s <- mkRegU();
rule step;
if (p(s)) begin s <= f(s);
end endrule
When the rule executes:
  the register s is read at the beginning of a clock cycle
  computations to evaluate the next value of the register and the sen are performed
  If sen is True then s is updated at the end of the clock cycle
A mux is needed to initialize the register
p
notDone
s0
f
sel
s
en
How should this circuit be packaged for proper use?
No “loop” syntax

## Slide 32: Takeaway
Sequential circuits are the essence of digital design; BSV provides a new and very different way of designing such circuits based on atomic actions and modules
Modules provide composability constrained by types
Modules also provide flexibility in implementation constrained by interface definitions
Next, we will study the concurrency issues in multi-rule systems