## Slide 1
Cost-effective control of SO2 emissions in Asia
Research paper based on linear programming
ENV-723
14.03.2023
Abdurahman Alsulaiman
ENV-723

## Slide 2
Summary
Abdurahman Alsulaiman
ENV-723
Interesting paper that discuss the possible ‘optimized’ paths in which human health and ecosystems could be protected from SO2 emissions with lower financial commitment by developing economies, in comparison to the ‘computed’ use of the best available technologies.
Significance

## Slide 3
RAINS-Asia model
Abdurahman Alsulaiman
ENV-723
Model structure
RAINS- Asia
Assumptions on applied emission control measures
Databases on fuel quality
Projections of energy use
SO2 emissions
Externally supplied data
The model makes it possible to quantify for all emission sources the impacts of emission- and fuel standards imposed by legislation.
The results are resolved over a spatial resolution of 1⁰ longitude x 1⁰ latitude (approximately 70 –110 km x 110 km)

## Slide 4
RAINS-Asia model
Abdurahman Alsulaiman
ENV-723
Formulation of the optimization problem
is the annual emissions of Sulphur dioxide of area I
is the annual emissions of Sulphur dioxide of large point j
, are the minimum and maximum emissions in region i
is the set of large point sources located in region i
Additional constraint in a given region. To set the upper limits to the emissions related to air pollution control plans developed by local or national authorities.

## Slide 5
RAINS-Asia model
Abdurahman Alsulaiman
ENV-723
Formulation of the optimization problem
For each source , emission control costs are described as piece-wise linear functions of the emission (reduction) level ().
RAINS-Asia estimates control costs based on technology- and country-specific cost parameters of individual technologies. The model calculates the marginal costs of each control option and constructs cost functions by ranking all available abatement options according to their marginal costs.
This methodology produces piece-wise linear curves, consisting typically of several dozens of segments for each source . Depending on the purpose of the analysis, the user can either employ cost curves starting from the uncontrolled situation or focus on emission control options that remain after implementation of certain emission and fuel standards, e.g. those imposed by current legislation.

## Slide 6
RAINS-Asia model
Abdurahman Alsulaiman
ENV-723
For each receptor point, Sulphur deposition is related to the decision variables and via a set of deposition constraints :
, which are the Sulphur deposition transfer coefficients for area- and large point sources,
which is the background Sulphur deposition in grid cell k,
which is the scaling factor to convert Sulphur deposition into units of acidity used in the quantification of critical loads
Formulation of the optimization problem

## Slide 7
RAINS-Asia model
Abdurahman Alsulaiman
ENV-723
A similar set of constraints is specified for ambient concentrations
Where
are SO2 concentration transfer coefficients for area- and large point sources,
is the background ambient concentration in grid cell .
Formulation of the optimization problem

## Slide 8
RAINS-Asia model
Abdurahman Alsulaiman
ENV-723
The Sulphur deposition transfer coefficients specify the proportion of total emissions from a source that is deposited at a receptor point . Similarly, the transfer coefficients for ambient concentrations determine to what extent emissions from a source contribute to ambient concentrations of SO2 at a receptor point
Background depositions and concentrations specify the contributions from natural sources (e.g. volcanoes) and sources outside the model domain. The RAINS model extracts this information from more detailed atmospheric dispersion models.
A user may specify deposition targets in relation to the sensitivity of ecosystems in each grid cell (the so-called critical loads for Sulphur) or may base the quantification of his ‘policy’ targets on other concepts. International or national air quality standards can be used to define constraints on ambient concentrations of SO2
Formulation of the optimization problem

## Slide 9
RAINS-Asia model
Abdurahman Alsulaiman
ENV-723
Formulation of the optimization problem
In the optimization problem, the objective function is to minimize total costs of Sulphur emission reductions subject to the constraints specified for deposition and/or concentration

## Slide 10
Model limitations and questions
Abdurahman Alsulaiman
ENV-723
Model limitations and questions
Comments
The model and algorithm was further described in earlier work done by the authors. Unfortunately, the cited work is inaccessible. Thus, there is a lack of clarity on the used algorithms.
With a model resolution of 1⁰ longitude x 1⁰ latitude (approximately 70 –110 km x 110 km), the authors had to apply a factor of 2-5x to average concentrations in urban areas. Given the large population concentration in urban areas, the multiplication factor provides a large range for the possible concentrations and thus a significant downside of using the model. (How would that be solved?)
Questions
Is the spatial resolution a function of the model or is it dependent on the external data?
Clarification on what piece-wise means?