## Slide 1: Paper Presentation
Yazan Lampert

## Slide 2: Computing architecture
compared to electronic approach, the implemented optical approach is “shallow-in-depth but broad-in-width network architecture”  large number of inputs
the work is based on diffractive elements on chip
chip based silicon photonics  dense structures compared to other platforms like Lithium Niobate

## Slide 3: Computing architecture
optical architecture is based on : William R. Clements, Peter C. Humphreys, Benjamin J. Metcalf, W. Steven Kolthammer, and Ian A. Walmsley, "Optimal design for universal multiport interferometers," Optica 3, 1460-1465 (2016)
representation of a unitary operator with beam splitters, phase shifters, and attenuators

## Slide 4: Components
the chip consists of:
encoder
matrix calculations
  unitary embedding
  diagonal embedding
  unitary embedding
decoder
hardware wise, encoder and decoder are identical: 64x8 inputs/outputs

## Slide 5: Components – encoder
64 grating couplers with specified distance of 127 um

## Slide 6: Components – encoder
64 grating couplers with specified distance of 127 um
input waveguides: 100 μm of width and 128 μm of height go through 64 tapers (50 μm of length and 2 μm of height
diffractive weights are mapped to length of slots
The diffractive encoding results will be received by 8 tapers (50 μm of length and 16 μm of height)

## Slide 7: Components – interference feature embedding

## Slide 8: Components – interference feature embedding

## Slide 9: Components – interference feature embedding
SVD: a matrix can be written as UDU: U is unitary matrix, D is diagonal matrix
reconfigurable interference embedding w/ 8 by 8 unitary matrix multiplication: 56 phase shifters
phase shifters: heaters with 320 μm vertical and 660 μm horizontal distances
electrical power supply: only 4 phase shifters share signal and ground
black trenches to decrease cross-talk

## Slide 10: Components – data readout

## Slide 11: Components – calibration
1% of light is coupled to grating couplers and light is collected by IR camera
3 stages for calibration and using phase shifters and variable optical attenuators VAO

## Slide 12: Stability over time
Problem: during operation, the heaters will change the whole temperature of the chip and ruin calibration  temperature controller was needed
With the temperature controller, calibration is maintained over 4 hours

## Slide 13: Prototypes
encoder/decoder and interference feature embedding were tested separated before the final chip

## Slide 14: Prototypes

## Slide 15: Optical setup

## Slide 16: Distributed computing architecture
in each path, 7 layers max
the “path” is defined by using the same chip but different weights

## Slide 17: Distributed computing architecture
in each path, 7 layers max
the “path” is defined by using the same chip but different weights
not clear:
In the prototype path
synthesizing chip, a maximum of 8 paths could be processed simultaneously. However, for more
paths, we can multiplex the same hardware several times to extend the path capacity.

## Slide 18: Taichi
sliding window for larger inputs
complex tasks are decomposed as multiple simple tasks, and each simple task is handled with a series of TEU clusters (marked as a “path”)
a TEU is a device with a given weights distribution  when moving from TEU-1 to TEU-2 only the weights will be changed

## Slide 19: Taichi
for training, structure is simulated in python: angular spectrum method for diffraction modeling and complex-field summation for interference modeling
nonlinear activation function the photodetection:

## Slide 20: CIFAR-10 dataset
single path is the “conventional” computing
they show using CIFAR-10 dataset that multipath can reach higher accuracy
the single-path network: each layer consisted of 16.8 thousand parameters, and with fewer than six layers
Multipath: each path had 20.9 thousand parameters and three layers to match the total parameter scale with the single-path one

## Slide 21: Comparison
“In energy efficiency calculation, the power consumptions for peripheral devices (a total of 260.32 Watts as listed above), and the on-chip power consumptions are counted”