## Slide 1
Tutorial 4
Werner Herr, Tatiana Pieloni, Léon Van Riesen-Haupt, Christophe Lannoy, Yi Wu, Raziyeh Dadashi
3rd October 2024
PHYS-448 Introduction to particle accelerators

## Slide 2
Thick and thin lenses
A thin quadrupole with
A drift of length followed by one thin quadrupole with
A thin quadrupole with in the centre, and drifts of length before and after it
Nothing; the only way is to consider the thick element.
The best way to approximate a thick quadrupole of length L by using the thin-lens approximation is to replace it with …

## Slide 3
is the correct answer.
Calculations in exercise 3 of this tutorial!
Thick and thin lenses
Thick quadrupole
Better approximation!

## Slide 4
The horizontal tune increases
Both the vertical and horizontal tunes change
The horizontal tune decreases
The maximum of the horizontal beta function will be smaller
Which of the following is false?
If you increase the strength of the horizontally focusing quadrupoles...
Betatron Tunes
Hint:

## Slide 5
Horizontal plane: Increasing the strength of the focusing magnets → Smaller beta function → The tune increases.
Vertical plane: Less focusing → The vertical tune decreases.
The horizontal tune does not decrease!
Betatron Tunes

## Slide 6
At the interaction points
At the horizontally defocusing quadrupoles
The β-function is constant everywhere
At the horizontally focusing quadrupoles
Where are the maxima of the horizontal β-function located in a circular collider?
Beta-functions

## Slide 7
In the middle of quadrupole magnets, where α=0, the β-function has an extreme value.
At the focusing quadrupoles
Beta-functions

## Slide 8
It will move on a smaller orbit
It will move on a larger orbit
Its orbit stays the same
It cannot be determined based on this information
Consider a particle with a momentum slightly higher than that of the design particle. How does its orbit differ compared to the orbit of the design particle? Assume
Dispersion (single particle dynamics)
Hint:

## Slide 9
It will move on a larger orbit
Dispersion (single particle dynamics)
Particular solution
Homogeneous solution
(betatron oscillation)
4.32
4.32
4.32
Larger momentum →Less bent by dipoles →Larger orbit

## Slide 10
There is no effect on the beam size
The horizontal beam size will be larger
The horizontal beam size will be smaller
Both the horizontal and the vertical beam sizes will be larger
Assuming that the horizontal and the vertical motions are uncoupled, at a location with non-zero dispersion:
Dispersion (beam dynamics)

## Slide 11
Horizontal plane: Dispersion is not zero → Particles with different momentum will have different bending radius → There will be a spread in the displacement → Beam size increases
Vertical plane: No dipoles → No dispersion → No effect on the vertical beam size
The horizontal beam size will be larger
Dispersion (beam dynamics)