## Slide 1
Constructive Computer Architecture
Sequential Circuits:
Circuits with state
Thomas – EPFL
Slides adapted from 6.1920 with Arvind
(Spring 23, MIT)
Notes: (Andy) Changed course website to correct website

## Slide 2: Plan for the day
Module 1: Folded Combinational Circuits
  Simple example: a naïve multiplier
Module 2: The different kind of memories

## Slide 3
Module 1: Folded “Combinational” circuits
Notes: (Andy) Changed course website to correct website

## Slide 4: Expressing a loop using registers
int s = s0;
while (p(s)) { s = f(s); } return s; C-code
sel = start
en = start | notDone
s
p
notDone
s0
f
sel
en
Such a loop cannot be implemented by elaborating/unfolding because the number of iterations is input-data dependent
A register is needed to hold s from one iteration to the next
s has to be initialized when the computation starts, and updated every cycle until the computation terminates

## Slide 5: Expressing a “loop computation” in BSV
sel = “start”
en = “start” | notDone
Reg#(t) s <- mkReg(s0);
rule step if (p(s)); s <= f(s); endrule
When the rule executes:
  the register s is read at the beginning of a clock cycle
  computations to evaluate the next value of the register and the sen are performed
  If sen is True then s is updated at the end of the clock cycle
A mux is needed to initialize the register
p
notDone
s0
f
sel
s
en
No “loop” syntax

## Slide 6: A more sophisticated example

## Slide 7: Multiplication by repeated addition
1101 (13)
1011 (11)
1101
x 1011
1101
+ 1101
+ 0000
+ 1101
10001111 (143)
b Multiplicand
a Multiplier *
mi = (a[i]==0)? 0 : b;
At each step we add either 1101 or 0 to the result depending upon a bit in the multiplier
We also shift the result by one position at every step
m0
m1
m2
m3
However, our addN circuit adds only two numbers at a time!

## Slide 8: Multiplication by repeated addition cont.
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Multiplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
At each step we add either 1101 or 0 to the result depending upon a bit in the multiplier
We also shift the result by one position at every step
Notice, the first addition is unnecessary because it simply yields m0

## Slide 9: Multiplication by repeated addition ckt
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Multiplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
add4
a1
m1
a2
m2
a3
m3
add4
add4
a0
m0
add4
0 0 0 0

## Slide 10: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) tp = 0; Bit#(32) prod = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0];
tp = sum[32:1];
end return {tp,prod}; endfunction
Combinational circuit uses 32 add32 circuits
We can reuse the same add32 circuit if we store the partial results in a register
Need registers to hold a, b, tp, prod and i
Update the registers every cycle until we are done

## Slide 11: Combinational 32-bit multiply
Long chains of gates
  32-bit multiply has 32 ripple carry adders in sequence!
  32-bit ripple carry adder has a 32-long chain of gates
  Total delay ?
  2(n-1) FAs?
  2*n FA delays, not nxn
  why?
Notes: Iteration I produces the ith bit of answer using only i FAs. The most significant 32 bits are produced in the last step which involves an additional 32FA delays

## Slide 12: Sequential Circuit for Multiply
Reg#(Bit#(32)) a <- mkRegU();
Reg#(Bit#(32)) b <- mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
rule mulStep;
if (i < 32) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] <= sum[0]; tp <= sum[32:1];
i <= i+1;
end endrule
state elements
a rule to describe the dynamic behavior
So that the rule has no effect until i is set to some other value
similar to the loop body in the combinational version

## Slide 13: Dynamic selection requires a mux
a[i]
a
i
a[0],a[1],a[2],…
a
>>
0
when the selection access pattern is regular one can use a shift operator (much fewer gates!)

## Slide 14: Replacing repeated selections by shifts
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= a >> 1; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], prod[31:1]}; tp <= sum[32:1];
i <= i+1; endrule

## Slide 15: Circuit for Sequential Multiply
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
s1 = start_en
s2 = start_en | !done
result (high)
31
0
add
0
0
32:1
0
<<

## Slide 16: Circuit analysis – Pros/Cons
Number of add32 circuits has been reduced from 31 to one, though some registers and muxes have been added
The longest combinational path has been reduced from 62 FAs to one add32 plus a few muxes
This sequential circuit will take 31 clock cycles to compute an answer
Notes: (Andy) longest combinational path was effectively 63 1-bit adders.

## Slide 17: Packaging Multiply as a Latency-Insensitive Module
Interface with guards
interface Multiply;
method Action startMul (Bit#(32) a, Bit#(32) b);
method ActionValue#(Bit#(64)) getResultMul;
endinterface
startMul
Multiply
getMulResult
ready
busy
en
en
64
32
32

## Slide 18: Multiply Module
Module mkMultiply (Multiply);
Reg#(Bit#(32)) a<-mkRegU(); Reg#(Bit#(32)) b<-mkRegU();
Reg#(Bit#(32)) prod <-mkRegU(); Reg#(Bit#(32)) tp <- mkReg(0);
Reg#(Bit#(6)) i <- mkReg(32);
Reg#(Bool) busy <- mkReg(False);
rule mulStep if (i < 32); Bit#(32) m = (a[0]==0)? 0 : b;
a <= a >> 1; Bit#(33) sum = add32(m,tp,0); prod <= {sum[0], prod[31:1]}; tp <= sum[32:1]; i <= i+1;
endrule
method Action startMul(Bit#(32) x, Bit#(32) y) if (!busy);
a <= x; b <= y; busy <= True; i <= 0; endmethod
method ActionValue Bit#(64) getMulRes if ((i==32) && busy);
busy <= False; return {tp,prod}; endmethod

## Slide 19: Circuit for Sequential Multiply
s1 = start_en; s2 = start_en | !done
bIn
b
a
i
== 32
0
done
+1
prod
result (low)
[30:0]
aIn
<<
31:0
tp
s1
s1
s1
s2
s2
s2
s2
s1
result (high)
31
0
add
0
0
32:1
0
<<
a
b
en
rdy
startMul
en
rdy
getMulRes
busy

## Slide 20: Module 2: Different kinds of memories

## Slide 21: It’s the memory, stupid
Richard L. Sites, DEC (Microprocessor Reports 1996)
  “I expect that over the coming decade memory subsystem design will be the only important design issue for microprocessors.”
Introduction to Comp Arch “speed of light”
https://safari.ethz.ch/architecture/fall2018/lib/exe/fetch.php?media=stupid_architects_look_to_future.pdf

## Slide 22: Most flexible: Vectors!
typedef struct { Bit#(5) src1; Bit#(5) src2; Bit#(5) dst} Req deriving (Bits, Eq, Show);
module mkAdderMachine(…);
FIFO#(Req) requests <- mkFIFO;
Vector#(32, Reg#(Bit#(32))) registers <- replicateM(mkReg);
rule a;
let req = requests.first();
requests.deq();
registers[req.dst] <= registers[req.src1] + registers[req.src2];
endrule
…
Vector#(6, GCD) q <- replicateM(mkGCD); //Parenthesis

## Slide 23: Register File 2 Read ports + 1 Write port
typedef Bit#(32) Word;
typedef Bit#(5) RIndx;
interface RFile2R1W;
method Word rd1(RIndx index) ;
method Word rd2(RIndx index) ;
method Action wr (RIndx index, Word data);
endinterface
Registers can be read or written any time, so the guards are always true (not shown)
rd1
rf
rd2
wr
en
data
index
data
index
data
index

## Slide 24: Register File - usage Reads are combinational
// rf was declared as a register file
rule example_use_rf;
Bit#(32) v1 = rf.rd1(0x1); // read value in register 1
Bit#(32) v2 = rf.rd2(0x10); // read value in register 16
rf.wr(0x11, v1+v2); // write the sum in register 17
endrule
rd1
rf
rd2
wr
en
data
index
data
index
data
index
rule nonexample; // DOES NOT WORK​
rf.wr(0x11, 1); // write 1 in register 17?​
rf.wr(0x12, 2); // write 2 in register 18?​
endrule

## Slide 25: Key properties of RF
Fixed number of ports
Return the value combinationally (read method directly returns the value)
Various sizes, typically < 5 ports, typically small

## Slide 26: SRAMs and BRAMs (memory on FPGAs)
A read takes at least a full cycle – therefore, a read is performed in two phases:
  A read request is sent
  After one or more cycles a response comes back
A write generates a response only if the write request asks for a response
Reading a response and sending a new request can be performed in the same cycle

## Slide 27: BRAM Interface – 1 port
interface BRAM1Port;
interface PORTIFC portA;
endinterface
interface PORTIFC;
interface Put request;
interface Get response;
endinterface
portA
BRAM
Response
interface Put;
method Action
put(BRAMRequest);
endinterface
interface Get;
method ActionValue#(DATA)
get();
endinterface
Request
Interface PORTIFC consists of two sub-interfaces Put and Get

## Slide 28: BRAM Interface – 2 port
interface BRAM2Port;
interface PORTIFC portA;
interface PORTIFC portB;
endinterface
portA
BRAM
Response
Request
portA
Response
Request

## Slide 29: BRAM: read/write request
Instantiation
BRAM1Port#(AddrType, Data) mem <-
mkBRAM1Server(defaultValue);
Read request
mem.portA.request.put(BRAMReq{write:False, responseOnWrite:False, address:addr, datain:?})
Write request
mem.portA.request.put(BRAMReq{write:True, responseOnWrite:False, address:addr, datain:val})
Read response
let x <- mem.portA.response.get();

## Slide 30: Summary: memory and their interfaces
Vectors
Register file
BRAM (1 or 2 ports)
DRAM
Flash

## Slide 31: Takeaway
Sequential circuits are the essence of digital design; BSV provides a different way of designing such circuits based on atomic actions and modules
Modules provide composability constrained by types
Modules also provide flexibility in implementation constrained by interface definitions
Next, we will study the concurrency issues in multi-rule systems