The Mechanics of Earthquakes and Faulting
Christopher H. Scholz
Chapter 1 : Brittle fracture of rock
Advances in Contact Mechanics, March 2, 2020
Noël Corentin, Roch Thibault

---
Mohr’s circle
Representation of the stresses
Principal stresses
%sigma_1 > %sigma_2 > %sigma_3
Increasing
%sigma_1
%sigma_3
%sigma_1 %sigma_1 %sigma_3 %sigma_3 %theta %theta

---
Macroscopic failure criteria
Coulomb criterion
Describe shear failure under compressive stress
Strictly empirical
Frictional criterion of cohesionless soils
Or with cohesion
%tau ~ = ~ %mu %sigma_n
%tau ~ = ~ %tau_0 + %mu %sigma_n
Rupture at an angle
%theta = %pi/4 - %phi / 2
The coefficient of internal friction
%mu = tan( %phi )
%sigma_1 [ (%mu^2 + 1)^{1/2} - %mu ] - %sigma_3 [ (%mu^2 + 1)^{1/2} + %mu ] = 2 %tau_0 ~ ~ if ~ %sigma_1 > C_0 [ 1-C_0 T_0 / 4 %tau_0^2 ]
The angle of internal friction
%sigma_3 = T_0 ~ ~ otherwise
%phi
%phi
%sigma_1 %sigma_1 %sigma_3 %sigma_3 %theta %theta

---
Macroscopic failure criteria
Griffith
Initiation of crack from the longest, most critically oriented Griffith crack
Based on microscopic failure mechanism
binom{(%sigma_1 - %sigma_3)^2 - 8 T_0 (%sigma_1 + %sigma_3) = 0 ~ if ~ %sigma_1 > -3 %sigma_3}{%sigma_3 = - T_0 ~ if ~ %sigma_1 < -3 %sigma_3}
%sigma_1 %sigma_1 %sigma_3 %sigma_3 %theta %theta

---
Macroscopic failure criteria
modified Griffith
Under compressive stress cracks would close and crack sliding would be resisted by friction
%tau ~ = ~ 2 T_0 + %mu %sigma_n
(%sigma_1 - %sigma_3)[(1-%mu^2)^{1/2}] = 4 T_0 + 2 %mu %sigma_3
%sigma_1 %sigma_1 %sigma_3 %sigma_3 %theta %theta

---
Macroscopic failure criteria
The modified Griffith criterion is equivalent to the Coulomb
     is the friction acting along preexisting cracks
%mu
%sigma_1 %sigma_1 %sigma_3 %sigma_3 %theta %theta

---
Effective stress
The effective stress law depends on the property under consideration
P(overline {%sigma_{ij}}) = P(%sigma_{ij} - %alpha p %delta_{ ij})
For strength, the behavior of cracks (often in frictional contact) is important
%alpha overline {%sigma_{ij}} = %sigma_{ij} - p %delta_{ ij}
%alpha = 1 - A_r / A
overline {%sigma_{ij}} = %sigma_{ij} - p %delta_{ ij}
The effective stress is expected to govern the macroscopic behavior as well:
%tau ~ = ~ %tau_0 + %mu ( %sigma_n - p )

---
Failure processes
Vast range of scales
Two principal modes of failure in lab experiments

---
Tensile failure
Tensile fracture form normal to the direction and parallel to the
%sigma_3
%sigma_1
Propagation within a cloud
 of microcracks : process zone
Only for isolated fracture
K_c prop sqrt( L )
%DELTA_{max} u prop L
r_p prop L
Multi-segment en echelon tension crack arrays
%DELTA_{max} u prop L^{ 1/n }

---
Shear failure in compression
Shear failure in compression
At Pc=cte, increasing σ1:
  - crack closure
  - elastic def
  - C’ onset of dilatancy
  - D’ passing from compactant to dilatant
  - peak stress before failure

---
Shear failure in compression Pc dependence
Shear failure in compression
Pc dependence

---
Shear failure in compression
Shear failure in compression
Shear localisation with AE location
Griffith criterion assumption: Macroscopic failure occur when the most critically crack propagates...
Whereas: rock fail by coalescence of crack + orientation of 30° from σ1
Lockner et al. (1991)

---
Shear failure in compression scale dependence
Shear failure in compression scale dependence
100 µm
2 m
2 km
Increasing scale decrease resistance because of inhomogeneities

---
Time dependent deformation: stress corrosion
Time dependent deformation: stress corrosion
Chemical reaction with environment:
 [Si-O-Si]+H2O <-> χ + [SiOH]
1) Occur at crack tip (strain enhanced), 2) replace Si-O by a H weaker bond
Freiman (1984)
Single crystal
Rocks brittle creep/static fatigue
v=AKIn

---
Brittle-Plastic/Ductile transition
Brittle-Plastic/Ductile transition
Ductility=rheology allowing for large strain and macro-homogeneous deformations, regardless of the mechanism
Plasticity=involve dislocation and diffusion mechanism
Brittle
Plastic
- Pc dependent - strain rate less dependent
- strain rate dependant
- Pc independent