## Slide 1: 9. Methods in Immunology
by Claudine Neyen and Bruno Lemaitre,
Ecole Polytechnique Fédérale de Lausanne
Web: http://ghi.epfl.ch

## Slide 2: Outline
9.1 Antibody-based tools
9.2 Identifying & quantifying antigens: ELISA and Western Blot
9.3 Cell-based assays to assess immune reactions: cytotoxicity and proliferation
9.4 Identifying, characterizing and purifying cell types: Flow cytometry and FACS

## Slide 3: Antibodies as tools to identify molecules
Antibodies (predominantly IgGs) are used for a variety of applications in research, diagnostics and therapy.
Antibodies can be polyclonal (recognize many epitopes of the same antigen) or monoclonal (recognize a single epitope of the same antigen)
Antibodies can be raised in different host species (e.g. mouse, rabbit, donkey, chicken, goat)
Polyclonal antibody
Monoclonal antibody
Antibodies from different species have species-specific Fc regions

## Slide 4: Antibodies as tools to identify molecules
Primary antibodies recognize a given antigen (e.g. mouse anti-ovalbumin IgG)
Secondary antibodies recognize the Fc portion of an antibody from a different species (e.g. goat anti-mouse IgG)
Antibodies can be coupled to fluorescent molecules (e.g. FITC, PE) or to effector molecules (e.g. enzymes like peroxidase)
Primary antibody:
mouse monoclonal anti-ovalbumin IgG
Secondary antibody:
Rabbit polyclonal anti-mouse IgG, coupled to a fluorophore

## Slide 5: ELISA (Enzyme-Linked ImmunoSorbent Assay)
What is it? | Microplate-based assay
What can it do? | Detect and quantify molecules (peptides, proteins, hormones,…) from complex mixtures (e.g. serum, cell culture supernatant)
How does it work? | Antigen is immobilized on a solid surface An antigen-specific antibody is added to detect the antigen The enzyme coupled to the antibody catalyses a coloured substrate (dye) reaction that can be quantified in a spectrophotometer
What does an ELISA look like? | 
Serial dilution of standard to generate standard curve
Samples with unknown quantity of antigen

## Slide 6: ELISA (Enzyme-Linked ImmunoSorbent Assay)
Direct versus indirect capture (‘sandwich ELISA’)
Direct versus indirect detection
Substrate reaction
Watch video of ELISA here

## Slide 7: Example: Cytokine levels in serum or tissue culture
Sample 1: resting T cells
Sample 2: activated T cells
Il-2 bound to coated antibody
Il-2 sandwich ELISA
Enzyme-coupled secondary antibody
IL-2 concentration (pg/ml)
Optical density
Standard curve
Sample 1: no IL-2
Sample 2: high IL-2
Resting
Activated
E
S
S
E

## Slide 8: Western Blot
What is it? | Solid-phase protein detection assay
What can it do? | Detect, quantify and characterize proteins and post-translational modifications (e.g. phosphorylation)
How does it work? | A protein mix is separated by gel electrophoresis and transferred to a nitrocellulose membrane (blot) An antigen-specific antibody is added to detect the antigen The enzyme coupled to the antibody catalyses a chemiluminescent reaction that can be visualized on film
What does a Western Blot look like? | 
Control protein for relative quantification
Protein of interest

## Slide 9: Western Blot

## Slide 10: Cell-based assays: Cr51 release assay to assess cytotoxicity
Used to assess CTL or NK cell function
CTLs or NK cells kill by releasing granzyme and perforin, which disrupts target cell membrane
Target cells are loaded with radioactive chromium
Target
+ 51Cr
CTL
Target
+ 51Cr
CTL
CTL
51Cr
No killing, 51Cr remains within cells
Killing, membrane lysis
Target cells release 51Cr into supernatant
Centrifugation
51Cr in cell pellet
51Cr in supernatant
Assess supernatant in scintillation counter

## Slide 11: Cell-based assays: proliferation
Cells are stimulated to induce proliferation
Radiolabelled nucleotides are added to the medium
Cells incorporate 3H-thymidine into their DNA during each round of replication
After several days, cells are harvested, lysed, and radioactivity is counted
Cells are labelled with a cytoplasmic fluorophore (e.g. CFSE)
Cells are stimulated to induce proliferation
At each division, daughter cells receive half the amount of the fluorophore
After several days, cells are fixed and their fluorescence measured by flow cytometry
Radioactive labelling
Fluorescent labelling
Resting T cell
+ IL-2 or anti-CD3
Addition of 3H-thymidine
Proliferating T cells accumulate radioactive nucleotide at each generation
Resting T cell
+ IL-2 or anti-CD3
Addition of CFSE
Proliferating T cells lose fluorescence at each generation
Divisions

## Slide 12: Example: T cell proliferation assay
Source: http://m.bdbiosciences.com/kr/instruments/accuri/sample_data/index.jsp
Notes: “If a fluorescent label is firmly attached to a cell, when the cell divides, the label will be shared equally between the two daughter cells. The number of cell divisions can be determined by following the dilution of the label as the cells divide. Two compounds have been used for this application - carboxyfluorescein diacetate, succinimidyl ester (CFDA-SE) and PHK26, an analogue of acridine orange with an N-linked 26 carbon alkyl chain. Because of its long alkyl side chain, PHK26 becomes anchored in the plasma membrane of cells. CFDA-SE diffuses into cells wherein it is converted to carboxyfluorescein succinimidyl ester; its reaction with amines stabilizes the fluorescent product in the cell. The method is best applied to resting lymphocytes before activation. These cells are homogeneous so that the fluorescent cells have a CV low enough to be able to resolve the different number of divisions. Cultured cells are more heterogeneous and the lack of resolution of the rounds of division makes interpretation of the data difficult.” http://flowbook.denovosoftware.com/chapter-8-cell-proliferation
http://m.bdbiosciences.com/kr/instruments/accuri/sample_data/index.jsp

## Slide 13: Flow cytometry: principle
What is it? | Laser-based single-cell fluidics technology
What can it do? | Characterize cells or particles
How does it work? | A single-cell suspension is passed in front of a laser Detectors measure how each cell scatters the laser beam fluorescence emitted from each cell
What does flow cytometry data look like? | 
Watch video of flow cytometry principles here
Sheath fluid inlet
Cell sample
(e.g. whole blood, cultured & stained cells, cells expressing fluorescent proteins, …)
Hydrodynamic focusing (cells line up in single file)
Fluorescence detector
Detector for forward/side scatter of laser beam
Laser beam
Outlet
Developed in 1954 by Walter Coulter
Notes: Nat Rev Microbiol. 2008 Nov; 6(11 Suppl): S7–15.
doi: 10.1038/nrmicro1998
Flow cytometry enables the examination of microscopic particles (such as cells) that are suspended in a stream of fluid which is termed sheath fluid. This fluid is focused hydrodynamically such that the cells flow in single file through a flow cell in which a beam of light (usually a laser) is focused. As the cells pass through the laser beam they scatter the light so that forward scatter (FSC) and side scatter (SSC) light is captured; this enables the size and granularity of the cells to be determined. In addition, if a cell is labelled with antibodies that carry a fluorochrome, as the cell passes in front of the laser beam the fluorochrome emits light at a wavelength that is higher than the single wavelength light source and which can be detected by fluorescent detectors. The flow cytometers that are in clinical use can analyse at least four fluorochromes simultaneously, in addition to the FSC and SSC. This is known as multiparametric analysis. The information that is generated is computer analysed so that specific analysis regions (known as gates) can be created, which allows the user to build up a profile of the size, granularity and antigen profile of the target cell population

## Slide 14: Flow cytometry: equipment
Laser light source
Fluidics input
(cells & sheath liquid)
Fluidics output (waste or collector if FACS)
Beam detectors
Computer & analysis software
Optics

## Slide 15: Flow cytometry with unstained cells
A cell passing through the laser scatters the beam
  Forward scatter (FSC) depends on cell size
  Side scatter (SSC) depends on cell granularity
Each event is counted and plotted on a scatter histogram
  Histograms show single-dimensional data of a cell population
  Scatter plots show multi-dimensional data
FSC
SSC
Laser
Forward scatter
Cell count
=
Side scatter
Forward scatter
Side scatter
Side scatter
Large cells with granular cytosol
= granulocytes
Small dense cells
= lymphocytes
Intermediary phenotype
= monocytes
Whole blood scatter plot

## Slide 16: Flow cytometry with fluorescence markers
Cells can be labelled with fluorophore-coupled antibodies
Fluorophores are chosen so as to have distinct emission spectra (e.g. ‘green’ and ‘red’ like FITC and Cy5)
A cell expressing the corresponding antigen(s) will bind fluorophore-antibody conjugates and emit fluorescence upon passing through the laser beam.
Laser

## Slide 17: Example: quantifying T cell populations from thymus
Cy5-coupled anti-CD4 antibody
FITC-coupled anti-CD8 antibody
Label cells with antibodies
Quantify cell-associated fluorescence
Plot cell counts
FITC (CD8)
Cy5 (CD4)
Cy5 (CD4)
Negative control Ab
Negative control Ab
FITC (CD8)
Gate on population of interest (T cells)

## Slide 18: Example: CD4+ T cell counts in HIV infection
Whole blood
Anti-CD45/CD3/CD4 antibody panel
CD45
SSC
CD4
CD3
‘gate’ on lymphocytes
CD4+ T cells
G
M
T
Notes: Rationale:
“When an individual’s CD4 level is 200 cells per μl, a patient is diagnosed as having AIDS19,53. At this point, there is a high probability that AIDS-related opportunistic infections and neoplasms will manifest5,54,55. The CDC recommends initiating prophylaxis against opportunistic infections when CD4 levels are <200 cells per μl56”
“Determination of the numbers of CD4 +ve lymphocytes in the peripheral blood is used to monitor patients with HIV infections (Mandy et al., 2002). The percentage of CD4 +ve cells can be obtained in a single tube by staining for CD45/CD3/CD4. A cytogram of SS versus CD45 is used to identify the lymphocytes and a cytogram of CD4 versus CD3 to enumerate the CD4+ve T cells.” http://flowbook.denovosoftware.com/chapter-7-some-clinical-applications

## Slide 19: FACS (Fluorescence-Activated Cell Sorting)
As cells pass through the laser beam, their characteristics are analysed
Cells are given a charge based on their fluorescence profile
Charged cells are deviated between deflector plates
FACS yields highly purified cell populations
Applications:
  purify cells expressing a GFP-tagged protein
  purify subpopulations of lymphocytes from blood
  purify bone marrow stem cells for transplantation
  …
-
-
-
+
+
+
+
-
-
-
-
Waste
Charge
Purified cells
-