## Slide 1
Lecture #8
Enzyme measurements
Aims:
Understand the basic principles and application-related significance of enzymes
Get introduced into enzyme screens via fluorescence-activated droplet sorting
Become familiar with your practical task

## Slide 3
Report & presentation
05.12.2025: presentations Groups A & B
12.12.2025: presentations Groups C & D
15.12.2025: submit reports
16.12.2025: individual Q&A
Final report: 8 – 10 pages
- introduction
- explain your design
- construction steps
- experimental analysis

## Slide 4
Your practical task
Uncharacterized sample
Target: Substrate
Value: Concentration
How…? Bioinstrument!
‘What can you measure with your setup?’
‘What kind of values do you get?’

## Slide 5
What are enzymes?
Sugars Amino acids Nucleotides Fatty acids
Enzymes
Ribozymes
Ochs, Raymond S., Biochemistry, 2022

## Slide 6
What are enzymes?
catalysis occurs in the active site
enzymes act specifically
Ochs, Raymond S., Biochemistry, 2022
https://www.sigmaaldrich.com/CH/de/product/sigma/f2756
https://www.caymanchem.com/product/28015
enzyme
substrate

## Slide 7
What are enzymes?
= biological catalysts
= increasing the reaction rate
= not affecting the thermodynamic equilibrium
ΔG0 = R T ln(Keq)
enzymes lower the activation energy
Ochs, Raymond S., Biochemistry, 2022
product
w/o enzyme
seconds
time
hours
+ enzyme
adapted from: Berg, Jeremy M., Tymoczko, John L., Gatto jr., Gregory J., Stryer Biochemie, 2017

## Slide 8
Why are enzymes of interest?
Enzymes = fundamental necessities for life
Ochs, Raymond S., Biochemistry, 2022
Research application
Industrial application
Medical application
… reactivity, specificity, kinetics
Bioinstrument: measures product formation or
substrate conversion

## Slide 9
Enzyme assays
monitoring formed product
monitoring consumed substrate
> what is preferred > why?
Punekar, N.S., Enzymes: Catalysis, Kinetics and Mechanisms, 2018
Mair et al., 2017 (doi: 10.1016/j.cbpa.2017.02.018)

## Slide 10
Enzyme assays
Fluorometric assays
= more sensitive vs. absorption-based methods
…however, providing a relative value
‘Which factors could vary between experiments?’

## Slide 11
Enzyme applications
Bunzel et al., 2018
(doi: 10.1016/j.sbi.2017.12.010)

## Slide 12
Substrate conversion
fluorescein
fluorescein di-β-D-galactopyranoside (FDG)
https://www.sigmaaldrich.com/CH/de/substance/fluorescein332312321075
https://www.sigmaaldrich.com/CH/de/product/sigma/f2756
cleavage in presence of an enzyme

## Slide 13
Substrate conversion
resorufin
resorufin di-β-D-galactopyranoside (RDG)
https://www.sigmaaldrich.com/CH/de/product/sigma/73144
https://www.caymanchem.com/product/28015
cleavage in presence of an enzyme

## Slide 14
Back to your practical task
4 groups and 2 different substrates
Enzyme: Beta-galactoside (EC 3.2.1.23)
Substrate: fluorescein di-β-D-galactopyranoside (FDG) (498 nm / 517 nm)
resorufin di-β-D-galactopyranoside (RDG) (571 nm / 585 nm)
‘What is your substrate concentration?’
‘What is the physiological role of your enzyme?’
‘What are (potential) applications?’
Final report

## Slide 15
How do enzymes work?
enzymes lower the activation energy
E + S ES E + P
kcat
k1
k-1
(1) Steady state: rate of ES formation = rate of ES destruction
(2) Enzyme concentration:
[E]total = [E] + [ES]
(3) Initial velocity (rate of reaction): v = kcat [ES]
Ochs, Raymond S., Biochemistry, 2022
E = enzyme
S = substrate
P = product
(4) Maximum velocity (maximum rate of reaction): vmax = kcat [E]total
Notes: Goal of the equation: you get to a steady state
It involves an enzyme E binding to a substrate S to form a complex ES that releases a product P regenerating the original form of the enzyme  The substrate is the starting molecule that attaches to the enzyme so the enzyme can chemically change it.
Activation energy (Ea) is the minimum amount of energy (thermal/kinetic, chemical bonds, concentration gradients or charges) required for a chemical reaction to occur.
V = reaction velocity (rate)
Vmax = maximum reaction rate (when the enzyme is saturated with the substrate)
where 𝑘_(+1) (forward rate constant), 𝑘_(−1) (reverse rate constant), and 𝑘_cat (catalytic rate constant) denote the rate constants,[14] the double arrows between A (substrate) and EA (enzyme-substrate complex) represent the fact that enzyme-substrate binding is a reversible process, and the single forward arrow represents the formation of P (product).
Start with equation + question: what do you think is determining how much product do we measure later on? A enzyme limiting, B substrate is limiting (B is the right choice, and that is why they should measure it) —> What limits the production of the product? —> There are other special reactions where the diffusion is the limit, where basically both the substrate and enzyme are largely in excess, but it just depends on how quickly it can diffuse (can sub this with a lot of the stuff)
Kcat is a kinetic constant in enzyme catalysis that describes how efficiently an enzyme converts substrate to product when it is saturated with substrate.  in synthesis, kcat is the number of substrate molecules that each enzyme active site converts to product per unit time under saturating substrate conditions.

## Slide 16
Michaelis-Menten equation
rate of ES formation = rate of ES destruction
k1 [E] [S] = k-1 [ES] + kcat [ES]
E + S ES E + P
kcat
k1
k-1
 Michaelis constant
(1)
(2)
[E]total = [E] + [ES]
(3)
v = kcat [ES]
v

## Slide 17
Michaelis-Menten equation
E + S ES E + P
kcat
k1
k-1
(4)
vmax = kcat [E]total
v
v
Ochs, Raymond S., Biochemistry, 2022

## Slide 18
Michaelis-Menten equation
E + S ES E + P
kcat
k1
k-1
v
case 1: [S] >>
v  enzyme is saturated
case 2: [S] <<
v  rate increases linearly with [S]
Ochs, Raymond S., Biochemistry, 2022
case 3: [S] =
v  enzyme is working 50% of capacity
/ mol/sec
maximum enzyme velocity

## Slide 19
Michaelis-Menten equation: Km
E + S ES E + P
kcat
k1
k-1
/ mol/L
v
v =
=
=
Ochs, Raymond S., Biochemistry, 2022
(mol/L)
Comparing different substrates (‘specificity’)
2.) low Km = enzyme has high affinity for substrate (reaches at low substrate)
3.) high Km = enzyme has lower affinity

## Slide 20
Enzyme kinetics and practical task
exemplary calculation:
‘How should the curve look like?’
substrate in excess, enzyme is limiting
‘Does the Km change?’
v / mol/min
[S] / mol
[E] is high
[E] is low
Km / mol

## Slide 21
Enzyme kinetics and practical task
exemplary calculation:
substrate in excess, enzyme is limiting
substrate is limiting, enzyme in excess
v / mol/min
[S] / mol
[E] is high
[E] is low
Km / mol
v / mol/min
[S] / mol
[E] is high
[E] is low
 Km / mol

## Slide 22
Some help…
Calibration curve  converts a bioinstrument signal into a known quantity
substrate concentration / uM
y = 76.95 x

## Slide 23
Enzyme assays
> direct assay vs. indirect assay (usually, coupled-enzyme assays)
> continuous assay vs. discontinuous/end-point assay
Punekar, N.S., Enzymes: Catalysis, Kinetics and Mechanisms, 2018
‘Difficulties with indirect assays?’

## Slide 24
Enzyme assays
> loss of linearity… why?
continuous substrate consumption
more product: increased backward reaction
formed product may inhibit the enzyme
product formation could change the pH
instability of enzyme or substrate
Punekar, N.S., Enzymes: Catalysis, Kinetics and Mechanisms, 2018

## Slide 25
Enzyme assays
Good practices
> apply concentrated stock solutions (why?)
> controls: enzyme minus & substrate minus
> consider: pH, ionic strength and temperature

## Slide 26
Enzyme applications
Directed evolution
new enzyme variants
desired activity
e.g., digesting unnatural substrates
Chiu & Stavrakis
(doi: 10.1002/elps.201900222)
Packer & Liu
(doi: 10.1038/nrg3927)

## Slide 27
Enzyme applications
Directed evolution
new enzyme variants
desired activity
e.g., digesting unnatural substrates
Vallejo et al., 2019
(doi: 10.1021/acssynbio.9b00103)

## Slide 28
References and further literature
https://doi.org/10.1007/978-981-13-0785-0
https://doi.org/10.1002/9783527806461
https://doi.org/10.1007/978-3-642-19624-9
https://doi.org/10.1007/978-3-662-54620-8
https://doi.org/10.1201/9781003029649
Ochs, Raymond S., Biochemistry, 2nd edition, Boca Raton, CRC Press, 2022
Punekar, N.S., Enzymes: Catalysis, Kinetics and Mechanisms, Singapore, Springer Nature, 2018
Bisswanger, Hans, Enzyme Kinetics: Principles and Methods, 3rd edition, Weinheim, Wiley-VCH, 2017
Fromm, Herbert & Hargrove, Mark, Essentials of Biochemistry, Berlin, Heidelberg, Springer, 2012
Berg, Jeremy M., Tymoczko, John L., Gatto jr., Gregory J., Stryer Biochemie, 8th edition, Berlin, Heidelberg, Springer Spektrum, 2017
Graphical illustrations were made with BioRender.com
Publications:
Mair et al., 2017 (doi: 10.1016/j.cbpa.2017.02.018)
Vallejo et al., 2019 (doi: 10.1021/acssynbio.9b00103)
Chiu & Stavrakis (doi: 10.1002/elps.201900222)
Obexer et al., 2016 (doi: 10.1093/protein/gzw032)
Bunzel et al., 2018 (doi: 10.1016/j.sbi.2017.12.010)
Packer & Liu, 2015 (doi: 10.1038/nrg3927)