## Slide 1: Details on mass meassurements

## Slide 2: A mass-spec has 4 tasks…
Create ions from analyte molecules
Separate the ions based on charge and mass
Select and fragment ions of interest to provide structural information (MS/MS)
Detect ions and determine their mass-to-charge (m/z)

## Slide 3: …and 5 parts
Sample inlet
Ionization
Mass analyser
Detector
Data acquisition
High or ultrahigh vacuum

## Slide 4
Sample inlet
Ionization
Mass analyser
Detector
Data acquisition
High or ultrahigh vacuum

## Slide 5: The basics of mass meassurements
Resolution
Mass accuracy
Isotopic distribution

## Slide 6: Resolution and mass accuracy
Resolution: The ability to discriminate molecules of similar mass
Mass accuracy: the ability to accurately measure the mass of a molecule

## Slide 7: Natural isotopic distribution: relative abundance of isotopes
Most elements occur in nature as a mixture of isotopes
Isotopes are atom species of the same chemical element that have different masses
They have the same number of protons and electrons, but a different number of neutrons (1Da)
The main elements occurring in proteins are CHNOPS

## Slide 8: Low vs high resolution
Average mass: equivalent to taking the centroid of the complete isotopic envelope
Monoisotopic mass: the mass of the first peak of the isotope distribution.
GluFib: EGVNDNEEGFFSAR
MW: 1569.6696 Da
Chemical Formula:
C66H95N19O26

## Slide 9: Mass meassurements
Average mass: equivalent to taking the centroid of the complete isotopic envelope
Monoisotopic mass: the mass of the first peak of the isotope distribution.
A
A+1
A+2
A+3
A+4
GluFib: EGVNDNEEGFFSAR
MW: 1569.6696 Da
Chemical Formula:
C66H95N19O26
Monoisotopic mass
(most abundants elements: 12C, 1H, 14N, 16O)
Signals related to lower abundance isotopes

## Slide 10: The distances between isotopic peaks reveal charge state
1002
m/z
1001
1003
Isotopic distribution
M = 1000 Da (not charged)
M = 1000 Da
[M+2H]2+ z = 2
m/z = 501 Da
1 Da
501.5
m/z
501
502
0.5Da
[M+1H]1+ z = 1
m/z = 1001 Da (Monoiso.)
M = 1000 Da
[M+3H]3+ z = 3
m/z = 334.33 Da
334.66
m/z
334.33
335
0.33Da

## Slide 11: The resolution drives mass accuracy and allows charge deconvolution
Charge state
Resolution
Mass accuracy

## Slide 12: Extra material

## Slide 13: The effect of electromagnetic fields on ions
The force applied to an ion in a field is governed by 2 laws:
Lorentz force law and Newton’s second law

## Slide 14: Mass analysers
Separate ions based on mass-to-charge (m/z) ratio
6 main types
Different analyser ☞different principle ☞ different characteristics ☞ different application
Time-of-Flight (TOF)
Ion Traps (IT)
Orbitrap
Quadrupole
Ion cyclotron resonance (ICR)
Magnetic sector
Field-free
Electric Field
Magnetic Field

## Slide 15: Quadrupole Theory
DC
Component
RF
Component
Resolving DC (a-value)
  RF amplitude (q-value)
Stable
Region
Unstable
Region
: DC voltage
: RF amplitude
: ion charge
: ion mass
: quadrupole radius
: RF frequency
4 parallel metal rods of opposite polarity
RF voltage applied between one pair of rods and the other
Direct Current (DC) voltage superimposed on the RF voltage
Ions can travel between the rods at given RF and DC voltages

## Slide 16: Isolation Using Quadrupoles
By varying the DC voltages and RF amplitudes, it is possible to select ions with different m/z values and to vary isolation width.
m/z
Resolving DC (a-value)
  RF amplitude (q-value)
Set DC voltage
Set RF amplitude
m/z
With Quadrupole Filtering
m/z
Full spectrum

## Slide 17: TOF
Consists of an acceleration region with a homogeneous electric field and a field-free drift region
Different m/z -> different velocities -> different time to reach the detector
Requires a pulsed ion source (ex. MALDI) or pulsing ion packages out of a continuous beam (pulser for ESI)
https://doi.org/10.1002/mas.21520

## Slide 18: TOF: reflector
Reasons for poor resolution
Different starting times
Different initial kinetic energies
Different starting locations
Different initial directions of motion

## Slide 19: Ion Traps (IT) 3D and 2D
Operate on the same plysical principles as quadrupoles
Filled with He
Trap
Isolate
Fragment (Collision Induced Dissociation, CID)
Quadrupole IT (aka 3D): Ions trapped in 3 dimensions, space charging effect
Advantages of Linear IT (aka 2D)
50x ion storage capacity
20x higher injection efficiency
simplicity of construction
http://dx.doi.org/10.1016/j.cplett.2016.11.011

## Slide 20: Orbitrap
Electrostatic field applied between 1 central spindle electrode and 2 halves of outer shell electrode
A short ion packet of one m/z enters the field tangentially, off-equator
Ions are squeezed towards the central electrode by increasing voltage on the central electrode
In the axial direction, ions are forced to move away from the narrow gap towards the wider gap near the equator
This initiates axial oscillations without the need for any further excitation
(“excitation by injection”)
After the voltage increase stops, ion trajectories become a stable spiral
r
φ
z
https://doi.org/10.1021/ac4001223

## Slide 21
The two outer electrodes are used to detect the image current produced by ions oscillating along the z-axis.
Many ions in the Orbitrap generate a complex signal whose individual frequencies are determined using a Fourier Transformation
z
Fourier Transform
Frequency 
Intensity
Data
Reduction
m/z
Intensity
Chart: 
Raw Transient
Amplitude
Time
Chart: 
Individual Ion Transients
Time
Amplitude

## Slide 22
Cost
100 - 4000
Normal
s
Very high
>100,000
Excellent
< 2 ppm
Orbitrap
100 – 4000
Normal
s
Low
Unit mass
Good
100 ppm
Quadrupole
100 – 4000
Fast
ms
Low
Unit mass
Good
100 ppm
Ion trap
Very wide
Very fast
s
High
20,000
Very good
5 ppm
TOF
m/z
Range
Scan
Rate
Resolution
(FWHM)
Mass
Accuracy
Mass
Analyzer
Characteristics of different mass analyzers
$$
$
$
$$$

## Slide 23: Disclaimer: No size fits all
Cost
Application
Question
Priorities