## Slide 1
COM-405: Mobile Networks
Lecture 4.0: MAC
Haitham Hassanieh
Laboratory of SEnsing
& Networking Systems

## Slide 2: Wireless Is Shared Medium
  interference from nodes in the network:
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors, microwaves, baby monitors, … ) interfere as well
X

## Slide 3: Wireless Interference
SNR is no longer the main metric!
Interference limited
Noise limited

## Slide 4: Multiple Access Protocols
Single shared broadcast channel
Two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
Multiple Access Protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit

## Slide 5: MAC Protocol Should be:
Efficient:
No idle channels, Maximize utilization, No Collisions
 No wasted resources
Fair:
No starvation, Equal distribution of resources
 based on what? Need?

## Slide 6: MAC Protocols
Reservation Based:
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Contention Based: (random access)
  channel not divided, allow collisions
  “recover” from collisions

## Slide 7: TDMA: Time Division Multiple Access
access to channel in "rounds"
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
Need some synchronization
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 8
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
Need guard bands
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable
FDMA: Frequency Division Multiple Access

## Slide 9: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence
Example codes: Gold Codes, Walsh Codes

## Slide 10: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 11: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2

## Slide 12: Code Division Multiple Access (CDMA)
Ideally, need codes to have good:
Auto-correlation properties:
Cross-correlation properties:
Need orthogonal codes:
For N users, length of code is exponential in N 
Near Far Effect Problem need power management

## Slide 13: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, these nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 14: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 15: Slotted ALOHA: efficiency
  Probability that a node transmits in a give slot:
  Probability that any node transmits without collision:
  To maximize , set
  N nodes
  Each node picks a slot uniformly at random to transmit in.

## Slide 16: Slotted ALOHA: efficiency
  Probability that a node transmits in a give slot:
  Probability that any node transmits without collision:
  To maximize , set
  N nodes
  Each node picks a slot uniformly at random to transmit in.

## Slide 17: Slotted ALOHA: efficiency
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
at best: channel
used for useful
transmissions 37%
of time!
!

## Slide 18: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 19: Pure ALOHA efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0,t0+1]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
even worse than slotted Aloha!

## Slide 20: CSMA/CA: Carrier Sense Multiple Access with Collision Avoidance
CSMA: listen before transmit:
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission

## Slide 21: CSMA/CA: Carrier Sense Multiple Access with Collision Avoidance
Contention Window (CW):
Sense, if channel idle, wait
Pick random number between
Wait slots (, then sense & transmit
Wait S for an ACK
If Collision:
If Success:

## Slide 22: CSMA/CA: Carrier Sense Multiple Access with Collision Avoidance
Throughput Efficiency
Data: 1500 bytes = 12000 bits
802.11n advertised rate: 300 Mbps
Data Packet Time
Overhead:
Actual Throughput:
80% Reduction in Throughput!!

## Slide 23
A
B
C
D
Distance
Signal
power
SINR threshold
Red signal >> Blue signal
X
Red < Blue = collision

## Slide 24
A
B
C
D
Distance
Signal
power
SINR threshold
Important: C has not heard A, but can interfere at receiver B
X
C is the hidden terminal to A

## Slide 25
A
B
C
D
Distance
SINR threshold
Important: X has heard A, but should not defer transmission to Y
X
X is the exposed terminal to A
Y
Signal
power

## Slide 26
Hidden and Exposed Terminal Problems
Critical to wireless networks even today

## Slide 27: IEEE 802.11
CTS = Clear
To Send
RTS = Request
To Send
D
Y
S
M
K
RTS
CTS

## Slide 28: IEEE 802.11
D
Y
S
X
M
K
silenced
silenced
silenced
silenced
Data
ACK

## Slide 29
WiFi Standards Medium Access: CSMA/CA
Carrier Sense Multiple Access with Collision Avoidance
802.11b, 802.11g, 802.11n, 802.11ac
Contention based with exponential backoff
RTS and CTS to avoid collisions

## Slide 30
DATA
ACK
AP
STA
E1
E2
E3
collision
decoding error
good transmission
WiFi Standards Medium Access: CSMA/CA

## Slide 31
RTS
CTS
DATA
ACK
AP
STA
E1
E2
E3
E4
collision
decoding error
good transmission
WiFi Standards Medium Access: CSMA/CA

## Slide 32
Orthogonal Frequency Division Multiple Access
Use OFDM: Assign different subcarriers to different users.
More efficient than FDMA since no guard bands are needed
Requires Time Synchronization
WiFi 6 802.11ax Medium Access: OFDMA

## Slide 33
CSMA/CA (802.11a/bg/n/ac)
Frequency
Time
OFDMA (802.11ax)
Frequency
Time
OFDM Subcarriers
Frequency
User 1
User 2
Collision
Orthogonal Frequency Division Multiple Access
Use OFDM: Assign different subcarriers to different users.
More efficient than FDMA since no guard bands are needed
WiFi 6 802.11ax Medium Access: OFDMA

## Slide 34
WiFi 6 802.11ax Medium Access: OFDMA

## Slide 35
1 User with 996 subcarriers
2 Users with 484 subcarriers each
4 Users with 242 subcarriers each
8 Users with 104 subcarriers each
16 Users with 52 subcarriers each
37 Users with 26 subcarriers each
OFDM Symbol with 1024 Subcarriers in 802.11ax
WiFi 6 802.11ax Medium Access: OFDMA

## Slide 36
STA
MURTS
MUCTS
DATA
BAR
AP
E1
E2
E3
E4
BA
collision
decoding error
good transmission
WiFi 6 802.11ax Medium Access: OFDMA+ CSMA/CA
Downlink: AP  Clients

## Slide 37
MURTS
MUCTS
DATA
AP
STA
E1
E2
E3
E4
TF
BA
BSRP
BSR
collision
decoding error
good transmission
WiFi 6 802.11ax Medium Access: OFDMA+ CSMA/CA
Uplink: AP  Clients

## Slide 38: MAC Protocols: Pros and Cons
Reservation Based:
  No Interference
  Fair
  Centralized
  Wasted resources
Contention Based: (random access)
  Distributed
  Good for bursty traffic
  Collisions
  Overhead
TDMA
FDMA
CDMA
OFDMA
CSMA
Alloha
Slotter Aloha
Token Passing
Polling
WiFi 6: OFDMA & CSMA