## Slide 1
COM-405: Mobile Networks
Lecture 8.0: Cellular Networks II
Haitham Hassanieh
Laboratory of SEnsing
& Networking Systems
slides shamelessly stolen from Prof. JP Hubaux & others

## Slide 2: Final Exam
Friday January 23, 2026 from 15:15 to 18:15 in CM 14
More details on Final Exam Later in the Semester.

## Slide 3: Cellular Networks Modeling
Infrastructure
  Base Station (BS)
  Fixed network
The most common model used for wireless networks is uniform hexagonal shaped areas, called cells.
Uniform cells with radius R.
Omnidirectional antennas
  radiate radio wave power uniformly in all directions in one plane
Base station with an omnidirectional antenna is positioned in the middle of each cell

## Slide 4: Area Coverage Planning
The received Signal-to-Noise (SNR) power by a receiver can be written as follows:
r – distance from receiver to base station
Pt – transmitted power
N – noise power
ct – constant =
– propagation constant
The minimum received SNR within the cell
  is the SNR at the cell border
  is given by
The radius of the coverage area (maximum range) is obtained as

## Slide 5: Cellular Networks Modeling
Infrastructure
  Base Station (BS)
  Fixed network
The most common model used for wireless networks is uniform hexagonal shaped areas, called cells.
Uniform cells with radius R.
Omnidirectional antennas
  radiate radio wave power uniformly in all directions in one plane
Base station with an omnidirectional antenna is positioned in the middle of each cell

## Slide 6: Area Coverage Planning – Effect of Fading
Considering shadowing and fading, the received SNR becomes random.
For a time availability of , we have
is assumed to be lognormal distributed with standard deviation dB.
is the outage probability (probability of failure to provide service)
To preserve the same cell coverage area, an extra fade margin, M, at the transmitter is needed.
The fade margin is then obtained as
    Q is the tail probability of the distribution of G (Q-function)
Once the radius is known, the number of cells required to cover the service area can be computed as:

## Slide 7: Frequency Planning – Frequency Reuse
An efficient way of managing the radio spectrum is to reuse the same frequency, within the service area, as often as possible.
Frequency reuse is possible thanks to the propagation properties of radio waves.
By properly setting the distance D, the same frequency can be used at two cells simultaneously.
D is called the reuse distance
R
R
R1
R2
D

## Slide 8: Frequency Planning – Frequency Reuse: 2 base stations
The worst SINR (Signal-to-Interference-Noise-Ratio) at the receiving mobile unit R1 (placed at the border of the cell) can be written as:
  Pt is the transmitted power for both base stations
With a required SINR minimum threshold of , we have
should be selected s.t.
R
R
R1
R2
D

## Slide 9: Frequency Planning – Frequency Reuse: B base stations
The same frequency can be used at B different cells.
The SINR at any receiver k (located in cell k) can be written as
    di - the distance from receiver k to base station i
    r - the distance from receiver k to base station k
    - the minimum required threshold of SNR
    N - noise power
With a proper choice of di, the minimum desired link quality can be achieved in all the links.

## Slide 10: Design of Wireless Networks – Fixed Channel Allocation for Frequency Reuse
Goal: for a certain available bandwidth, design a system with the highest possible capacity
For a hexagonal cell structure, cells are grouped in clusters of K (called the reuse factor) cells. Let R be the radius of the cell and D the distance between 2 base stations using the same frequency band
Let be the total number of orthogonal channels available.
Divide into disjoint groups
Assign each group to a different cell of a cell cluster.
Repeat the same distribution of channels in the other clusters.
i=2, j=0
i=2, j=1
i=1, j=1
i=1, j=0
Notes: The geometry of hexagons is such that K can only have values which satisfy K =(i+j)ˆ2 - ij

## Slide 11: Fixed Channel Allocation for Frequency Reuse – Example=7
Cells with the same number use the same channel

## Slide 12
Example: system of 32 cells with cell radius of 1.6km
Total frequency bandwidth supporting 336 traffic channels
Reuse factor (or cluster size) = 7
What geographic area is covered?
Total number of supported channels?
Solution:
Cell area = 6.65 km2
Covered area: 32*6.65=213 km2
Channels/cell = 336/7=48
Total channel capacity: 32*48=1536 channels
Same question for a system of 128 cells with cell radius of 0.8km. As before:
- total frequency bandwidth supporting 336 traffic channels
reuse factor (or cluster size) = 7
Solution:
Cell area: 1.66 km2
Covered area: 128*1.66=213 km2
Total channel capacity: 128*48=6144
Area of the hexagon:

## Slide 13: Capacity of Wireless Networks
The capacity of a wireless network is measured as the average number of simultaneous radio links supported by the system
  – total number of channels available
  K – reuse factor
indicates the maximum number of simultaneous connections in each cell
The area capacity is defined as follows:
is the cell area, e.g., the area of the hexagon is
users/cell
users/cell/unit area

## Slide 14: Quality(SINR) vs. Capacity() Tradeoff
Ideal case: high SINR and high
But the interference cause by frequency reuse is proportional with the reuse distance (distance between cells using the same channel, D)
  Large K
    -> large D -> High SINR
  -> Low
  Small K
    -> Small D -> Low SINR
    -> High
D

## Slide 15
A
R
D-R
D-R
D
D+R
D+R
D
First tier of co-channel cells for a cluster size of K=7
Note: the marked distances are approximations
Co-channel Interference

## Slide 16
If the transmit power of each base station is equal and α is the same throughout the coverage area, in a corner of a cell (most remote place from the base station in the cell) we have:
i0 - number of co-channel interfering cells
Di - distance from corner A to the center
of the interfering co-channel cell i
R - radius of a cell
K - cluster size (or “reuse factor”)
Co-channel Interference (cont’d)
A
R
D-R
D-R
D
D+R
D+R
D

## Slide 17: Co-channel Interference (cont’d)
Considering only the first layer of interfering cells and assuming that they are equidistant from the desired base station (all at distance D):
Approximation of the SINR at point A
A
R
D-R
D-R
D
D+R
D+R
D

## Slide 18: Directional Antennas in Wireless Networks
Directional antennas in wireless networks reduce the number of sites by allowing multiple BS to share the same site (120 degree site patterns for 1/3 reuse)

## Slide 19: Directional Antennas
The interference received at the mobile or the base station is dependent on the directivity of the antenna.
is the base station antenna gain.
More reduction in interference can be obtained through the use of narrower sector antennas.
Notes: Add more info about Sb

## Slide 20: Frequency Management
In all countries of the world, the licensed spectrum is managed by the government and (usually) leased to private operators
Regulation authority
  In Switzerland: Federal Commission for Communications, or ComCom; assisted by BAKOM
  In the US: FCC
  In the EU: each country still has its national regulation authority
Some political willingness (especially in the US) to reduce the role of the FCC  Dynamic Spectrum Allocation (cognitive radios) See the IEEE DySPAN conference (ieee-dyspan.org)

## Slide 21: Procedure for Frequency Allocation
2 main options
  Auction
  “Beauty contest”
    Usually fixed price
    Based on very detailed dossiers
    + : price pre-determined
    : temptation/suspicion of bribery; no price discovery

## Slide 22: Auctioning of Frequencies
Goal of auction: best possible allocation of frequencies to operators
Auctions are not meant to maximize the revenue for the government
Splitting of the frequency bands in blocks (e.g., of 2*5Mhz)
Issue: how to combine the auctioned blocks
Caps in high-value bands to avoid unfair behavior
Typical duration of allocation: 10 to 20 years
Minimal (or starting) price: xxx CHFrs/MHz*Year (defined by law in the case of CH)

## Slide 23: The case of Switzerland
3 main cellular operators (cellcos)
  Swisscom (state-controlled) has 60% of the mobile market
  Failed attempt of merger of Orange and Sunrise (in 2010)
  Orange  Salt Mobile (2015)
Good quality of service, but high prices
Swiss peculiarities: topography, super-tight emission regulations, site acquisitions (to set up base stations) often problematic, expensive manpower, high-revenue and change-averse population
All licenses already available at that time (800, 900, 1800, 2100 and 2600MHz) (re-)allocated as of 2013 or 2016 until 2028

## Slide 24: 5G Requires Low and High Frequencies
Use of low frequencies (e.g., 700, 800 et 900 MHz) in macrocells for service across the territory
Use of high frequencies (e.g., 3.5 GHz and higher) in small cells located in streets and buildings. This allows very high bandwidths over short distances
Source: amta.org.au

## Slide 25: Frequency Allocation for Operators In Switzerland (before 5G)
Note: This slide and some of the following adapted from a slide show kindly provided by Urs von Arx (BAKOM)

## Slide 26
5G New Mobile Frequencies

## Slide 27: 5G Frequencies Auction Results
700 MHz FDD | 0 | 20 MHz | 10 MHz | 30 MHz
700 MHz SDL | 0 | 0 | 10 MHz | 0
1400 MHz SDL | 0 | 10 MHz | 15 MHz | 50 MHz
2600 MHz TDD | 0 | 0 | 0 | 0
3500 - 3800 MHz TDD | 0 | 80 MHz | 100 MHz | 120 MHz
Surcharge in CHF | 0 | 94'500’625 | 89'238’101 | 195'554’002
 | Total Revenue: 379’292’728 CHF |  |  | 

## Slide 28: New Frequency Allocation for Operators in Switzerland

## Slide 29
https://map.geo.admin.ch/#/map?lang=en&center=2660000,1190000&z=1&topic=funksender&layers=ch.bakom.radio-fernsehsender,f;ch.bakom.standorte-mobilfunkanlagen&bgLayer=ch.swisstopo.pixelkarte-farbe&catalogNodes=funksender,403,408

## Slide 30: Association: Radio Resource Management problem
To each active terminal, we need to assign:
Transmit power
Waveform
Base station(s)
in order to maximize system utility
Association on the move: handover
Notes: RRM = Radio Resource Management

## Slide 31: Mobility management
While inactive
Tracking location of terminal and waking it up when necessary
  Location area updates
  Paging
While connection in progress:
Handover (or “handoff”, US English): timely selection (transition) of base stations based on signal quality measurements

## Slide 32: Handover types
Involved networks
Horizontal handover
  Within a single network of homogeneous radio access technology (RAT)
Vertical handover (or network selection)
  Between different networks, usually with heterogeneous RATs
2 families of handover
Hard handover
  Only one base station serving at a time
Soft handover
  Multiple base stations can simultaneously serve a mobile terminal

## Slide 33: Handover phases
Handover measurement & decision
Decides when and where to handover
Handover resource management
Radio resources available in the target base station?  allocate them
Handover execution
Reliable handover signaling (handshaking) procedure

## Slide 34: Handover decision

## Slide 35: Performance metric
Two main metrics
Handover failure probability
  Measures how often handover attempts fail
  Probability that signal quality is below the required value for more than a given time interval
Handover frequency (or rate)
  Measure of how frequently handover decisions are made
Tradeoff between handover frequency and failure probability

## Slide 36: Handover Decisions
Handover decision algorithms:
Algorithm I: instantaneous decision
  AP with the highest signal level is chosen at any sample point
Algorithm II: moving average
  Average over the last 10 samples determines the serving AP
Algorithm III: expected value
  AP is selected based on expected signal level rather than on measurements
1 km

## Slide 37: Handover Decisions
NHO: number of handovers
Pout: probability of outage

## Slide 38: Handover decision criteria
Received signal strength (RSS)
Detecting cell boundaries
Designed for (low capacity) macro-cellular systems (noise-limited)
Signal to interference ratio (SIR)
Efficient in micro-cellular environments (interference-limited)

## Slide 39: Example
Limitation of RSS-based handover in microcells
Rapid RSS level changes at street corners
RSS is not a good indicator of connection quality in microcells
BS1 and BS2 use the same frequency channel, while BS3 and BS4 utilize another one.

## Slide 40: Practical handover algorithm
Typical hard handover decision in LTE system
Hysteresis & time-to-trigger
This is the very basic handover mode in LTE

## Slide 41: Handover execution
It is mostly about signaling procedure
The system and mobile should reach agreement on
  Which Base station?
  Which waveform? (frequency, timeslot, code, etc.)
  Authentication
The signaling should be fast & reliable
  Handover is performed under difficult SIR conditions
Notes: SIR = Signal to Interference Ratio

## Slide 42: 5G Deployment Strategies
UE
5G-RAN
LTE-RAN
Non-Standalone (NSA)
LTE CORE
Data plane
Control plane
Supplement existing infrastructure investments
Control plane over LTE network
UE
5G-RAN
LTE-RAN
LTE CORE
5G CORE
UE
Standalone (SA)
No dependency on LTE
Fully exploit features provided by 5GC
Requires heavy infrastructure investments
https://networking.umn.edu/research-projects/5g-measurements
Notes: We now take a look at how carriers can deploy 5G. Two deployment models have been standardized to meet initial market requirement.
[click]
The first one is called as “Non-Standalone 5G or NSA”.
In NSA, [click] the user equipment is able to simultaneously connect to both the LTE and 5G base stations.
[click] Such dual connectivity allows carriers to roll out 5G faster with minimal infrastructure investment.
[click] However, all the control plane signaling -- including that of 5G -- is now performed over LTE.
[click] The second deployment model is called the Standalone 5G or SA. In this model, at any given time, the user equipment can connect to either LTE or 5G base station.
[click] Thus there is no dependency of 5G on LTE.
[click] Standalone 5G will allow carriers to fully exploit 5G core architecture’s features such as network slicing, etc.
[click] This model however requires heavy investment.
[next]

## Slide 43: 5G Deployment Strategies
UE
5G-RAN
LTE-RAN
Non-Standalone (NSA)
LTE CORE
Data plane
Control plane
UE
5G-RAN
LTE-RAN
LTE CORE
5G CORE
UE
Standalone Mode (SA)
No dependency on LTE
Fully exploit features provided by 5GC
Requires heavy infrastructure investments
“Main drop”
All current 5G deployments follow this model
Supplement existing infrastructure investments
Control plane over LTE network
https://networking.umn.edu/research-projects/5g-measurements
Notes: All current commercial 5G deployments worldwide follow the NSA model.
Next, let’s take a look at the commercial 5G landscape in the US.
[next]

## Slide 44: 5G Deployment Strategies
UE
5G-RAN
LTE-RAN
Non-Standalone (NSA)
LTE CORE
Supplement existing infrastructure investments
Control plane over LTE network
https://networking.umn.edu/research-projects/5g-measurements
Notes: All current commercial 5G deployments worldwide follow the NSA model.
Next, let’s take a look at the commercial 5G landscape in the US.
[next]

## Slide 45: Handoffs in NSA 5G
Tower
A
right
left
A
left
left
Tower/Panel
Active Radio Type
5G
A
right
5G
A
right
5G
B
4G
left
B
5G
A
4G
vertical
Tower
B
horizontal
vertical
5G to 5G
(same tower)
5G to 5G
(diff. tower)
vertical
vertical
Primitive
Combinational
Handoff
Type
Alice
https://networking.umn.edu/research-projects/5g-measurements
Notes: Consider Tower A is a 5G base station having two panels –
[click] one on the left side and
[click] another on the right.
[click]
Assume, Alice is connected to the left panel of tower A with 5G connectivity.
[click]
As she walks along the path, there is a handoff from the left-5G panel to the right-5G panel.
But since all the control signaling is happening over LTE, we observed such a 5G to 5G handoff associated with the same tower happens in two stages.
[click]
In the first stage, Alice experiences a handoff from 5G to 4G. Such a change in wireless technology is referred to as a vertical handoff.
[click]
in the second stage, another vertical handoff takes place but this time the radio type changes from 4G to 5G. Note, in this whole process, we were connected to the same tower A, but moved between panels.
[click]
The combination of the two primitive vertical handoffs resulted into a 5G to 5G handoff associated with the same tower.
In general, we define a combinational handoff as a type of handoff that corresponds to a high-level event that cannot be realized by a single primitive handoff type.
[click]
Now as Alice continues to walk towards another Tower, say B which again has two panels - left and right.
[click]
This time we see that she experienced a different type of combinational handoff – a 5G to 5G handoff involving two different towers A to B.
[click]
We observed this handoff event also consisted of two stages, the first one is when Alice having 5G connectivity moved from tower A to Tower B but with 4G active, resulting in a horizontal and vertical handoff occurring together as a single primitive handoff.
[click]
In the second stage, Alice -- who is now connected to tower B experiences a vertical handoff making her 5G connection active with tower B.
While these two scenarios illustrate two combinational handoffs, we observe that often times the primitive handoffs form more complex sequences and other 5G carriers also exhibit similar behavior. More details about handoffs observed in NSA 5G is explained in the paper.

## Slide 46: Handoff Analysis
UE experiences a total of 31 primitive handoffs (16 combinational) within 8 minutes!
Frequent handoffs causes frequent throughput fluctuations
Walking a 700m loop @ MPLS
mmWave
US East
Setup:
https://networking.umn.edu/research-projects/5g-measurements
Notes: Given the knowledge about the primitive and combinational handoffs in non-standalone 5G, we conduct an experiment with low mobility in Minneapolis area using Verizon’s 5G service. Holding the phone in our hand, we walk a loop of 700 meters spanning for roughly 8 minutes. While walking, we keep a downloading session active on the phone, and [click] log the perceived throughput and handoff activity events over time.
[click]
We find that the phone experiences a total of 31 primitive handoffs and bounces between 4G and 5G for 13 times.
While this may seem to be a side effect of non-standalone 5G, we still find a total of 16 combinational handoffs during this short walk. Such high number of handoffs especially while using millimeter wave is inevitable due to the small footprints of the 5G base stations.
[click]
Frequent handoffs results the throughput to highly fluctuate between 0 to 1Gbps.

## Slide 47: 5G Network
The 5G network consists of two subsystems.
  The Mobile Core and the Radio Access Network (RAN)
The Mobile Core provides and ensures Internet connectivity.
The RAN corresponds to a distributed set of base stations, named gNodeB (or gNB).

## Slide 48: Mobile Core
The Mobile Core is divided into a Control Plane and a User Plane.
  An architectural feature known as control and user plane separation

## Slide 49: Mobile Core: User Plane
The User Plane forwards traffic between the RAN and the Internet (i.e., IP packet forwarding)
  It is also responsible for policy enforcement, lawful intercept, traffic usage measurement, and QoS policing
Internet
Uplink
Traffic
Downlink
Traffic

## Slide 50: Mobile Core: Control Plane
The Control Plane contains the Access and Mobility Management Function (AMF) and the Session Management Function (SMF)
  The AMF is responsible for connection and reachability management, mobility management, access authorization, and location services.
  The SMF manages each UE session, such as IP address allocation.
Internet
Uplink
Traffic
Downlink
Traffic

## Slide 51: Radio Access Network (RAN)
The main function of the RAN is to transfer packets between the Mobile Core and a set of UEs.
  Deeply involved in the management and scheduling of radio spectrum

## Slide 52: RAN Processing Pipeline (Protocol Stack)
The packet processing pipeline integrated in 5G base stations
  Specified by the 3GPP standard
  Including both user and control plane components
It can also be viewed as the 5G protocol stack

## Slide 53: RAN Processing Pipeline: RRC
Radio Resource Control (RRC) layer
This layer is responsible for the establishment, configuration, maintenance, and release of radio bearers (logical channels between the base station and the UE).

## Slide 54: RAN Processing Pipeline: PDCP
Packet Data Convergence Protocol (PDCP) layer
This layer handles tasks such as header compression and decompression, ciphering and deciphering, and integrity protection and verification.

## Slide 55: RAN Processing Pipeline: RLC
Radio Link Control (RLC) layer
This layer is responsible for segmentation and reassembly, as well as reliably transmitting or receiving segments using error correction through automatic repeat request (ARQ).

## Slide 56: RAN Processing Pipeline: MAC
Media Access Control (MAC) layer
This layer addresses all real-time scheduling regarding physical resource allocation.

## Slide 57: RAN Processing Pipeline: PHY
Physical (PHY) layer
This layer, including the upper and lower PHY layers, manages (de)coding and (de)modulation.

## Slide 58: RAN Processing Pipeline: Radio Head
Radio head (RH)
The RH converts Radio Frequency (RF) signals into digital data and vice versa.

## Slide 59: Frequency Bands
Credit: Dallas Thomas/Gadget Hacks

## Slide 60: Frequency Bands
Credit: 6G Wireless Communications in 7-24 GHz Band: Opportunities, Techniques, and Challenges

## Slide 61: Scheduling
Centralized scheduling
  The base station manages physical resource allocation to UEs
OFDM modulation
  14 OFDM symbols = Time transmission interval (TTI) (or time slot)

## Slide 62: Scheduling
 | SCS [kHz] | Tslot [ms] | FR1 | FR2
0 | 15 | 1 |  | 
1 | 30 | 0.5 |  | 
2 | 60 | 0.25 |  | 
3 | 120 | 0.125 |  | 
4 | 240 | 0.0625 |  | 
5 | 480 | 0.03125 |  | 
6 | 960 | 0.015625 |  | 
 | SCS [kHz] | Tslot [ms] | FR1 | FR2
0 | 15 | 1 |  | 
1 | 30 | 0.5 |  | 
2 | 60 | 0.25 |  | 
3 | 120 | 0.125 |  | 
4 | 240 | 0.0625 |  | 
5 | 480 | 0.03125 |  | 
6 | 960 | 0.015625 |  | 
Subcarrier spacing
Slot duration
Numerology (𝜇) table

## Slide 63: Scheduling
MCS Index IMCS | Modulation Order Qm | Target code Rate x [1024] R | Spectral efficiency
0 | 2 | 120 | 0.2344
1 | 2 | 193 | 0.377
2 | 2 | 308 | 0.6016
3 | 2 | 449 | 0.877
4 | 2 | 602 | 1.1758
5 | 4 | 378 | 1.4766
6 | 4 | 434 | 1.6953
7 | 4 | 490 | 1.9141
8 | 4 | 553 | 2.1602
9 | 4 | 616 | 2.4063
10 | 4 | 658 | 2.5703
11 | 6 | 466 | 2.7305
12 | 6 | 517 | 3.0293
13 | 6 | 567 | 3.3223
MCS Index IMCS | Modulation Order Qm | Target code Rate x [1024] R | Spectral efficiency
14 | 6 | 616 | 3.6094
15 | 6 | 666 | 3.9023
16 | 6 | 719 | 4.2129
17 | 6 | 772 | 4.5234
18 | 6 | 822 | 4.8164
19 | 6 | 873 | 5.1152
20 | 8 | 682.5 | 5.332
21 | 8 | 711 | 5.5547
22 | 8 | 754 | 5.8906
23 | 8 | 797 | 6.2266
24 | 8 | 841 | 6.5703
25 | 8 | 885 | 6.9141
26 | 8 | 916.5 | 7.1602
27 | 8 | 948 | 7.4063
Modulation and Coding Scheme (MCS) Table 2

## Slide 64: 5G Frame Structure
5G introduces a novel frame structure, which is designed to be more flexible than its predecessors.
At the heart of this flexibility is the concept of numerology, labelled by μ.

## Slide 65: Duplex Modes

## Slide 66: Downlink Scheduling & Uplink Scheduling
Downlink scheduling
  The gNB has full knowledge on its queue and buffer
  The gNB needs Channel Quality Indicators (CQI) from UEs
Uplink scheduling
  The gNB has no knowledge on UEs’ queues and buffers
  The gNB knows the SNR of UEs

## Slide 67: Grant-Based Access & Grant-Free Access
Grant-based access
  A UE first sends a scheduling request to the gNB
  The gNB schedules and sends an uplink grant to the UE
  The UE transmits uplink data to the gNB
Grant-based access

## Slide 68: Grant-Based Access & Grant-Free Access
Grant-based access
  A UE first sends a scheduling request to the gNB
  The gNB schedules and sends an uplink grant to the UE
  The UE transmits uplink data to the gNB
Grant-free access
  The gNB always allocates a fixed number of resources to the UE
  The UE can directly transmit uplink data to the gNB
Grant-based access
Grant-free access

## Slide 69
SR: Scheduling Request
BSR: Buffer Status Report
Uplink Scheduling

## Slide 70: 5G Network Slicing
With its high capacity and low latency, 5G paves the way for new business models across various vertical markets
Credit: https://brunch.co.kr/@b047a588c11b462/90

## Slide 71: 5G Network Slicing
With its high capacity and low latency, 5G paves the way for new business models across various vertical markets
A 5G network is usually shared among many users and may not always be able to guarantee different requirements
Traffic Class | SST | Slice Type | Acronym
eMBB | 1 | eMBB | Enhanced Mobile Broadband
URLLC | 2 | URLLC | Ultra-Reliable Low-Latency Communication
mMTC | 3 | mIoT | Massive Internet of Things
 | 4 | V2X | Vehicle-to-Everything
 | 5 | HMTC | High-Performance Machine-Type Communication

## Slide 72: 5G Network Slicing
5G network slicing is a technique that divides a single physical network into several virtualized slices
Credit: What is network slicing? | https://www.youtube.com/watch?v=kqpo9LCspiI

## Slide 73: 5G Network Slicing
5G network slicing is a technique that divides a single physical network into several virtualized slices
Each slice can be designed to guarantee diverse service level agreements (SLA) as for throughput, latency, and reliability

## Slide 74: 5G Network Slicing
Network slices can be specialized to meet eMBB, URLLC, and mMTC and dedicated for specific services.
  eMBB: Live broadcasting, VR/AR
  URLLC: Automotive, health & wellness
  mMTC: Utilities & logistics

## Slide 75: Traditional RAN vs Open RAN
Traditional RANs focused on providing end-to-end service from a geographical perspective to millions of customers.
  These networks follow the 3GPP standard.
Credit: 5G Challenge - Traditional RAN vs. O-RAN | https://www.youtube.com/watch?v=RtYwkDYSBFU

## Slide 76: Traditional RAN vs Open RAN
Each operator tends to buy equipment for large markets from a single vendor (e.g., Ericsson and Nokia).
  It is unlikely to be interoperable with other vendors’ equipment.
Credit: 5G Challenge - Traditional RAN vs. O-RAN | https://www.youtube.com/watch?v=RtYwkDYSBFU

## Slide 77: Traditional RAN vs Open RAN
This end-to-end focus and single vendor solution raised significant barriers to new entrants.
  Traditional RAN typically relied on specialized hardware.
Credit: 5G Challenge - Traditional RAN vs. O-RAN | https://www.youtube.com/watch?v=RtYwkDYSBFU

## Slide 78: Traditional RAN vs Open RAN
Open RAN (O-RAN) represents an ongoing shift from closed, proprietary solutions towards open, modular, interoperable, multi-vendor solutions.
Credit: 5G Challenge - Traditional RAN vs. O-RAN | https://www.youtube.com/watch?v=RtYwkDYSBFU

## Slide 79: Traditional RAN vs Open RAN
O-RAN seeks to separate the hardware and software within the RAN segment of the network and to create open interfaces between these segments.

## Slide 80: Traditional RAN vs Open RAN
Allow more competition in building the hardware and software
Allow multiple vendor components to interoperate
  Like how keyboards, monitors, and mice can connect to any computer

## Slide 81: O-RAN Alliance
The O-RAN Alliance defines the specifications for Open RAN.
It disaggregates the RAN’s functionalities into central units (CUs), distributed units (DUs), and radio units (RUs), many of which can be virtualized or containerized.

## Slide 82: O-RAN Splitting
The RAN’s functionalities is split across centralized and distributed locations.
  The CU can be located near the Mobile Core.
  The DU is physically located at or near the RU.

## Slide 83: Cloud RAN (C-RAN)
Cloud RAN operates by centralizing the baseband processing functions of mobile networks into cloud-based environments
  Baseband processing functions, such as (de)coding and (de)modulation of radio signals, are centralized in a data center.
  The remote radio heads are distributed across various cell sites.
Credit: What Is Cloud RAN & How Does It Work? | https://nybsys.com/what-is-cloud-ran/

## Slide 84: C-RAN vs Traditional RAN
C-RAN centralizes baseband processing in a data center.
  Enable efficient resource utilization and easier management
Traditional RAN keeps baseband processing distributed across individual cell sites.

## Slide 85: C-RAN vs O-RAN
C-RAN centralizes baseband processing in a data center.
  Enable efficient resource utilization and easier management
O-RAN disaggregates the RAN components.
  Allow standardized, open interfaces between various network functions

## Slide 86: O-RAN & V-RAN & C-RAN

## Slide 87: RAN Intelligent Controller (RIC)
The RIC is a key component in the O-RAN framework
  It enables intelligent and dynamic control of RAN resources
Near-real-time (near-RT) RIC and non-real-time (non-RT) RIC
  The near-RT RIC manages RAN functions within milliseconds
  The non-RT RIC handles them with a longer time horizon

## Slide 88: RAN Intelligent Controller (RIC)
Intelligent Control
  Artificial intelligence
  Machine learning
  Optimize network performance
Credit: O-RAN ALLIANCE e.V | https://www.o-ran.org/

## Slide 89: RAN Intelligent Controller (RIC)
Intelligent Control
  Artificial intelligence
  Machine learning
  Optimize network performance
Open Interfaces (e.g., E2, A1)
  Open, standardized interfaces
  Interoperability between vendors
  Seamless integration

## Slide 90: RAN Intelligent Controller (RIC)
Intelligent Control
  Artificial intelligence
  Machine learning
  Optimize network performance
Open Interfaces (e.g., E2, A1)
  Open, standardized interfaces
  Interoperability between vendors
  Seamless integration
Dynamic Orchestration
  Adaptive resource allocation
  Adaptive Load balancing
  Automated configuration adjustments

## Slide 91: Open-Source 5G RAN Software
srsRAN: https://www.srslte.com/
Written in C and C++
GNU Affero General Public License v3.0
3GPP Release 17
Open Air Interface: https://openairinterface.org/
Written in C
OAI Public License V1.1
3GPP Release 17
Both offers software-based implementation of 5G RANs

## Slide 92: Open-Source 5G Mobile Core Software
Open5GS: https://open5gs.org/
Written in C
GNU Affero General Public License v3.0
3GPP Release 17
free5GC: https://free5gc.org/
Written in Golang
Apache License 2.0
3GPP Release 15
Both offers software-based implementation of 5G Mobile Cores

## Slide 93: A Real-World 5G System

## Slide 94: Open Projects
Build Real-World 5G Testbed
  Simplify complex 5G deployment tasks through an intuitive framework with minimal overhead, making it easier to scale, monitor, and troubleshoot
Comprehensive API for Private 5G Network Control
  Develop comprehensive API for private 5G networks to provide seamless control over user management, network slicing, and infrastructure optimization.
Offloading 5G Lower PHY Processing onto Digital Signal Processors (DSPs)
  Offload lower PHY processing onto dedicated DSPs to maximize efficiency and reduce latency
Customized RF Amplifier Circuit with Digital Predistortion
  Create a high-power amplifier with digital predistortion to boost software-defined radio integrated circuits for reliable 5G communication
Developing Interference-Resilient RAN for Robust 5G Connectivity
  Build a RAN that resists both self and external interference by exploring adaptive interference mitigation techniques for enhanced network stability

## Slide 95: Open Projects
Dynamic TDD Adaptation
  Enable real-time uplink/downlink slot reconfiguration in 5G to match changing traffic patterns, improving latency and throughput for dynamic, uplink-heavy applications.
Learning the Traffic Shaping Effects of 5G RAN
  Model how the 5G RAN transforms user traffic using AI, enabling RAN-aware analysis and predictive resource allocation.
Integrated Sensing and Communication
  Unify communication and environment sensing in 5G using AI to enable applications like motion detection, gesture recognition, and vehicular radar.
ILLIXR AR/VR Headset: Building and 5G Integration
  Build the open-source ILLIXR AR/VR headset and enable 5G-based edge processing by replacing the wired PC link with real-time wireless connectivity.

## Slide 96: Open Projects
SwissCat+ Robot 5G Integration and Testing
  Integrate and evaluate 5G connectivity for a chemistry lab robots, comparing Wi-Fi vs. 5G performance and enabling wireless charging and remote access in sealed reactors.
Network APIs for Core Management
  Design API-driven tools to automate user, slice, and infrastructure management in 5G core networks for scalable and flexible control.
Complete list of Projects and Description: