## Slide 1
Fundamentals of Electrical Circuits and Systems
Chapter 7: Three-Phase Circuits
Farhad Rachidi
École Polytechnique Fédérale de Lausanne
Lausanne, Switzerland

## Slide 2: Three-Phase circuits
Three-phase circuits allow an optimal use of the electrical networks both at the source and the charge.
They were proposed by Tesla in 1888 and commercially implemented for the first time at Niagara Falls on November 16, 1896.
Nicola Tesla (1856-1943),
Serbian engineer and physicist.

## Slide 3: Three-Phase circuits
Circuits powered by three sinusoidal sources out of phase with each other by 120o.
Symmetrical (balanced) source: the three source voltages have the same amplitude (rms value)
Balanced load: the three loads connected to the three-phase source consume the same active and reactive powers.

## Slide 7
?

## Slide 8: Balanced three-phase systems
Direct system:

## Slide 9: Balanced three-phase systems
Direct system:
Notes: Dans le sens des aiguilles d’une montre

## Slide 10: Balanced three-phase systems
Reverse system:
Notes: Dans le sens trigonométrique

## Slide 11: Homopolar system

## Slide 12: How to generate a balanced three-phase system?
Winding 1
Winding 2
Winding 3
Rotating
field

## Slide 13: How to generate a balanced three-phase system?

## Slide 14: How to generate a balanced three-phase system?

## Slide 15: How to generate a balanced three-phase system?

## Slide 16: How to generate a balanced three-phase system?
The total magnetic field generated by the 3 windings is a rotating field
A rotating field (produced by a magnet fixed on the rotor) will induce three-phase currents in the coils arranged symmetrically.
N
S

## Slide 17: Three-phase source (Wye connection)
R, S, T: phase conductors
N: neutral conductor

## Slide 18: Three-phase source Phase voltages and line voltages
Phase voltages
or line-to-neutral voltages:
with:

## Slide 19
Line-to-line voltages or
line voltages:
Relationships between phase voltages and line voltages
Three-phase source Phase voltages and line voltages

## Slide 20: Three-phase source Phase voltages and line voltages
Balanced three-phase system
Compared to phase voltages :
- Ahead of 30o,
- Module is times the one of phase voltages

## Slide 21: Three-phase source Line currents
Line currents:
Return current:

## Slide 22: Balanced three-phase load
A balanced three-phase load is characterized by three identical impedances (same module and argument) that we call the three phases of the user.
The three impedances can be connected in ‘wye (star)’ or ‘delta (triangle)’.

## Slide 23: Balanced three-phase load Wye connection

## Slide 24
Load voltages are the same as the line-to-neutral voltages
Balanced three-phase load Wye connection

## Slide 25: Balanced three-phase load Wye connection
Load currents:

## Slide 26: Balanced three-phase load Wye connection
The line current is equal to
load current and they have as module:

## Slide 27: Balanced three-phase load Wye connection
Thus in the case of a symmetrical source with balanced load, it is not necessary to connect the neutral point of the load to the one of the source.

## Slide 28: Balanced three-phase load Delta connection

## Slide 29: Balanced three-phase load Delta connection
Load voltages are the same as line voltages
Phase voltages:

## Slide 30: Balanced three-phase load Delta connection
Load currents:

## Slide 31: Balanced three-phase load Delta connection
Line currents:
with

## Slide 32: Summary Load quantities expressed in terms of line quantities

## Slide 33: Power in a three-phase systems
Delta load
Wye load
Instantaneous power:
Active and reactive powers:

## Slide 34: Power in balanced three-phase systems
Phase UX:
Phase VY:
Phase WZ:

## Slide 35: Power in balanced three-phase systems
=0
Instantaneous power has no pulsed component and
it is equal to the active power.

## Slide 36: Power in balanced three-phase systems Active, reactive and apparent power
In the same way:
being the rms values of the phase voltages and
phase currents
Complex apparent power:

## Slide 37: Power in balanced three-phase systems Active, reactive and apparent power
The powers expressed according to the line quantities:
Notes: Réduction momentanée de la puissance (démarrage de moteur)
Adaptation à un niveau ayant une tension sqrt(3)* plus élevée

## Slide 38: Power in balanced three-phase systems Delta-Wye conversion
Reminder: Equivalent tripoles

## Slide 39: Power in balanced three-phase systems Delta-Wye conversion
Equivalent tripoles
(equal impedances)

## Slide 40: Power in balanced three-phase systems Delta-Wye conversion
Both charges are equivalent provided that:
ou
Case of a capacitor bank:

## Slide 41: Example 1
A balanced three-phase load is connected in wye on a direct three-phase network at 6kV. The active power consumed is 48 kW, with a power factor of 0.94. Calculate the rms value of the line current. Repeat the calculation for the case where the load is connected in delta (with the same active power and the same power factor) and determine the rms value of the current flowing in the user's phases.

## Slide 42: Example 2
The phase impedance of a balanced three-phase load is formed of a resistor R = 10 Ω in series with a capacitor C = 185 μF. This load is connected in star to a 50 Hz network whose line voltage is 380 V. Determine the load voltage, the load current and the phase shift. Also calculate the active and reactive powers absorbed by each load and by the total load.

## Slide 43: Example 3
The active power and the apparent power consumed by a user having a balanced three-phase load are known: P = 20 kW and S = 30 kVA. The supply voltage (line) is 500 V. It is asked to calculate the impedance Z for the two connection modes (wye and delta).

## Slide 44: Example 4
A balanced three-phase load in delta is formed by putting in series a resistor R = 15 Ω and an inductor L = 32 mH. The network supply is 380 V (line voltage). Determine the active power P supplied by the network.

## Slide 45: Unbalanced three-phase systems
An unbalanced state occurs when the impedances of the load are not identical.
Such a situation is caused by the connection of single-phase loads connected either between a phase conductor and the neutral conductor, or between two phase conductors.
It can also intervene in case of disturbances such as short-circuit, lightning strike on a phase conductor, etc.

## Slide 46: Unbalanced three-phase systems Delta load

## Slide 47: Unbalanced three-phase systems Wye load
And the return current:

## Slide 48: Unbalanced three-phase systems Wye load
On the other hand, from Kirchhoff’s
law on currents :

## Slide 49: Unbalanced three-phase systems Wye load
By eliminating IN in the last two equations, we obtain the expression of the voltage UN :
with:
et
The impedance Zp is equivalent to putting in parallel all impedances of the charge, including the neutral conductor.
The current IN0 represents the return current in the neutral that we would observe if the impedance ZN of the neutral was zero.

## Slide 50: Unbalanced three-phase systems Wye load
In summary, we first calculate:
then:
et
and finally:
et

## Slide 51: Example: Unbalanced three-phase circuit
Between the line conductors R, S and T are connected two identical receivers whose active powers are P1=P2= 70 kW for a power factor of 0.92 (inductive). The third receiver connected between the T and R conductors has a power factor cos φ = 1 and an active power P3 = 30.4 kW. Determine the active power of the circuit, as well as the currents I1, I2, I3 and IR, if the line voltages are equal to 380 V.
R
S
T

## Slide 52: Example: Unbalanced three-phase circuit
Total active power:
R
S
T

## Slide 53
and
are in phase delay of an angle
is in phase with
φ1=arccos 0.92=23o relative to the corresponding voltages.
Example: Unbalanced three-phase circuit

## Slide 54
Example: Unbalanced three-phase circuit

## Slide 55: Example: Unbalanced three-phase circuit
R
S
T

## Slide 56: Symmetrical components method
A non-symmetric system can be broken down into three symmetrical systems: a direct system, an inverse system and a homopolar system.

## Slide 57: Symmetrical components method

## Slide 58: Symmetrical components method
denoting
and noticing that
the following relationships can be established

## Slide 59: Symmetrical components method
Denoting for simplicity
The system of equations is then written:
In matrix form:

## Slide 60: Symmetrical components method