## Slide 1
Fundamentals of Electrical Circuits and Systems
Chapter 4: AC Circuits 1
Farhad Rachidi
École Polytechnique Fédérale de Lausanne
Lausanne, Switzerland

## Slide 2: AC Circuits 1
Periodic functions
Sinusoidal quantities
Importance of AC circuits
Response of a linear circuit to a sinusoidal excitation
Example

## Slide 3: Periodic functions
A periodic function is a function that satisfies the relation f(t) = f(t + nT), where n is an integer and T is the period measured in unit of time.
x(t)
t
T

## Slide 4: Some definitions
Peak value or amplitude A :
maximum value of a periodic function
x(t)
t
T
A

## Slide 5: Some definitions
Peak-to-peak value :
maximum amplitude difference reached during a period
x(t)
t
T
Peak-to-peak

## Slide 6: Some definitions
Mean value:
x(t)
t
T
X

## Slide 7: Some definitions
Root Mean Square (RMS):
The rms value is always positive!

## Slide 8: Sinusoidal function

## Slide 9: Sinusoidal function: frequency
Frequency: Number of cycles per unit of time

## Slide 10: Sinusoidal function: frequency
The unit of measure of the frequency: hertz (Hz)
A hertz corresponds to the frequency of a periodic phenomenon whose period T is a second
Heinrich Hertz (1857-1894), German physicist. His work confirmed Maxwell's electromagnetic theory of light.

## Slide 11: Sinusoidal function: angular frequency or pulsation
Angular frequency or pulsation : ω
Unit rad/s

## Slide 12: Sinusoidal function: mean and rms values
Mean value
Rms value

## Slide 13: Rms value of a sinusoidal quantity:
Rms values

## Slide 14: Question
When we talk about a sinusoidal voltage of 230 V, it is about
Its peak value
Its mean value
Its rms value
None of the above
Notes: A

## Slide 15: Phase difference between two sinusoidal quantities
Phase difference between u(t) and i(t):
: voltage ahead of the current
: voltage behind the current
Note: we always consider the main value of the phase difference between -π and π.

## Slide 16: Heating of a resistor
When the voltage is sinusoidal, the average power dissipated in a resistor is equal to the integral, over a period of time, of the product of instantaneous current and voltage.

## Slide 17: Heating of a resistor

## Slide 18: Heating of a resistor

## Slide 19: Heating of a resistor
The rms value has been defined so that a continuous volt or 1 volt alternating produces the same heating in a resistor!

## Slide 20: Importance of AC circuits
Classical production of electrical energy provides a sinusoidal voltage: conversion mechanical energy - electrical energy: rotation of a coil placed in a magnetic field
B
w

## Slide 21: Importance of AC circuits
The only periodic function that has a derivative and a similar integral

## Slide 22: Importance of AC circuits
The sum of two sinusoidal functions is a sinusoidal function

## Slide 23: Importance of AC circuits
Fourier series development: representation of a periodic signal f(t) by sinusoidal functions
with

## Slide 24: Representation of a periodic signal by sinusoidal functions: Example 1
Rectified sinusoidal function:
2 first terms of the Fourier series:

## Slide 25: Representation of a periodic signal by sinusoidal functions: Example 1
Rectified sinusoidal function:
4 first terms of the Fourier series:

## Slide 26: Representation of a periodic signal by sinusoidal functions: Example 2
Triangular function:
4 first terms of the Fourier series:

## Slide 27
- Java Applet
http://www.jhu.edu/~signals/fourier2/index.html
Representation of a periodic signal by sinusoidal functions

## Slide 28: Importance of AC circuits
Fourier transform:
Generalization of the Fourier series
Frequency analysis of non-periodic signals

## Slide 29: Question
A sinusoidal voltage is applied to a linear circuit (R, L, C). What can be said of the currents and voltages in the circuit?
They are all sinusoidal
They are all sinusoidal with the same frequency (as that of the source)
They are all periodic
None of the above
Notes: A

## Slide 30: Response of a linear circuit to a sinusoidal excitation

## Slide 31: Response of a linear circuit to a sinusoidal excitation

## Slide 32: Response of a linear circuit to a sinusoidal excitation
All currents and all voltages of the circuit will be sinusoidal with the same frequency.

## Slide 33: Example
Evaluate rms value, frequency and period of total current i(t)
Analytically determine the current in each element and that provided by the source
Draw each of these currents

## Slide 34: Example
Evaluate rms value, frequency and period of total current i(t)
Analytically determine the current in each element and that provided by the source
Draw each of these currents
Calculation on the board!

## Slide 35: Example

## Slide 36: Example
This example shows us that the solution for a simple circuit is already laborious and would quickly become unusable for complex problems.
Phasors!