## Slide 1: EE-426 RF circuits design techniques 4. Intermodulation and distortion
David Ruffieux & Christian Enz
Swiss Federal Institute of Technology, Lausanne (EPFL), Switzerland

## Slide 2: Outline
Effects of nonlinearity
  Single tone input
    Harmonic distortion
    Gain compression
  Two-tone input
    Desensitization and blocking
    Cross modulation
    Intermodulation
    Third-order Intercept Point
Cascade of nonlinear stages

## Slide 3: Effects of Nonlinearity
Distinction between single tone input and multiple (two) tone input
Single tone input
  Harmonic distortion
  Gain compression
Two-tone input
  Desensitization and blocking
  Cross modulation
  Intermodulation

## Slide 4: Single Tone Input – Harmonic Distortion
If a sinusoid is applied to a nonlinear system, the output exhibits frequency components that are integer multiples of the input frequency
In the case of a 3rd-order memoryless and time invariant system given by where is the gain of the linear system, with , we get
Even order harmonics result from with even and vanish if the system has odd symmetry (fully differential)
Amplitude of the nth harmonic consists of terms proportional to and other terms proportional to higher powers of . Neglecting the latter for small the nth harmonic can be assumed proportional to

## Slide 5: Single Tone Input – Harmonic Distortion
Output still periodic and can therefore be expressed as a Fourier series
since signal has no dc component
since signal is an even function (i.e. )
Only odd-order harmonics since is an odd function (i.e. )
gain a1=Ymax/Xmax
Ymax
−Ymax
−Xmax
Xmax
A

## Slide 6: Single Tone Input – Gain Compression
The coefficient corresponding to the fundamental is given by
The compression rate is defined as

## Slide 7: Single Tone Input – Sign of and
The nonlinear characteristic can either be expansive () or compressive ()
Most voltage RF circuits are compressive whereas current mode circuits may be expansive
Expansive
(for example MOSFET current)
Compressive
(for example differential pair)

## Slide 8: Single Tone Input – 1-dB Compression Point
In most circuits of interest, the output is a compressive (or saturating) function of the input, i.e. the gain approaches zero for sufficiently high input levels. In this case coefficient . The gain for the fundamental is therefore a decreasing function of
The 1dB compression point is defined as the amplitude for which the gain drops by 1dB compared to the linear asymptote and can be approximated by

## Slide 9: Gain Compression: Effect on FM and AM Waveforms
FM signal carries no information in its amplitude and hence tolerates compression
AM contains information in its amplitude, hence distorted by compression

## Slide 10: Two-tone Input – Intermodulation Products
Input signal with two sinusoidal components at two different frequencies and
The output of a memoryless and time invariant nonlinear system defined by
The linear term is simply equal to the input multiplied by the gain
The 2nd-order term is given by

## Slide 11: Two-tones Input – Intermodulation Products
The 3rd-order term is given by
The 3rd-order term produces fundamentals, 3rd-order harmonics and 3rd-order intermodulation (IM) products at , , and
If and are close, IM products at and can be troublesome because they are close to and and might fall in the passband

## Slide 12: Two-tones Input – Desensitization and Blocking
Assuming that is the desired signal and is an out-of-band interferer
Looking only at the fundamental component at of the output signal
The 3rd term shows that the output signal at the desired frequency is affected by the interferer amplitude
In the case the interferer is much stronger than the desired signal ()
If (compressive nonlinear characteristic), the amplitude of the desired signal can be reduced by the interferer causing desensitization
A sufficiently large interferer can even reduce the amplitude to zero causing blocking (in RF the term blocking signal refers to interferers that can desensitize a circuit causing blocking)

## Slide 13: Desensitization and Blocking – Example
Consider an odd-order memoryless nonlinear system defined by
The output signal at for (no saturation) is given by
In the case the interferer is much stronger than the desired signal ()
Blocking occurs for (not consistent with assumption that and )
y
x
+16
−16
+2
−2

## Slide 14: Example of Gain Compression
Problem:
A 900-MHz GSM transmitter delivers a power of 1 W to the antenna. By how much must the second harmonic of the signal be suppressed (filtered) so that it does not desensitize a 1.8-GHz receiver having P1dB = -25 dBm? Assume the receiver is 1 m away and the 1.8-GHz signal is attenuated by 10 dB as it propagates across this distance.
Solution:
The output power at 900 MHz is equal to +30 dBm. With an attenuation of 10 dB, the second harmonic must not exceed -15 dBm at the transmitter antenna so that it is below P1dB of the receiver. Thus, the second harmonic must remain at least 45 dB below the fundamental at the TX output. In practice, this interference must be another several dB lower to ensure the RX does not compress.

## Slide 15: Two-tone Input – Cross Modulation
Another phenomenon that occurs when a weak signal and a strong interferer pass through a nonlinear system is the transfer of modulation (or noise) on the amplitude of the interferer to the amplitude of the weak signal
For example if the amplitude of the interferer is modulated by a sinusoid where is the modulation index (), assuming , the output is given by

## Slide 16: Two-tone Input – Cross Modulation
The desired signal at the output contains amplitude modulation at and
A common case of cross modulation arises in amplifiers that must simultaneously process many independent signal channels (e.g. in cable television transmitters). Nonlinearities in the amplifier corrupt each signal with the amplitude variations in other channels

## Slide 17: Example of Cross Modulation
Problem:
Suppose an interferer contains phase modulation but not amplitude modulation. Does cross modulation occur in this case?
Solution:
Expressing the input as , where the second term represents the interferer ( is constant but varies with time)
We now note that (1) the second-order term yields components at but not at ; (2) the third-order term expansion gives , which results in a component at . Thus,
The desired signal at does not experience cross modulation

## Slide 18: Two-tones Input – Intermodulation Products
Discarding the DC and harmonics we obtain the following IM products
And these fundamental components
2w1−w2=w1−Dw
Dw=w2−w1
Dw
Dw
Dw
2w2−w1=w2+Dw

## Slide 19: Two-tone Input – Intermodulation
The 3rd-order IM product of two strong out-of-band interferers may fall in the band of interest corrupting the desired weak signal
While operating on the amplitude, this effect degrades the performance even if the modulation is on the phase (zero-crossing points are still affected)
This phenomenon cannot be quantized by harmonic distortion
It requires another characterization called third-order intercept point (IP3)

## Slide 20: Example of Intermodulation
Problem:
Suppose four Bluetooth users operate in a room as shown in the above figure. User 4 is in the receive mode and attempts to sense a weak signal transmitted by User 1 at 2.410 GHz. At the same time, Users 2 and 3 transmit at 2.420 GHz and 2.430 GHz, respectively. Explain what happens.
Solution:
Since the frequencies transmitted by Users 1, 2, and 3 happen to be equally spaced, the intermodulation in the LNA of RX4 corrupts the desired signal at 2.410 GHz

## Slide 21: Intermodulation: Tones and Modulated Interferers
In intermodulation analysis:
  approximate the interferers with tones
  calculate the level of intermodulation products at the output
  mentally convert the intermodulation tones back to modulated components so as to see the corruption.

## Slide 22: Example of Gain Compression and Intermodulation
Problem:
A Bluetooth receiver employs a low-noise amplifier having a gain of 10 and an input impedance of 50 Ω. The LNA senses a desired signal level of -80 dBm at 2.410 GHz and two interferers of equal levels at 2.420 GHz and 2.430 GHz. For simplicity, assume the LNA drives a 50-Ω load.
(a) Determine the value of that yields a P1dB of -30 dBm.
(b) If each interferer is 10 dB below P1dB, determine the corruption experienced by the desired signal at the LNA output.
Solution:
(a) From previous equation,
(b) Each interferer has a level of -40 dBm (= 6.32 mVpp), we determine the amplitude of the IM product at 2.410 GHz as:

## Slide 23: Two-tone Input – Third-order Intercept Point
Allows to characterize nonlinearity by a two-tone test signal with each tone having equal amplitude
The amplitude of the fundamental and of the 3rd-order IM products at and at are given by
If , the input level for which the output components at and have the same amplitude as those at and is given by

## Slide 24: Two-tone Input – Third-order Intercept Point
IP3 can be measured at a single input level chosen well below the -1dB compression point, considering that
where is the input amplitude, the amplitude of the fundamental at and and the amplitude of the 3rd-order intermodulation products
If all signals levels are expressed in dBm, the input 3rd-order intercept point is equal to half the difference between the magnitudes of the fundamentals and the IM3 product at the output plus the corresponding input level

## Slide 25: Two-tone Input – Third-order Intercept Point
Because fundamental and IM3 components are both subject to compression, the IP3 is not a directly measureable quantity, but a point obtained by extrapolation of measurements made at low amplitude (as shown on the right)

## Slide 26: Comparison Between Single Tone and Two-tone
4.8 dB
9.6 dB
4.8 dB
slope=1
Pin [dBm]
Yn
IMn
[dBm]
P-1dB
(two-tone)
−1dB
Single tone −1 dB compression point:
Two tones IIP3:
slope=3
PIIP3
PHDI
P-1dB
(single-tone)
−1dB

## Slide 27: Effects of nonlinearity – Summary
Single signal leading to harmonic distortion
Single + one large interferer leading to desensitization
Single + two large interferers leading to intermodulation

## Slide 28: Examples: Differential Pair in Weak Inversion
The differential output current of a MOS differential pair biased in weak inversion (or with for bipolar) is given by
Taylor series expansion:
and hence:

## Slide 29: Examples: Differential Pair in WI – Single and Two-tone

## Slide 30: Examples: Differential Pair in WI – HB Simulations
These results are confirmed by harmonic balanced (HB) simulations (Aplac)
For large amplitude, the output becomes a square wave with Y1=4/p and Y3=4/(3*p)
0.1
0.3
1.0
3.0
10.0
-70
-60
-50
-40
-30
-20
-10
0
10
Dual tone analysis for diff. pair in weak inversion tanh(x)
IMx
dB
x=A/(2nUT)
0.1
0.3
1.0
3.0
10.0
-80
-70
-60
-50
-40
-30
-20
-10
0
10
20
Single tone analysis for diff. pair in weak inversion tanh(x)
Yx/dB
x=A/(2nUT)

## Slide 31: Examples: Differential Pair in Strong Inversion
The differential output current of a MOS differential pair biased in strong inversion is given by
Taylor series expansion (in linear range):
and hence:

## Slide 32: Examples: DP in Strong Inversion – HB Simulations
0.1
0.3
1.0
3.0
10.0
30.0
100.0
-140.00
-120.00
-100.00
-80.00
-60.00
-40.00
-20.00
0.00
20.00
40.00
alpha1 and alpha3 versus overdrive voltage
ax
(VG-VT0)/(nUT)
alpha1 (sim)
alpha1 (th)
alpha3 (sim)
alpha3 (th)
0.1
0.3
1.0
3.0
10.0
30.0
100.0
-10.00
0.00
10.00
20.00
30.00
40.00
50.00
IIP3 versus versus overdrive voltage
IIP3
dB
(VG-VT0)/(nUT)
IIP3 (sim)
IIP3 (th)

## Slide 33: Examples: MOST in Weak Inversion
In the case of weak inversion, the nonlinearity is a simple exponential function
Assuming the sinewave is applied to the gate and the transistor is in saturation with , we have
The output current can then be normalized to the quiescent value (value for )
The Fourier series of is then given by
where are the modified Bessel function of the 1st kind. The harmonics can be calculated and compared to the approximation obtained from the Taylor series

## Slide 34: Examples: MOST in Weak Inversion – Single Tone
Since the characteristic is expanding instead of compressing, the −1dB compression point becomes a +1dB expansion point

## Slide 35: Examples: MOST in Weak Inversion – Two-tone
The two-tone characteristics are plotted below and compared to the single tone

## Slide 36: Examples: MOST in Weak Inversion – HB Simulations
These results are confirmed by harmonic balanced (HB) simulations (Aplac)
0.3
1.0
3.0
-50
-40
-30
-20
-10
0
10
20
30
40
Dual tone analysis for MOS transistor in weak inversion exp(x)
IMx
dB
x=A/(nUT)
0.3
1.0
3.0
-60
-50
-40
-30
-20
-10
0
10
20
30
40
Single tone analysis for transistor in weak inversion exp(x)
Yx/dB
x=A/(nUT)

## Slide 37: Examples: MOST in Strong Inversion
In the case of strong inversion and assuming a long channel and constant mobility, the nonlinearity is a simple quadratic function. Therefore there is no 3rd-order term and hence the IP3 is infinite!
A more realistic model accounting for mobility reduction due to the vertical field is given by
For it can be written in simple normalized form as
Adding the sine wave at the gate it becomes
where parameter Q is typically 0.1 1/V

## Slide 38: Examples: MOST in Strong Inversion
The current can be rewritten as , where is the normalized bias current
The nonlinear behavior is then captured by the single function which can be developed in a Taylor series as
Usually and the coefficients can be simplified as

## Slide 39: Examples: MOST in Strong Inversion
The IIP3 and -1dB points are then given by

## Slide 40: Examples: MOST in Strong Inversion – HB Simulations
HB simulations (Aplac) for for ideal MOST in strong inversion
0.1
0.3
1.0
3.0
10.0
30.0
100.0
-140.00
-120.00
-100.00
-80.00
-60.00
-40.00
-20.00
0.00
20.00
40.00
alpha1 and alpha3 versus overdrive voltage
ax
(VG-VT0)/(nUT)
alpha1 (sim)
alpha1 (th)
alpha1 (as)
alpha3 (sim)
alpha3 (th)
alpha3 (as)
0.1
0.3
1.0
3.0
10.0
30.0
100.0
0.00
10.00
20.00
30.00
40.00
50.00
60.00
IIP3 versus versus overdrive voltage
IIP3
dB
(VG-VT0)/(nUT)
sim.
si
si asymptote

## Slide 41: Examples: Continuous Model of MOST– HB Simulations
HB simulations (Aplac) for for ideal MOST from weak to strong inversion
1.0m
10.0m
0.1
1.0
10.0
100.0
1.0k
-40.00
-30.00
-20.00
-10.00
0.00
10.00
alpha1 versus inversion coefficient
ax
IC
sim.
wi
si
si asymptote
1.0m
10.0m
0.1
1.0
10.0
100.0
1.0k
-120.00
-100.00
-80.00
-60.00
-40.00
-20.00
0.00
alpha3 versus inversion coefficient
ax
IC
sim.
wi
si
si asymptote

## Slide 42: Examples: Continuous Model of MOST– HB Simulations
HB simulations (Aplac) for for ideal MOST from weak to strong inversion
1.0m
10.0m
0.1
1.0
10.0
100.0
1.0k
0.00
10.00
20.00
30.00
40.00
50.00
IIP3 versus inversion coefficient
IIP3
dB
IC
sim.
wi
si
si asymptote

## Slide 43: Examples: Compact Model of MOST– HB Simulations
Simulations with complete EKV v2.6 model for a generic 0.18µm CMOS process
1.0m
10.0m
0.1
1.0
10.0
100.0
1.0k
0.00
10.00
20.00
30.00
40.00
50.00
IIP3 versus inversion coefficient
IIP3
dB
IC
VS=0 V
W=3µm
L=3µm

## Slide 44: Outline
General considerations
Nonlinearity and time variance
Effects of nonlinearity
  Single tone input
    Harmonic distortion
    Gain compression
  Two-tone input
    Desensitization and blocking
    Cross modulation
    Intermodulation
    Third-order Intercept Point
Cascade of nonlinear stages

## Slide 45: Cascade of Nonlinear Stages
The overall IIP3 is then given by
In worst case the above expression reduces to
As the 1st-stage gain increases, the overall IIP3 decreases
Considering only the 1st- and 3rd-order terms

## Slide 46: Cascade of Nonlinear Stages
RF amplifiers are usually narrow-band and therefore the components at , and are filtered and hence the bottom components can be neglected leaving only fundamental and IM3 terms
Fundamental terms
IM3 of 1st-stage
amplified by 2nd stage
IM3 of 2nd-stage
IM2 of 1st-stage
and IM2 of 2nd stage
2nd-harmonics of 1st-stage and IM2 of 2nd stage

## Slide 47: Cascade of Nonlinear Stages
Considering only the 1st- and 3rd-order terms, we have
Assuming that the 2nd harmonics and IM2 are filtered before the 2nd stage, the 2nd term in front of the 3rd-order term can usually be neglected, resulting in considering only the IM3 of the 1st and 2nd stage
The IIP3 for two stages is then given by
Finally the general relation for cascaded stages under the above assumptions is given by

## Slide 48: References
Most of this Chapter is based on Chapter 2 of Reference [1]
[1] B. Razavi, RF Microelectronics, 2nd ed. Pearson, 2012.
[2] T. H. Lee, The Design of CMOS Radio-Frequency Integrated Circuits, 2nd ed. Cambridge University Press, 2004.
[3] G. D. Vendelin, A. M. Pavio and U. L. Rohde, Microwave Circuit Design Using Linear and Nonlinear Techniques, 2nd ed. Wiley, 2006.

## Slide 49: Equation Size Definition
The L symbol used for phase noise comes from the Mathematica5 font