## Slide 1: Lab on cell-free synthetic biology
Week 3
Maerkl Lab
September 2025
EPFL

## Slide 2
Aim: Compare different protein production methods
Cell density measurement by spectrophotometry
Protein expression in E. coli
SDS-PAGE
Today’s tasks

## Slide 3
Cell density measurement by spectrophotometry
https://www.implen.de/od600-diluphotometer/od600/
Principle: Measure cell concentration by detecting light scattering from a cell suspension
1. Incoming light (600 nm)
2. Light scattering (prevents from reaching the detector)
3. Detector (sensor measures amount of light not scattered but that is transmitted, compared to blank)
4. Output: optical density (OD600 nm measures how much light scattered by cells)

## Slide 4
Cell density measurement by spectrophotometry
https://www.sigmaaldrich.com/deepweb/assets/sigmaaldrich/product/documents/426/740/sq-cell-density-od600-appnote-mk.pdf
OD600 nm correlates positively with cell density
Standard curve to determine unknown cell concentration, based on experimental data (OD versus cell count)
  Example factor: 1 OD600 nm equivalent to 8 x 10^8 E. coli cells/mL
Determine cell concentration:
Limitations:
Depends on light scattering, much less on light absorbance
  Beer-Lambert law not accurate for high-cell density
  Linear correlation fades with high cell concentration (>1.2 OD600 nm )
OD600 nm depends on optical setup (distance between the cell holder and instrument exit slit, monochromator optics, slit geometry, etc.)
  Different instruments give different results
OD600 nm depends on cell shape and size
  Similar cell concentrations of different cells may give the same OD600 nm

## Slide 5
Protein expression in E. coli
https://www.thermofisher.com/ch/en/home/life-science/cloning/cloning-learning-center/invitrogen-school-of-molecular-biology/molecular-cloning/transformation/competent-cell-selection-applications.html

## Slide 6
Protein expression in E. coli: basic requirements (on plasmid)
The Cell: a Molecular Approach. 2nd edtion, https://www.ncbi.nlm.nih.gov/books/NBK9850/
Transcription:
  Promoter: recognition site of RNA-polymerase
  Gene of interest
  Terminator: signals end of transcription

## Slide 7
Protein expression in E. coli: basic requirements (on plasmid)
Mahalik et al., 2014, https://microbialcellfactories.biomedcentral.com/articles/10.1186/s12934-014-0177-1/figures/3
Translation:
  Ribosome binding site (binding site of 16S RNA)
  Start codon(s)
  Stop codons

## Slide 8
Protein expression in E. coli: growth curve
https://www.thermofisher.com/ch/en/home/life-science/cloning/cloning-learning-center/invitrogen-school-of-molecular-biology/molecular-cloning/transformation/competent-cell-selection-applications.html
Highest protein production
yield: from mid-log phase (OD600 nm 0.4 for E. coli)

## Slide 9
Gel electrophoresis for proteins
https://www.excedr.com/resources/protein-gel-electrophoresis
Huang et al., 2018, https://www.researchgate.net/figure/Gelation-mechanism-of-polyacrylamide-hydrogels-Ammonium-persulfate-APS-acts-as-a_fig1_322216388
Definition: standard laboratory technique by which proteins are separated by size
(and charge)
Use: Compare production yields, confirm presence/absence, assess purity of sample,
proteomics, etc.
Principle (SDS-PAGE):
Sample preparation:
Gel: acrylamide + bisacrylamide + ammonium persulfate (APS, polymerizing agent)
-> polyacrylamide
Stacking gel: gel that stacks into a tight band before separation
Resolving gel: gel that separates proteins based on size
Sample buffer: buffer/solution where sample is (proteins)
Stacking gel buffer: buffer within stacking gel
Resolving gel buffer: buffer within resolving gel
Running buffer: buffer within gel tank
Note: other types of PAGE exist (native PAGE, 2D-PAGE, etc.)

## Slide 10
Gel electrophoresis for proteins
https://www.mblbio.com/bio/g/support/method/sds-page.html
Gel parameters:
Higher polyacrylamide concentration -> smaller pores -> resolve smaller proteins
Lower polyacrylamide concentration -> bigger pores -> resolve bigger proteins
Concentration of substrates and time of polymerization inversely correlates with pore size
Two systems:
Laemmli: less expensive, homemade ; Bis-Tris: higher resolution, better protein stability
 | Laemmli system | Bis-Tris system
Gel | polyacrylamide, Tris-HCl (pH 6.8 or 8.8), SDS | polyacrylamide (gradient), Bis-Tris (pH 6.4-7.0), SDS
Sample buffer | SDS, glycerol, tris-HCl, DTT, dye | SDS, glycerol, tris-HCl, DTT, dye (and more…)
Stacking gel buffer | Tris-HCl (pH 6.8) | Bis-Tris (pH 6.4-7)
Resolving gel buffer | Tris-HCl (pH 8.8) | 
Running buffer | Tris, glycine, SDS | MOPS/MES,Tris, SDS, EDTA
Stacking effect:
Proteins electrophoretic mobility between Cl- and glycine
Proteins compressed in narrow zone between the 2 fronts due to generated electric field
MES: better for small proteins, MOPS: better for big proteins