## Slide 1: Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl Sascha Nick et al.
September 29, 2025
Kamila & Laure

## Slide 2
The challenges today
Swiss human habitat: buildings, open spaces between buildings and daily mobility
Habitant related issues
High use of materials and Low circularity rate (6.9%)
Ecological habitat degradation
High mobility
travel time
Wellbeing outcomes are mixed
30% of Swiss energy use, 17% of GHGs (of total Swiss energy)
Every single one of these issues is a sustainability issue, affecting both current and future generations’ ability to meet their needs
accidents
air pollution
noise
Urban sprawl accelerating
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl

## Slide 3
Systems thinking
Different perspective on the public good
Cities
Communes
Builders
Investors
Farmers
Nature protection groups
Companies
Scientists
General population
Workers
Students
CO2 emission
Climate plans
Housing shortage
Low vacancies
Rising rental prices
urban sprawl
car dependency
increasing floor space per capita, wellbeing
needs and satisfiers
Sufficiency
use of public, private, or shared spaces
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl

## Slide 4
What is the link between housing resource use and resulting wellbeing?
What are the current dynamics?
What would be the resource impact, in terms of labor, building stocks, and energy, of transforming Swiss housing?
What is the potential to reverse urban sprawl?
Wellbeing & respecting planetary boundaries
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl

## Slide 5
Core proposal
Designing a system intervention to solve all major housing issues
Nationwide moratorium on new construction until 2100.
Focus on renovation
Limit on total building space
Reduced urban sprawl
The climate and biodiversity emergency - one decade
climate neutrality and wide-area ecosystem restoration - two decades.
This moratorium is complemented by additional policies to ensure coordination, renovation quality, de-sprawl and material reuse, availability of essential services, and support for people during the transition.
Low risk intervention
Limitation factor
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl

## Slide 6
Four interventions
Designing a system intervention to solve all major housing issues
Renovate to class A efficiency
Complete renovation to highest efficiency standards of the whole Swiss habitat in <20 years
Create shared spaces
Build a new culture of sharing spaces
Usage of materials
Reduce the need for new materials, extraction, embodied energy, reuse materials available from the deconstruction of existing urban sprawl
Positive feedback loop of de-sprawl
Available skilled labor, culture of sharing, and widespread reuse of materials reinforce each other, and accelerate the deconstruction of car dependency, based or reversing the process described above.
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl

## Slide 7
Four interventions
Designing a system intervention to solve all major housing issues
The actual implementation would require several additional policies and measures beyond the moratorium, with an illustrative overview in
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl

## Slide 8
Methods & Model Constraints
A stock-flow simulation model from 2025 to 2100
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Stock-flow simulation
Calculates
floor space per capita
Energy demand
Potential to reduce sprawl
OUTPUT
MODEL
Assumes
Renovation productivity improves when done at scale
INPUT
Keep track of
Changes/year
Low vacancy rates
Workforce
Long-term population growth

## Slide 9
Methods & Model Constraints
A stock-flow simulation model from 2025 to 2100
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Stock-flow simulation
MODEL
LEVERAGE POINTS
System rules
New building moratorium until 2100 changes the “rules of the game.”
Stops new construction and redirects.
System goals
Reorienting housing toward wellbeing within planetary boundaries rather
than maximizing growth.
System structure
Communities set neighborhood governance rules, shifting who has power.
Feedback loops
Breaking car-dependency and urban sprawl while creating reinforcing loops of
renovation, sharing, and reuse.
Material flows
Renovation, reuse of materials, and limits on per capita space (35 m²).
Reinforce each other
Changes = faster & more resilient

## Slide 10
Results
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Full renovation possible in 14-18years
Per capita space stabilizes at 35m2 (down from 76m2)
Energy use decreased to 82% by 2039
Urban sprawl reversible to 1935 or even 1885 levels
Deconstruction 20-30% of current floor space no longer needed

## Slide 11
Results
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Full renovation possible in 14-18years
Per capita space stabilizes at 35m2 (down from 76m2)
Energy use decreased to 82% by 2039
Urban sprawl reversible to 1935 or even 1885 levels
Deconstruction 20-30% of current floor space no longer needed
Existing workforce
Proven technologies
Demand-side focus
Sufficiency + sharing
Builds resilience
Energy, mobility, ecosystems
Cultural redefinition
From growth to sufficiency

## Slide 12
Policy examples
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Equity & sufficiency
Governance & Trust
Mobility shift
Supply resilience
Needed to make this happen.

## Slide 13
Conclusion
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Technically & Economically feasible
With technology and workforces of today
Low risk transformation
Reduces the risk instead of increasing it.
High resilience transformation
Moves our culture from endless growth to sufficiency and wellbeing with planetary boundaries.
Demand-side sufficiency = wellbeing + climate action

## Slide 14
Thank you for
your attention
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl

## Slide 15
Discussion
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
How to manage relocation during renovations?

## Slide 16
Discussion
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Could this approach transfer to other countries?

## Slide 17
Discussion
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Can shared spaces really improve wellbeing in Swiss culture?

## Slide 18
Discussion
Systems perspectives on transforming Swiss housing by 2040: wellbeing, shared spaces, sufficiency, and de-sprawl
Social & Political feasibility of building moratorium?