## Slide 1: Soil science Computer lab 3
Guo-Shiuan Lin (Steven)
URBES lab, EPFL

## Slide 2: Schedule of computer lab
Date | Subject
13. Oct | Introduction
20. Oct | Break
27. Oct | Exercise 1: Pedotransfer functions
3. Nov | Exercise 2: Soil water retention curves
10. Nov | Report/Academic writing
17. Nov | Exercise 3: Richards equation
24. Nov | Bonus exercise: Soil data challenge
1. Dec | Group work and consultation time
5. Dec | Report submission deadline

## Slide 3
Can you find these values in the figure?
Saturated water content
Porosity
Residual water content
Notes: Field capacity (the potential matric where water content starts to drop)
Wilting point (the potential matric where water content drops to residual zone, close to the residual water content)

## Slide 4: How was the fitting done?

## Slide 5: Fitting the soil water retention curve with different models
Measurements
Fitted line
x_curve = np.logspace(-3,5,1000)
Which model is better?
Change this line of code to:

## Slide 6
Uncertainty

## Slide 7
How many of these are compulsory inputs for using scipy.optimize.curve_fit()?
A. Function/model used for fitting
B. X values
C. Y values
D. Bounds for the parameters
Notes: Ans: Except D

## Slide 8: Why do we need to set the bounds?
To get realistic values
To save some computation time
Notes: Save time

## Slide 9: Soil science
Observing and measuring the soil
Understanding the physical processes
Parameterizing the processes (i.e., equations)
Validating the equations
Modeling and predicting

## Slide 10: Assignment 3: 1D infiltration model

## Slide 11: Infiltration, runoff, and groundwater recharge
https://www2.hawaii.edu/~dennis/GeoBook/chapter_7/balance.htm

## Slide 12
Richard’s equation
How water infiltrate in unsaturated soils
Movement of water

## Slide 13
Richard’s equation
2 common expressions of Richard’s equation
Moisture-content form
(mass balance)
Chain rule
Specific moisture capacity
Darcy’s law
Pressure-head form

## Slide 14
Richard’s equation: how it is done in the code
def RichardsModel(psi,t,dz,n,p,vg,qTop,qBot,psiTop,psiBot)
return dpsidt
def CFun(psi,pars)
def KFun(psi,pars)
Use scipy.odeint to Integrate
Get the variables at different time steps

## Slide 15: 1.Download Richards Equation.ipynb and vanGenuchten.py 3.Put in the same folder 4.Follow the video tutorial together (16 mins)

## Slide 16: How many soil types to choose? (Tips: in the vanGenuchten.py file)
Notes: 6

## Slide 17: To change the soil type
p=vg.SoilType()

## Slide 18
How are upper and lower boundary conditions defined and what they are?
Upper boundary
Lower boundary
Flow in (Infiltration)
Flow out (discharge)

## Slide 19
How many levels (z) and time steps?
50
101

## Slide 20: Start to run the notebook
The first group to achieve these will get a prize
Get Figure 1, 2, 3 for the soil type vg.GuelphLoamDrying() with simulation period (t) up to 100 days
Correctly explain to me what are the different lines in Fig 2 (vertical profile)
Correctly explain to me, in Fig 3 (temporal profile), when does ‘change in storage’ start to reduce? Why does it become zero at the end?

## Slide 21: 知識是生命的土壤
Knowledge is the soil of life
zhi shi shi sheng ming de tu rang
Science du sol 2025

## Slide 22
Where is the bottom of the soil?
Which is the curve (t=0)?
Notes: the top of the soil column 5 meters above the ground is height (elevation)=5

## Slide 23
for i in range(0, t.size, 10):
pl.subplot(121)
pl.plot(psi[i,:],z)
How to adjust the plot?
1.Change frequency to plot a line to, e.g., every 10 timesteps
pl.ylim((0,0.02))
pl.xlim((5,10))
2.Zoom in/out to a certain range
3. Change figure size
pl.figure(figsize=(4,5))

## Slide 24
Next week: soil data challenge 2025
Bonus points for the assignment
Useful to have all team members present

## Slide 25: Appendix

## Slide 26: Explaining the code

## Slide 27
Import a .py file
import vanGenuchten as vg
vg.CFun()
vg.KFun()
Have to type vg. when calling a function or variable from vanGenuchten.py
Just like what you are already familiar with:
import numpy as np
from vanGenuchten import Cfun, Kfun
CFun()
KFun()
No need to type vg.
1.
2.
from vanGenuchten import *
* means everything

## Slide 28: Next week
Time for group work
Questions answering
Tips on report writing

## Slide 29: Assignment submission
1.Moodle link opens in December
2. Upload by December x th per group
3.Merge all 3 assignments in one PDF
4.Team members’ names in the report

## Slide 30: What is the shortcut key for running current cell?
1. Ctrl + Enter
2. Enter
3. Shift + Enter

## Slide 31: What is the shortcut key for commenting code?
1. Ctrl + Enter
2. Ctrl + A
3. Ctrl + /