## Slide 1: Part 4 MILP optimization of Energy Systems and Scenario Analysis
Sai Ravi, Michele Poli
2025

## Slide 2
.run
.dat
.mod
Model + Buildings
Energy Technologies
.dat
.mod
.dat
.mod
…
HP + Heat Recovery
.mod
.mod
Boiler | Geothermal cogeneration system
Two 1-stage heat pumps | Cogeneration engine
2-stage heat pump | Solid oxide fuel cell (SOFC)
Photovoltaic panels | Your ideas
Project Structure

## Slide 3: Overview
Adapt your current model of EPFL energy systems with the results obtained from the previous parts
(Part 1: heating clusters and buildings characteristics, Part 2: Heat recovery scenarios, Part 3: Heat pump model)
Suggest at least three different new energy systems (different scenarios  different objective function)
  EPFL has very little money to invest at present and wants to minimize the costs of installing new technologies.
  Due to the financial crisis, EPFL expects to have much less money in the coming years and wants to minimize the operating costs.
  EPFL wants to become a greener university and wants to minimize the total equivalent carbon emissions.
Conduct a multi-objective (Pareto) optimization: analyzing the trade-off between different objectives
Assess the sensitivity of your solutions to variations: natural gas and electricity prices, carbon tax..

## Slide 4: Structure of the sets
Building 1
Building 2
Building 3
Building …
Building 24
Low T
Medium T
Buildings
LowTemp Buildings
MediumTemp Buildings
HeatingLevel

## Slide 5: Utilities Set
ElecGridBuy
ElecGridSell
NatGasGrid
Boiler
HP
Fuel Cell
PV
…
Technologies
Resources
Utilities
Technologies: List of ETs
Grids: units to buy resources
Utilities: Technologies + Grids
1. Binary Variables (use, use_t)
var use{Utilities} binary;
var use_t{Utilities, Time} binary;
2. Continuous variables (mult, mult_t)
var mult{Utilities} >= 0
var mult_t{Utilities, Time} >= 0

## Slide 6: Layers and other sets
ElecGridBuy
ElecGridSell
NatGasGrid
Boiler
HP
Fuel Cell
PV
…
Heating
ElectricitySup
ElectricityCon
NatGas
Electricity
UtilitiesType
Layer
UtilitiesType:
  Type of technology
  List of ET sub-sets
Layer:
  Type of consumed/produced resource
  List of ET sub-sets

## Slide 7: Overall structure of the sets
ElecGridBuy
ElecGridSell
NatGasGrid
Boiler
HP
Fuel Cell
PV
…
Heating
ElectricitySup
ElectricityCon
NatGas
Electricity
Building 1
Building 2
Building 3
Building …
Building 24
Low T
Medium T

## Slide 8: Constraints: heating balances
HP
Qheatingdemand['LowT’,t] = * mult_heating_t[u,t,'LowT']
Qheatingdemand[‘MediumT’,t] = * mult_heating_t[u,t,’MediumT']
In the model
Your task
Decision variable for operation
Qheatingsupply ['HP2stage']
Flowin['Electricity','HP2stage'] = Qheatingsupply ['HP2stage'] / COP
cinv1['HP2stage']
cinv2['HP2stage']

## Slide 9: Constraints: resource balance
Resource balance:
=
FlowInUnit[l,u,t] = mult_t[u,t] * Flowin[l,u]
FlowOutUnit[l,u,t] = mult_t[u,t] * Flowout[l,u]
HP
Qheatingsupply ['HP2stage']
Flowin['Electricity','HP2stage'] = Qheatingsupply ['HP2stage'] / COP
cinv1['HP2stage']
cinv2['HP2stage']
Your task
reference size

## Slide 10: Constraints: electricity balance
Edemand[t] + =
Observe that:
Sum over UtilitiesOfType[‘ElectricityCons’] and UtilitiesOfType[‘ElectricityProd’]
These are subset of utilities consuming and producing electricity

## Slide 11: Objective function: TOTEX
OPEX =
CAPEX =
cop1[u]: fixed operating cost of the utility u [CHF/h]
cinv1[tc]: fixed investment cost of the technology tc [CHF/h]
cop2[u]: variable operating cost of the utility u [CHF/h] = energy tariff
cinv2[tc]: variable investment cost of the technology tc [CHF/y]
You can easily change the energy tariffs in moes.dat: c_spec

## Slide 12: Your TODOs
Read part 4 of Project description.pdf
Check that your ampl files is running with PVs and boilers
Add your typical days
Include your best heat recovery option as a new unit (the model should be linear)
Add heatpumps using the COP from Part 3
Add other types of units you would like to integrate and new layers if needed (biogas, biomass, H2, …)
Run scenarios, sensitivity analysis on energy tariffs, pareto fronts