## Slide 1: Optical fibers
https://www.imec-int.com/en/integrated-photonics

## Slide 2: Today
Orga:
  Script!
Last week:
  Dispersion in waveguides
  Start optical fibers
Today:
  Continue optical fibers

## Slide 3: The beginning of a modern world
A couple of courageous people in the 1840s and 1850s advocated for the construction of a telegraph cable.
Notes: https://en.wikipedia.org/wiki/Transatlantic_telegraph_cable

## Slide 4: The beginning of a modern world
A couple of courageous people in the 1840s and 1850s advocated for the construction of a telegraph cable.
The technology: first cable 550 kg/km.
Notes: https://en.wikipedia.org/wiki/Transatlantic_telegraph_cable

## Slide 5: After many failed attempts ….
The first attempt was a failure: cable broke right at the shore
Was repaired, broke again over Telegraph plateau (3200 m deep) and 480 km of cable were lost
Two ships ships met in the middle of the Atlantic and spliced the two cables together
Agamemnon sailed eastwards towards Valentia and Niagara westwards towards Newfoundland
The cable broke again several times
Source: https://atlantic-cable.com/1858NY/index.htm

## Slide 6: 1858: the first successful transmission

## Slide 7: 1858: the first successful transmission
The Atlantic Telegraph Jubilee, New York. Photograph by William England.

## Slide 8: 1858: the first successful transmission
The Atlantic Telegraph Jubilee, New York. Photograph by William England.

## Slide 9: Data rush .. Towards more b/s , kb/s and Mb/s?
The first message of the Queen of 98 words took 16 hours to send (1 word in 10 mins)
Cable bandwidth was limited by an imbalance between capacitance and inductance, leading to distortion
The original cables were not fitted with repeaters, no practical way to power them in a submarine cable.
Telegraph equations from Oliver Heaviside!
Trans-Atlantic telephone cable (TAT-1) with 1 kHz bandwidth: co-axial cable
O. Heaviside, “On the extra current”, Aug. 1876

## Slide 10: In parallel…. Optical fibers
Colladon’s and Babinet’s light fountain in 1840
Tyndal formulates total internal reflection in 1870
Charles K. Kao and George Hockham proposed that transmission should be possible with attenuation below 20 dB/km in silica fibers
Corning demonstrated attenuation of 17 dB/km and then 4 dB/km using impurities
“Dielectric-fibre surface waveguides for optical frequencies”, K.C.Kao & G.A.Hockham, Proceedings of the IEE, Vol. 113, No.7 (1966)

## Slide 11: Properties and wavelengths
R.-J. Essiambre et al., “Capacity limits of optical fiber networks”, J. Lightwave Technol. 28 (4), 662 (2010);
https://doi.org/10.1109/JLT.2009.2039464

## Slide 12: Why do we care about fibers?
Worldwide
Prevent tangling
Select right type of fiber
Durability
Separating copper from fiber
https://bbmaps.itu.int/bbmaps/
Data centers
Low maintenance
High bandwidth

## Slide 13: The math…
Helmholtz equation:
Cylindrical coordinates:
Ansatz:
To solve:

## Slide 14: The math…continued
Angular dependence:
Radial dependence:
Substituting

## Slide 15: Bessel functions
What do you notice from the spatial field profile?
To which functions do these ressemble?
What is different?

## Slide 16: We start from….

## Slide 17: Now we use
And using cylindrical coordinates

## Slide 18: Reshuffling
We get
We can apply the boundary conditions for , all tangential to the interface.
(…. Ex 1 of Assignment 2)

## Slide 19: Boundary conditions
Defining we get the transcendental equation for fibers:

## Slide 20: What are the solutions?

## Slide 21: l = 0
(derive in class)
= 0 corresponds to ? mode
= 0 corresponds to ? mode

## Slide 22: TE and TM modes
= 0 corresponds to TE mode
= 0 corresponds to TM mode