## Slide 1
Question 1 – In a biosensor, the target molecules in the sample are specifically captured by the biorecognition elements. By designing various transducing mechanisms, the molecular binding event can be transferred into measurable signals to achieve qualitative/quantitative analysis.
Please give some examples of biorecognition elements. What does the “Kd” define in the molecular binding events? What is the trade-off of using high Kd/ low Kd biorecognition elements in a biosensor?
Please give three different transducing mechanism examples in the biosensor development. Explain how can they transfer the molecular binding event into measurable signals.
What could be the possible reasons of the sensing signal drift with time?
Question 2 – In the last lecture, we have learned the electrochemical glucose biosensor.
What is the working principle of electrochemical-based glucose sensor?
Current glucose sensors rely on H₂O₂ oxidation at +0.6–0.8 V on the electrode. What limitations does this introduce?
Instead of using electrochemical sensing mechanism, the optical sensing based on Raman spectroscopy was also introduced in last lecture. What are the pros and cons of Raman-based sensors?
Question 3 – You are tasked to design a lateral-flow-assay for a new target molecule for blood tests.
Explain your design briefly. How does it work? What is the function of control line? Why do you need it?
What factors should you consider to ensure the detection accuracy? And what is the improvement strategy for each aspect that you mentioned.

## Slide 2
Question 1
Antibody, Enzyme, DNA aptamer, peptides; Kd reflects the binding affinity of the bioreceptor to the target (how strong they bind with each other);
High Kd – Limitation of detecting targets of low concentrations – Low Kd – Binding too strong – Difficult for target molecule dissociation, Sensor not resuable.
Optical SPR sensor: target molecule binding onto bioreceptors on the SPR surface change the local refractive index, resulting in change of SPR angles.
Enzyme-based electrochemical sensor: Generation of H2O2 during enzymatic reaction (Glucose). The oxidation of H2O2 on the electrode surface generates electrical signals.
Acoustic-based QCM: Molecule binding onto the oscillated sensor surface changes resonance frequency.
Non-specific binding of interferent molecules on the bioreceptors
Degradation/ Detachment of bioreceptors

## Slide 3
Enzymatic reaction of glucose generates H2O2. The H2O2 oxidation happens on the electrode surface, where the generated electrons give measurable electrical signal.
Applied potential +0.6–0.8 V can also induce redox reaction of other electroactive molecules in the sample.
Pros: Enabling non-invasive detection; Bioreceptors not needed – eliminating the issue regarding bioreceptor degradation/detachment
Cons: Difficulty to isolating the target molecule signal from background noise of various interferent molecules in complex biological samples; Higher cost of hardware
Question 2

## Slide 4
Question 3
Sandwich assay using bioreceptor modified gold nanoparticles; A visible control line indicates sufficient sample volume, proper flow, and active reagents.
Bioreceptor density on the test line; Bioreceptor density on the gold nanoparticles; Applying backfill material to prevent non-specific binding