## Slide 1
Question 1 – A gas sensor detects target molecules through their adsorption on a sensing surface, which produces a measurable signal. At first, the sensor is fast and accurate, but after several months its sensing performance drops noticeably.
What is the potential reason to the reduction of sensing performance?
Weak adsorption and efficient desorption is favorable for the gas sensor design. Can you give some opposite examples where the performance relies on strong molecule adsorption on the surface?
If you were to design a regeneration process for the poisoned surface, what methods could you apply?
How do grain boundaries, oxide layers, and nanoscale roughness collectively determine how biological fluids interact with the surface?
Question 3 - A biomedical implant must encourage bone cell attachment while preventing bacterial biofilm formation. Titanium surfaces can be modified to alter their wettability and microstructure.
Question 2 - During fabrication of advanced microchips, engineers deposit a thin layer of metal (e.g., Cu or Au) on a reconstructed silicon substrate to create electrical contacts. After deposition, surface analyses reveal that:
The underlying Si(111)-(7×7) reconstruction partially disappears under the metal film.
Line defects (dislocations) propagate through the thin metallic layer after thermal cycling.
Why might the Si surface reconstruction disappear once the metal layer is deposited?
What are the positive & negative effect of the line defect formation here?

## Slide 2
Question 1 - A gas sensor detects target molecules through their adsorption on a sensing surface, which produces a measurable signal. At first, the sensor is fast and accurate, but after several months its sensing performance drops noticeably.
Q1 – Surface contamination/ No efficient desorption of gas molecules; Reactive sites occupied – surface poisoned
Q2 – Surface coating/modification;
Q3 – Heat treatment enhancing desorption; UV plasma to break strong surface bonds
Grain boundaries – local change on chemical composition & charge density at boundaries -> different protein binding/cell adhesion behaviors
Oxide layers – increased hydrophilicity; surface charged can be varied with pH
Nanoscale roughness – amplifying the hydrophilicity/hydrophobicity; increased surface area  more biomolecule adsorption
Question 3 - A biomedical implant must encourage bone cell attachment while preventing bacterial biofilm formation. Titanium surfaces can be modified to alter their wettability and microstructure.
Question 2 - During fabrication of advanced microchips, engineers deposit a thin layer of metal (e.g., Cu or Au) on a reconstructed silicon substrate to create electrical contacts. After deposition, surface analyses reveal that:
The underlying Si(111)-(7×7) reconstruction partially disappears under the metal film.
Line defects (dislocations) propagate through the thin metallic layer after thermal cycling.
Q1 - Metal – Metallic bonds; Si – Covalent bonds; Metal-Si interaction can disrupt the covalent bonds inside the Si reconstruction
Q2 - Positive: thermal stress released by line defect; reducing the risk of thin film cracking – Negative: Higher reactivity on line defect sites – can initiate corrosion or trap contaminant