## Slide 1: MRI Contrast – Simulator toolbox
7.10.2025

## Slide 2: Scenario
Focus on TE, TR and flip angle
Volume resolution = 192x192x128
No proton density difference between WM and GM
Ernst angle:

## Slide 3: Question 1
To the nearest degree, what is the flip angle that maximises the contrast between tissues with T1 values of 600 ms and 900 ms when a TR of 20 ms is being used? (Use the zoom tool [magnifying glass] in the plot to find this).

## Slide 4: Question 1
To the nearest degree, what is the flip angle that maximises the contrast between tissues with T1 values of 600 ms and 900 ms when a TR of 20 ms is being used? (Use the zoom tool [magnifying glass] in the plot to find this).  about 23°
Set flipAngle equal to this new angle and run simContrast again.

## Slide 5: Question 2
Find a flip angle small enough to provide little visible contrast (T1-weighting) without making the image look too noisy (CNR ~= 1).

## Slide 6: Question 2
Find a flip angle small enough to provide little visible contrast (T1-weighting) without making the image look too noisy (CNR ~= 1). 13°
Now increase TE (it will increase the T2-weighting but will also make the image look noisier). Approximately what is the TE which maximises the T2-weighted CNR? (only an approximate answer is required as there is a large range of TE values with similar CNR)

## Slide 7: Question 2
Find a flip angle small enough to provide little visible contrast (T1-weighting) without making the image look too noisy (CNR ~= 1). 13°
Now increase TE (it will increase the T2-weighting but will also make the image look noisier). Approximately what is the TE which maximises the T2-weighted CNR? (only an approximate answer is required as there is a large range of TE values with similar CNR) TE = 100 ms

## Slide 8: Question 3
For TR=1 sec, TE = 5 ms, flip angle = 40°, find the approximate TI which corresponds to:
  Nulling’ white matter (i.e. no signal from white matter)
  Grey and white matter are the same intensity

## Slide 9: Question 3
For TR=1 sec, TE = 5 ms, flip angle = 40°, find the approximate TI which corresponds to:
  Nulling’ white matter (i.e. no signal from white matter) TI = 300-325 ms
  Grey and white matter are the same intensity TI = 200 ms