## Slide 1
CHAPTER 1: https://medium.com/advances-in-biological-science/nuclear-magnetic-resonance-spectroscopy-the-overlooked-powerhouse-of-biology-chapter-1-7b3d74dad714
CHAPTER 2: https://medium.com/advances-in-biological-science/nuclear-magnetic-resonance-spectroscopy-the-overlooked-powerhouse-of-biology-chapter-2-f1e80e7a4b3
CHAPTER 3: https://lucianosphere.medium.com/nuclear-magnetic-resonance-spectroscopy-the-overlooked-powerhouse-of-biology-chapter-3-5fed9865afce
CHAPTERS 4 & 5: COMING SOON
These classes are not at all deep (whole courses can be done dedicated to different sub-fields of NMR spectroscopy)…
… but neither are them too shallow: I try to balance practical applications with giving you some basic theoretical concepts.
NEW IN 2024: Blog posts with a written form of everything I tell you here
THIS + NEXT WEEK:
Nuclear Magnetic Resonance (NMR) spectroscopy
applied to Structural Biology
Luciano Abriata – Lab. for Biomol Model. / PTPSP facility / NMR facility

## Slide 2
CLASS 1 (today): Intro to Nuclear Magnetic Resonance for proteins
including an exercise on interpreting a protein-protein titration
Tomorrow: 8:15 at the NMR facility, then we come here to measure remotely
CLASS 2 (next week): More exotic bio-NMR: ligand screening, disordered proteins & biochemistry at atomic level
including an example application

## Slide 3
Part 1
Nuclear Magnetic Resonance
as one more Spectroscopic tool

## Slide 4
Spectroscopy = study of how energy interacts with matter
Quantified as spectra 
Tools for chemistry &
structural biology 
Energy, frequency, wavenumbers, etc.
Absorption, Emision, Scattering, etc

## Slide 5
Wavelength = c/frequency
Electronic spectroscopies
Wavelength = c/frequency
Wavenumbers = 1/wavelength
Chemical shift = c x frequency

## Slide 6
Wavenumbers = 1/wavelength
Transmittance
Infrared spectroscopies

## Slide 7
Magnetic spectroscopies (NMR, EPR)
Static (external) magnetic field
In the classical analogy of all these quantum systems,
nuclei & electrons behave as tiny precessing magnets
Chemical shift = c x frequency

## Slide 8
15N nucleus
13C nucleus
1H nucleus
electron
Increasing energy
15N NMR
13C NMR
1H NMR
EPR
Nuclear Magnetic Resonance
Electron Paramagnetic Resonance

## Slide 9
Magnet’s coil
Magnetic field lines
Magnetic field is strongest here
NMR sample

## Slide 10
Put S>0 nuclei in a magnetic field and you can do NMR
Bo
S=1/2 => ms = +1/2 or -1/2
S=nuclear spin ms=quantum spin number

## Slide 11: NMR-active nuclei, best spin=1/2
1H 13C 15N 31P
Isotope
Spin
Natural abundance
Relative sensitivity
Absolute sensitivity
F. Bloch

## Slide 12
Bo
B1
Detector
Frequency
Generator
Recorder
Magnet
NMR instr. is basically a huge magnet
with expensive radio equipment
N
S
(Actually a superconducting magnet in liquid helium)
To manipulate magnetization and record signals (“pulse sequences”)
Excite resonances (+ possibly encode information)
Read signal (“Free Induction Decay”)
Time
Fourier Transform
Frequency
Spectrum

## Slide 14
Nuclear Magnetic Resonance in Biology
1H 13C 15N 31P
< 1%
Notes: The NMR phenomenon can be used in many ways. It’s the basic of MRI, which we will not cover but there are labs working on that here. Then one clear application is in solving structures of small molecules, and I wanted to highlight here that since these are very easy spectra, very different for different molecules, you can relatively easily analyze complex mixtures of them and then track in real time how they evolve, so you can monitor a chemical process, metabolism, etc. The last application, most relevant to this talk, is about studying the structure, dynamics, interactions, etc of proteins.

## Slide 15
D E = g h Bo / 2p = h
 : Gyromagnetic constant
NMR spectroscopy  energy levels
(In this case induced by magnetic field)
Larger gyromagnetic constant or larger external field  higher frequency  higher sensitivity & resolution
1 T = 50 MHz 1H
10 T = 500 MHz 1H
Ribonuclease, 15% concentration (around 10 mM), in D2O to remove H2O signals.
Saunders, Wishnia & Kirkwood, JACS (1957) 79:3289
Lysozyme < 1mM at 900 MHz in H2O (suppressed by pulse sequence)

## Slide 16
  To improve signal/noise:
  Use concentrated samples
  VERY strong magnetic field: 10s of Tesla
  Use nuclei with large g 1H > 13C > 15N
  May need to enrich: 1H almost 100%, 13C and 15N ~ 1%
  Average signals many times  long experiments (days!)
  Protein stable and unchanged for experiment time
ΔE is small so NMR has low sensitivity!

## Slide 17: Methods for Isotope Enrichment (a.k.a. “labeling”)
Purpose: to produce protein sample enriched in 15N, 13C and/or 2H.
Biosynthetic methods preferred.
Host organisms: Bacterial (E. coli), Yeast, Fungal, Insect or Mammalian cells; Algae or cyanobacteria. Production in E. coli dominates (>95%)
Labeling reagents: 15NH4Cl, [13C]glucose, D2O.
  Requires high expression in minimal media
  Extra $ (13C > 15N)
   Ask at Protein Structure Core Facility
Gene coding protein
DNA
15NH4
13C-glucose
RNA
Protein
Notes: A pesar de la gran revolución que representó la RMN bidimensional, y los primeros ejemplos de estructura de proteínas, cuando los investigadores se enfrentaban a moléculas de mayor tamaño, no era posible asignar todas las frecuencias de los protones que las constituían, porque los espectros contenían demasiadas señales. Era necesario utilizar otros núcleos activos desde un punto de vista RMN, como el C-13 o el N-15 para “editar” los espectros (ya veremos cómo), pero este tipo de trabajos no pudo ser realizado hasta que no se desarrollaron protocolos para marcar las biomoléculas (al principio sólo proteínas) y enriquecerlas artificialmente con estos núcleos de baja abundancia natural. También la parcial deuteración ayudaba a simplificar los espectros y ya volveremos sobre este argumento más adelante.
Dado que la síntesis química de proteínas es un proceso altamente ineficiente, se recurrió a métodos biosintéticos, en los cuales se introduce la información genética para la producción de la proteína de interés en un organismo huésped, que puede ser una bacteria, una levadura, un hongo, un insecto o incluso células de mamífero, algas o cianobacterias. Este organismo crece en un medio en el cual su fuente principal de nitrógeno es una sal de amonio con nitrógeno 15, su fuente de carbono es glucosa marcada con carbono 13 y en ciertos casos se usa agua pesada en lugar del agua normal. Estos núcleos se incorporan así a todas las proteínas que fabrica el organismo, y también a la proteína de interés que viene luego purificada.

## Slide 18
Part 2
NMR spectra(l features)  Structure

## Slide 19
NMR and molecular structure
One nucleus
One signal (or “resonance”)
 Each resonance reports about one atom (its covalent and noncovalent environment, its motions, etc.)

## Slide 20
1H
13C
15N
400 MHz
100 MHz
40 MHz
Each nucleus has its main frequency, whose exact value depends on its chemical environment: CHEMICAL SHIFT
Nuclei are “coupled” through bonds and space: COUPLINGS
Excited nuclei relax through processes regulated by their motions  RELAXATION
The 3 main signal features that are sensitive to structure and motions

## Slide 21
HO-CH2-CH3
wo
low
field
high
field
(1) Chemical shift = slight variation in resonance frequency relative to a standard
δ (ppm)

## Slide 22
0
TMS
ppm
2
10
7
5
15
Aliphatic
Alcohols, protons a
to ketones
Olefins
Aromatics
Amides
Acids
Aldehydes
1H Chemical Shifts
13C Chemical Shifts
ppm
50
150
100
80
210
Aliphatic CH3,
CH2, CH
Carbons adjacent to
alcohols, ketones
Olefins
Aromatics,
conjugated alkenes
C=O of Amides
0
TMS
C=O in
ketones

## Slide 23: 1H chemical shifts in proteins
δ 1H (ppm)

## Slide 24
Protein folded
Protein unfolded
δ 1H (ppm)
Protein folded or not? From inspection of 1H spectrum

## Slide 25
b-sheet
a-helix
Random coil
Secondary structure of each residue from 1Hα chemical shifts
Same with 13CA, 13CB, 13CO  consensus

## Slide 26
(2) Couplings = nucleus-nucleus interactions
Dipolar (through space)
internuclear distances
Scalar (through bonds)
dihedral angles
Internuclear interactions (couplings) provide structural constraints

## Slide 27
Dipolar Interactions
Through space
Various mechanisms
One of them is the “nuclear Overhauser effect” (NOE)
NOEij ~ 1/rij6  Main piece of information for structure determination by NMR, together with dihedral angles from chemical shifts
i-j: short range (sec. struct.) ; long range (tert. struct.)

## Slide 28
Example on two consecutive 13C,15N-labeled residues (all Js in Hz)
Scalar Interactions
Through bonds “couplings” (J)
Atom-atom and residue-residue connectivity
Dihedral angles

## Slide 29
Simulated Annealing
Under NMR restraints (distances and angles)
Random seed models
Structure determination by solution NMR
Refinement
NMR-consistent ensemble

## Slide 30
Heteronuclear NOE
High NOE = rigid
Low NOE = ps-ns flexible
Residue number
Deviation from mean structure
F. Sesterhenn , C. Yang, B. Correia

## Slide 31
(3) Relaxation = rate at which
magnetization returns to equilibrium
Depends and reports on atomic motions in a large timescale
 Next class

## Slide 32
Part 3
Real spectra and data you get to see in papers
A quick look at some key spectra and concepts,
and we then move to hands-on work

## Slide 33
A very important 2D spectrum: 1H-15N HSQC
2D 15N / 1H correlation through a single bond,
One 15N-1H per residue
-15N - Ca- CO -15N - Ca
H
R
R
H
90Hz
(13C,15N…)
1/J
X evolution
(becomes indirect dimension frequencies upon FT)
INEPT (magnetization transfer)
FID (becomes direct dimension upon FT)
2-5 min in perfect sample (even seconds with special pulse sequence) to a couple of hours for diluted/bad samples

## Slide 34
Very sharp resonances
1 per nucleus
Info on structure & dynamics
15N
1H
1H,15N HSQC
15N & 13C “labeling”
Clear against 14N & 12C background
Resolve signals
More structural, chemical & dynamical information
Notes: Here you have a 1D spectrum of a ubiquitin. You can see how despite being sharp, the signals are so many that you have large overlap. You can alleviate this by resolving the resonances in 2D or 3D or moreD spectra, where you see crosspeaks only for pairs of atoms that are connected. The HSQC is especially important, and you have seen it a lot in publications for sure, because it gives a fingerprint of the backbone units quite easily, with high sensitivity, and is very robust. Each crosspeak in this 2D spectrum reports on one amino acid. Note how I’m talking about 15N. 1H here in this axis is the normal H, but abundant N is 14, not 15. So this means I have to incorporate 15N in the sample. I can also incorporate 13C. These “labels” are good not only because they are NMR active but also because they allow us to distinguish from the background, which is 14N and 12C. So we get resolution but also the possibility to see our protein in very complex environments, even full cells or highly concentrated solutions. Note that 14N and 12C are not radioactive, and do not entail any change in chemistry, compared to other probes.

## Slide 35: Quick Assay of Mutations Mutations can effect folding and stability
Wild type, well-folded
Partially destabilized & hetero-geneous
Partially destabilized
Unfolded, looks like an intrinsically disordered protein
Ohi et al., NSB (2003)

## Slide 36: Resonance Assignment Assign each resonance to a specific atom
CH3-CH2-OH
OH
CH2
CH3

## Slide 37: Proteins Have Too Many Signals! 1H NMR Spectrum of Ubiquitin
~500 resonances
How to resolve and assign these spectra???

## Slide 38
For proteins, additional dimensions provided by 13C and 15N

## Slide 39: 2D NMR: Coupling is the Key
2 times  2 frequencies
Same as 1D experiment
90º pulse
t1
t2
t1
t2
Transfers between
coupled spins
2D NMR Pulse Sequences can be designed to selectively detect dipolar or scalar couplings
COSY & TOCSY type spectra: Scalar
NOESY: Dipolar

## Slide 40
COSY:2D spectrum of 1H-1H scalar couplings
HN resX
HA resX
HA resX
HB resX
HG resX
HB resX
1H (ppm)
1H (ppm)

## Slide 41
TOCSY: 2D spectrum of 1H spin systems
HN resX
HA
HB
HG
1H (ppm)
1H (ppm)

## Slide 42
NOESY: 2D spectrum of 1H-1H dipolar couplings
HN resX
Hs from resX, resX-1..4, resX+1..4, and residues located far in sequence but close in structure
1H (ppm)
1H (ppm)
HN resX
Hs from resX, resX-1..4, resX+1..4, and residues located far in sequence but close in structure
residue i
residue i+1
residue j

## Slide 43: Assignments using 13C and 15N labeling Because 1H – 1H is not enough to overcome signal overlap and 1H is not very informative per se

## Slide 44
HSQC
3D = HSQC + 13C dimension
(CO, CA, CB, CO-1, CA-1, CB-1)
13C strips

## Slide 45
3D = HSQC + 13C dimension
(CO, CA, CB, CO-1, CA-1, CB-1)
HNCA

## Slide 46
Result: An assigned HSQC spectrum

## Slide 47
Part 4
Visit to the NMR facility and
hands-on work on some spectra (tomorrow)

## Slide 48
Tomorrow at 8:15 SHARP in the entry to the BCH
Visiting the NMR center at 8:15 SHARP
Then back to this office, we’ll collect some spectra on a sample and look at them together
Resources you’ll need:
https://www.protein-nmr.org.uk/solution-nmr/spectrum-descriptions/
http://triton.iqfr.csic.es/guide/eNMR/proteins/aa/xxx.html (xxx = ala, arg, asp…)

## Slide 49
Hands-on: Explore 2D and 3D spectra used to assign a protein, and complete assignments
Goals: To get familiar with navigating spectra, general info from chemical shifts, and more globally to demystify NMR.
Not goals: To learn all chemical shifts, pulse sequences or even spectra by heart, etc.
Resources you’ll need:
https://www.protein-nmr.org.uk/solution-nmr/spectrum-descriptions/
http://triton.iqfr.csic.es/guide/eNMR/proteins/aa/xxx.html (xxx = ala, arg, asp…)