## Slide 1
Exercise 1
Industrial Examples (ESA/MSA)?
Example | What physical process is involved | Why does this process exploit | Write down ESA/MSA
Hydrogen and nitrogen from ammonia | Partial condensation |  | 
Water from sea | Reverse osmosis |  | 
Petrol from crude oil | Distillation |  | 
Carbon dioxide from industrial emissions | Absorption |  | 
Carbon dioxide from amines | Stripping |  | 
Penicillin from fermented products | Liquid-liquid extraction |  | 
Wastewater treatment | Membranes |  | 
Oxygen in blood stream | Adsorption |  | 

## Slide 2
Exercise 2: Separation of propylene from propane
Propane and propylene are among the light hydrocarbon stream produced by cracking heavy petroleum fraction. Propane is a valuable fuel (LPG), and propylene is a useful precursor for many chemicals (acetonitrile, isopropyl alcohol, cumene, polypropylene, etc.). Propose 3 separate separation processes and rank them. Discuss in groups of 3.
Property | Propane | Propylene
Molecular Weight [g/mole] | 42.081 | 44.096
Dipole moment [Debye] | 0.4 | 0.0
Kinetic diameter [nm] | 0.43 | 0.45
Melting point [degree C] | -185.1 | -187.5
Boiling point [degree C] | -47.6 | -41.9

## Slide 3
Calculate degree of freedom for when liquid and vapor phases of water/ethanol mixture are in contact with each other and are at equilibrium.
What independent variables you can assign?
How can you relate liquid composition to the vapor composition?
What other equations you can write for the system?
Exercise 3: Degree of Freedom
Liquid
mixture
Vapor
mixture