## Slide 1
1) Constant feed fed-batch
In a fed-batch culture of Escherichia coli operating with feed of a glucose solution, values of the following parameters are given at time t = 2 h, when the system is at quasi-steady state.
V = 1000 mL dV/dt = 200 mL h-1
s0 = 100 g glucose L-1 µmax = 0.3 h-1
Ks = 0.1 g gluscose L-1 YX/S = 0.5 g cells (g glucose)-1
X0 = 30 g (total = xot)
Find V0 ( the inital volume of the culture)
The feed flow in the fed-batch reactor will be:
dV/dt = F = 200 mL/h
V = V0 + F*t => V0 = V - F*t => V0 = 1000 - 200*2 = 600 ml or 0.6 L
b) Determine the concentration of growth-limiting substrate in the vessel at quasi-steady state at t = 2 h.

## Slide 2
c) Determine the concentration and total amount of biomass in the vessel at t = 2 h (at quasi-steady state)
The concentration at steady state (t = 2h) will be:
or by assuming the volume of the reactor at t = 2h, V = 1 L, then 50 g/L
d) If qp = 0.2 g product (g cells)-1 h-1, pO = 0, determine the concentration of product in the vessel at t = 2 h.
The product will be given by:

## Slide 3
2) Design of a multi-phase fed-batch for the production of lipase
A fed-batch for the production of a lipase is carried out with a recombinant strain Yarrowia lipolytica (see also figure below):
Phase 1: Batch on glucose (s0 (Glucose) = 6 g L-1)
Phase 2: Fed-batch on glycerol Feed1 s0 (Glyc) = 1260 g L-1
Phase 3: Fed-batch on lactose with Feed2 s0 (Lact) = 500 g L-1.
Inoculum batch : X0 = 0.1 g
a) Calculate the culture volume of the bioreactor at times B, C, D, E, and F
Note: V0 = A = 2.0 L, VB = VA = 2.0 L
From B to D: feed influx F=0.1 L h-1 and from D to F: feed influx F=0.06 L h-1. Vt = V0 + Ft
B : 2.0 L….. C : 2.4 L….. D : 2.8 L…. E : 3.1 L….. F : 3.4…..
b) Calculate the dilution rates for the time points A, C, and E.
A=0……; C: …0.1/2.4=0.041 h-1 ………………; E: 0.060/3.1 = 0.019 h-1

## Slide 4
c) Calculate the total biomasses for the time points B, D, and F.
Note: YX/Gluc = 0.5 g g-1, YX/Glyc = 0.1 g g-1, YX/Lact = 0.3 g g-1
B: 6+0.1 g; D: 6.1+0.1*1260*0.1*8=106.9g; F:106.9+0.3*500*0.06*10=196.9 g
d) Calculate the concentration of lipase at the end of the fed-batch (time point F).
Note: YLipase/X (Glucose) = 0 g g-1, YLipase/X (Glyc) = 0.01 g g-1, YLipase/X (Lac) = 0.5 g g-1
To calculate the concentration of the product lipase at the end of each of the three phases (B, D and F) we work in the same manner as in question (c). The formula for calculation of the product is:
e) Calculate volumetric productivity of lipase and of the biomass for the whole bioprocess (time point F).
The volumetric productivity at time point F (corresponds to the productivity of the overall process) will be give by

## Slide 5
3) Different feed profiles
Please complement the following figures with the trends you are expecting for the respective parameters for the following feed conditions:
Exponential feed; 2) Pulsed feed; 3) Constant feed
Note: Dashed line represents end of batch culture
Maintenance energy