## Slide 1: Solutions Tasks 11-15
Manfred Zinn
ChE-437

## Slide 2: Task 11: Steady-state concentration in a chemostat
Zymomonas mobilis is used for a chemostat culture in a 60 m3
fermenter. The feed contains 12 g L-1 glucose; Ks for the organism is
0.2 gL-1.
What flow rate is required for a steady-state substrate concentration
of 1.5 g L-1?
At the flow rate of (a), what is the cell density?
At the flow rate of (a), what concentration of ethanol is produced?
Following is known:
YX/S = 0.06 g g-1; YP/X = 7.7 g g-1; max = 0.3 h-1; Ks = 0.2 g L-1;
s0 = 12 g L-1; V = 60 m3
D = 0.265 h-1 F=15.88 m3 h-1
x = 0.63 g L-1
c = 4.851 g L-1

## Slide 3
Task 12: Application of chemostat
A bacterium is used to absorb (uptake) uranium from contaminated water in a continuous process operated at steady state. It incorporated uranium into cell mass, which is then removed from the bioreactor as solid waste. The advantage of the process is in converting a diluted contaminated water into a solid form for easier disposable.
Methanol is added to the feed water stream at a concentration of 5 g/l, which also contains 10 mg/l of uranium. The biomass yield on methanol is 0.6 g dry mass/g methanol. The Ks for methanol is 0.1 g/l, while the maximum specific growth rate is 0.345 hr-1. The absorption of uranium follows zero order kinetics with respect to uranium concentration. The absorption kinetics can thus be described as R=-kx
Where R is the absorption rate and x is the cell concentration. Because of the environmental concern the discharge methanol concentration has to be no higher than 0.05 g/l, while the target uranium concentration at discharge is 0.5 mg/l. It has been assumed that about 0.5 g uranium can be bound by one gram biomass.
What is the value of the reaction rate constant for absorption that will allow the uranium to be discharged in a continuous culture?
As it turns out, the absorption rate constant is only half of the needed to accomplish the decontamination process. What will you do to meet the discharge regulation?

## Slide 4
MeOH: 5 g L-1
Uranium in: 0.01 g L-1
Uranium out: 0.5 mg L-1
YX/MeOH: 0.6 g g-1
Ks: 0.1 g L-1
mmax: 0.345 h-1
s < 0.05 g L-1
R = -kx
YU/X: 0.5 mg g-1
D = 0.115 h-1
x = 2.97 g L-1
With the biomass of 2.97 g L-1 about 1.485 mg of uranium could be removed. However, this is valid when there is infinite reaction time available.
a) k under steady-state conditions:
0.736 h-1
b) Assumption that k is only 0.368 h-1:
x = 5.94 g L-1

## Slide 5: Task 13: Substrate conversion and biomass productivity in a chemostat
A 5 m3 fermenter is operated continuously with a feed substrate concentration of 20 kg m-3. The genetically engineered microorganism cultivated in the reactor has the following characteristics:
max = 0.45 h-1; Ks = 800 g m-3; YX/S = 0.55 kg kg-1
What feed flow rate is required to achieve 90% substrate conversion?
How does the biomass productivity at 90% substrate conversion compare with the maximum possible?
What is the biomass concentration in case a and at the optimal dilution rate?
D = 0.321 h-1, F = 1.61 m3 h-1
D is higher: Dm = 0.362 h-1
In case of D = 0.321 h-1 x = 9.91 g L-1
and for D = 0.362 h-1 x = 9.19 g L-1

## Slide 6: Task 14: Substrate conversion and biomass productivity in a chemostat
The specific growth rate for inhibited growth in a chemostat is given
by the following equation:
µ = µmax s /(Ks + s + I Ks / Ki )
Where
s0 = 10 g L-1, Ks = 1 g L-1; I = 0.05 g L-1, Yxs = 0.1 g g-1
x0 = 0 g L-1, Ki = 0.01 g L-1, µmax = 0.5 h-1
a) Determine X and S as function of D when I = 0
b) With inhibitor added to a chemostat, determine the effluent substrate concentration and x as function of D
c) Determine the cell productivity, Dx, as a function of dilution rate
s=DKs/(mmax-D)
x=YX/S(s0-s)
x=YX/S(s0-DKs/(mmax-D))
b) s=D(Ks+(I*Ks/Ki)/(mmax-D)
x=YX/S(s0-(D(Ks+(I*Ks/Ki))/(mmax-D)
c) Px=D(YX/S(s0-(D(Ks+(I*Ks/Ki))/(mmax-D)

## Slide 7: Task 15: Pirt Equation & Lineweaver-Burk Plot
A new strain of yeast is being considered for biomass production. The following data were obtained using a chemostat. An influent substrate concentration of 800 mg/l and an excess of oxygen were used at a pH of 5.5 and T = 35°C. Using following data, calculate µmax, Ks, YX/S, kd and ms, assuming µ = µmax S / (KS + S) - kd
D [h-1] | C-source Concentration in steady-state [mg L-1] | Cell concentration [mg/l]
0.1 0.2 0.3 0.4 0.5 0.6 0.7 | 16.7 33.5 59.4 101 169 298 702 | 366 407 408 404 371 299 59

## Slide 8: Lineweaver-Burk Plot
-1/KS
1/m
1/S
1/mm
KS/mm
µmax, Ks, YX/S, kd and ms, assuming µ = µmax S / (KS + S) - kd

## Slide 9
1/mmax = 1.0637 h
mmax = 0.94 h-1
Chart: 1/s [L g-1]
| 59.880239520958085 | 29.850746268656714 | 16.835016835016834 | 9.9009900990099009 | 5.9171597633136095 | 3.3557046979865772 | 1.4245014245014247
 | 10 | 5 | 3.3333 | 2.5 | 2 | 1.6667 | 1.4286
Ks=0.137 g L-1