## Slide 1
COM-405: Mobile Networks
Lecture 10.0: Wireless Localization
Haitham Hassanieh
Laboratory of SEnsing
& Networking Systems

## Slide 2: RADAR: RAdio Detection And Ranging
Invented during world war 2 to detect planes
Changed the course of the war
Transmit wireless signals, detect the reflections

## Slide 4: Radar: Interested in Detecting
Range: Distance from the radar
  UWB: Ultra Wide Band
  FMCW: Frequency Modulated Carrier Wave
Direction: Angle from which the object is coming
Directional antenna that is rotating.
Phased Antenna Array that is always Scanning.

## Slide 5: UWB: Ultra Wide Band
x
x
Transmit a Narrow Pulse in Time (1 ns)
time
1ns
1ns
Reflection Time

## Slide 6: UWB: Ultra Wide Band
x
x
Transmit a Narrow Pulse in Time (1 ns)
time
1ns
1ns
Reflection Time
Distance =Reflection Time Speed of Light

## Slide 7: UWB: Ultra Wide Band
Transmit a Narrow Pulse in Time (1 ns)
Bandwidth = 1/pulse time = 1 GHz  UWB
To detect pulse need to sample at Multi-GigaSample/sec
time
1ns
1ns
Reflection Time
Distance =Reflection Time Speed of Light

## Slide 8: UWB: Ultra Wide Band
Pros:
High resolution
Simple idea
Used also for communication (UWB 802.15.3a, 3 - 10 GHz)
Cons:
Very High Speed Sampling Rate!

## Slide 9: FMCW: Frequency Modulated Carrier Wave
Use chirps: signals where the frequency changes with time
Measure time using a frequency change
Time
Frequency
Transmitted
t
t+ΔT
Received
Reflection Time
ΔF
ΔF
slope
=

## Slide 10: How do we measure ΔF ?
Mixer
Transmitted
Received
Signal whose frequency is ΔF
FFT
Power
ΔF
Chart: 
ΔF ➔Reflection Time ➔ Distance
Subtracting frequencies is easy (e.g., removing carrier in WiFi)
Done using a mixer (low-power; cheap)

## Slide 11
FMCW: Frequency Modulated Carrier Wave
FMCW Transmitted Signal:
FMCW Received Signal: (Single reflector)
Mix TX and RX Signal:
Slope
Reflection Time
Phase
Frequency at

## Slide 12
FMCW: Frequency Modulated Carrier Wave
FMCW Transmitted Signal:
FMCW Received Signal: (Multiple reflectors)
Mix TX and RX Signal:
Slope
Reflection Time
Phase
Frequencies at

## Slide 13
FMCW: Frequency Modulated Carrier Wave
FMCW Transmitted Signal:
Mix TX and RX Signal:
Time
Frequency
t
t+ΔT
ΔF
ΔT
Sweep Time
Sweep Bandwidth
B

## Slide 14
FMCW: Frequency Modulated Carrier Wave
Time
Frequency
t
t+ΔT
ΔF
ΔT
Sweep Time
Sweep Bandwidth
B
Max Range:
Resolution:

## Slide 15: Radar: Interested in Detecting
Range: Distance from the radar
  UWB: Ultra Wide Band
  FMCW: Frequency Modulated Carrier Wave
Direction: Angle from which the object is coming
Directional antenna that is rotating.
Phased Antenna Array that is always Scanning.

## Slide 16
Phased Arrays Primer

## Slide 17
Phased Arrays Primer
Digital Phased Arrays

## Slide 18
Phased Arrays Primer
Digital Phased Arrays

## Slide 19
Phased Arrays Primer
Digital Phased Arrays
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
LPF
BPF
PLL
Mixer
LPF
BPF
Mixer
LNA
ADC
Digital Processing
ADC
Every antenna connected to full fledged RX
Sample & Process Signals in Digital

## Slide 20
Phased Arrays Primer
Digital Phased Arrays
LPF
BPF
PLL
Mixer
LPF
BPF
Mixer
LNA
ADC
Digital Processing
ADC
Every antenna connected to full fledged RX
Sample & Process Signals in Digital
Analog Phased Arrays
RX
All antennas connected to a single receiver
Each antenna connected to a phase shifter.
Phase shifter changes the phase of the signal on each antenna by multiplying with .
Steer the beam electronically by changing the phases of the signals.
Get the sum along a certain direction.
Very expensive and high power for large arrays & mmWave
Cheap & low power but requires scanning
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX
RX

## Slide 21
Analog Phased Arrays
RX
To get signal along direction , set the phases on the phase shifters to

## Slide 22
Analog Phased Arrays
RX

## Slide 23
Analog Phased Arrays
RX
Set the phase shifters to receive signals from a given direction.
Send FMCW signals.
Receiver FMCW reflections, down convert, sample and compute range FFT.
Repeat until you get 2D range image: AoA + Range

## Slide 24
Analog Phased Arrays
RX

## Slide 25
Analog Phased Arrays
RX

## Slide 26
Analog Phased Arrays
Ganis, A.; Miralles-Navarro, E.; Schoenlinner, B.; Prechtel, U.; Meusling, A.; Heller, C.; Spreng, T.... (2018). A portable 3D Imaging FMCW MIMO Radar Demonstrator with a 24x24 Antenna Array for Medium Range Applications. IEEE Transactions on Geoscience and Remote Sensing. 56(1):298-312. https://doi.org/10.1109/TGRS.2017.2746739

## Slide 27
Analog Phased Arrays
RX
Larger Array  Narrower Beams  Higher Resolution
8 Antenna
16 Antenna
32 Antenna

## Slide 28
2D Phased Arrays
Can recover:
Range:
Azimuth AoA:
Elevation AoA:
Fix :
Fix :

## Slide 29
2D Phased Arrays
Can recover:
Range:
Azimuth AoA:
Elevation AoA:

## Slide 30
2D Phased Arrays
Can recover:
Range:
Azimuth AoA:
Elevation AoA:

## Slide 31
2D Phased Arrays
Can recover:
Range:
Azimuth AoA:
Elevation AoA:

## Slide 32
2D Phased Arrays
Pick the phase shift on each antenna to create a beam in each 3D direction.
Transmit FMCW signals and receive reflections.
Mix RX signal with TX and take range FFT .
Repeat in every direction.
3D Heatmap Image
3D Point Cloud

## Slide 33
Phased Arrays Primer
Digital Phased Arrays
Analog Phased Arrays
Pick the phase shift on each antenna to create a beam in each 3D direction.
Transmit FMCW signals and receive reflections.
Mix RX signal with TX and take range FFT .
Repeat in every direction.
Single RX Chain
3D Heatmap Image
RX Chains
Mix the RX signal with TX.
Compute Range FFT.
Multiply the resulting signal on each antenna with and sum the signals.
Repeat in every direction.
Could Potentially Do the Same thing:

## Slide 34
Phased Arrays Primer
Digital Phased Arrays
Analog Phased Arrays
Pick the phase shift on each antenna to create a beam in each 3D direction.
Transmit FMCW signals and receive reflections.
Mix RX signal with TX and take range FFT .
Repeat in every direction.
Single RX Chain
3D Heatmap Image
RX Chains
Could Potentially Do the Same thing:
Compute Range FFT.
Multiply the resulting signal on each antenna with and sum the signals.
Mix the RX signal with TX.
Repeat in every direction.

## Slide 35
Phased Arrays Primer
Digital Phased Arrays
RX Chains
Algorithm 1:
Compute Range FFT.
Multiply the resulting signal on each antenna with and sum the signals.
Mix the RX signal with TX.
Repeat in every direction.
Algorithm 2: (Faster)
IDEA: antenna arrays are Fourier Transforms

## Slide 36
Phased Arrays Primer
Digital Phased Arrays
RX Chains
Algorithm 1:
Compute Range FFT.
Multiply the resulting signal on each antenna with and sum the signals.
Mix the RX signal with TX.
Repeat in every direction.
Algorithm 2: (Faster)
IDEA: antenna arrays are Fourier Transforms
Use 2D FFT

## Slide 37
Phased Arrays Primer
Digital Phased Arrays
RX Chains
Algorithm 1:
Compute Range FFT.
Compute 2D FFT across antennas
Mix the RX signal with TX.
Repeat in every direction.
Algorithm 2: (Faster)
IDEA: antenna arrays are Fourier Transforms
Mix the RX signal with TX.
Compute Range FFT.
Multiply the resulting signal on each antenna with and sum the signals.
3D FFT

## Slide 38
Phased Arrays Primer
Digital Phased Arrays
RX Chains
Algorithm 1:
Compute Range FFT.
Compute 2D FFT across antennas
Mix the RX signal with TX.
Repeat in every direction.
Algorithm 2: (Faster)
Mix the RX signal with TX.
Compute Range FFT.
Multiply the resulting signal on each antenna with and sum the signals.
3D FFT
Algorithm 3: (More Accurate)

## Slide 39
Phased Arrays Primer
RX Chains
Algorithm 3: (More Accurate)
Assumes parallel waves
Reflector is far away

## Slide 40
Phased Arrays Primer
RX Chains
Algorithm 3: (More Accurate)
Assumes parallel waves
Reflector is far away
RX Chains

## Slide 41
Phased Arrays Primer
RX Chains
Algorithm 3: (More Accurate)
Assumes parallel waves
Reflector is far away
RX Chains
Reflector is not far
IDEA: use the exact equation
Received FMCW signal from reflector after mixing with TX
: FMCW Slope

## Slide 42
Phased Arrays Primer
RX Chains
Algorithm 3: (More Accurate)
Assumes parallel waves
Reflector is far away
RX Chains
Reflector is not far
IDEA: use the exact equation
Assume antenna 0,0 at origin

## Slide 43
Phased Arrays Primer
RX Chains
Algorithm 3: (More Accurate)
Assumes parallel waves
Reflector is far away
RX Chains
Reflector is not far
IDEA: use the exact equation
Assume antenna 0,0 at origin

## Slide 44
Phased Arrays Primer
RX Chains
Algorithm 3: (More Accurate)
Assumes parallel waves
Reflector is far away
RX Chains
Reflector is not far
IDEA: use the exact equation
Assume antenna 0,0 at origin

## Slide 45
Phased Arrays Primer
RX Chains
Algorithm 3: (More Accurate)
Assumes parallel waves
Reflector is far away
RX Chains
Reflector is not far
IDEA: use the exact equation
Assume antenna 0,0 at origin

## Slide 46
Phased Arrays Primer
Digital Phased Arrays
RX Chains
Algorithm 1:
Compute Range FFT.
Compute 2D FFT across antennas
Mix the RX signal with TX.
Repeat in every direction.
Algorithm 2: (Faster)
Mix the RX signal with TX.
Compute Range FFT.
Multiply the resulting signal on each antenna with and sum the signals.
3D FFT
Algorithm 3: (More Accurate)
Descritize space into grid.
For each point in space compute the received signal using the below equation.

## Slide 47
Phased Arrays Primer
Digital Phased Arrays
Analog Phased Arrays
Pick the phase shift on each antenna to create a beam in each 3D direction.
Transmit FMCW signals and receive reflections.
Mix RX signal with TX and take range FFT .
Repeat in every direction.
Single RX Chain
3D Heatmap Image
RX Chains
Algorithm 1:
Algorithm 2: (Faster)
3D FFT
Algorithm 3: (More Accurate)
Similar to Analog