## Slide 1
COM-405: Mobile Networks
Lecture 12.0: Multi-Hop Networks
Haitham Hassanieh
Laboratory of SEnsing
& Networking Systems

## Slide 2: Elements of a wireless network
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network
network
infrastructure

## Slide 3: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 4: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 5: Wireless network characteristics
Problem: A wants to transmit a packet to C
A
B
C
Option 1: A increases its power such that its packet reaches C
Option 2: A sends that packet to B which intern send it to C
A
B
C
A
B
C
d
d

## Slide 6: Wireless network characteristics
Problem: A wants to transmit a packet to C
A
B
C
Option 1: A increases its power such that its packet reaches C
Option 2: A sends that packet to B which intern send it to C
A
B
C
A
B
C
d
d
To double transmission range, we need: 4x more overall power!
To transmit over two hops, we need: 2x more overall power!

## Slide 7: Wireless network characteristics
Multi-hop wireless networks:
A
B
C
Increase TX power: increase transmission range by times, need more power
d
d
Multi-hop links: increase transmission range by times, need more power
Multi-hop wireless networks!

## Slide 8: Multi-hop Wireless Networks
Wireless Sensor Networks (WSN)
Wireless Ad Hoc Networks (WANETs)
Mobile Ad Hoc Networks
(MANETs)
A wireless Ad hoc network consists of a collection of mobile hosts dynamically forming a temporary network without the use of an existing network infrastructure.
Vehicular Ad Hoc Networks (VANETs)
A sensor network consists of one or more base stations and a large number of inexpensive sensors.

## Slide 9: Wireless Mesh Networks
Very low installation and maintenance cost
Easy to provide coverage outdoors
Ubiquitous access.
Rapid deployment.

## Slide 10: Wireless Mesh Networks
Roofnet
1 kilometer
Wireless Philly
Dense 802.11-based multi-hop network
Goal is high-throughput in the presence of lossy links

## Slide 11
TARF Rice Mesh Network
Facebook WiFi Mesh Network

## Slide 12: Traditional Single Path Routing
Represent the wireless network as a graph
  Two nodes have an edge if they can communicate (i.e., are within radio range)
  Each edge is labeled with a weight (where a smaller weight indicates a preferred edge)
Run shortest path algorithm on the graph (e.g., Dijkstra, Bellman Ford)
  Produce the minimum weight path between every pair of nodes
How do you pick the edge weights?
  i.e., what metric should shortest path minimize?

## Slide 13: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
c(x,x’) = cost of link (x,x’) e.g., c(w,z) = 5
cost could always be 1, or inversely related to bandwidth, or related to congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 14: Link-state Routing
Dijkstra’s algorithm
net topology, link costs known to all nodes
computes least cost paths from one node (“source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
1. Find not in set such that is a minimum
2. Add to
3. Update for all adjacent to and not in
4. Loop to 1.
Distance Vector Routing
Bellman-Ford (Dynamic Programming)
let := cost of least-cost path from to
then
  maintains distance vector
  knows cost to each neighbor v:
  maintains its neighbors’ distance vectors
  1. From time-to-time, each node sends its own distance vector estimate to neighbors
  2. When receives new DV estimate from neighbor, it updates its own DV using B-F equation:

## Slide 15
Cannot use classical wired routing in wireless!
Channel is Broadcast
  Interference: Cannot transmit on all links in parallel.
  Opportunity!
Unreliable
  Packet loss due to collision
  Packet loss due to bit errors
Overhead
  Nodes not as powerful (e.g. Sensor networks).
  Link bandwidth is typically lower than wired.

## Slide 16: Dynamic Source Routing (DSR)
On demand routing
 No periodic updates
When a source wants to route packets, routes generated
Consists of two parts
  Route discovery
  Route maintenance
Routing in Wireless Ad-Hoc Networks
Ad hoc On-demand distance vector (AODV )
Best of both worlds of DSR and DV
Like DV it is next hop based routing, full route path not included in packet
Like DSR, does not need periodic route maintenance messages

## Slide 17
Challenge: How to select the link cost?

## Slide 18
Reasoning:
Links in route share radio spectrum
Extra hops reduce throughput
A straw-man route metric (1):
Assign all edges the same weight  Minimize number of hops
Throughput = 1/2
Throughput = 1
Throughput = 1/3
But is not good enough because different edges many have very different packet loss rates

## Slide 19
Challenge: links are lossy and asymmetric
Different links have different loss rates
Further, the loss rate may be different in each direction
Very asymmetric links.

## Slide 20
Bottleneck throughput:
A straw-man route metric (2):
Maximize bottleneck throughput
50%
Delivery ratio = 100%
51%
51%
D
A
B
C
Actual throughput:
A-B-C : ABBABBABB = 33%
A-D-C : AADDAADD = 25%
A-B-C = 50%
A-D-C = 51%
Key Idea: In a shared medium links are not independent

## Slide 21
A-B-C = 51%
A-C = 50%
A straw-man metric (3):
Maximize end-to-end delivery ratio
51%
100%
50%
A
B
C
Actual throughput:
A-B-C : ABBABBABB = 33%
A-C : AAAAAAAA = 50%
End-to-end delivery ratio:
Key Idea: Again, links are not independent

## Slide 22
Minimize total transmissions per packet
(ETX, ‘Expected Transmission Count’)
Wireless routing metric: ETX
Link throughput  1/ Link ETX
Delivery Ratio
100%
50%
33%
Throughput
100%
50%
33%
Link ETX
1
2
3

## Slide 23
Route ETX
Route ETX
1
2
2
3
Route ETX = Sum of link ETXs
5
Throughput
100%
50%
50%
33%
20%

## Slide 24
Calculating Link ETX
Assuming 802.11 link-layer acknowledgments (ACKs) and retransmissions:
Estimating link ETX
  P(Data success)  measured fwd delivery ratio
  P(ACK success)  measured rev delivery ratio
  Link ETX

## Slide 25
Measuring delivery ratios
Each node broadcasts small link probes once per second
Nodes remember probes received over past 10 seconds
Reverse delivery ratios estimated as
rrev  pkts received / pkts sent
Forward delivery ratios obtained from neighbors (piggybacked on probes)

## Slide 26
ETX Caveats
It is really hard to measure link quality/loss
  Changes as a function of load
  Changes with time
ETX ignores differences in bit-rate and packet size
  ETT = ETX *(pkt_size/link-bit-rate)
  ETX ignores spatial re-use (i.e., assumes all links interfere)

## Slide 27: Traditional routing
packet
packet
packet
Identify a route, forward over links
Abstract radio to look like a wired link
src
A
B
dst
C

## Slide 28: Radios aren’t wires
Every packet is broadcast
Receptions are probabilistic and independent (Spatial diversity)
1
2
3
4
5
6
1
2
3
6
3
5
1
4
2
3
4
5
6
1
2
4
5
6
src
A
B
dst
C

## Slide 29: ExOR Idea: exploit probabilistic broadcast
packet
packet
packet
packet
packet
packet
src
A
B
dst
C
packet
packet
packet
Decide who forwards after reception
Goal: for each packet, receiver closest to the destination should forward
Challenge: agree efficiently on which node should forward, and avoid duplicate transmissions

## Slide 30: Why ExOR might increase throughput (1)
Traditional routing picks the path via R  on average 2 tx per packet
Throughput  1/# transmissions
Traditional routing ignores that 33% of the packets make it to the destination in one transmission
ExOR exploits these opportunistic receptions  1.67 tx per packet
src
dst
R
100%
100%
Delivery Prob.
Delivery Prob.
33%
Delivery Prob.

## Slide 31: Why ExOR might increase throughput (2)
Traditional routing: 1/0.25 + 1 = 5 tx
ExOR: 1/(1 – (1 – 0.25)4) + 1 = 2.5 transmissions
N1
src
dst
N2
N3
N4
25%
25%
25%
25%
100%
100%
100%
100%
Delivery Prob.
Delivery Prob.

## Slide 32: Challenge
Overlap in received packets  Routers forward duplicates

## Slide 33: Challenge
src
R1
dst
R2
Overlap in received packets  Routers forward duplicates
P1
P2
P10
P1
P2
P1
P2
ExOR imposes a global scheduler:
Nodes have to agree on who transmits what
Only one node transmits at a time, others listen

## Slide 34
Limitations of ExOR
Learning who received what  too much overhead
Forcing only one transmitter at a time  prevents spatial reuse of the medium
Src
Dst

## Slide 35
Src
Dst
Can we eliminate these problems?
Limitations of ExOR
Learning who received what  too much overhead
Forcing only one transmitter at a time  prevents spatial reuse of the medium

## Slide 36: Solution: Random Network Coding
Each router forwards random combinations of packets

## Slide 37: Solution: Random Network Coding
src
R1
dst
R2
Each router forwards random combinations of packets
3 P1+ 7 P2
2 P1+ 4 P2
P1
P2
P1
P2
Randomness prevents duplicates
No need to know who received what
Can exploit spatial reuse

## Slide 38: Network Coding Also Benefits Multicast
src
dst1
dst2
dst3
P1
P2
P3
P4
P1
P2
P2
P3
P3
P4
8 P1+ 6 P2+ P3+ P4
7 P1+2 P2+3 P3+4 P4
P3
P4
P1
P4
P1
P2
Without coding  source has to retransmit all 4 packets
With network coding  2 packets are sufficient

## Slide 39: MORE
MAC-independent Opportunistic Routing & Encoding.
An opportunistic routing protocol that reduces overhead and enables spatial reuse
It is based on network coding, where routers code packets together before forwarding them

## Slide 40: How Does MORE Work?
Source sends packets in batches
Forwarders keep all heard (innovative) packets in a buffer
Nodes transmit linear combinations of buffered packets
src
A
B
dst
P1
P2
P3
P1
P2
P3
=
+ b
+ c
a
a,b,c
4,1,3
0,2,1
4,1,3
P1
P2
P3
=
+ 1
+ 3
4
4,1,3
P1
P2
P3
=
+ 2
+ 1
0
0,2,1

## Slide 41: How Does MORE Work?
src
A
B
dst
P1
P2
P3
P1
P2
P3
=
+ b
+ c
a
a,b,c
4,1,3
0,2,1
4,1,3
=
2
+ 1
0,2,1
8,4,7
4,1,3
8,4,7
8,4,7
Source sends packets in batches
Forwarders keep all heard (innovative) packets in a buffer
Nodes transmit linear combinations of buffered packets

## Slide 42: How Does MORE Work?
1,3,2
5,4,5
4,5,5
P1
P2
P3
=
+ 3
+ 2
1
P1
P2
P3
=
+ 4
+ 5
5
P1
P2
P3
=
+ 5
+ 5
4
Source sends packets in batches
Forwarders keep all heard (innovative) packets in a buffer
Nodes transmit linear combinations of buffered packets
Destination decodes once it receives enough combinations
  Say batch is 3 packets
Decoding is solving linear equations
Once it decoded a batch, the destination acks the batch and the source moves to next batch

## Slide 43: Network Coding
Requires less coordination
  No scheduler
More flexibility
  One framework for unicast and multicast
More throughput
  22% more than ExOR and 95% more than current shortest path routing

## Slide 46: Traditional Approach
Requires 4 transmissions
  Alice to router; Router to Bob; Bob to router; Router to Alice
  Can we exploit broadcast to do better?
Router
Bob
Alice

## Slide 47: COPE
Router
XOR
=
XOR
=
XOR
=
Bob
Alice
Requires 3 transmissions instead of 4
  Alice to router; Bob to router; and router to both Alice and Bob
Network Coding  3 Transmissions instead of 4
 Increases Throughput

## Slide 48: Beyond Duplex Communications
Router
D2
S2
S1
D1
  Two communication flows that intersect at a router

## Slide 49: Beyond Duplex Communications
Router
D2
S2
S1
D1
  D2 overhears S1’s packet
  D1 overhears S2’s packet

## Slide 50: Beyond Duplex Communications
Router
XOR
=
XOR
=
XOR
=
3 transmissions instead of 4  Higher Throughput
D2
S2
S1
D1

## Slide 56
çç

## Slide 58
A.
B.
C.
D.

## Slide 68
Router
Bob
Alice
Alice and Bob Experiment
3 transmissions instead of 4
 Throughput Gain = 4/3 = 1.3333

## Slide 70
Router
Bob
Alice
Why the Gain is more than 1.33 ?
802.11 is fair  Each node transmits 1/3
Without COPE: Router needs to transmit twice as much
With COPE: All nodes need equal rate.

## Slide 73
Traditional Approach: requires 4 transmissions
COPE: requires 3 transmissions
Can we do it in 2 transmissions?
Router
Alice
Bob

## Slide 74: Analog Network Coding (ANC)
Instead of router mixing packets…
Exploit that the wireless channel naturally mixes signals

## Slide 75: Analog Network Coding
Router
Alice
Bob

## Slide 76: Analog Network Coding
Router
Alice and Bob transmit simultaneously
Interference
Alice
Bob

## Slide 77: Analog Network Coding
Alice and Bob transmit simultaneously
Router amplifies and broadcasts interfered signal
Router
Alice
Bob

## Slide 78: Analog Network Coding
Alice and Bob transmit simultaneously
Router amplifies and broadcasts interfered signal
Alice subtracts known signal from interfered signal
Router
Alice
Bob

## Slide 79: Analog Network Coding
Dina and Robert transmit simultaneously
Router amplifies and broadcasts interfered signal
Dina subtracts known signal from interfered signal
Analog Network Coding requires 2 time slots
Higher throughput
Router
Alice
Bob

## Slide 80: X topology
Router
Capture!
Capture!
Interference
D2
S2
S1
D1

## Slide 81: X topology
Router
Capture!
Capture!
Interference
D2
S2
S1
D1

## Slide 82: X topology
Router
ANC decodes interference using overheard signals
D2
S2
S1
D1

## Slide 83: It Is More Than Going From 3 To 2!
Philosophical shift in dealing with interference
  Strategically exploit interference instead of avoiding it
Promises new ways of dealing with hidden terminals

## Slide 84: Hidden Terminal Scenario
C
C
C
C
R1
R2
Src
Dst

## Slide 85: Hidden Terminal Scenario
P1
C
C
C
C
R1
R2
Src
Dst

## Slide 86: Hidden Terminal Scenario
P2
P1
Src and R2 transmit simultaneously
C
C
C
C
R1
R2
Src
Dst

## Slide 87: Hidden Terminal Scenario
Src and R2 transmit simultaneously
R1 subtracts P1, which he relayed earlier to recover P2 that he wants
P1
P2
C
C
C
C
R1
R2
Src
Dst

## Slide 88: Hidden Terminal Scenario
R2 and Src are hidden terminals
  Today : Simultaneous transmission  Collision
  ANC : Simultaneous transmission  Success!
P1
P2
C
C
C
C
R1
R2
Src
Dst