## Slide 1
Constructive Computer Architecture:
Multirule systems and Concurrent Execution of Rules
Yann Herklotz - EPFL
Slides adapted from 6.1920 with Thomas and Arvind
(Spring 23, MIT)

## Slide 2: Systems with multiple rules

## Slide 3: A one-instruction vector machine
Adds k to each element of an n-element vector a and store it in b
Vectors are too large to be stored in registers and therefore stored in BRAM
BRAM interface is single ported
Let a and b be the current pointers to the vectors, and n be the number of elements in the vector that remain to be processed
BRAM
a
b
a
b
+k
n
Let us build such a machine

## Slide 4: Steps in processing
Assume a, b, n and BRAM have been initialized properly
Initiate a BRAM request to read an element of a; increment a
Wait for the result; add k;
initiate a write of the result in b; increment b; decrement n
Repeat these steps if n>0
BRAM
a
b
a
b
+k
n
Let a and b be the current pointers to the vectors, and n be the number of elements in the vector that remain to be processed

## Slide 5: Rules for the vector machine
rule init_read_a if (n>0 && turn == 0);
mem.portA.request.put(BRAMReq{write:False,writeRes:False,
address:a, datain:?});
a <= a + 1;
n <= n – 1;
turn <= 1;
endrule
rule read_result if (turn == 1);
let x <- mem.portA.response.get();
mem.portA.request.put(BRAMReq{write:True, writeRes:False,
address:b, datain:x + k});
b <= b + 1;
turn <= 0;
endrule

## Slide 6: Multi-rule Systems
Repeatedly:
Select a rule to execute
Compute the state updates
Make the state updates
One-rule-at-a-time-semantics: Any legal behavior of a Bluespec program can be explained by observing the state updates obtained by applying only one rule at a time
Non-deterministic choice; User annotations can be used in rule selection
However, for performance we execute multiple rules concurrently whenever possible

## Slide 7: Rules for the vector machine
rule init_read_a if (n>0 && turn == 0);
mem.portA.request.put(BRAMReq{write:False,writeRes:False,
address:a, datain:?});
a <= a + 1;
n <= n – 1;
turn <= 1;
endrule
rule read_result if (turn == 1);
let x <- mem.portA.response.get();
mem.portA.request.put(BRAMReq{write:True, writeRes:False,
address:b, datain:x + k});
b <= b + 1;
turn <= 0;
endrule
The design still works without taking turn! Or does it?

## Slide 8: Homework
To get familiarized with this programming/execution model:
  Lab1-b: debug a simple multi-rule machine that fail to compute dot products
  Lab2: write your own matrix/matrix multiply module

## Slide 9: Multi-rule systems and concurrency

## Slide 10: Elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
rule stage1;
fifo1.enq(f1(inQ.first));
inQ.deq(); endrule
rule stage2;
fifo2.enq(f2(fifo1.first));
fifo1.deq; endrule
rule stage3;
outQ.enq(f3(fifo2.first));
fifo2.deq; endrule
Can these rules fire concurrently?
Yes, but it must be possible to do enq and deq on a fifo
simultaneously

## Slide 11: One-Element FIFO Implementation
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action deq if (v);
v <= False;
endmethod
method t first if (v);
return d;
endmethod
endmodule
not full
not empty
not empty
n
n
rdy
enab
rdy
enab
rdy
enq
deq
first
FIFO
Can enq and deq methods be ready at the same time?
No! Therefore, they cannot execute concurrently!

## Slide 12: Concurrency when the FIFOs do not permit concurrent enq and deq
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
not empty
not empty
&
not full
not empty
&
not full
not full
At best alternate stages in the pipeline will be able to fire concurrently

## Slide 13: Two-Element FIFO
Initially, both va and vb are false
First enq will store the data in da and mark va true
An enq can be done as long as vb is false; a deq can be done as long as va is true
Assume, if there is only one element in the FIFO it resides in da
db da
vb va

## Slide 14: Two-Element FIFO BSV code
module mkFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False);
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
method t first if va; return da;
endmethod
endmodule
Assume, if there is only one element in the FIFO it resides in da
Can both enq and deq be ready at the same time?
yes
db da
vb va

## Slide 15: Two-Element FIFO Sequential behavior analysis
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
Suppose, initially vb=false and va=true (there is an element)
Suppose enq executes before deq
  enq executes: db <= x; vb <= True;
  deq executes: da <= x; vb <= False;
  Final values: da == x; db == x; va == True; vb == False;
Suppose deq executes before enq
  deq executes: va <= False;
  enq executes: da <= x; va <= True;
  Final values: da == x; db == ?; va == True; vb == False;
db da
vb va

## Slide 16: Two-Element FIFO concurrency analysis
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
no double-write error
Will concurrent execution of enq and deq cause a double write error?
  Initially vb=False and va=True
  enq will execute: db <= x; vb <= True;
  deq will execute va <= False;
  The final state will be va = False and vb = True; with the old data in da and new data in db
db da
vb va
oops!
we can’t get into this state if enq and deq are performed in some order

## Slide 17: Two-Element FIFO concurrency analysis - continued
method Action enq(t x) if !vb;
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if va;
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
  In this implementation, enq and deq should not be called concurrently
    later we will present a systematic procedure to decide which methods of a module can be called concurrently
  First, we will study when two rules that only use registers can be executed concurrently
db da
vb va

## Slide 18: Concurrent execution of rules
Two rules can execute concurrently, if concurrent execution would not cause a double-write error, and
The final state can be obtained by executing rules one-at-a-time in some sequential order

## Slide 19: Can these rules execute concurrently? (without violating the one-rule-at-a-time-semantics)
rule ra;
x <= x+1;
endrule
rule rb;
y <= y+2;
endrule
Final value of (x,y) (initial values (0,0))
Exam 1 Exam2 Exam3
Concurrent
Execution
ra<rb
rb<ra
Example 1
rule ra;
x <= y+1;
endrule
rule rb;
y <= x+2;
endrule
Example 2
rule ra;
x <= y+1;
endrule
rule rb;
y <= y+2;
endrule
Example 3
(1,2)
(1,2)
(1,2)
(1,2)
(1,3)
(3,2)
(1,2)
(1,2)
(3,2)
No Conflict
Conflict
ra<rb

## Slide 20: Rule scheduling
The BSV compiler schedules as many rules as possible for concurrent execution among the rules that are enabled (i.e., whose guards are true), provided it can ensure that the chosen rules don’t conflict with each other
Conflict:
  Double write
  If the effect of rule execution does not appear to be as if one rule executed after the other

## Slide 21: Scheduling, systematically
First register only, and with arbitrary modules

## Slide 22: some insight into Concurrent rule execution
There are more intermediate states in the rule semantics (a state after each rule step)
In the HW, states change only at clock edges
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 23: Parallel execution reorders reads and writes
In the rule semantics, each rule sees (reads) the effects (writes) of previous rules
In the HW, rules only see the effects from previous clocks, and only affect subsequent clocks
Rules
HW
clocks
rule
steps
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes
reads
writes

## Slide 24: Correctness
The compiler will schedule rules concurrently only if the net state change is equivalent to a sequential rule execution
Rules
HW
Ri
Rj
Rk
clocks
rule
steps
Ri
Rj
Rk

## Slide 25: Compiler test for concurrent rule execution James Hoe, Ph.D., 2000
Let RS(r) be the set of registers rule r may read
Let WS(r) be the set of registers rule r may write
Rules ra and rb are conflict free (CF) if
  (RS(ra)WS(rb) = )  (RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
Rules ra and rb are sequentially composable (SC) (ra<rb) if
(RS(rb)WS(ra) = )  (WS(ra)WS(rb) = )
If Rules ra and rb conflict if they are not CF or SC

## Slide 26: Compiler analysis
rule ra;
x <= x+1;
endrule
rule rb;
y <= y+2;
endrule
Exam 1 Exam2 Exam3
RS(ra) {x} {y} {y}
WS(ra) {x} {x} {x}
RS(rb) {y} {x} {y}
WS(rb) {y} {y} {y}
  RS(ra)WS(rb)  {y} {y}
  RS(rb)WS(ra)  {x} 
  WS(ra)WS(rb)   
  Conflict? CF C SC
Example 1
rule ra;
x <= y+1;
endrule
rule rb;
y <= x+2;
endrule
Example 2
rule ra;
x <= y+1;
endrule
rule rb;
y <= y+2;
endrule
Example 3

## Slide 27: Concurrent scheduling
The BSV compiler determines which rules among the rules whose guards are ready can be executed concurrently
It builds a simple greedy list-based scheduler:
  Picks the first enabled rule in the list
  Schedules the next enabled rule if it does not conflict with any of the rules scheduled so far
  Repeats the process until no more rules can be scheduled
Such a scheduler can be built as a pure combinational circuit, but it is not fair
In practice it does fine, and one can get around it programmatically
The list is built using textual ordering of rules but can be changed by user annotations

## Slide 28: Scheduling and Control Logic

## Slide 29: Compiling a Rule
f
x
current
state
next
state
d
p
guard
f
x
rule r (f.first() > 0) ;
x <= x + 1 ; f.deq ();
endrule
rdy signals,
read methods
next state values
Notes: In a circuit, pi maps to combination logic that looks at the current state and generates a boolean enable signal for this rule
The delta functions is another combination logic that computes the next state value from the current state value. Actually, delta has to compute the control signals to set the state element to the new value

## Slide 30: Combining State Updates: strawman
next state
value
flip-flop
enable
R
OR
p1
pn
d1,R
dn,R
OR
p’s from the rules
that update R
d’s from the rules
that update R
What if more than one rule is enabled?
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 31: Combining State Updates
next state
value
R
Scheduler:
Priority
Encoder
OR
f1
fn
p1
pn
d1,R
dn,R
OR
d’s from the rules
that update R
Scheduler ensures that at most one fi is true
p’s from all
the rules
one-rule-at-a-time
scheduler is
conservative
Enable for register R
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 32: Scheduling and control logic
Modules
(Current state)
Rules
d1
p1
Scheduler
f1
fn
p1
pn
Muxing
d1
dn
dn
pn
Modules
(Next state)
cond
action
“CAN_FIRE”
“WILL_FIRE”
Compiler synthesizes a scheduler such that at any given time f’s for only non-conflicting rules are true
Notes: After mapping all the rules, we have to combine their logic some how.
For a particular state elemetn like the PC register,
the latch enable is the or the enable signals from all the rules that updates PC.
The actual next state value of PC has to be selected through a multiplexer.
Notice, this circuit only works if only one of these pi signal is asserted at a time

## Slide 33: Takeaway
One-rule-at-a-time semantics are very important to understand what behaviors a system can show
Efficient hardware for multi-rule system requires that many rules execute in parallel without violating the one-rule-at-time semantics
BSV compiler builds a scheduler circuit to execute as many rules as possible concurrently