## Slide 1
Constructive Computer Architecture:
Scheduling Constraints on Interface methods
Thomas Bourgeat - EPFL
(Slides prepared with Arvind, MIT, Spring 23)

## Slide 2: Goals for Today
Back to concurrency problems
Concurrency for completion buffers - non-queue module! More problems
Systematic formalization of the problem: Scheduling and conflict matrices
Solution: Swiss-army knife of scheduling (EHR)

## Slide 3: Elastic pipeline
x
fifo1
inQ
f1
f2
f3
fifo2
outQ
The rules for this pipeline can fire concurrently only if one can concurrently enq and deq in fifo1 and fifo2
There are many different ways in which enq and deq can be done concurrently in a fifo

## Slide 4: FIFOs with concurrent enq and deq
Conflict-Free FIFO: Both enq and deq are permitted concurrently as long as the FIFO is not-full and not-empty, i.e., enq CF deq
  The effect of enq is not visible to deq, and vise versa
Pipeline FIFO: An enq into a full FIFO is permitted provided a deq from the FIFO is done simultaneously, i.e., deq < enq
Bypass FIFO: A deq from an empty FIFO is permitted provided an enq into the FIFO is done simultaneously, i.e., enq < deq
Such FIFOs can be “derived” starting with one and two element FIFO designs without concurrency

## Slide 5: The problem is more general: Streaming the GCD module
outQ
inQ
rule invokeGCD;
gcd.start(inQ.first); inQ.deq;
endrule
invoke
GCD
get
result
rule getResult;
let x <- gcd.getResult; outQ.enq(x);
endrule
start
GCD
getResult
Can these rules fire concurrently?
Depends if start and getResult can fire concurrently, and behave as if getResult < start
Performance implications if they can’t fire concurrently?
Dead Cycle

## Slide 6: Another example: IP Lookup block in a router
Queue
Manager
Packet Processor
Exit functions
Control
Processor
Line Card (LC)
IP Lookup
SRAM
(lookup table)
Arbitration
Switch
LC
LC
LC
A packet is routed based on the “Longest Prefix Match” (LPM) of it’s IP address with entries in a routing table
Line rate and the order of arrival must be maintained
line rate  15Mpps for 10GE
Notes: The design example you’ll be seeing is from an IP switch. We’ll be looking at the IP lookup function that you typically find on the ingress port of a line card.

## Slide 7: Sparse tree representation of the routing table
18
2
3
IP address | Result | M Ref
7.13.7.3 | F | 
10.18.201.5 | F | 
7.14.7.2 |  | 
5.13.7.2 | E | 
10.18.200.7 | C | 
3
A
…
A
…
B
C
…
C
…
5
D
F
…
F
…
14
A
…
A
…
7
F
…
F
…
200
F
…
F
…
F
*
E
5.*.*.*
D
10.18.200.5
C
10.18.200.*
B
7.14.7.3
A
7.14.*.*
F
…
F
…
F
F
…
E
5
7
10
255
0
1
4
4
A
In this lecture:
Level 1: 16 bits Level 2: 8 bits Level 3: 8 bits
 1 to 3 memory
accesses
Routing table

## Slide 8: IP-Lookup module
done?
CAM
fifo
no
enter
exit
cbuf
put
getToken
The IP table (Tree) is stored in a Content Addressable Memory (CAM) and the input IP makes several lookups to find a match. Different IP addresses require different number of lookups
Completion buffer ensures that departures take place in order even if lookups complete out-of-order
Since cbuf has finite capacity, it gives out tokens to control the entry into the Lookup module
The fifo holds the remaining IP address and the “token” while the memory access is in progress

## Slide 9: Completion buffer: Interface
cbuf
interface CBuffer#(type t);
method ActionValue#(Token) getToken;
method Action put(Token tok, t d);
method ActionValue#(t) getResult;
endinterface
getResult
getToken
put (result & token)
For no dead-cycles, cbuf.getToken and cbuf.put and cbuf.getResult must be able to execute concurrently

## Slide 10: Inside the Completion buffer
The tag in the slot indicates whether it contains a value
A circular buffer with two pointers iidx and ridx, and a counter cnt
  getToken returns iidx and increments iidx and cnt, unless the buf is full
  put puts the value in the indicated slot and marks it V
  getResult returns the value in the slot pointed by ridx and increments ridx
I
I
V
I
V
I
cnt
iidx
ridx
buf
A straightforward implementation will not permit concurrent execution of the three methods

## Slide 11: Completion buffer: Concurrency requirements
cbuf
getResult
getToken
put (result & token)
If we make these methods CF then everything will work concurrently, i.e. (enter CF exit), (enter CF getResult) and (exit CF getResult).
But CF methods are difficult and sometimes impossible to design
Suppose
  (getToken < put), (getToken < getResult),(put < getResult)
  ==> (enter < exit), (enter < getResult), (exit < getResult)
enter
exit

## Slide 12: Concurrency Analysis

## Slide 13: “Happens before” (<) relation
“happens before” relation between the methods of a module governs how the methods behave when called by a rule, action, method or exp
  f < g : f happens before g
  (g cannot affect f within an action)
  f > g : g happens before f
  C : f and g conflict and cannot be called together
  CF : f and g are conflict free and do not affect each
  other
This relation is defined as a conflict matrix (CM) for the methods of primitive modules like registers and derived for the methods of all other modules

## Slide 14: Conflict Matrix for an Interface
Conflict Matrix (CM) defines which methods of a module can be called concurrently
CM for a register:
  Two reads can be performed concurrently
  Two concurrent writes conflict and are not permitted
  A read and a write can be performed concurrently, and it behaves as if the read happened before the write
CM of a register is used systematically to derive the CM for the interface of a module and the CM for rules
 | reg.r | reg.w
reg.r | CF | <
reg.w | > | C
The upper half and lower half of CM are duels

## Slide 15: Conflict ordering
There is a natural ordering between the values of CM entries
This ordering permits us to take intersections of conflict information, e.g.,
  {>}{<,>} = {>}
  {>}{<} = {}
CF = {<,>}
{<} {>}
C = {}

## Slide 16: Deriving the Conflict Matrix (CM) of a module interface
Let g1 and g2 be the two methods defined by a module, such that
  mcalls(g1)={g11,g12...g1n}
  mcalls(g2)={g21,g22...g2m}
conflict(x,y) = if x and y are methods of the same module then CM[x,y] else CF
Derivation
  CM[g1,g2] = conflict(g11,g21)  conflict(g11,g22) ...
   conflict(g12,g21)  conflict(g12,g22) ...
  …
   conflict(g1n,g21)  conflict(g1n,g22) ...
Conflict relation is not transitive
  m1.g1 < m2.g2, m2.g2 < m3.g3 does not imply m1.g1 < m3.g3
Compiler can derive the CM for a module by starting with the innermost modules in the module instantiation tree
Methods called by g1

## Slide 17: Two-Element FIFO Deriving the CM
method Action enq(t x) if (!vb);
if (va) begin db <= x; vb <= True; end
else begin da <= x; va <= True; end
endmethod
method Action deq if (va);
if (vb) begin da <= db; vb <= False; end
else begin va <= False; end
endmethod
db da
vb va
We can derive a conservative CM by ignoring the conditionals
mcalls(enq) = {vb.r, va.r, db.w, vb.w, da.w, va.w}
mcalls(deq) = {va.r, vb.r, da.w, db.r, vb.w, va.w}
  CM[enq,deq] =
  CM[vb.r,va.r]CM[vb.r, vb.r]CM[vb.r,da.w]CM[vb.r,db.r]CM[vb.r,vb.w]CM[vb.r,va.w]
  CM[va.r,va.r]CM[va.r, vb.r]CM[va.r,da.w]CM[va.r,db.r]CM[va.r,vb.w]CM[va.r,va.w]
  CM[db.w,va.r]CM[db.w,vb.r]CM[db.w,da.w]CM[db.w,db.r]CM[db.w,vb.w]CM[db.w,va.w]
  CM[vb.w,va.r]CM[vb.w,vb.r]CM[vb.w,da.w]CM[vb.w,db.r]CM[vb.w,vb.w]CM[vb.w,va.w]
  CM[da.w,va.r]CM[da.w,vb.r]CM[da.w,da.w]CM[da.w,db.r]CM[da.w,vb.w]CM[da.w,va.w]
  CM[va.w,va.r]CM[va.w,vb.r]CM[va.w,da.w]CM[va.w,db.r]CM[va.w,vb.w]CM[va.w,va.w]
  = CF  {<}  CF  {<}  {>}  {>}  C  C  {>}  C
  = C

## Slide 18: Two-Element FIFO another implementation
module mkCFFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False)
rule canonicalize if (vb && !va);
da <= db;
va <= True; vb <= False; endrule
method Action enq(t x) if (!vb);
begin db <= x; vb <= True; end
endmethod
method Action deq if (va);
va <= False;
endmethod
method t first if (va); return da;
endmethod
endmodule
Can both enq and deq execute concurrently?
yes
db da
vb va
But neither enq or deq execute again until the canonicalize rule fires!
…and canonicalize cannot execute concurrently with enq or deq!
 Dead-cycle

## Slide 19: Limitations of registers
Can’t express a FIFO with concurrent enq and deq with no dead cycles!
It is because in a language with only the register primitive no communication can take place in the same atomic action (i.e., clock cycle) between two methods or between two rules or between a rule and a method
EHRs to rescue …

## Slide 20: EHR: Ephemeral History Register
A new primitive element to design modules with concurrent methods

## Slide 21: Ephemeral History Register (EHR) Dan Rosenband [MEMOCODE’04]
D
Q
0
1
0
1
w[0].data
w[0].en
r[0]
normal
bypass
r[1]
w[1].data
w[1].en
r[0] < w[0]
w[0] < w[1] < ….
r[1] < w[1]
r[1] returns:
the current state if w[0] is not enabled
the value being written (w[0].data) if w[0] is enabled w[i+1] takes precedence over w[i]

## Slide 22: Conflict Matrix of Primitive modules: Registers and EHRs
 | EHR.r0 | EHR.w0 | EHR.r1 | EHR.w1
EHR.r0 |  |  |  | 
EHR.w0 |  |  |  | 
EHR.r1 |  |  |  | 
EHR.w1 |  |  |  | 
 | reg.r | reg.w
reg.r | CF | <
reg.w | > | C
Register
EHR
CF
>
CF
>
<
C
>
>
CF
<
CF
>
<
<
<
C

## Slide 23: Making One-Element FIFO into a Pipelined FIFO
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action deq if (v);
v <= False;
endmethod
method t first if (v);
return d;
endmethod
endmodule
Pipelined FIFO behavior
deq < enq
first < deq
first < enq
Ehr#(2, Bool) v <- mkEhr(False);
v[0]
(v[0]);
(v[0]);
v[1]
(!v[1]);
No double write error

## Slide 24: One-Element Pipelined FIFO
module mkPipelineFifo(Fifo#(1, t));
Reg#(t) d <- mkRegU;
Ehr#(2, Bool) v <- mkEhr(False);
method Action enq(t x) if (!v[1]);
d <= x;
v[1] <= True;
endmethod
method Action deq if (v[0]);
v[0] <= False;
endmethod
method t first if (v[0]);
return d;
endmethod
endmodule
deq < enq
first < deq
first < enq
In any given cycle:
If the FIFO is not empty, then simultaneous enq and deq are permitted;
Otherwise, only enq is permitted

## Slide 25: Making One-Element FIFO into a Bypass FIFO
module mkFifo (Fifo#(1, t));
Reg#(t) d <- mkRegU;
Reg#(Bool) v <- mkReg(False);
method Action enq(t x) if (!v);
v <= True; d <= x;
endmethod
method Action deq if (v);
v <= False;
endmethod
method t first if (v);
return d;
endmethod
endmodule
v[1]
(v[1]);
(v[1]);
v[0]
(!v[0]);
No double write error
Bypass FIFO behavior
enq < deq
first < deq
enq < first
d[1];
Ehr#(2, t) d <- mkEhr(?);
Ehr#(2, Bool) v <- mkEhr(False);
d[0] <= x;
In any given cycle:
If the FIFO is not full then simultaneous enq and deq are permitted;
Otherwise, only deq is permitted

## Slide 26: Making a Two-Element Conflict-Free FIFO
module mkCFFifo (Fifo#(2, t));
Reg#(t) da <- mkRegU();
Reg#(Bool) va <- mkReg(False);
Reg#(t) db <- mkRegU();
Reg#(Bool) vb <- mkReg(False)
rule canocalize (vb && !va);
da <= db; va <= True;
vb <= False; endrule
method Action enq(t x) if (!vb);
db <= x; vb <= True;
endmethod
method Action deq if (va);
va <= False;
endmethod
method t first if (va);
return da; endmethod
endmodule
db da
vb va
Desired behavior
enq CF deq
first < deq
first CF enq
Turn all registers into EHRs
Let enq and deq read and write 0th port
Let canocalize read and write the 1st port

## Slide 27: Two-Element Conflict-free FIFO
module mkCFFifo(Fifo#(2, t))
Ehr#(2, t) da <- mkEhr(?);
Ehr#(2, Bool) va <- mkEhr(False);
Ehr#(2, t) db <- mkEhr(?);
Ehr#(2, Bool) vb <- mkEhr(False);
rule canonicalize (vb[1] && !va[1]);
da[1] <= db[1]; va[1] <= True;
vb[1] <= False; endrule
method Action enq(t x) if (!vb[0]);
db[0] <= x; vb[0] <= True;
endmethod
method Action deq if (va[0]);
va[0] <= False;
endmethod
method t first if (va[0]);
return da[0]; endmethod
endmodule
Desired behavior
enq CF deq
first < deq
first CF enq
In any given cycle:
Simultaneous enq and deq are permitted only if the FIFO is not full and not empty
db da
vb va

## Slide 28: CM for Pipelined FIFO
method Action enq(t x) if (!v[1]);
d <= x; v[1] <= True; endmethod
method Action deq if (v[0]);
v[0] <= False; endmethod
method t first if (v[0]);
return d; endmethod
mcalls(enq)={v.r1, d.w, v.w1}
mcalls(deq)={v.r0, v.w0}
mcalls(first)={v.r0, d.r}
= {>}  {>} = {>}
conflict[v.r1,v.r0]  conflict[v.r1,v.w0]  conflict[d.w,v.r0]  conflict[d.w,v.w0]  conflict[v.w1,v.r0]  conflict[v.w1,v.w0]
This is what we expected!
 | Enq | Deq | First
Enq | C | > | >
Deq | < | C | >
First | < | < | CF
CM[enq,deq]=

## Slide 29: Making GCD methods concurrent
module mkGCD (GCD);
Reg#(Bit#(32)) x <- mkReg(0);
Reg#(Bit#(32)) y <- mkReg(0);
Ehr#(2,Bool) busy <- mkEhr(False);
rule gcd;
if (x >= y) begin x <= x – y; end //subtract
else if (x != 0) begin x <= y; y <= x; end //swap
endrule
method Action start(Bit#(32) a, Bit#(32) b)
x <= a; y <= b; busy[1] <= True;
endmethod
method ActionValue (Bit#(32)) getResult
busy[0] <= False; return y;
endmethod
endmodule
Assume b /= 0
interface GCD;
method Action start
(Bit#(32) a,Bit#(32) b);
method ActionValue(Bit#(32))
getResult;
endinterfacecons
if (!busy[1]);
if (x==0);

## Slide 30: Scheduling Hierarchically with Conflict Matrices
The Bluespec Compiler compiles modules with (* synthesize *) attributes separately
  The inner-most modules are compiled first
  For each module, the compiler organizes rules into a list scheduler and computes which rules conflict with each other
  The compiler produces a CM for the interface methods which is used when compiling outer modules
Modules that are not compiled separately are effectively inlined wherever they are used

## Slide 31: Takeaway
Concurrent execution of methods and rules is necessary for performance
Concurrent semantics of a BSV program are still constrained by the one-rule-at-a-time semantics
Many useful modules that use EHRs are in the BSV library but at times you will have to use EHRs explicitly
Methodologically, first get the functionality of your design correct and then introduce EHRs to increase concurrency