## Slide 1: Constructive Computer Architecture: Pipelined Processors
Thomas Bourgeat – EPFL
Slides prepared with Arvind (6.192 – Spring 23 MIT)

## Slide 2: Ordre du jour
Entrée: Pipelining
Plat: Pipelining
Dessert: Pipelining
So pipelining left and right, But first, why so much pipelining?

## Slide 3: Las Meninas (The Maids of Honour) Diego Velázquez 1656
Portrait of Infanta Margarita, the daughter of King Philip IV, in Royal Alcazar, Madrid
By some measures, the most important painting in the Western art history

## Slide 4: Different lighting

## Slide 5: It is big! Museo del Prado, Madrid

## Slide 6: Engages the viewer

## Slide 7: Picasso
Picasso had left Spain because of the Spanish civil war in nineteen thirties and had never seen Las Meninas
In 1956, at the 300th anniversary of Diego Velázquez’s Las Meninas, Picasso revisited Madrid to see the painting
The story goes he came back and locked himself in his studio for three months and painted 58 versions of it – deconstructing and constructing – not copying
  Can be seen at Museo Picasso in Barcelona

## Slide 8: Deconstructing & Constructing: Las Meninas

## Slide 9: Infanta Margarita
Perplexed? Distracted by sun light?

## Slide 10: Deconstructing & Constructing: Las Meninas – Infanta Margarita

## Slide 11: Deconstructing & Constructing: Las Meninas

## Slide 12: Deconstructing & Constructing: Las Meninas

## Slide 13: Deconstructing & Constructing: Las Meninas

## Slide 14: Why?
Picasso was 75 and very aware of his Spanish heritage. Was he trying to improve upon the master’s work?
Picasso reportedly said:
  “I would say..what if you put them a little more to the right or left? I'll try to do it my way, forgetting about Velazquez. The test would surely bring me to modify or change the light because of having changed the position of a character. So, little by little, that would be a detestable Meninas for a traditional painter, but would be my Meninas.”

## Slide 15: Let’s build detestable pipelined processors!

## Slide 16: Multicycle Processor: Analysis
Lot of unused hardware in any given clock cycle!
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
Execute
LoadWait
Fetch
Non-Load Instructions
Load Instructions
Assuming 20% load instructions, and memory latency of one, the average number of cycles per instruction:
  2 x .8 + 3 x .2 = 2.2
higher memory latency will make this number much worse
 pipeline
Notes: 16

## Slide 17: Processor pipelines
Pipelining a processor encompasses many core challenges of computer architecture
  Stringent correctness requirements
  Requires speculative execution of instructions to pipeline at all!
  Requires dealing with a variety of feedback in the pipeline
There are simple pipelined cores, there are also tremendously sophisticated pipelined cores

## Slide 18: New problems in pipelining instructions (over arithmetic pipelines)
Control hazard: pc for Insti+1 is not known until at least Insti is decoded. So which instruction should be fetched?
  Solution: Speculate and squash later if the prediction is wrong
Data hazard: Insti may be data dependent on Insti-1, and thus, it must wait for the effect of Insti-1 on the state of the machine (pc, rf, dMem) to take place
  Solution: Stall instruction Insti until the dependency is resolved
  Number of stalls can be reduced by bypassing, that is by providing additional datapaths
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
Insti
Insti+1
Insti-1

## Slide 19: Plan
Develop a two-stage pipeline by providing a solution for control hazards
Develop a two-stage pipeline by providing a solution for data-hazard
Develop a three-stage pipeline by providing a solution for data hazards and control hazards
To keep the explanations simple, we will first show the solutions with magic memory and then discuss pipelining multicycle processors

## Slide 20: Control hazard
Fetch stage initiates instruction fetch and sends the pc to Execute stage via f2d. It speculatively updates pc to pc+4
Execute stage picks up instruction from f2d and executes it. It may take one or more cycles to do this
These two stages operate independently except in case of a branch misprediction when Execute redirects the pc to the correct pc. All “wrong path” instructions have to be squashed
pc
rf
fetch
D+execute
iMem
dMem
f2d
We will offer a solution that is independent of how many cycles each stage takes
redirect

## Slide 21: Timing diagrams and bubbles
Ex
LW
F
t0 t1 t2 t3 t4 t5 t6 t7 t8 t9 t10 Fetch
Ex
LW
I0
I2
I1
Ex
LW
F
I0
I1
I2
I2
I3
I3
Multicycle Processor
Execution of
I0; I1; I2; I3; ...
only I2 is a load instruction
t0 t1 t2 t3 t4 t5 t6 t7 t8 t9 t10
Fetch
Ex
LW
I0
I2
I1
I0
I1
I2
I2
I3
I3
Two-stage Pipeline
Fetch
Ex
LW
I0
I1
I0
I7
I8
I8
I7
Suppose I0 is a branch instruction which jumps to I7 instead of I1
I1
prediction
squash
Is speculation correct?
If squashing takes more than one cycle, then I7 will get further delayed
bubble: Ex/LW can hold only one instruction

## Slide 22: How do we detect a misprediction?
We initiate a fetch for the instruction at pc, and make a prediction for the next pc (ppc)
The instruction at pc carries the prediction (ppc) with it as it flows through the pipeline
At the Execute stage we know the real next pc. It is a misprediction if the next pc ≠ ppc

## Slide 23: What does it mean to squash a partially executed instruction?
The instruction should have no effect on the processor state
  must not update register file or pc
  must not launch a Store
These conditions are easy to ensure in our two-stage processor because there is at most one instruction in the Ex/LW state

## Slide 24: Killing fetched instructions
In a simple 2-stage design, all the mispredicted instructions were present in f2d. So, the Execute stage can atomically:
  Clear f2d
  Set pc to the correct target
  Hmmm, actually, can it clear f2d?
In highly pipelined machines there can be multiple mispredicted and partially executed instructions in the pipeline; it generally takes more than one cycle to kill all such instructions
Need a more general solution then clearing the f2d FIFO

## Slide 25: Epoch: a method to manage control hazards
Add an epoch register to the processor state
The Execute stage changes the epoch whenever the pc prediction is wrong and sets the pc to the correct value
The Fetch stage associates the current epoch to every instruction sent to the Execute stage
The epoch of the instruction is examined when it is ready to execute. If the processor epoch has changed the instruction is thrown away
nap
inst
targetPC
iMem
rf
execute
dMem
f2d
pc
epoch
Next address predictor,
e.g., pc+4

## Slide 26: An epoch-based solution
rule doFetch ;
let instF=iMem.req(pcF);
let ppcF=nap(pcF); pcF<=ppcF;
f2d.enq(Fetch2Decode{pc:pcF,ppc:ppcF,epoch:epoch,
inst:instF});
endrule
rule doExecute;
let x=f2d.first; let pc=x.pc; let inEp=x.epoch;
let inst = x.inst;
if(inEp == epoch) begin
...decode, register fetch, exec, memory op,
rf update nextPC ...
if (x.ppc != nextPC) begin pcF <= eInst.addr;
epoch <= next(epoch); end
end
f2d.deq; endrule
Can these rules execute concurrently ?
How many epoch values are sufficient?
Notes: Fetch reads and writes PC, writes epoch and enqs ir
Execute writes PC, writes epoch and deqs ir
Fetch < Execute within the same cycle
The machine works with both CF and Bypass FIFOs for ir, but only CF Fifo gives pipelined behavior
If inEp was replaced by epoch in Execute, then Fetch and Execute can not be scheduled concurrently

## Slide 27: An epoch-based solution For concurrency, turn pcF in an EHR
rule doFetch ;
let instF=iMem.req(pcF[0]);
let ppcF=nap(pcF[0]); pcF[0]<=ppcF;
f2d.enq(Fetch2Decode{pc:pcF[0],ppc:ppcF,epoch:epoch,
inst:instF});
endrule
rule doExecute;
let x=f2d.first; let pc=x.pc; let inEp=x.epoch;
let inst = x.inst;
if(inEp == epoch) begin
...decode, register fetch, exec, memory op,
rf update nextPC ...
if (x.ppc != nextPC) begin pcF[1] <= eInst.addr;
epoch <= next(epoch); end
end
f2d.deq; endrule
two values for epoch are sufficient!
Notes: Fetch reads and writes PC, writes epoch and enqs ir
Execute writes PC, writes epoch and deqs ir
Fetch < Execute within the same cycle
The machine works with both CF and Bypass FIFOs for ir, but only CF Fifo gives pipelined behavior
If inEp was replaced by epoch in Execute, then Fetch and Execute can not be scheduled concurrently

## Slide 28: Discussion
Epoch based solution kills one wrong-path instruction at a time in the execute stage
It may be slow, but it is more robust in more complex pipelines, if you have multiple stages between fetch and execute or if you have outstanding instruction requests to the iMem
It requires the Execute stage to set the pc and epoch registers simultaneously which may result in a long combinational path from Execute to Fetch

## Slide 29: Epoch mechanism is independent of the sophisticated branch prediction schemes that we will study later

## Slide 30: 4-Cycle Harvard Processor into a 2-stage pipeline
module mkProcHarvard3cycle(Empty);
Code to instantiate pc, rf, mem, and registers that hold
the state of a partially executed instruction
rule doFetch if (state == Fetch);
Code to initiate instruction fetch; hold pc in a reg;
go to Decode
rule doDecode if (state == Decode);
let inst <- mem.resp;
Code to decode and read the operands from rf; hold
partially executed inst in a reg; go to execute
rule doExecute if (state == Execute);
Code to execute all instructions and initiate dMem request;
hold the (partial) results in a reg; go to LoadWait
rule doLoadWait if (state == LoadWait);
(if Load then wait for the load value), update rf and pc,
go to Fetch
endmodule
Insti
Insti+1

## Slide 31: 4-Cycle Harvard Processor into a 2-stage pipeline
module mkProcHarvard3cycle(Empty);
Code to instantiate pc, rf, mem, and registers that hold
the state of a partially executed instruction
rule doFetch if (state == Fetch);
Code to initiate instruction fetch; hold pc in a reg;
go to Decode
endrule
rule doDecode if (state == Decode);
rule doExecute if (state == Execute); …
rule doLoadWait if (state == LoadWait); …
endmodule
Initiate iMem req; let ppcF=nap(pcF); pcF<=ppcF;
f2d.enq(Fetch2Decode{pc:pcF,ppc:ppcF,epoch:epoch});
let x=f2d.first; let pc=x.pc; let inEp=x.epoch;
let inst <- iMem.res(); f2d.deq;
if(inEp == epoch) // correct path instruction
then ...decode, register fetch, set d2e, go to Execute
else go to Decode

## Slide 32: 4-Cycle Harvard Processor into a 2-stage pipeline
rule doDecode if (state == Decode); …
rule doExecute if (state == Execute);
  Extract fields from d2e, execute and compute nextPC
  if prediction is correct
  then initiate memory op, set e2w, goto LoadWait
  else update pcF; epoch <= next(epoch); goto Decode
rule LoadWait if (state == LoadWait);
Extract fields from e2w;
If necessary, wait for dMem response;
update rf; goto Decode
Can doDecode, doExecute and LoadWait rules fire concurrently?
Can any of these rules fire concurrently with doFetch?

## Slide 33: A 4-cycle, 2-stage pipeline – detestable machine
PC
Decode
Register File
Execute
Data
Memory
Inst
Memory
nap
f2d
Fetch
Execute
MemReq
Insti
Insti+1
Decode,
RegisterFetch
e2w
f2d
MemRes
WriteBack
scoreboard
Notes: 33

## Slide 34: 4-Cycle Harvard Processor into a 2-stage pipeline
module mkProcHarvard2stagePipeline(Empty);
instantiate pc, rf, mem, and registers that hold
the state of a partially executed instruction
rule doFetch if (state == Fetch);
initiate instruction fetch; hold pc in a reg; go to Decode
rule doDecode if (state == Decode);
let inst <- mem.resp;
decode inst and read operands from rf;
hold partially executed inst in a reg; go to Execute
rule doExecute if (state == Execute);
Code to execute all instructions and initiate dMem request;
hold the (partial) results in a reg; go to WB
rule doWB if (state == WB);
(if Load then wait for the load value), update rf and pc,
go to Fetch
endmodule
Insti
Insti+1

## Slide 35: 4-Cycle Harvard Processor into a 2-stage pipeline 1 (correct?)
module mkProcHarvard3cycle(Empty);
instantiate pc, rf, mem, instantiate d2e, epoch and regs ..;
rule doFetch if (stateFD == Fetch);
Initiate iMem req(pc); ppc=nap(pc); pc<=ppc;
f2d <= Fetch2Decode{pc:pc, ppc:ppc, epoch:epoch}
stateFD <= Decode
rule doDecode if (stateFD == Decode);
let inst <- mem.resp; decode inst; read operands from rf;
d2e.enq(Decode2Execute{pc:pc, ppc:ppc, epoch:epoch
v1:rvalv1, v2:rval2}); stateFD <= Fetch
rule doExecute if (stateEW == Execute);
execute all instructions; if mem inst, initiate dMem req;
hold the (partial) results in a reg; go to WB
rule doWB if (stateEW == WB);
(if Load then wait for the load value), update rf,
(if needed, redirect pc;) go to Execute; endmodule
Insti
Insti+1

## Slide 36: 4-Cycle Harvard Processor into a 2-stage pipeline 2a (correct?)
module mkProcHarvard3cycle(Empty);
instantiate pc, rf, mem, instantiate d2e, registers…;
rule doFetch if (stateFD == Fetch);
Initiate inst fetch (pc); ppc=nap(pc); pc<=ppc;
f2d <= Fetch2Decode{pc:pc, ppc:ppc, epoch:epoch}
stateFD <= Decode
rule doDecode if (stateFD == Decode);
let inst <- mem.resp; // suppose the epoch has changed?
let x=f2d; let pc=x.pc; let inEp=x.epoch;
if(inEp == epoch) // correct path instruction
then decode inst; read operands from rf;
d2e.enq(Decode2Execute{pc:pc, ppc:ppc, epoch:epoch
v1:rvalv1, v2:rval2});
else // wrong path instruction and do nothing
stateFD <= Fetch
Insti
Insti+1

## Slide 37: 4-Cycle Harvard Processor into a 2-stage pipeline
rule doFetch if (stateFD == Fetch); …
rule doDecode if (stateFD == Decode); …
rule doExecute if (stateEW == Execute);
  Extract fields from d2e, execute and compute nextPC
  if prediction is correct
  then
  initiate memory op; nextEp = epoch
  set e2w; stateEW <= WB;
  else correct pc; nextEp = next(epoch);
rule doWB if (stateEW == WB);
Extract fields from e2w;
If necessary, wait for dMem response;
update rf; update pc; update epoch
Are these rules correct?
2b (correct?)
Data Hazards!

## Slide 38: 4-Cycle Harvard Processor into a 2-stage pipeline 2a (correct?)
rule doFetch if (stateFD == Fetch);
Initiate inst fetch (pc); ppc=nap(pc); pc<=ppc;
f2d <= Fetch2Decode{pc:pc, ppc:ppc, epoch:epoch}
stateFD <= Decode
rule doDecode if (stateFD == Decode);
let inst <- mem.resp;
let x=f2d; let pc=x.pc; let inEp=x.epoch;
if(inEp == epoch) // correct path instruction
then decode inst; read operands from rf;
d2e.enq(Decode2Execute{pc:pc, ppc:ppc, epoch:epoch
v1:rvalv1, v2:rval2});
else // wrong path instruction and do nothing
stateFD <= Fetch
rule doExecute if (stateEW == Execute); …
rule doWB if (stateEW == WB); …
Insti
Insti+1
If data- hazard then stall

## Slide 39: Data Hazards
An instruction read a register that is updated by another recent instruction

## Slide 40: Pipelining Decode and Execute
pc
rf
fetch
execute
iMem
dMem
f2d
epoch
pc
rf
fetch
decode
iMem
dMem
f2d
epoch
d2e
execute
Execute step probably has the longest propagation delay (decode + register-file read + execute)
Separate Execute into two stages:
  Decode and register-file-read
  Execute – including the initiation of memory instructions
This introduces a new problem known as a Data Hazard, that is, the register file, when it is read, may have stale values

## Slide 41: Three stage pipeline data hazard
D
LW
Ex
I1 must be stalled until I0 updates the register file, i.e., the data hazard disappears
The data hazard will disappear as pipeline drains
F
RF
I0 R1  Ld R2
I1 R4  R1+R2
I2 ...
I0
I1
t1 t2 t3 t4 t5 t6 t7 t8 t9 t10 Fetch
Decode
Ex
LW
I0
I0
E1
W1
I1
I0
I0
I2
I1
I2
E2
W2
D2
mutually exclusive
I1
I1
I2
I2
Complication: the stalled instruction may be a wrong-path instruction
rd < wr
 need a mechanism to stall

## Slide 42: Data Hazard
Data hazard arises when a source register of the fetched instruction matches the destination register of an instruction already in the pipeline
Both the source and destination registers must be valid for a hazard to exist

## Slide 43: Dealing with data hazards (aka read-after-write (RAW) hazard)
Introduce a Scoreboard -- a data structure to keep track of the destinations of the instructions in the pipeline beyond the Decode stage
  Initially the scoreboard is empty
Compare sources of an instruction when it is decoded with the destinations in the scoreboard
Stall the Decode from dispatching the instruction to Execute if there is a RAW hazard
When the instruction is dispatched, enter its destination in the scoreboard
When an instruction completes, delete its source from the scoreboard
  A stalled instruction will be unstalled when the RAW hazard disappears. This is guaranteed to happen as the pipeline drains.

## Slide 44: Scoreboard
method insert(dst): inserts the destination of an instruction or Invalid in the scoreboard when the instruction is decoded
method search1(src): searches the scoreboard for a data hazard, i.e., a dst that matches src
method search2(src): same as search1
method remove: deletes the oldest entry when an instruction commits
scoreboard
search1
search2
insert
remove

## Slide 45: Two designs for scoreboard
A fifo of depth equal to the number of pipeline stages in Execute
Insert: enq (dst)
Remove: deq
Search: compare source against each entry
Counter design takes less hardware, especially for deep pipelines, and is more efficient because it avoids searching each element of the fifo
versus
One Boolean flag for each register (Initially all False)
Insert: set the flag for register rd to True (block if it is already True)
Remove: set the flag for register rd to False
Search: Return the value of the flag for the source register

## Slide 46: Scoreboard implementation using searchable Fifos
function Bool isFound
(Maybe#(RIndx) dst, Maybe#(RIndx) src);
return isValid(dst) && isValid(src) &&
(fromMaybe(?,dst)==fromMaybe(?,src));
endfunction
module mkCFScoreboard(Scoreboard#(size));
SFifo#(size, Maybe#(RIndx), Maybe#(RIndx))
f <- mkCFSFifo(isFound);
method insert = f.enq;
method remove = f.deq;
method search1 = f.search1;
method search2 = f.search2;
endmodule

## Slide 47: Scoreboard in the pipeline
pc
rf
fetch
execute
iMem
dMem
f2d
epoch
pc
rf
fetch
decode
iMem
dMem
f2d
epoch
d2e
execute
If search by Decode does not see an instruction in scoreboard, then that instruction must have updated the state
Thus, when an instruction is removed from the scoreboard, its updates to Register File must be visible to the subsequent register reads in Decode
  remove and wr should happen simultaneously
  search, and rd1, rd2 should happen simultaneously
scoreboard
remove
insert
search
This will require a bypass register file

## Slide 48: WAW hazards
Can a destination register name appear more than once in the scoreboard ?
If multiple instructions in the pipeline can update the register which the current instruction wants to read, then the current instruction has to read the update for the youngest of those instructions; two solutions
  avoid WAW hazard by stalling the decode if the destination is already present in sb
  Use a more complex sb and make sure a destination stays in sb as long as necessary
Notes: WAW – Write-after-write Hazard

## Slide 49: Bypassing
Bypassing is a technique to reduce the number of stalls (that is, the number of cycles) by providing extra data paths between the producer of a value and its consumer
Bypassing introduces new combinational paths, and this can increase combinational delay (and hence the clock period) and area
The effectiveness of a bypass is determined by how often it is used
D
E/LW
F
RF
bypass

## Slide 50: Normal vs Bypass Register File
module mkRFile(RFile);
Vector#(32,Reg#(Data)) rfile <- replicateM(mkReg(0));
method Action wr(RIndx rindx, Data data);
if(rindx!=0) rfile[rindx] <= data;
endmethod
method Data rd1(RIndx rindx) = rfile[rindx];
method Data rd2(RIndx rindx) = rfile[rindx];
endmodule
{rd1, rd2} < wr
Can we design a bypass register file so that:
wr < {rd1, rd2}
Notes: 50

## Slide 51: Processor Performance
Pipelining lowers tClk. What about CPI?
CPI = CPIideal + CPIhazard
  CPIideal: cycles per instruction if no stall
CPIhazard contributors
  Data hazards: long operations, cache misses
  Control hazards: branches, jumps, exceptions
CPI
tClk

## Slide 52: Bypassing
Bypassing is a technique to reduce the number of stalls (that is, the number of cycles) by providing extra data paths between the producer of a value and its consumer
Bypassing introduces new combinational paths, and this can increase combinational delay (and hence the clock period) and area
The effectiveness of a bypass is determined by how often it is used
D
E/LW
F
RF
bypass

## Slide 53: Normal vs Bypass Register File
module mkRFile(RFile);
Vector#(32,Reg#(Data)) rfile <- replicateM(mkReg(0));
method Action wr(RIndx rindx, Data data);
if(rindx!=0) rfile[rindx] <= data;
endmethod
method Data rd1(RIndx rindx) = rfile[rindx];
method Data rd2(RIndx rindx) = rfile[rindx];
endmodule
{rd1, rd2} < wr
Can we design a bypass register file so that:
wr < {rd1, rd2}
Notes: 53

## Slide 54: Bypass Register File using EHR
module mkBypassRFile(RFile);
Vector#(32,Ehr#(2, Data)) rfile <- replicateM(mkEhr(0));
method Action wr(RIndx rindx, Data data);
if(rindex!=0) (rfile[rindex])[0] <= data;
endmethod
method Data rd1(RIndx rindx) = (rfile[rindx])[1];
method Data rd2(RIndx rindx) = (rfile[rindx])[1];
endmodule
wr < {rd1, rd2}
Notes: 54

## Slide 55: Bypass Register File with external bypassing
module mkBypassRFile(BypassRFile);
RFile rf <- mkRFile;
Fifo#(1, Tuple2#(RIndx, Data))
bypass <- mkBypassSFifo;
rule move;
begin rf.wr(bypass.first); bypass.deq end;
endrule
method Action wr(RIndx rindx, Data data);
if(rindex!=0) bypass.enq(tuple2(rindx, data));
endmethod
method Data rd1(RIndx rindx) =
return (!bypass.search1(rindx)) ? rf.rd1(rindx)
: bypass.read1(rindx);
method Data rd2(RIndx rindx) =
return (!bypass.search2(rindx)) ? rf.rd2(rindx)
: bypass.read2(rindx);
endmodule
wr < {rd1, rd2}
rf
move
rd
Notes: 55

## Slide 56: A correctness issue
If the search by Decode does not see an instruction in the scoreboard, then its effect must have taken place. This means that any updates to the register file by that instruction must be visible to the subsequent register reads 
  remove and wr should happen atomically
  search and rd1, rd2 should happen atomically
Fetch
Decode
Execute
WB
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2

## Slide 57: Concurrency and Performance Suppose: doFetch < doExecute
For correctness:
  rf: rd < wr (normal rf)
  sb: {search, insert} < remove
  d2e: enq {<, CF} {deq, first} (CF Fifo)
performance ?
  Dead cycle after each misprediction
  Dead cycle after each RAW hazard
Bypass FIFO does not make sense here
Fetch
Decode
Execute
WB
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2

## Slide 58: Concurrency and Performance suppose: doExecute < doFetch
For correctness;
  rf: wr < rd (bypass rf)
  sb: remove < {search, insert}
  d2e: {first, deq} {<, CF} enq (pipelined or CF Fifo)
Also, no dead cycle after a misprediction
Fetch
Decode
Execute
WB
d2e
redirect
Register File
Scoreboard
remove
search
insert
wr
rd1
rd2
To avoid a stall due to a RAW hazard between successive instructions
  sb: remove ? search
  rf: wr ? rd
<
<
  (bypass rf)

## Slide 59: Summary
Instruction pipelining requires dealing with control and data hazards
Speculation is necessary to deal with control hazards
Data hazards are avoided by withholding instructions in the decode stage until the hazard disappears
Concurrency and performance issues are subtle
  For instance, bypassing necessarily increases combinational path lengths which can slow down the clock

## Slide 60: Non-atomic prediction correction

## Slide 61: Decoupled Fetch and Execute
<inst, pc, ppc, epoch>
<corrected pc, new epoch>
In decoupled systems a subsystem reads and modifies only local state atomically
  In our solution, pc and epoch are read by both rules
Properly decoupled systems permit greater freedom in independent refinement of subsystems
Fetch
Execute

## Slide 62: A decoupled solution using epochs
Add fEpoch and eEpoch registers to the processor state; initialize them to the same value
The epoch changes whenever Execute detects the pc prediction to be wrong. This change is reflected immediately in eEpoch and eventually in fEpoch via a message from Execute to Fetch
Associate fEpoch with every instruction when it is fetched
In the execute stage, reject, i.e., kill, the instruction if its epoch does not match eEpoch
fEpoch
eEpoch
Fetch
Execute

## Slide 63: Control Hazard resolution A robust two-rule solution
PC
Inst
Memory
Decode
Register File
Execute
Data
Memory
+4
f2d
FIFO
FIFO
redirect
Execute sends information about the target pc to Fetch, which updates fEpoch and pc whenever it examines the redirect (PC) fifo
fEpoch
eEpoch
Notes: 63

## Slide 64: Two-stage pipeline Decoupled code structure
module mkProc(Proc);
Fifo#(Fetch2Execute) f2d <- mkFifo; Fifo#(Addr) redirect <- mkFifo; Reg#(Bool) fEpoch <- mkReg(False); Reg#(Bool) eEpoch <- mkReg(False);
rule doFetch; let inst = iMem.req(pcF); ...
f2d.enq(... inst ..., fEpoch); endrule
rule doExecute;
if(inEp == eEpoch) begin Decode and execute the instruction; update state;
In case of misprediction, redirect.enq(correct pc); end f2d.deq; endrule
endmodule

## Slide 65: The Fetch rule
rule doFetch;
let inst = iMem.req(pcF);
if(redirect.empty)
begin let newPcF = nap(pcF);
pcF <= newPcF; f2d.enq(Fetch2Execute{pc: pcF, ppc: newPcF,
inst: inst, epoch: fEpoch});
end
else
begin fEpoch <= !fEpoch; pcF <= redirect.first;
redirect.deq;
end endrule
Notice: In case of PC redirection, nothing is enqueued into f2d

## Slide 66: The Execute rule
rule doExecute; let x = f2d.first;
let inst = x.inst; let pc = x.pc; let inEp = x.epoch; if(inEp == eEpoch) begin ...decode, register fetch, exec, memory op,
rf update nextPC ...
if (x.ppc != nextPC) begin redirect.enq(eInst.addr);
eEpoch <= !inEp; end
end
f2d.deq;
endrule
Can doFetch and doExecute execute concurrently?
yes, assuming CF FIFOs