## Slide 1
Electromagnetic Coupling to Shielded Cables
F. Rachidi
École Polytechnique Fédérale de Lausanne
EMC Laboratory
Farhad.Rachidi@epfl.ch
http://emc.epfl.ch

## Slide 2
Propagation in coaxial structures
Coupling to coaxial cables: Tramsfer impedance and admittance
Outline

## Slide 3
We have been using the concepts of TEM modes for transmission line models
  Let’s review in more depth the derivation of TEM field propagation from a rigorous point of view
Consider a system of ideal conductors (2) and assume that we have an EM field propagating in the z-direction
  With a propagation constant g, such that
A good reference for this material is: Ramo, Whinnery and Van Duzer, “Fields and Waves in Communication Electronics”, John Wiley, 1984.
Further Details of Propagation on TLs

## Slide 4
For this wave-guiding structure, we can categorize the propagating EM fields into 3 classes (or modes)
  Modes with E and H components in the transverse plane, and with a component of H in the propagation direction (TE modes)
  Modes with E and H components in the transverse plane, and with a component of E in the propagation direction (TM modes)
  Modes with E and H components only in the transverse plane (TEM modes)
The TEM modes are the transmission line modes
E & H
Hz
Ez
Hz = Ez =0
Keep in mind that a general excitation of these lines may require all 3 mode for a complete solution !
Propagation on TLs (con’t.)

## Slide 5
For perfectly conducting structures, these 3 modes can be determined separately
  and combined according to the excitation and loading (boundary conditions)
However, for cases involving conductor loss, the modes couple together and are described as hybrid modes
We can derive the properties of these modes from Maxwell’s equations
Propagation on TLs (con’t.)

## Slide 6
Starting with Maxwell’s equations in a source-free region (J = 0)
the vector wave equations can be derived:
This is done by taking the curl of the curl-E equation and simplifying:
The same is done for the curl-H equation
Propagation on TLs (con’t.)

## Slide 7
Noting the vector identity
the vector wave equations reduce to the vector Helmholtz equation for the E and H fields:
In rectangular coordinates (only) these vector equations separate into the individual scalar equations
  With a similar equation for H
This uses the auxiliary relations
Propagation on TLs (con’t.)

## Slide 8
The vector Helmholtz equation for can be written as
Assuming that the z-dependence of all field quantities is of the form
  we have
Thus, the Helmholtz equations for E and H becomes
Propagation on TLs (con’t.)

## Slide 9
For waves propagating in the +z direction (where all fields have a z dependence of ) the Maxwell curl equations are
From these equations, the transverse E and H field components can be expressed in terms of the longitudinal (z) E and H components
Eliminating Ey from these two equations gives an expression for Hx in terms of the Ez and Hz field components.
Propagation on TLs (con’t.)

## Slide 10
The resulting expressions for the transverse fields are
Where Ez and Hz are solutions to the scalar Helmholtz equations
kc2
These equations must be solved together with the appropriate boundary conditions on the conductors.
Propagation on TLs (con’t.)

## Slide 11
TEM fields have Ez and Hz both equal to zero.
  According to the previous expressions for the transverse fields, all fields are zero, unless
In this case, the “wave” equations are
which are Laplace equations for the vector E-field
E and H are in the transverse plane only
We define these as Et and Ht
TEM Fields on TLs (con’t.)

## Slide 12
Thus, the TEM fields on the line can be described by the expressions
and
The fields Et and Ht are related through Maxwell’s equations
0
Impedance of free-space (377 W)
Similarly, the other component is
Caution
On such a line, the E and H fields are related by the free-space impedance . This is not the same impedance as the characteristic impedance of the transmission line, which is a ratio of the line voltage and current.
TEM Fields on TLs (con’t.)

## Slide 13
Using the TEM field description, let us now derive the Telegraphers’ equations
Consider a 2-conductor line of arbitrary cross-section:
  Since E is a solution to the Laplace equation, we can define the potential as
  Differentiating with respect to z gives
  From we have
Derivation of the Telegraphers’ Equations

## Slide 14
Substituting the previous expressions gives
And using the definition of the line inductance (per-unit-length) of the conductors, L´, this expression becomes
  Where I is the current flowing in the conductors
Magnetic flux (per-unit-length) flowing between the two conductors
This is the first Telegrapher equation
Derivation of the Telegraphers’ Equations (con’t)

## Slide 15
The second Telegraphers’ equation is derived by integrating H-field over path 2:
Taking the derivative in z gives
  Using the curl-H equation with Ez = 0 gives
Substituting gives
  Or by relating the charge to the voltage by the line capacitance we have
This is the total charge (per-unit-length) on the conductor.
This is the second Telegrapher equation
Derivation of the Telegraphers’ Equations (con’t)

## Slide 16
Consider the coaxial line (a “shielded” line)
  TEM, TE and TM modes exist
The wave equation for Ez (TM) or Hz (TE) fields is written in cylindrical coordinates as
   denotes either Ez or Hz
  The equation to be solved for (r,) is
  This equation can be solved by the method of separation of variables
The Coaxial Line

## Slide 17
The differential equations for g() and f(r) become
  Where
  The solutions for g() and f(r) are given as
  Thus, the total solution for  is
k = w/c
Propagation constant of waves in the z-direction: e z
Bessel functions of integer order
The Coaxial Line (con’t)

## Slide 18
The coefficient kc is constrained from the boundary conditions on :
This leads to the following characteristic equations that must be solved for kc
Note that for lossless coaxial lines, kc is real
The Coaxial Line (con’t)

## Slide 19
From the definition of
  we have the z propagation constant given by
  For low frequencies, where w/c < kc the propagation constant  is real and the mode propagation in z is attenuated as
  For higher frequencies, where w/c > kc the propagation constant  is imaginary and the mode propagation in z is
Thus, as long as the frequency is lower than the cutoff frequencies of the TE or TM modes, they are attenuated on the line
Cutoff frequencies are w c = c kc
The Coaxial Line (con’t)

## Slide 20
At low frequencies, the only propagating mode on the line is the TEM mode:
With the following derived relationships for the inductance and capacitance
  and propagation constant and transmission line impedance
TEM Propagation on the Coaxial Line

## Slide 21
Low frequency losses in the coaxial line occur in 2 ways:
  Dielectric loss – represented by a shunt element G´
  Conductor loss – represented by a series element R´
The dielectric loss is usually small for practical cables
  It may be calculated using the same form of the equation as for the capacitance
The conductor loss invalidates the TEM assumption
  To get around this problem, we assume losses are small, and use a quasi-TEM approximation
  Thus, the resulting line model is similar to that previously considered for the 2-conductor line
sd is the conductivity of the dielectric material in the cable
A longitudinal E-field exists on the conductor surface
Due to the non-zero conductivity of the conductors
Losses in the Coaxial Line (con’t)

## Slide 22
General expressions are available for the impedance of a lossy coaxial line at higher frequencies
  The per-unit-length “resistance” of the cable is frequency dependent and is complex – it is an impedance
  See Schelkunoff’s paper or Vance
Z´in represents an additional voltage drop along the line due to the internal conductor
A similar term is found for the outer conductor
E. F. Vance, “Coupling to Shielded Cables, Krieger Publishing Co, 1987, page 37.
Losses in the Coaxial Line (con’t)

## Slide 23
Expressions for the internal impedance of the inner conductor
  Define the wave propagation constant in the conducting material (metal)
  Z´in is given by
Modified Bessel functions
Losses in the Coaxial Line (con’t)

## Slide 24
Expressions for the internal impedance of the outer conductor
Modified Bessel functions
Losses in the Coaxial Line (con’t)

## Slide 25
For most EMC applications involving cables, the skin depth in the metal is small compared with the cable radius
The high-frequency expressions for these impedances are applicable
Losses in the Coaxial Line (con’t)

## Slide 26
Propagation in coaxial structures
Coupling to coaxial cables: Transfer impedance and admittance
Outline

## Slide 27
Coupling to Shielded Cables

## Slide 28
A coaxial line can be excited by a voltage or current source at the end of the line
Another type of excitation occurs when an external current produces EM fields that diffuse into the interior, and excite the inner conductor
Excitation of a Coaxial Line

## Slide 29
The two-circuit (inside and outside) problem involves coupled solutions to Maxwell’s equations in four (4) regions
  This is tedious to solve
  However, it is possible to use a good shielding approximation where we assume that the outside problem is not affected by the inside geometry
Excitation of a Coaxial Line (cont’d)

## Slide 30
Inside the coax, we note that the effect of the external current as it diffuses through the shield is to create a voltage drop along the inside of the shield
  This internal voltage drop appears as an excitation voltage source to the internal conductor
External problem computes current and voltage on the outside of the coax, neglecting the internal details
The internal problem is modeled by the per-unit-length transmission line model, together with a distributed voltage source V´s
Excitation of a Coaxial Line (cont’d)

## Slide 31
Ei
The current flow in the cable sheath will create an axial electric field inside the sheath.
Due to the skin effect, the current distribution and the associated E-field distribution in the sheath cross section are not uniform
Excitation of a Coaxial Line (cont’d)

## Slide 32
The internal voltage source V´s arises from the external current Iexternal acting on the conductive shield material
As such, it can be represented by a per-unit-length transfer impedance, Z´t as
Excitation of a Coaxial Line (cont’d)

## Slide 33
The transfer impedance of a thin tubular shield has been developed by Schelkunoff:
Note the exponential decrease of the transfer impedance with shield thickness Δ at high frequencies
Equals Ro, the DC resistance of the shield
The Transfer Impedance

## Slide 34
Plot of the calculated Z´t
At DC, the transfer impedance is just the tube resistance
At higher frequencies, it decreases, due to the skin effect.
Magnitude
Phase
Illustration of the Transfer Impedance

## Slide 35
The internal line is thus represented by a transmission line with a distributed voltage source excitation
The response of the internal line can be computed by integrating over the source distribution:
See Chapter III on Field-to-Line Coupling.
Solution for the Internal Responses

## Slide 36
As frequencies of operation become higher, we observe that the model for Z´t is inadequate for some shielded cables
Higher frequency response appears to be growing as ω
This is due to an additional contribution to the transfer impedance that occurs in braided shields
Problems with the Transfer Impedance

## Slide 37
The braid is not really a homogeneous shield
  It has small openings
  The external B-field is able to penetrate inside and the flux introduces an additional component to the transfer impedance
Thus, at high frequencies, the transfer impedance for braided cables can be written as
Problems with the Transfer Impedance (cont’d)

## Slide 38
Various models for computing Z’t are available
An alternate (and more accurate) approach is to measure this cable parameter
Measured surface transfer impedance of 1-1/4” diameter copper pipe with a single hole
Determination of the Transfer Impedance

## Slide 39
For a number of years, the shielding model for braided cables still did not agree well with measurements
  Excitation was provided by only 1 field component – the H-field
  What was missing was the dual current source excitation – from the external the E-field
  This source is not included in the classical formulation of Schelkunoff, but it is present if the shield has holes in it.
I´s(x)
Improvements in the Shielding Model

## Slide 40
E-field penetration inside the shield of a coaxial cable through a single aperture
Improvements in the Shielding Model

## Slide 41
The per-unit-length current source for the internal line is represented by a transfer admittance, Y´t
In this manner, the total internal load response contains two contributions, just like the previous cross-talk calculation
For solid coaxial shields, this term is neglected.
See Chapter III on Field-to-Line Coupling.
Improvements: The Transfer Admittance

## Slide 42
Transfer impedance is specified as
Transfer admittance is
C’t is often specified through the “shield coupling factor”
Internal and external line capacitances
Measurements Provide Practical Cable Data

## Slide 43
Vance provides computed data for real cables
D
M´t
S´t
Ro
Measurements Provide Practical Cable Data

## Slide 44
For L << λ:
Measurements of Transfer Impedance and Admittance

## Slide 45
Notice that in the triaxial setup, both transmission lines, the external and the internal, are terminated in their characteristic impedances Zcs and Zci respectively.
Measurements of Transfer Impedance and Admittance: Improved Setup
Triaxial Adapted Measurement Setup

## Slide 46
The current and the voltage in the external line (neglecting the effect of the internal wire) will be given by
Under the condition of an electrically short cable, we can derive the following expressions for the transfer impedance and admittance
Measurements of Transfer Impedance and Admittance: Improved Setup

## Slide 47
Examples of Measured Transfer Impedance

## Slide 48
- RG-58 coaxial cable
- L=30 m, h = 1 m
- σg = 0.01 S/m and εr = 10.
- = 100 Ω and = 100 Ω.
Matched internal impedances
( 50 Ω).
- Incident plane wave with
Eo=52.5 kV/m, α = 4x106 s-1, β = 4.76x108 s-1.
- Elevation angle ψ=30o , azimuth angle ϕ=0 o, polarisation angle α=0 o.
Numerical Example of the Response of
a Shielded Cable

## Slide 49
Spectral magnitude
Transient Response
Numerical Example of the Response of
a Shielded Cable: External Response

## Slide 50
Spectral magnitude
Transient Response
Numerical Example of the Response of
a Shielded Cable: Internal Response

## Slide 51
[1] F. M. Tesche, Electromagnetic Compatibility, Clemson University.
[2] F. M. Tesche, M. Ianoz, T. Karlsson, EMC analysis methods and computational models. New York: Wiley, 1997.
[3] Ramo, Whinnery and Van Duzer, “Fields and Waves in Communication Electronics”, John Wiley, 1984.
[4] E. F. Vance, Coupling to shielded cables / Edward F. Vance. New York : Wiley, 1978.
[5] B. Démoulin and L. Koné. (2010) Shielded Cables Transfer Impedance Measurement. IEEE EMC Society Newsletter. 38-45.
References