## Slide 1
Introduction to Electromagnetic Compatibility
F. Rachidi
École Polytechnique Fédérale de Lausanne
Electromagnetic Compatibility Laboratory
Farhad.Rachidi@epfl.ch
http://emc.epfl.ch

## Slide 2
EMC Overview
  Problem definition
  Various EMI environments
  Examples of EMI effects on systems
  EMC Specifications and Standards
History of EMC
Decibels and Common EMC Units
Outline

## Slide 3
EMC deals with interference and the prevention of it through the design of electronic systems.
What is EMC?
Notes: It’s a very broad discipline ranging from nano and microelectronics to communications and power systems.
Sources of interference can be natural or man-made

## Slide 4
Electromagnetic Disturbance (EMD)
  Any electromagnetic phenomenon which may degrade the performance of a device, equipment or system.
Electromagnetic Interference (EMI)
  Degradation of the performance of a device, transmission channel or system caused by an electromagnetic disturbance.
Electromagnetic Susceptibility (to a disturbance)
  The inability of a device, equipment or system to perform without degradation in the presence of an electromagnetic disturbance.
  NOTE - Susceptibility is a lack of immunity.
Electromagnetic Immunity (to a disturbance)
  The ability of a device, equipment or system to perform without degradation in the presence of an electromagnetic disturbance.
Useful Definitions

## Slide 5
Study and characterization of the sources producing the interfering EM environment.
Evaluation of the propagation of the EM environment from the source to the “victim”.
By E-field (or capacitive) interaction mechanisms.
By H-field (or inductive) interaction mechanisms.
By conducted (hard-wired) interactions.
Study of the effects of the EM environment on equipment (damage, upset, loss of function, etc.
Fundamental Elements of EMC

## Slide 6
A system is electromagnetically compatible with its environment if it satisfies three criteria:
  It does not cause interference with other systems
  It is not susceptible to emission from other systems
  It does not cause interference with itself
EMC: Definition

## Slide 7
Interference occurs if the received energy causes the receptor to behave in an undesired manner.
Three ways to prevent interferences:
  Suppress the emission at its source
  Make the coupling path as inefficient as possible
  Make the receptor less susceptible to the emission
Aspects of EMC
Coupling Path
Source
Victim
(receptor)

## Slide 8
Fast (short) rise/falltimes of digital pulses are the primary contributors to the high frequency spectral content of these signals.
In general, the higher the frequency of the signal to be passed through the coupling path, the more efficient the coupling path.
So we should increase (slow) the rise/falltimes of digital signals as much as possible.
However, these can be increased only to a point at which the digital circuitry malfunction
Example: Reduction of Emission at its Source

## Slide 9
Digital signals
x(t)
t
tr
tr
τ
T
A
A/2
GTL+ : tr = 300 ps
ECL: tr = 100 ps
Example: Reduction of Emission at its Source (cont’d)

## Slide 10
Spectrum Envelope
f
2Aτ/T
1/(πτ)
1/(πtr)
-20 dB/decade
-40 dB/decade
Example: Reduction of Emission at its Source (cont’d)

## Slide 11
Radiated EMI is most often found in the frequency range from 30 MHz to 10 GHz (according to the Standards).
Emission Sources Clocks, clock lines, data lines; switching power supplies
Susceptibility Clock lines & data lines poorly laid out, improperly terminated
Solutions Balanced transmission lines, proper terminations, groundplanes, shielding, limited rise & fall time drivers
Solutions Shielding, layout, filtering, groundplanes, differential line receivers
Overview of Radiated EM Interference (EMI)

## Slide 12
Conducted EMI is most often found in the frequency range of several kHz to 30 MHz (according to the Standards).
Emission Sources Power supplies (switching), power rails, motors, relays
Susceptibility A.C. power cord poorly filtered, power rails poorly decoupled
Solutions Good bypassing & decoupling practices, layout, groundplanes, shielding
Solutions Good bypassing & de-coupling practices, layout, groundplanes, shielding, power line filtering
Overview of Conducted EM Interference (EMI)

## Slide 13
Categories of EMC Problems

## Slide 14
Natural Sources
  Lightning
  Electrostatic discharge (ESD)
  Triboelectric charging effects
  Solar & cosmic noise, and
  Geomagnetic field effects
There Are Many Different Types of Sources in EMC

## Slide 15
Lightning Discharge
Lightning Incidence
0.2 | 0.4 | 0.6 | 0.8 | 1 | 2 | 4 | 6 | 8 | 10 | 15 | 20 | 30 | 40 | 50 | 70
Source: NASA, observation period: 04/1995 – 02/2003
Notes: A global map of total lightning flash density (per square kilometer per year) based on data from two satellite detectors, OTD (5 years) and LIS (3 years)

## Slide 16
Lightning Discharge
Major Types of Lightning

## Slide 17
Lightning Discharge
Lightning effects in the middle and upper atmosphere

## Slide 18
200’000 discharges per year
Lightning Activity in Switzerland:
Flash Density: Number of Flashes per km2 per year

## Slide 19
Notes: Example of a recent event illustrating EMC. This happened a couple of weeks ago and following a lightning strikes, a number of disks were damaged in the Google data center in Belgium.
Lightning is one of the most important sources of electromagnetic disturbances, epecially considering the fact that every second more than 50 lightning flashes strike the earth on average!

## Slide 20
Kamatzu airforce base, Japan
Lightning to Aircraft

## Slide 21
Entire Hydro Quebec power system collapsed due to G5 geomagnetic storm
6 million customers lost power
Entire system collapsed in 90 seconds
Restoration took 9 hours
Geomagnetic storms: March 13, 1989
Notes: Coronal mass ejection (CME) from the Sun: If this massive bubble of plasma and radiation is aimed right at Earth, it can pose a serious threat to satellite operations and even to power grids on the ground. On March 10, 1989, a coronal mass ejection (CME) about the size of 36 Earths erupted from the sun's roiling surface and ripped through space at 1.6 million kilometers per hour. Two days later, the torrid gas cloud crashed against Earth's magnetosphere—the magnetic field generated by the planet's spinning molten iron core that helps deflect the solar wind and more potent solar jetsam. This blast from the sun severely disrupted the magnetosphere and set off a geomagnetic superstorm.
These electrical surges infiltrated power grids all over North America and northern Europe, and even destroyed a transformer at a nuclear power plant in New Jersey.
Such storms occur every 60 years or so.

## Slide 22
Man-made Sources
  Electric power system noise
  Computer clock circuitry
  Switching power supplies
  Electric motors
  Radio/radar transmissions
  Automotive and railroad noise, and
  Nuclear electromagnetic pulse (NEMP)
EMC Sources (cont’d)

## Slide 23
The first HEMP
400 km above Pacific
EMP affected electric power in Hawaii
July 9, 1962
High Altitude EMP: Starfish Prime
Notes: The first human-caused EMP occurred in 1962 when the 1.4 megaton Starfish Prime thermonuclear weapon detonated 400 km above the Pacific Ocean.
One hundred times bigger than what dropped on Hiroshima, Starfish Prime resulted in an EMP which caused electrical damage nearly 900 miles away in Hawaii. It knocked out about 300 streetlights, set off numerous burglar alarms, and damaged a telephone company microwave link that shut down telephone calls from Kauai to the other Hawaiian islands.
And that was from 900 miles away.
and in 1962, we were not using sensitive electronic devices as we are today.

## Slide 24
Narrow-band, or continuous wave (CW) spectra
Transients
Large-amplitude signals (lightning & NEMP), and
Weak signals (radio signals, micro-circuitry signals)
With Such Diverse Sources, Many Different Types of Signal are Found

## Slide 25
Examples of EMI Sources

## Slide 26
Radio and TV Services Also Can Produce EMI

## Slide 27
Example of a Complex System

## Slide 28
Example of a Complex System

## Slide 29
The relationship between the frequency spectral content F(ω) and the transient waveform f(t) is given by the Fourier Transform relationships:
Transient Signals and Spectra Are Related

## Slide 30
Relationships Between Transient and Spectral Responses

## Slide 31
Transient and Spectral Relationships (cont’d)

## Slide 32
Unwanted or unplanned EM stresses have caused equipment upset and damage to components
Let’s examine a few cases ……
Improper EMC Design May Cause Problems

## Slide 33
Example of a 7.5 kV voltage surge on a silicon-based microprocessor
  Typical of what might be expected from a lightning-induced surge or electrostatic discharge (ESD)
Burn-out damage of the aluminum interconnects on the chip
Electrical Damage to Components

## Slide 34
Examples of damage to copper vias on a printed circuit board, subjected to large currents
The basic damage mechanism is the vaporization of the circuit material by heat (I2R loss) in the conductor
Electrical Damage to Components (cont’d)

## Slide 35
There can be many different types of effects of an electromagnetic disturbance (EMD) on an electrical system, which is comprised of many individual components
  Temporary EM interference (EMI)
    noise in analog systems or recoverable upset in digital systems
  Permanent loss of function of the system (permanent upset)
    requiring manual intervention (computer reboot)
  Equipment damage due to component failure
Increasing power level of the EMD
Effects of EMD on Systems

## Slide 36
Experimental study of EM field coupling to PCs
  Performed in an anechoic chamber
  PC was illuminated by a horn antenna from a distance of 1m
  E-field varied up to 100 V/m.
Three different PCs were tested
  Varying frequencies, field strengths and modulation of the carrier.
1. LoVetri, J, A.T.M. Wilbers and A.P.M. Zwamborn, “Microwave Interaction with a Personal Computer: Experiment and Modeling”, Proceedings of the 1999 Zurich EMC Symposium.
Data on Computer System Upset1

## Slide 37
Data on Computer System Upset (cont’d)

## Slide 38
High Power EM (HPEM) susceptibility testing was conducted on automobiles, PC's and unshielded military equipment
  Used radar pulses at 1-3 GHz with a few microsecond pulse length and pulse repetition frequencies around 1 kHz
Results included
  Interference/upset (requiring a reboot or restart of a car) occurred for field strengths of a few 100 V/m
  Permanent damage required 20-30 dB higher levels.
2. M. Bäckström, "HPM Testing of a Car: A Representative Example of the Susceptibility of Civil Systems," Workshop W4, Proceedings of the 13th International Zurich Symposium and Technical Exhibition on EMC, February 1999, pp. 189-190.
Possibility of Permanent Damage2

## Slide 39
Conclusions:
  Upset could be caused in unprotected electronic systems from a maximum distance of around 500 meters for a high-power microwave (HPM) source
    Possibly located in a vehicle like a van or truck
  For a source of a smaller size, such that it can be located in a suitcase, the estimated distance decreases to 50 meters.
  The maximum distance for causing permanent physical damage was estimated to be around 15 meters for the HPM van,
    while the suitcase source had to be placed very close to, or even in direct contact with the system.
Possibility of Permanent Damage (cont’d)

## Slide 40
Summary of HPEM Effects from Bäckström

## Slide 41
This depends on many factors:
  EM source parameters
    Distance, orientation, polarization
  Waveform characteristics
    Carrier frequency, pulse repetition, signal strength
  System (victim) electrical configuration
    Coupling characteristics (topology), shielding, cable design
  System robustness
    Failure levels of components, upset levels of electronics
  State of the system (for upset issues)
With so many parameters describing upset and/or damage thresholds, statistical methods are often used to describe system behavior to EMD.
Predicting Upset and/or Damage is Very Complicated

## Slide 42
The basic idea is to deliberately illuminate a system with EM fields, thereby causing failure or damage
High power microwave (HPM) sources and radiators (antennas) are being studied and developed, and
Fast-pulse sources (ultra-wide band) have been developed
Demonstrated EMI Effects Have Led to the Concept of an Electromagnetic Weapon

## Slide 43
http://bcove.me/h1kel0mp
Counter-electronics High-Powered Missile Project Test

## Slide 44
Other Applications of High Power Electromagnetic (HPEM) Sources

## Slide 45
Other Applications of HPEM Sources

## Slide 46
There are two major disciplines within the EMC area
  One dealing with regulatory and administrative issues
  The other with design, modeling and analysis
Functional Divisions in EMC

## Slide 47
These two different disciplines are related by testing
  Component “bench” testing,
  EMC compliance testing, and
  System susceptibility testing
Functional Divisions in EMC (cont’d)

## Slide 48
Many EMC activities are mandated by governmental standards or requirements:
  for promotion of health and safety, and
  for compatible operation of electrical equipment
Pertinent activities include the development of
  Emission standards for equipment,
  Susceptibility standards for equipment,
  Test methodology and protocol, and
  Design standards.
EMC Specifications and Standards

## Slide 49
Two different classes of digital equipment are defined
  Class A - Devices operating in a commercial, industrial or business environment
  Class B - Devices operating in a residential environment
Limitations on the EM interference from these devices are specified through
  Conducted emissions
  Radiated emissions
Class B requirements are more stringent that Class A
Common Standards for Commercial Products

## Slide 50
Example: Immunity Test in a Semi-Anechoic Chamber

## Slide 51
Conducted emission limits EN55022 (CISPR 22) for information technology equipment.
Industrial and Commercial
Devices
Residential Devices
International Standards Example: Conducted Emission Limits

## Slide 52
Radiated emission limits EN55022 (CISPR 22) for information technology equipment.
Class A equipment: 30 m
Class B Equipment: 10 m
International Standards Example: RadiatedEmission Limits

## Slide 53
Measurement of Radiated Emissions

## Slide 54
Measurement of Radiated Immunity

## Slide 55
Product Development, Time
Research
Phase
Design
Phase
Production
Phase
Costs
Available technical solutions
Test
Phase
EMC Intervention

## Slide 56
1930s: Radio interference from electrical apparatus (motors).
1933: Formation of CISPR (Comité International Spécial de Perturbations radioélectriques). Issues addressed by CISPR: definition of acceptable limits for radio interference and measuring methods.
World War II: Extensive interest in using telecommunication and radar facilities by military. Development of military standards for electromagnetic interferences up to 20 MHz.
The most significant increase in the interference problems occurred with the invention of high-density electronic components such a sthe bipolar transistor in 1950s, the integrated circuit in 1960s and the microprocessor chip in the 1970s.
History of EMC

## Slide 57
The frequency spectrum also became more crowded with the increased demand for voice and data transmission. This required considerable planning with regard to spectrum utilization.
1979: American regulations by the FCC (Federal Communications Commission) was published limiting the electromagnetic emissions of all digital devices to be below certain limits. Because no digital device could be sold in the United States unless its EM emissions met these limits imposed by FCC, the subject of EMC generated intense interest.
In Europe, starting from 1996, no electrical device could be sold unless its emissions and immunity met the limits imposed by CENELEC.
History of EMC (cont’d)

## Slide 58
Primary quantities of interest in EMC problems are:
  Conducted emissions Voltage (V) and current (A)
  Radiated emissions E-field (V/m) and H-field (A/m).
Associated with these primary quantities are:
  Power (W) or power density (W/m2)
The numerical range of these quantities can be quite large.
  For example, E-fields can have values ranging from 1 µV/m to 200 V/m or more. This represents a dynamic range of over 8 orders of magnitude.
Thus, EMC units are often expressed in decibels (dB).
  Decibels have the property of compressing data, e.g., a range of 108 is 160 dB.
Decibels and Common EMC Units

## Slide 59
Decibels are the logarithmic ratio of two quantities. Initially, dB has been used to express the ratio of two powers P1 et P2 :
Absolute power, voltage or current levels are expressed in dB by giving their value value referenced to some base quantity. For example, voltages are commonly expressed relative to 1 µV as dBµV:
Example : U1 = 120 dBµV  U1 = 106 µV= 1 V
Decibels and Common EMC Units (cont’d)

## Slide 60
In general, a quantity X referenced to y:
Common reference values in EMC:
Quantity
‘Unit’
Reference value
Voltage
dBμV
1 μV
Current
dBμA
1 μA
Power
dBm
1 mW
E-field
dBμV/m
1 μV/m
H-field
dBμA/m
1 μA/m
Decibels and Common EMC Units (cont’d)