## Slide 1
Electromagnetic Field Coupling: Frequency-Domain Solutions
Farhad Rachidi
Swiss Federal Institute of Technology (EPFL)
EMC Laboratory
Farhad.Rachidi@epfl.ch
http://emc.epfl.ch

## Slide 2
The voltage wave equation is found by taking the derivative of the first Telegrapher’s equation with respect to line position (x) :
and then substituting in the second equation
  To yield the voltage wave equation
A similar procedure is used to derive the current wave equation
𝛾2
Frequency Domain Solution
Classical Telegrapher’s Equations

## Slide 3
Thus, the telegrapher's equations can be manipulated into two uncoupled wave equations for the line voltage and current:
where 𝛾 is a complex, frequency-dependent propagation constant of the line defined as
  with Z'(ω) = R' + jωL' and Y'(ω) = G' + jωC' .
Frequency Domain Solution
Classical Telegrapher’s Equations

## Slide 4
The solutions to the wave equations for the voltage V is in the form of exponential functions:
  and the same is true for the current, I
  Note that the e –𝛾 x terms correspond to positive traveling waves on the line
And the e +γx terms correspond to negative traveling waves
Frequency Domain Solution
Classical Telegrapher’s Equations

## Slide 5
The voltage and current traveling wave components are related by the line parameters
  Consider the positive traveling waves:
  Substituting V+ into the first Telegrapher equation
  gives
This is the characteristic impedance of the transmission line, Zc
Frequency Domain Solution
Classical Telegrapher’s Equations

## Slide 6
Complex propagation constant
Characteristic impedance
Positive voltage wave:
Phase velocity:
Different frequencies in the spectrum of a pulse propagate at different speeds and suffer different attentuation: Dispersion effect
Attenuation constant
Phase constant
Lossy line
Input pulse
Output pulse
Frequency Domain Solution
Classical Telegrapher’s Equations

## Slide 7
Frequency Domain Solution
Characteristic Impedance of Common TLs

## Slide 8
Frequency Domain Solution
Characteristic Impedance of Common TLs

## Slide 9
Frequency Domain Solution
Characteristic Impedance of Common TLs

## Slide 10
Frequency Domain Solution
Characteristic Impedance of Common TLs

## Slide 11
Frequency Domain Solution
Characteristic Impedance of Common TLs

## Slide 12
Frequency Domain Solution
Characteristic Impedance of Common TLs

## Slide 13
Consider an infinite transmission line excited by a series voltage source Vo at location xs
  The voltage source launches voltage and current waves in both + and – directions
Away from the source, the voltage and current is described by the previously derived traveling wave solutions
Because the line is infinite, there are no reflections from the ends
  Thru, for x > xs, only positive traveling waves exist
  and for x < xs, the waves are only negative traveling.
Frequency Domain Solution
Infinite line excited by a series voltage source

## Slide 14
For this line, the responses are expressed as
  where A and B must be determined from the excitation conditions.
At x = xs, the current must be continuous
  I(xs+) = I(xs–)
And the voltage is discontinuous by the source voltage
  V(xs+) = V(xs–)+ Vo
Frequency Domain Solution
Infinite line excited by a series voltage source

## Slide 15
From the current condition I(xs+) = I(xs–) we obtain
From the voltage condition V(xs+) = V(xs–)+ Vo we get
Thus, the total solution is
  V(x) = (Vo/2)e - 𝛾(x- xs) for x > xs
  V(x) = (-Vo/2)e 𝛾(x-xs) for x < xs
  and
  I(x) = (Vo/2Zc )e - 𝛾(x-xs) for x > xs
  I(x) = (Vo/2Zc )e 𝛾(x-xs) for x < xs
Frequency Domain Solution
Infinite line excited by a series voltage source

## Slide 16
The same analysis procedure can be used for a shunt current source Io exciting the line
The expressions for the line voltage and current are
  V(x) = (IoZc/2) e -𝛾(x-xs) for x > xs
  V(x) = (IoZc/2) e 𝛾(x-xs) for x < xs
  and
  I(x) = (Io/2)e - 𝛾(x-xs) for x > xs
  I(x) = (–Io/2)e 𝛾(x-xs) for x < xs
x
Reference conductor
I
o
x
s
Frequency Domain Solution
Infinite line excited by a parallel currentsource

## Slide 17
Consider a line of length L with termination impedances Z1 and Z2 at the ends:
  For x < xs, both positive and negative traveling waves exist
    due to reflections at the load
Same is true for x > xs
On each section of line, 2 sets of coefficients A & B are needed to represent the responses
  Thus, a total of 4 unknowns are required:
Line is excited by both a series voltage source Vo and a shunt current source, Io at x = xs
Frequency Domain Solutions
Finite line excited by a series voltage/shunt current source

## Slide 18
The 4 unknown coefficients are determined from 4 conditions imposed on the solution:
  At the source at xs, the line current is discontinuous by the amount Io  I(xs+) = I(xs–)+ Io
  At the source, the line voltage is discontinuous by the amount Vo  V(xs+) = V(xs–)+ Vo
  At the ends of the line at x = 0 and L, the total line voltage and current are related by the load impedance ZL as
Note that the change of sign occurs here due to the definition of the direction of the “line current”
Frequency Domain Solutions
Finite line excited by a series voltage/shunt current source

## Slide 19
Voltage Reflection Coefficient:
Realistic lines are not infinite in length. Consider the case of a finite line extending from x = 0 to x = L as shown in Figure below. At the end of a line there is an impedance element ZL, which is assumed to be a complex valued quantity relating the total load voltage VL to the load current IL. A traveling wave propagating in the positive direction and incident on the load will create a reflected wave which propagates in the negative direction away from the load. Due to this reflection, at any point on the line there will be a combination of both positive and negative propagating waves. It is useful to define the ratio of the reflected voltage wave at any point along the line to the incident voltage wave as a general reflection coefficient as
ρ(x) =
=
Frequency Domain Solutions
Finite line excited by a series voltage/shunt current source

## Slide 20
Voltage Reflection Coefficient (cont’d):
The voltage and current at any point on the line can now be expressed in terms of the voltage reflection coefficient as
The ratio of line voltage to current defines an impedance quantity which is the input impedance of the line at the location x looking towards the load. This is expressed as
At the load, the input impedance is just the load impedance
V(x) = ae-𝛾x + be 𝛾 x = ae- 𝛾 x + ρ(x)ae- 𝛾 x = ae- 𝛾 x [1 + ρ(x)]
I(x) = Yc(ae- 𝛾 x - be 𝛾 x) = Yc(ae- 𝛾 x - ρ (x)ae- 𝛾 x) = Ycae- 𝛾 x [1 - ρ (x)]
Frequency Domain Solutions
Finite line excited by a series voltage/shunt current source

## Slide 21
And from this expression, the reflection coefficient at the load can be determined to be
If ZL = Zc, ρ = 0 and there is no reflected wave
  We say that the line is “matched”
For an open circuit load, ZL = ∞ and ρ= 1
For a short circuit load, ZL = 0 and ρ= –1
Load impedance
Characteristic impedance of the transmission line
Frequency Domain Solutions
Finite line excited by a series voltage/shunt current source

## Slide 22
Using the source and load termination conditions, the 4 coefficients can be evaluated to yield the line voltage and current expressions for x > xs:
V(x) = [(eγxs - ρ1e–γxs)Vo + (eγxs + ρ1e–γxs)ZcIo]
I(x) = [(eγxs - ρ1e–γxs)Vo + (eγxs + ρ1e–γxs)ZcIo]
Notes:
Voltage and current source terms
Observation location on line, with x > xs
Source location, xs
Resonance term
Also observe that the excitation terms are identical for the current and the voltage
The only difference here is the impedance term and the sign change!
Frequency Domain Solutions
Line excited by a series voltage/shunt current source

## Slide 23
Similar expressions exist for the line voltage and current for x < xs:
Frequency Domain Solutions
Line excited by a series voltage/shunt current source

## Slide 24
Responses at line terminals:
Frequency Domain Solutions
Line excited by a series voltage/shunt current source

## Slide 25
Frequency Domain Solutions
Line excited by a series voltage/shunt current source

## Slide 26
Frequency Domain Solutions
Line excited by a series voltage/shunt current source

## Slide 27
BLT equations
Frequency Domain Solutions
Line excited by a series voltage/shunt current source

## Slide 28
Frequency Domain Solutions
Line excited by a series voltage/shunt current source
BLT equations
Dr. Carl Baum (1940-2010)

## Slide 29
Frequency Domain Solutions
Line excited by a series voltage/shunt current source
BLT equations
Dr. T.K. Liu
?

## Slide 30
Frequency Domain Solutions
Line excited by a series voltage/shunt current source
BLT equations
Dr. Fred M. Tesche

## Slide 31
Frequency Domain Solutions
Line excited by a distributed voltage/shunt current source
where:

## Slide 32
Consider the case of a 30 m long line with a vertically polarized plane wave field with ψ = 60° and ϕ= 0°
Load impedances are Zc/2 (not matched)
  We want to compute the current at the Z2 load impedance
Two-Conductor TL Solutions
Example of Load Response

## Slide 33
Consider a unit amplitude transient, double exponential waveform for the incident E-field
Transient response for the load current is obtained from a standard FFT method
Two-Conductor TL Solutions
Example of Load Response

## Slide 34
The shape of the induced current waveform can be explained by looking at the times of arrival of various wave contributions
Two-Conductor TL Solutions
Example of Load Response

## Slide 35
Two-Conductor TL Solutions
Example of Load Response
The shape of the induced current waveform can be explained by looking at the times of arrival of various wave contributions
Waveform first strikes the line at t = 0

## Slide 36
Two-Conductor TL Solutions
Example of Load Response
The shape of the induced current waveform can be explained by looking at the times of arrival of various wave contributions
First response occurs at t = t1

## Slide 37
Two-Conductor TL Solutions
Example of Load Response
The shape of the induced current waveform can be explained by looking at the times of arrival of various wave contributions
After t = t1, the effects of the distributed sources on the line arrive, giving rise to a continuous response that looks similar to the incident field

## Slide 38
Two-Conductor TL Solutions
Example of Load Response
The shape of the induced current waveform can be explained by looking at the times of arrival of various wave contributions
Effect from end of line arrives at t = t2 and partially cancels with the response.

## Slide 39
Two-Conductor TL Solutions
Example of Load Response
The shape of the induced current waveform can be explained by looking at the times of arrival of various wave contributions

## Slide 40
Two-Conductor TL Solutions
Example of Load Response
The shape of the induced current waveform can be explained by looking at the times of arrival of various wave contributions

## Slide 41
[1] F.M. Tesche, M. Ianoz, T. Karlsson, Emc Analysis Methods and Computational Models, Wiley, 1997.
[2] C.R. Paul, Transmission Lines in Digital and Analog Electronic Systems, Wiley, 2010.
[3] F. Rachidi, A Review of Field-to-Transmission Line Coupling Models with Special Emphasis to Lightning-Induced Voltages, IEEE Transactions on Electromagnetic Compatibility, Vol. 54, No. 4, pp. 898 - 911, 2012.
References and Further Reading