## Slide 1
EM Crosstalk: Solutions for Multiconductor Lines
Farhad Rachidi
Swiss Federal Institute of Technology (EPFL)
EMC Laboratory
Farhad.Rachidi@epfl.ch
http://emc.epfl.ch

## Slide 2
This Chapter is based on the lecture of Prof. F.M. Tesche, Clemson University

## Slide 3
Consider a bundle of N wires, plus a N + 1 “reference” conductor, located in free-space
  we can define line currents in each of the N-wires
  Together with a return current in the reference conductor
  Note that a requirement for the TEM mode is that the sum of all such currents (in any cross-section of the line) must equal zero
Multiconductor Line Parameters
Line Currents

## Slide 4
For the same bundle of N wires, we can define N voltages, using the N+1 conductor for the 0-volt reference
  For the case of a line over a groundplane, the N+1st reference wire is the ground
  For a shielded multiwire line, the N+1st reference wire is the shield
+ V1
+ V2
Multiconductor Line Parameters
Line Voltages

## Slide 5
Consider an N-wire line (plus reference) with 1 wire carrying current I1
  With a return current –I in the reference
The H-field from the current in wire 1 is
Adding the return current provides another H-field
In the thin-conductor approximation, these H-fields are independent of the presence of other conductors
Multiconductor Line Parameters
Line Inductance Matrix

## Slide 6
The partial, per-unit-length magnetic flux flowing between wire #1 and the reference conductor is proportional to the wire current I1, as where L’11 is the per-unit-length inductance of the wire #1 circuit
Similarly, the partial flux from circuit #1 that links wire #2 and the reference conductor is given by the mutual inductance L’12 and the current in wire #1 as:
Multiconductor Line Parameters
Line Inductance Matrix

## Slide 7
Combining these partial fluxes gives the total per-unit-length flux linking wire #1 and the reference conductor as
This is the flux for circuit #1. As there are N such circuits, all fluxes can be expressed in matrix form as
  Or in a shorthand notation,
The (N x N) per-unit-length inductance matrix of the N-wire line
Multiconductor Line Parameters
Line Inductance Matrix

## Slide 8
Because the self and mutual inductances are independent of the presence of other conductors, they are easy to compute
For an N-wire line, the inductance matrix is expressed as
  where [F] is an NxN matrix of terms depending only on the geometry of the conductors
  This matrix is given in the next vugraph
Multiconductor Line Parameters
Line Inductance Matrix

## Slide 9
Matrix [F]
Multiconductor Line Parameters
Line Inductance Matrix

## Slide 10
N conductors in the free space. The conductor N is the return conductor.
Line Inductance Matrix
Example: N-conductor line in free space

## Slide 11
Magnetic field distribution around the conductors
Line Inductance Matrix
Example: N-conductor line in free space

## Slide 12
Integration
contour
Assume that the currents are concentrated on the conductors’ surface. Let us calculate as an example the mutual inductance between conductors 2 and 3. To do this, we will first determine the magnetic flux due to the current i2 through the circuit formed by the conductor 3 and the return conductor n
Line Inductance Matrix
Example: N-conductor line in free space

## Slide 13
This flux has two terms: first the contribution of the current i2 flowing in the conductor 2
Line Inductance Matrix
Example: N-conductor line in free space

## Slide 14
And the second the contribution of the current i2 returning in conductor n
Line Inductance Matrix
Example: N-conductor line in free space

## Slide 15
The total flux is then given by
And therefore the mutual inductance per unit length
Line Inductance Matrix
Example: N-conductor line in free space

## Slide 16
The per-unit-length capacitance matrix is the dual of the inductance
  Providing a relationship between the per-unit-length charge on each conductor and the wire voltages (with respect to the reference):
Unfortunately, unlike the L’ matrix, the individual elements of C’ cannot be written simply
  Due to the charge on one conductor affecting the voltage of another wire
or
Multiconductor Line Parameters
Line Capacitance Matrix

## Slide 17
Consider a 3-wire line over a ground
  The capacitances C’ij denote the partial (physical) capacitances between all wires and the neutral conductor
On wire #1, the charge is expressed as
Q’1 = C’12·v12 + C’13·v13 + C’11·v1 = C’12(v1 - v2) + C’13(v1 - v3) + C’11·v1
= (C’11 + C’12 + C’13)·v1 - C’12·v2 - C’13·v3
In a similar way one finds
Q’2 = - C’21·v1 + (C’21 + C’22 + C’23)·v2 - C’23·v3
and
Q’3 = - C’31·v1 - C’32·v2 + (C’31 + C’32 + C’33)·v3
Neutral
+
-
11
C'
22
C'
33
C'
Wire 1
Wire 2
Wire 3
12
C'
23
C'
13
C'
V
12
V
23
V
13
+
-
+
-
+
-
+
-
+
-
V
V
V
1
2
3
Multiconductor Line Parameters
Line Capacitance Matrix

## Slide 18
Thus for an N-conductor line, we have the Q’-V relationship in terms of the physical capacitances,
or
The C’s are all positive-valued capacitance elements
And the off-diagonal terms of the [C´] matrix are negative.
Multiconductor Line Parameters
Line Capacitance Matrix

## Slide 19
The [C´] matrix is difficult to calculate directly, since each element depends on the geometry of all conductors
  However, we can evaluate its inverse:
This and the other terms of K’ij are related to the elements in the [F’] matrix used to compute the line inductance
With only 1 wire charged, the voltages of each wire can be calculated independently
0
Observe that for 2 thin conductors of radius a and separation b, the term K’11 is given as
Multiconductor Line Parameters
Line Capacitance Matrix

## Slide 20
Multiconductor Line Parameters
Line Capacitance Matrix
For a configuration of n arbitrary conductors, the potential of the kth conductor with respect to the ground (taken as the (n+1)st conductor) due to the charges on all of the other conductors (j = 1 to n) is expressed as

## Slide 21
Thus, the [K´] matrix can be calculated from the geometry matrix [F] used to calculate the inductance matrix:
And the capacitance matrix is given by
Multiconductor Line Parameters
Line Capacitance Matrix

## Slide 22
Note that for the multiconductor line with no dielectric filling, we have
Observe that the product of these matrices is
Where c is the speed of light and [U] is the NxN unit matrix
As we show later, this relationship implies that all of the multiconductor fields (modes) propagate at the same velocity, c
Multiconductor Line Parameters
L’ and C’ Matrix

## Slide 23
If the entire region surrounding the conductors is filled with a dielectric, the capacitance is still given by the relationship with the modified dielectric constant
  And of course, the wave speed is less than in free space
If the line has a dielectric surrounding each conductor, then finding the capacitances becomes more difficult
  And the velocity relationships are more interesting
Multiconductor Line Parameters
Effect of dielectrics on capacitance parameters

## Slide 24
Dielectric effects can occur in lines like the isolated line shown here
For microstrip lines on a printed circuit board
Or for a power line over the earth
Multiconductor Line Parameters
Effect of dielectrics on capacitance parameters

## Slide 25
Unfortunately, in these cases we cannot compute the capacitance coefficient matrix [C’] from the inductance (or [F] matrix)
  We must use a numerical solution, taking into account the presence of the dielectric
  Consider the following dielectric coated wire (one of many in a bundle)
One approach is to develop an integral equation solution for the charge, and then find [C’]
For the conductor at a specified potential V, the conductor charge and the dielectric polarization charges are unknown. These need to be evaluated to determine the [C’] matrix.
In addition, if adjacent wires are close enough, they will modify the charge distribution, and this affects [C’]
Multiconductor Line Parameters
Effect of dielectrics on capacitance parameters

## Slide 26
For λ >> L
with
N-wire line
+
U
Wire j
Wire i
V
i
High impedance voltage meter
measuring Uj
x =
L
Conductors short-circuited
at x=L
Reference conductor
x =0
+
Voltage
source
V
i
L
Conductors open-circuited
at x=0
Multiconductor Line Parameters
Experimental Determination of Inductances

## Slide 27
For λ >> L
with
N-wire line
+
U
Wire j
Wire i
V
i
High impedance voltage meter
measuring Uj
x =
L
Conductors short-circuited
at x=L
Reference conductor
x =0
+
Voltage
source
V
i
L
Conductors open-circuited
at x=0
Multiconductor Line Parameters
Experimental Determination of Inductances

## Slide 28
For λ >> L
with
N
-
wire line
+
Wire j
Wire i
V
Low impedance
current meter
x =
L
Conductors open
-
circuited
at x=L
Reference conductor
x =0
+
j
Voltage
source
A
L
Conductors short
-
circuited
at x=0
N
-
wire line
+
Wire j
Wire i
V
Low impedance
current meter
x =
L
-
circuited
at x=L
Reference conductor
x =0
+
Voltage
source
A
L
-
at x=0
U
Multiconductor Line Parameters
Experimental Determination of Capacitances

## Slide 29
The [L’] and [C’] matrices can be used in a per-unit-length model to describe the behavior of voltage and current on a multiconductor line
This circuit can be used to derive the Telegraphers’ equations for the multiconductor line
Neglect, for the moment, the resistance and conductance elements – we are discussing a lossless line
Remember that these values of capacitance are the physical elements, C, not the elements of the [C’] matrix!
Telegrapher’s Equations for
Multiconductor Lines

## Slide 30
Note that for this line, the voltage and line current can be represented compactly as N-vectors
By examining the voltage-flux relationships on the multiconductor circuit,
we have
First Telegrapher Equation
Telegrapher’s Equations for
Multiconductor Lines

## Slide 31
Similarly, from the charge-voltage equation
We get
Second Telegrapher Equation
Telegrapher’s Equations for
Multiconductor Lines

## Slide 32
Thus, these Telegraphers’ equations are two coupled NxN matrix equations of the form
These must be solved in a self-consistent manner for the line voltage and current vectors
  Taking into account the termination impedances and the excitation sources of all of the lines.
Telegrapher’s Equations for
Multiconductor Lines

## Slide 33
From these first-order differential equations, two wave equations can be derived, just like for the 2-conductor line.
  These are
  We can solve these symbolically, as
  However, we must define what is meant by
Note that the order of matrix multiplication is important.
Telegrapher’s Equations for
Multiconductor Lines

## Slide 34
Consider first the NxN matrix wave equation for the voltages on the N-wire line
Recall from the definitions of [Z’] and [Y’], we have
If [P] were diagonal as,
Multiconductor Lines
Solutions to the Matrix Wave Equations

## Slide 35
  Then the overall matrix equation could be written in terms of individual, uncoupled wave equations as
However, in the general case, [P] is not diagonal
The task, therefore, is to find some way to diagonalize the propagation matrix [P]
Multiconductor Lines
Solutions to the Matrix Wave Equations

## Slide 36
Let’s define a matrix transformation using the N x N matrix [S] operating on the voltage vector [V] as
Conversely, we have the inverse transformation
Substituting this last equation into the matrix voltage wave equation gives a wave equation for the modal voltages [v]
N-vector transformed voltages (modes)
N-vector of physical voltages
Multiconductor Lines
Solutions to the Matrix Wave Equations

## Slide 37
This latter equation is easy to solve, if [S] is chosen properly:
Choose [S] to that this term is diagonal
For details, see F. B. Hildebrand, Methods of Applied Mathematics, 1965.
Multiconductor Lines
Solutions to the Matrix Wave Equations

## Slide 38
Consider finding the eigenvalues (or characteristic roots) and eigenvectors of [P]
This is done by solving for the N roots of the equation
  Or, in component form, this is
Solutions for λ i and the corresponding [Φi] generally require an iterative numerical procedure
Eigenvalues of the matrix [P] --- don’t confuse this with wavelength
Eigenvectors of the matrix [P]
Multiconductor Lines
Solutions to the Matrix Wave Equations

## Slide 39
These N eigenvalue equations may be put into a matrix form
Or in shorthand notation,
Multiplying by [Φ]-1 thus gives a diagonal equation
Columns in the matrix [Φ] correspond to the individual eigenvectors of [P]
The eigenvalue matrix is diagonal, with terms corresponding to each eigenvalue of [P]
Diagonalization of the Propagation Matrix

## Slide 40
Recall that our modal voltage wave equation was
Comparing this with the previous expression for the matrix diagonalization, we find the following:
  The eigenvalues λi are the squares of the modal propagation constants γi2
  Since we can write the propagation constants γi2 as
  where the ci correspond to different modal velocities
  And, the columns of the [S]-1 matrix correspond to the eigenvectors of [P]
Diagonal matrix [λ] --- denote as [γ2]
The Modal Voltage Wave Equation

## Slide 41
Thus we have
Or, in component form, we have N uncoupled voltage wave equations in the variable vi to solve:
The Modal Voltage Wave Equation

## Slide 42
The set of N uncoupled voltage modal equations can be solved by inspection as
Or, in compact notation,
Solution to the Modal Voltage Wave Equation

## Slide 43
Recalling that the physical and modal voltages are related as
We can now solve for the physical voltages on the line as
N-vectors of wave amplitudes (to be determined from source and loading conditions)
NxN matrices giving forward and backward propagating modes on the N-conductor line.
Care is advised in using these expressions, as the order of the terms is important.
NxN modal transformation matrix
Solution to the Physical Voltage Wave Equation

## Slide 44
A similar diagonalization procedure can be applied to the current wave equation
  where
  Note that [P] ≠[R], as the matrices [L’] and [C’] do not commute
The Modal Voltage Wave Equation

## Slide 45
As with the voltage equation, we can define current modes, [i] using a transformation matrix [T] as
And with this transformation, the modal current wave equation results
The transformation matrix [T] is chosen to diagonalize [R], so
As a consequence, we have
Note that the eigenvalues of [R] are the same as for [P]. The current modes must propagate at the same velocity as the voltage modes.
The Modal Voltage Wave Equation

## Slide 46
The current modal equation is written as
The set of N uncoupled current modal equations can be solved by inspection as
The physical currents on the line become
The N-vector coefficient [C] and [D] must be determined from [A] and [B] coefficients from the voltage equation and the Telegrapher’s equations.
Unknown mode amplitude N-vectors
Mode propagation matrix
Be careful to note that this is [C], not [C’] (the per-unit-length capacitance
Solution to the Modal Voltage Wave Equation

## Slide 47
Two solutions for the voltage and current modes in terms of modal traveling waves have been found:
The two solutions for the traveling current and voltage waves can be related by the Telegraphers’ equation
Using [V] = [S]-1 [v] and [I] = [T]-1 [i] , we have upon substituting
Mode Characteristic Impedances

## Slide 48
Considering only the forward propagating component,
This term has dimensions of an admittance, and is the characteristic modal admittance matrix [yc] for [i] and [v] on the line
  Consequently [A] and [C] are related by
Mode Characteristic Impedances

## Slide 49
A similar consideration of the backward propagating terms shows
Thus, the expressions for the voltage and current modes are expressed in terms of 2 unknown N-vector coefficients as
with
Remember that [yc] is the modal characteristic impedance matrix
Mode Characteristic Impedances

## Slide 50
From the modal solutions, the physical solutions can be summarized as
The current equation can be manipulated as
  Where the physical line characteristic admittance matrix [Yc] is
  Noting that
  This characteristic admittance matrix becomes
Solutions for the Physical Voltages and Currents

## Slide 51
The inverse of the [Yc] is the characteristic impedance matrix [Zc] and this is given as
Solutions for the Physical Voltages and Currents

## Slide 52
where
For the special case of a lossless line in a homogeneous medium, [P] and [R] are diagonal and given by:
where is the velocity of propagation along the line and [U] is the unit matrix.
Solutions for Multicondutor Lines: Summary

## Slide 53
For a lossless, homogeneous line, the general solution is given by
with
The vectors [A] and [B] contain the amplitudes of the forward and reverse voltage modes. These constant vectors must be determined from the boundary conditions and line excitation functions.
Solutions for Multicondutor Lines:
Case of Lossless, Homogeneous Line

## Slide 54
The general solution is given by
where λi are eigenvalues of [P]
Solutions for Multicondutor Lines: Summary
General Solutions

## Slide 55
Consider the 5-conductor
cable in free-space
  This has 4 wires, plus a reference conductor
The computed [L’] and [C’] matrices are
Illustration of Mode Velocities and Distributions

## Slide 56
A numerical evaluation of the modal velocities for this line gives the following values
Illustration of Mode Velocities and Distributions

## Slide 57
The voltage mode distributions on the wires are as follows:
Remember, these correspond to the columns of [S]-1, and each mode propagates with a different velocity
Illustration of Mode Velocities and Distributions

## Slide 58
The current mode distributions on the wires are as follows:
These modes correspond to the columns of [T]-1, and the propagation velocities are the same as the voltage modes
Illustration of Mode Velocities and Distributions

## Slide 59
Consider an infinite multiconductor line with an N-voltage source
In section #1 (0 ≤ x ≤ xs) we have
At position x = 0, the current [I] = 0
  This gives so the line voltage is
Example

## Slide 60
In section #2 (x > xs) we have
At the source position as x = xs, we have the conditions
This leads to the following solutions for the constants
Voltage jump condition
Continuity of current
Example (con’t)

## Slide 61
Evaluating the voltage in section #1 gives
  evaluated at x = 0
  with [A1], which has been found to be
  This gives the final expression for the open circuit voltage N-vector at the end of the line
Mode propagation occurs at different velocities
Transformation matrices “mix-up” the modes for the responses in each conductor.
Example (con’t)

## Slide 62
A major complication has been introduced by the multi-velocity analysis
  Caused by the presence of the dielectric around the wires
  How important is this effect?
For the case of no dielectric present
  All modes propagate with the speed of light
  The matrix [γ] is given by γo [U]
  And [Voc] simplifies considerably:
Consider a simple example with a step-function excitation of the cable
The Equal Velocity Approximation

## Slide 63
Assume wire #1 is excited by a step function voltage source
  With the other wires unexcited
This excitation is defined as
In the frequency domain, this excitation is
For the “rigorous” multimode analysis, the voltage at x = 0 is
And for the single velocity approximation, we have
Step function excitation
No excitation
Source position is xs = 1 meter
We wish to illustrate the open circuit voltage at the end of the semi-infinite line
Illustration: Computed Voltage Waveform

## Slide 64
For this example, we will use the per-unit-length parameters determined for the 4-wire (+ reference) ribbon cable treated previously.
Illustration: Computed Voltage Waveform (con’t)

## Slide 65
Plots of the spectra of the wire voltages at x = 0
Multimode analysis Single velocity approximation
Illustration: Computed Voltage Waveform (con’t)

## Slide 66
The transient responses can be determined from a FTT of the spectra
Wire 1 responses Wire 2, 3 & 4 responses
Illustration: Computed Voltage Waveform (con’t)

## Slide 67
[1] F.M. Tesche, M. Ianoz, T. Karlsson, EMC Analysis Methods and Computational Models, Wiley, 1997.
References and Further Reading