## Slide 1: EPFL Space Center eSpace
Space Propulsion ENG-510

## Slide 2: Lecture # 2 Part # 2 Introduction in Propulsion Systems
Brief overview on all space propulsion systems

## Slide 3: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
In its simplest form, a propulsion system accelerates matter to provide a force of thrust that moves or rotates a vehicle
Example: Small row boat on the lake of Geneva
Basic rocket equation (Tsiolkovsky rocket equation): The basis principle of a classical rocket engine is to eject mass with a high velocity. The recoil of this ejection is then increasing the velocity of the Spacecraft (S/C) including the Payload (P/L) as well as the remaining propellant
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 4: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Basic rocket equation (Tsiolkovsky rocket equation)
Space Propulsion ENG-510
L2 – Propulsion Systems
Konstantin Tsiolkovsky

## Slide 5: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Basic rocket equation (Tsiolkovsky rocket equation)
...Delta v - maximal change of velocity of the vehicle (with no external forces acting like gravitational forces or drag) [m / s]
…Exhaust velocity [m / s]
…Mass @ [kg]
… Mass @ [kg]
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 6: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Mass relations for different time steps:
...Ejected mass [kg]
…Initial total mass (including propellant – i.e. wet mass) [kg]
…Final total mass (without propellant – i.e. dry mass) [kg]
...Propellant mass [kg]
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 7: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Basic rocket equation (Tsiolkovsky rocket equation)
...Delta v - maximal change of velocity of the vehicle (with no external forces acting like gravitational forces or drag) [m / s]
…Exhaust velocity [m / s]
…Initial total mass (including propellant – i.e. wet mass) [kg]
…Final total mass (without propellant – i.e. dry mass) [kg]
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 8: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Basic rocket equation (Tsiolkovsky rocket equation)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 9: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Basic rocket equation (Tsiolkovsky rocket equation)
Exhaust velocity describes the magnitude for the performance of the propulsion system in relation with complexity, risk, cost, …
=>
…Mass ratio between initial mass and final mass [-]
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 10: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Performance of orbital maneuvers (small changes of orbit trajectory)
Compensation of perturbations (orbit raising to compensate drag losses)
Long duration burns (for significant Δv increases)
Attitude control (with short, directed thrust (impulse, force push) linked to 3-axis control)
Landing burns (for landing on the Moon)
Lift-off burns requiring high thrust levels
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 11: What is the principle of Space Propulsion?
Basic Working Principle for Propulsion:
Example: How can we maximize the speed of the row boat on the Water?
Example: What was the problem with the Water rocket failing to reach an orbit respectively the targeted altitude of 100 m?
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 12: What is important on Δv?
Objective: To understand some specific points on Δv
First one must differ between v and Δv
v is the current velocity of a Spacecraft on his trajectory
v could be constant on a circular orbit or changing permanently on an elliptical orbit (w/o any propulsion)
Δv is the impulse which must be given to a Spacecraft to change the trajectory (e.g. change from elliptical to circular orbit or vice-versa)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 13: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only resulting from space propulsion systems
Δv is not only velocity change but also orbit change
Δv is not only linked to start point and end point only but also on the way between the two points (orbital trajectory)
Δv is not equal to velocity change
Δv is the same for deceleration and acceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 14: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only resulting from space propulsion systems
Δv is not only velocity change but also orbit change
Δv is not only linked to start point and end point only but also on the way between the two points (orbital trajectory)
Δv is not equal to velocity change
Δv is the same for deceleration and acceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 15: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only resulting from space propulsion systems
Δv changes are also given due to drag forces, gravitational forces, … and similar
Example: ISS is altitude is reduced every day by about 50 to 150 m linked to residual drag forces
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 16: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only resulting from space propulsion systems
Δv is not only velocity change but also orbit change
Δv is not only linked to start point and end point only but also on the way between the two points (orbital trajectory)
Δv is not equal to velocity change
Δv is the same for deceleration and acceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 17: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only a velocity change but also directly an orbit change (which makes rendezvous maneuver is space very tricky…)
Δv could be called as index / key increment of a space journey
Changing the Δv is changing the orbit and also changing the energy of the spacecraft …Standard gravitational parameter [m³ / s²] (Earth 3.986E14 m³/s²)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 18: What is important on Δv?
Objective: To understand some specific points on Δv
Important Δv impulse on circular orbit changes the trajectory to an elliptical orbit (assuming escape velocity is not reached) and increasing the energy
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 19: What is important on Δv?
Objective: To understand some specific points on Δv
On the elliptical orbit the real velocity is permanently changing (as well as radius of flight trajectory) considering the Energy conservation
This velocity change is occurring without any further space propulsion impulse, just linked to the orbital trajectory and the Energy conservation which is described by the vis-viva equation
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 20: What is important on Δv?
Objective: To understand some specific points on Δv
Vis-viva equation in astrodynamics the orbital-energy-invariance law: …Speed of an orbiting body [m / s] …Standard gravitational parameter [m³ / s²] (Earth 3.986E14 m³/s²) …Distance of the orbiting body from the primary focus / body [m] …Semi-major axis of the body's orbit [m]
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 21: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not (really) time dependent following the basic rocket equation
In other words, the efficiency of orbit changes is increased in case the impulse is given in a very short time span
In that sense it is helpful to consider multiple engines for increasing mass exhaust but on the other hand mass ratio MR is also changed
Trade-off needs to be performed between efficiency gain versus mass penalty
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 22: What is important on Δv?
Objective: To understand some specific points on Δv
For same Δv need, the mass ratio (MR) between initial mass (dry mass + propellant mass) to final mass (dry mass) is smaller for higher exhaust velocity (ve), i.e. efficiency is higher
Space Propulsion ENG-510
L2 – Propulsion Systems
Delta v [km / s]
0
5
10
15
0
20
MR [-]
1
10
100
ve = 2 km / s
ve = 4 km / s
ve = 10 km / s
ve = 30 km / s

## Slide 23: What is important on Δv?
Objective: To understand some specific points on Δv
Exhaust velocity is often referred to as specific impulse
…Specific impulse [s]
…Earth gravitational acceleration [m / s²] (9.807 m/s²)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 24: What is important on Δv?
Objective: To understand some specific points on Δv
For given mass ratio (MR) between initial mass (dry mass + propellant mass) to final mass (dry mass), maximal achievable Δv is depending on the effective exhaust velocity (ve)
Necessary wet mass grows exponentially with the desired Δv
Space Propulsion ENG-510
L2 – Propulsion Systems
Delta v / v exhaust [-]
MR [-]

## Slide 25: What is important on Δv?
Objective: To understand some specific points on Δv
Example 1: Assume an exhaust velocity of 4500 meters per second and a delta v target of 9700 meters per second (corresponding to the needed delta v for a Low Earth Orbit (LEO) including delta v need to overcome gravitational and drag forces) for a single-stage-to-orbit
=> =>
So 88.4 % is the required mass fraction, i.e. 88.4 % of the initial mass must be propellant. The remaining 11.6 % is dry mass, which could be difficult to achieve without special measures (e.g. staging of launchers)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 26: What is important on Δv?
Objective: To understand some specific points on Δv
Example 2: To achieve a delta v of 10 000 meters per second with an exhaust velocity of 2 000 meters per second a mass ratio of 147 is needed and so a required mass fraction of 99,3 %
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 27: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only resulting from space propulsion systems
Δv is not only velocity change but also orbit change
Δv is not only linked to start point and end point only but also on the way between the two points (orbital trajectory)
Δv is not equal to velocity change
Δv is the same for deceleration and acceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 28: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only linked to start point and end point only but also on the way between the two points (orbital trajectory)
Two main different trajectories are discussed hereafter (not considering any change of inclination for simplification [inclination is the angular distance of the orbital plane from the plane of the planet's equator, stated in degrees])
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 29: What is important on Δv?
Objective: To understand some specific points on Δv
Two classical orbital changes must be known
  Hohmann transfer (impulsive maneuver – two short impulses)
  Edelbaum transfer (long duration maneuver with low thrust – spiral orbit raising)
Space Propulsion ENG-510
L2 – Propulsion Systems
Hohmann Transfer
Edelbaum Transfer

## Slide 30: What is important on Δv?
Objective: To understand some specific points on Δv
Hohmann transfer is a two-impulse orbit transfer
  Acceleration in a period sufficiently smaller than the orbital period
  Basic maneuver in chemical propulsion
  Transfer from perigee (point close to Earth) to apogee (point far from Earth) on an elliptical trajectory
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 31: What is important on Δv?
Objective: To understand some specific points on Δv
Δv need for a Hohmann transfer is determined by (as derived from the vis-viva-equation considering instantaneous impulses): +
Space Propulsion ENG-510
L2 – Propulsion Systems
Perigee
Apogee

## Slide 32: What is important on Δv?
Objective: To understand some specific points on Δv
Example: Δv need for a geostationary transfer considering the Hohmann transfer beginning at r1 = 6 678 km (altitude 300 km) and ending in a geostationary Earth orbit with r2 = 42 164 km (altitude 35 786 km)
In the smaller circular orbit, the speed is 7.73 km / s; in the larger one, 3.07 km / s. In the elliptical orbit in between the speed varies from 10.15 km / s at the perigee to 1.61 km / s at the apogee
Therefore, the Δv for the first burn is 10.15 − 7.73 = 2.42 km / s, for the second burn 3.07 − 1.61 = 1.46 km / s, and for both together the total Δv is 3.88 km / s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 33: What is important on Δv?
Objective: To understand some specific points on Δv
Spiral orbit raising is a continuous thrust orbit transfer
  Basic maneuvers in electric propulsion (Assumptions: tangential thrust, constant thrust and velocity = circular orbit velocity at its radius
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 34: What is important on Δv?
Objective: To understand some specific points on Δv
Δv need for an Edelbaum transfer (spiral orbit raising) is determined by the following equations:
Space Propulsion ENG-510
L2 – Propulsion Systems
Perigee
Apogee

## Slide 35: What is important on Δv?
Objective: To understand some specific points on Δv
Example: Δv need for a geostationary transfer considering the Edelbaum transfer beginning at r1 = 6 678 km (altitude 300 km) and ending in a geostationary Earth orbit with r2 = 42 164 km (altitude 35 786 km)
In the smaller circular orbit the speed is 7.73 km / s; in the larger one, 3.07 km / s
Therefore the total Δv need for an Edelbaum transfer is 7.73 − 3.07 = 4.66 km / s, so higher compared to a Hohmann transfer requiring a total Δv of 3.88 km / s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 36: What is important on Δv?
Objective: To understand some specific points on Δv
Hohmann transfer versus spiral orbit raising
  Hohmann transfer is much faster
  Hohmann transfer requires high thrust
  Δv increase is higher for spiral orbit raising
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 37: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only resulting from space propulsion systems
Δv is not only velocity change but also orbit change
Δv is not only linked to start point and end point only but also on the way between the two points (orbital trajectory)
Δv is not equal to velocity change
Δv is the same for deceleration and acceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 38: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not equal to velocity change
Δv and actual velocity depend on the orbit like for LEO (ℎ = 420 km, 𝑣 = 7.66 km/s)
Assuming continuous thrust in the direction of acceleration
Altitude will increase, but “velocity” will decrease in this circular orbit raise (ℎ = 620 km, 𝑣 = 7.55 km/s)
Also as stated before, Energy will increase
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 39: What is important on Δv?
Objective: To understand some specific points on Δv
Changing the energy of the spacecraft during spiral transfer in circular orbit
Energy level # 1 for initial orbit (ℎ = 420 km, 𝑣 = 7.66 km/s)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 40: What is important on Δv?
Objective: To understand some specific points on Δv
Energy level # 2 for final orbit raise (ℎ = 620 km, 𝑣 = 7.55 km/s)
Example: Hohmann transfer / Edelbaum transfer from Low Earth Orbit to Geostationary Earth Orbit compared to escape orbit
Δv required for an escape obit is 10.93 − 7.73 = 3.20 km / s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 41: What is important on Δv?
Objective: To understand some specific points on Δv
Applying a Δv at LEO of only 0.78 km / s more (3.20 − 2.42) would give the rocket the escape velocity, which is less than the Δv of 1.46 km / s required to circularize the geosynchronous orbit
This illustrates the Oberth effect, that at large speeds the same Δv provides more specific orbital energy, and energy increase is maximized if one spends the Δv as quickly as possible, rather than spending some, being decelerated by gravity, and then spending some more to overcome the deceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 42: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is not only resulting from space propulsion systems
Δv is not only velocity change but also orbit change
Δv is not only linked to start point and end point only but also on the way between the two points (orbital trajectory)
Δv is not equal to velocity change
Δv is the same for deceleration and acceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 43: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is the same for deceleration and acceleration
Δv is the same going from LEO to GEO or from GEO to LEO
One transfer is only supported by acceleration whereas the other one is referring to deceleration
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 44: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is the same for deceleration and acceleration
One can reach Mars by escaping the Earth with Δv of + 2.9 km / s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 45: What is important on Δv?
Objective: To understand some specific points on Δv
One can reach Venus by escaping the Earth with Δv of - 2.5 km / s as a deceleration maneuver
Deceleration is not easy at all, but completely same effort is needed as for acceleration (while traveling on the Earth we do have already a certain velocity…)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 46: What is important on Δv?
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 47: What is important on Δv?
Objective: To understand some specific points on Δv
Δv is key parameter for understanding of space journeys, but
Δv is not the only parameter…
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 48: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
How thrust is produced?
How efficiently thrust can be produced?
How thrust and thrust efficiency affect the vehicle mass in terms of:
  Propellant mass?
  Inert mass required to hold the propellant and provide the thrust?
Some key topics related to thrust:
  Launcher versus Satellite propulsion
  Thrust level on ground
  Minimization of propellant mass and therefore maximizing of c (efficiency)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 49: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Thrust equation
...Momentum thrust magnitude [N]
Mass flow rate of the propellant [kg/s]
…Exhaust velocity [m/s]
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 50: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Thrust equation linked to pressure
...Pressure thrust magnitude [N]
…Nozzle exit pressure [N/m²]
…Ambient pressure [N/m²]
…Nozzle exit cross-sectional area [m²]
…Nozzle efficiency [-] (typical range between 0.85 – 0.98)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 51: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Relation thrust to specific impulse
…Specific impulse [s]
Mass flow rate of the propellant [kg/s]
…Earth gravitational acceleration [m/s²] (9.807 m/s²)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 52: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Effective exhaust velocity
…Effective exhaust velocity [m/s]
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 53: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Needed propellant mass
Notice that this equation gives a fundamental limit on vehicle performance. If the denominator is less than or equal to zero, it is impossible to build the vehicle as designed
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 54: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Inert mass fraction
…Inert mass fraction [-] (typical range 0.08 to 0.7)
Inert mass fraction is a performance parameter showing how well the structure is engineered. A small number indicates a high-performance structure whereas a higher number indicates lower performance
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 55: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Mission feasibility limit related to specific impulse
Notice that this equation states that for a given mission () and a given technology () the specific impulse must be above a certain value for the system to work
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 56: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Total impulse
For a system with constant thrust magnitude it follows
Total impulse and Δv are related to each other
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 57: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
Thrust-to-Weight ratio
…Thrust-to-weight ratio [-]
Launch vehicles must have an initial thrust-to-weight ration greater than 1.0 or the vehicle cannot get off the ground
Thrust-to-weight ratios for upper stage engines can range from 10-4 for electric systems to 0 for solid rockets at burn-out
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 58: What is the importance of thrust?
Objective: To discuss thrust + relation to Isp
How thrust is produced?
How efficiently thrust can be produced?
How thrust and thrust efficiency affect the vehicle mass in terms of:
  Propellant mass?
  Inert mass required to hold the propellant and provide the thrust?
Some key topics related to thrust:
  Launcher versus Satellite propulsion
  Thrust level on ground
  Minimization of propellant mass and therefore maximizing of c (efficiency)
Space Propulsion ENG-510
L2 – Propulsion Systems
Engine | Launcher | Propellant | Exhaust Velocity | Thrust
F1 | Saturn V | LOx / RP-1 | 3.0 km / s | 7.7 MN
RD-107 | Soyuz | LOx / RP-1 | 3.1 km / s | 1.0 MN
RD-264 | Dnepr | NTO / UDMH | 3.2 km / s | 4.5 MN
SSME | Shuttle | LOx / LH2 | 4.5 km / s | 2.2 MN
LE7A | H2A | LOx / LH2 | 4.3 km / s | 1.1 MN
Vulcain 2 | Ariane 5 | LOx / LH2 | 4.3 km / s | 1.3 MN
SSRB | Shuttle | Composite | 2.7 km / s | 13.8 MN
SRB-A | H2A | Composite | 2.8 km / s | 2.3 MN
M-V-1 | M-V | Composite | 2.8 km / s | 2.4 MN

## Slide 59: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Key equations are given in this section for launcher performance analysis
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 60: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Example: Assume an exhaust velocity of 4500 meters per second and a delta v target of 9700 meters per second (corresponding to the needed delta v for a Low Earth Orbit (LEO) including delta v need to overcome gravitational and drag forces) for a single-stage-to-orbit
=> =>
So 88.4 % is the required mass fraction, i.e. 88.4 % of the initial mass must be propellant. The remaining 11.6 % is dry mass, which could be difficult to achieve without special measures (e.g. staging of launchers)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 61: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
First part is linked to launcher staging
A multistage rocket or step rocket is a launch vehicle that uses two or more rocket stages, each of which contains its own engines and propellant
A tandem or serial stage is mounted on top of another stage; a parallel stage is attached alongside another stage
The result is effectively two or more rockets stacked on top of or attached next to each other
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 62: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Two-stage rockets are quite common, but rockets with as many as five separate stages have been successfully launched
By jettisoning stages when they run out of propellant, the mass of the remaining rocket is decreased
Each successive stage can also be optimized for its specific operating conditions, such as decreased atmospheric pressure at higher altitudes
Staging allows the thrust of the remaining stages to more easily accelerate the rocket to its final orbit
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 63: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
For multistage rockets standard performance equations are still valid
Basic rocket equation (Tsiolkovsky rocket equation)
Exhaust velocity is often referred to as specific impulse
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 64: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Thrust equation
On top of the classical performance equations, dimensionless ratio are interesting in order to optimize launcher staging
Initial to final mass ratio
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 65: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Structural ratio, which is the ratio between the empty mass of the stage, and the combined empty mass and propellant mass
Payload ratio, which is the ratio between the payload mass and the combined mass of the empty rocket stage and the propellant mass
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 66: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
After comparing the three equations for the dimensionless quantities, it is easy to see that they are not independent of each other, and in fact, the initial to final mass ratio can be rewritten in terms of structural ratio and payload ratio
The dimensionless ratio can be established for single stage launchers as well as multiple stage launchers
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 67: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Example: Multi-stage launcher with ε = 0.15
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 68: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Example: Multi-stage launcher with ε = 0.10
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 69: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Performance analysis for a tandem or serial stage is very simple as only one propulsion system is acting at a certain time with clear performance parameter like thrust, specific impulse
It must only be determined when stages are jettisoned
The result is effectively two or more rockets stacked on top of or attached next to each other
Performance analysis for a parallel stage is more tricky
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 70: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Example: H2A launch vehicle with liquid main engine LE7A with exhaust velocity of 4.31 km / s and two solid rocket booster SRB with exhaust velocity of 2.78 km / s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 71: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Performance of a launch vehicle using different parallel stages can be assessed by using the effective exhaust velocity
Effective exhaust velocity
with Ftot as sum of all thrust levels
  Example: H2A launch vehicle with one main liquid engine (1100 kN and 260 kg / s) and two solid rocket boosters (2500 kN and 900 kg / s)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 72: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Example: H2A launch vehicle performance
Effective exhaust velocity
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 73: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Second part is linked to engine / throat / nozzle performance with flow parameter ρ…density, p…pressure, T…temperature and v…velocity
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 74: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Basic considerations are:
  Steady flow: All flow variables are independent on the time
  Quasi-1D flow: All flow variables are function of the axial coordinate
  Adiabatic flow: No heat transfer to the flow
  Ideal gas relation is given
  No viscosity: No momentum loss to the wall
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 75: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Recap: Thrust is linked to mass flow rate, exhaust velocity and engine nozzle parameter
...Pressure thrust magnitude [N]
…Nozzle exit pressure [N/m²]
…Ambient pressure [N/m²]
…Nozzle exit cross-sectional area [m²]
…Nozzle efficiency [-] (typical range between 0.85 – 0.98)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 76: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Recap: Thrust is linked to mass flow rate, exhaust velocity and engine nozzle parameter
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 77: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Recap: Thrust is linked to mass flow rate, exhaust velocity and engine nozzle parameter
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 78: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Important parameter are also speed of sound (propagation velocity of small disturbances) and the Mach number M (ratio of the flow velocity to the local speed of sound)
Speed of sound
Mach number
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 79: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Ma number is important in terms of flow acceleration / deceleration for different nozzle types
Space Propulsion ENG-510
L2 – Propulsion Systems
Ma < 1
Ma > 1

## Slide 80: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Once the flow reaches to Ma = 1 at the throat (= choked conditions), only downstream conditions determine the flow rate
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 81: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Thrust equation using the thrust coefficient (thrust coefficient is depending on the aperture ratio and the gas type and is expressing the acceleration of the gas by the nozzle)
…Thrust coefficient
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 82: Which general Performance Equations are given?
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 83: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Final important parameter is c* (is depending on the temperature and gas type and is expressing the performance of combustion chamber)
… Characteristic velocity
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 84: Which general Performance Equations are given?
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 85: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Nozzle layout considerations
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 86: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Nozzle layout considerations
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 87: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Nozzle layout considerations
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 88: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Nozzle layout considerations
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 89: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Test as you fly and fly as you test…
Example: Sea-level testing of large engines instead of altitude (vacuum) testing
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 90: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Bell-shaped nozzle extensions compared to aerospike engines
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 91: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Aerospike engines allow:
  Optimal performance over wider external pressure range (wider altitude range)
  Spike and surrounding air flow form a virtual bell
Aerospike engines lead:
  Increased thermal loads on spike
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 92: Which general Performance Equations are given?
Objective: To analyze propulsion systems performance
Aerospike engines exist as:
  Toroidal aerospike
  Linear aerospike
But no commercial application is given today
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 93: Which general Performance Equations are given?
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 94: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Space propulsion / in-space propulsion / towards space propulsion - Everything that accelerates a vehicle (launcher, rocket, satellite, orbital vehicle) by ejection of material
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 95: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Energy and Propellant:
  Energy is needed to throw out the propellant / mass to get the push
  Some energy must be converted to kinetic energy
A propulsion system is an energy converter / accelerator
Space Propulsion ENG-510
L2 – Propulsion Systems
Mass
Energy
Conversion / Acceleration
Impulse

## Slide 96: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Useable Energy:
  Nuclear fusion
  Nuclear fission
  Chemical reaction
  Pressure release
  Electrical battery
  Solar power
  Muscle power
  Mechanical acceleration
  Others…
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 97: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Transferring into space propulsion systems:
  Nuclear fusion -> Not existing today
  Nuclear fission -> Nuclear reactor is coming back again
  Chemical reaction -> In use
  Pressure release -> In use
  Electrical battery -> In use
  Solar power -> In use
  Muscle power -> Not sufficient
  Mechanical acceleration -> Under investigation (centrifuge)
  Others… -> To be discussed
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 98: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Energy type and propulsion systems:
  Nuclear fusion -> Not applicable
  Nuclear fission -> Nuclear thermal propulsion and nuclear electric propulsion
  Chemical reaction -> Chemical propulsion
  Pressure release -> Pneumatic propulsion
  Electrical battery -> Electric propulsion
  Solar power -> Solar (radiant) electric propulsion
  Muscle power
  Mechanical acceleration -> Mechanical propulsion
  Others… -> To be discussed
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 99: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Propulsion System categorization linked to energy conversion type:
  Thermal Propulsion Systems (e.g. cold gas systems but also including electrothermal + solar thermal + nuclear thermal propulsion)
  Chemical (Combustion) Propulsion Systems
  Electrical Propulsion Systems (including nuclear electric propulsion)
  Mechanical Propulsion Systems (e.g. gun, centrifuge, …)
  Others…like radiant energy / solar wind / lasers
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 100: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Comparison of different Propulsion Systems:
  Thermal Propulsion Systems
  Chemical (Combustion) Propulsion Systems
  Electrical Propulsion Systems
  Mechanical Propulsion Systems
  Others…
Space Propulsion ENG-510
L2 – Propulsion Systems
Δv [m / s]
Prop Ratio (Prop Mass / Wet Mass) [-]
Possible Performance as Function of Propulsion Technology
Cold Gas
GIT
HET
Hydrazin
MON / MMH

## Slide 101: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Generic block diagram for propulsion systems:
Space Propulsion ENG-510
L2 – Propulsion Systems
Propellant
Propellant Storage
Energy Source
Propellant Feed System
Energy Conversion
Accelerator
Mass Ejection

## Slide 102: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Thermal Propulsion Systems
  Cold gas propulsion systems
  Cold gas / liquid propulsion systems (e.g. Water rocket…)
  Solid powder / cold gas propulsion systems
  Cryogenic boil-off propulsion systems
  Liquefied gas propulsion systems
  Electrothermal propulsion systems
  Solar thermal propulsion systems
  Nuclear thermal propulsion systems
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 103: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Thermal Propulsion Systems – Group 1
  Cold gas propulsion systems
  Cold gas / liquid propulsion systems (e.g. Water rocket…)
  Solid powder / cold gas propulsion systems
  Cryogenic boil-off propulsion systems
  Liquefied gas propulsion systems
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 104: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Thermal Propulsion Systems – Group 2
  Electrothermal propulsion systems
  Thermal Propulsion Systems – Group 3
  Solar thermal propulsion systems
  Nuclear thermal propulsion systems
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 105: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Application
  Small Δv missions (e.g. only attitude control)
  Small spacecrafts (e.g. cubesats)
Architecture
  Blow-down systems
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 106: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
1
  B
Space Propulsion ENG-510
L2 – Propulsion Systems
Propellant Phase in Tanks
Solid
Liquid
Gas
Chemical Reaction
No
Decomp
Combustion
Liquified Gas Gas (Xe, N2, Ar)
Cold Gas Propulsion System / Thruster
Powder

## Slide 107: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Block diagram for Thermal Cold Gas Propulsion Systems:
Space Propulsion ENG-510
L2 – Propulsion Systems
Propellant (Gas)
Propellant Storage (Pressure Tank)
Energy Source
(Compressed Gas)
Propellant Feed System
Conversion
(De-pressurization)
Accelerator (Nozzle Extension)
Mass (Gas) Ejection

## Slide 108: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Characteristics of Thermal Cold Gas Propulsion Systems:
  High degree of reliability
  Low system complexity (no combustion involved)
  Low Δv
  Extremely safe operation
  No contamination from exhaust (combustion) gases
  Low thrust
  High pressure on ground
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 109: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Thermal Cold Gas Propulsion Systems (as a cold gas reaction control system):
Space Propulsion ENG-510
L2 – Propulsion Systems
Tank
Valve
Exhaust
R
Regulator

## Slide 110: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Thermal Cold Gas Propulsion Systems:
  Consideration of a pressure regulator is not mandatory, but
  It allows to operate all Equipment below the regulator at lower pressure and therefore has lower strength requirements
  It allows to operate the thruster at constant inlet pressure until the storage tank pressure drops below the regulator pressure and therefore ensures consistent level of thrust
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 111: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Thermal Cold Gas propulsion characteristics (needed propellant mass @ T = 298 K for different gases with same Δv requirement)
Space Propulsion ENG-510
L2 – Propulsion Systems
Gas | a0 [m/s] | C* [m/s] | m [kg/s] | Isp [s] | M [kg]
Air | 346.1 | 427.2 | 0.051 | 78.9 | 51.6
Argon | 320.7 | 343.6 | 0.071 | 57.0 | 71.5
CO2 | 269.3 | 356.8 | 0.056 | 72.3 | 56.3
He | 1013.8 | 1085.6 | 0.022 | 180.1 | 22.6
H2 | 1314.4 | 1617.4 | 0.013 | 297.8 | 13.7
N2 | 351.9 | 434.4 | 0.050 | 80.2 | 50.8
O2 | 328.7 | 406.9 | 0.054 | 75.4 | 54.0

## Slide 112: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Example: Cold Gas propulsion system
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 113: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Example: Cube Sat propulsion system
Space Propulsion ENG-510
L2 – Propulsion Systems
General specification:
Four 1mN thrusters with closed loop thrust control
Thrust resolution: <10µN
Propellant: Butane
Total impulse: 40Ns
Size: 10*10*3cm
Mass: 250g
Operating pressure: 2-5 bar
Power consumption: 2 W

## Slide 114: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Basic performance equations:
  Sonic velocity
  Characteristic velocity
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 115: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Basic performance equations:
  Thrust
  Mass flow
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 116: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Basic performance equations:
  Isp
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 117: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Thermal Cold Gas / Liquid Propulsion Systems (as student project):
Space Propulsion ENG-510
L2 – Propulsion Systems
Tank
Valve
Exhaust
Liquid phase
Gas phase

## Slide 118: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Example: Plasti Blast and others
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 119: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Thermal Gas Propulsion Systems solid powder on ground for storage:
Space Propulsion ENG-510
L2 – Propulsion Systems
Tank
Valve
Exhaust
R
Regulator
Powder Tank
Ignitor

## Slide 120: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Characteristics of Thermal Gas Propulsion Systems:
  High degree of reliability
  Medium low system complexity (no combustion involved)
  Low Δv
  Extremely safe operation
  No contamination from exhaust (combustion) gases
  Low thrust
  High pressure on ground
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 121: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Cryogenic Boil-off:
Space Propulsion ENG-510
L2 – Propulsion Systems
Tank
Valve
Exhaust

## Slide 122: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Example: LH2 boil-off in cryogenic upper stages
  Permanent LH2 boil-off is given as propellant temperature is @ 20 K
  Tank pressure is important parameter to control liquid temperature
  Also de-pressurization is performed to cool-down the propellant
  Available gas pressure can be used for propellant settling, as attitude control system…but might also be just vented (not providing any impulse to the upper stage)
  No pressure regulator is needed as tank pressure is already very low
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 123: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Example: A5ME / A6 launch vehicles and TEC Nyx Moon capsule
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 124: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Storable Propellant Boil-off @ ambient temperatures considering high vapor pressures:
Space Propulsion ENG-510
L2 – Propulsion Systems
Tank
Valve
Exhaust
Heater

## Slide 125: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Example: N2O boil-off in
  Forced N2O boil-off due to high vapor pressure and correlation between liquid temperature and gas pressure
  is important parameter to control liquid temperature
  But also other way round liquid temperature is important parameter to control tank pressure
  Available gas pressure can be used for propellant settling, as attitude control system…but might also be just vented (not providing any impulse to the upper stage)
  Pressure regulator might be needed in order to get constant thrust (but could also controlled by effective temperature control of liquid N2O)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 126: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Block diagram for Thermal Liquefied Gas Propulsion Systems:
Space Propulsion ENG-510
L2 – Propulsion Systems
Propellant (Liquefied Gas)
Propellant Storage (Liquid Tank)
Energy Source
(Heat Exchanger)
Propellant Feed System
Conversion
(Vaporization)
Accelerator (Nozzle Extension)
Mass (Gas) Ejection

## Slide 127: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Thermal Liquefied Gas Propulsion Systems (as a cold gas reaction control system):
Space Propulsion ENG-510
L2 – Propulsion Systems
LOx
LHe
Tank with liquefied gas @ cryogenic temperature
Valve
Exhaust
P
Pump
Tank with cryogenic propellant
Heat Exchanger

## Slide 128: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Architecture of Thermal Liquefied Gas Propulsion Systems:
  Means must be provided for storage of liquefied gas (e.g. by storage of gas inside cryogenic propellant tank)
  Heat Exchanger must be used in order to ensure sufficient vaporization rate
  Most probably pump is needed to increased pressure of vaporized gas @ thruster (nozzle extension) inlet
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 129: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Characteristics of Thermal Liquefied Gas Propulsion Systems:
  High degree of reliability
  High system complexity (no combustion involved but storage of liquefied gas)
  Low Δv
  Extremely safe operation
  No contamination from exhaust (combustion) gases
  Low thrust
  Additional equipment (Heat Exchanger and potentially pump)
  Gas tank in liquid tank
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 130: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Example: SSHEL of ARIANE 5
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 131: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Performance comparison of different pneumatical propulsion systems
Space Propulsion ENG-510
L2 – Propulsion Systems
 | Cold Gas | Solid Powder | Cryogenic Boil-off | Liquefied Gas | Water Rocket
Medium | GN2 | GN2 | GH2 | GHe | Air
Temperature | 293 K | 1300 K | 20 K | 4 K up | 293 K
Use case | Cubesat propulsion Attitude control | Pressurant gas De-orbit burn | Attitude control | Attitude control Pressurant gas | Fun