## Slide 1: EPFL Space Center eSpace
Space Propulsion ENG-510

## Slide 2: Lecture # 2 Exercise
Δv and trajectories
Propulsion subsystem design for a LEO cargo return capsule

## Slide 3: Which Spacecraft can reach Moon?
Objective: To analyze performance need
The Space Shuttle – Fly me to the moon?
  Would it have been possible to fly to the moon with the Space Shuttle?
Space Shuttle data
  Lunar distance : 384,000 km
  Shuttle Orbital Speed : 7,680 m / s
  Maximum cargo mass : 28,000 kilograms
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 4: Which Spacecraft can reach Moon?
Objective: To analyze performance need
The Space Shuttle – Fly me to the moon?
  The Moon is ‘located’ at an orbit speed of 1.0 km / s. What must be the Space Shuttle speed change to reach lunar orbit?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule
  Δv1 = 3.08 km / s
  Δv2 = 0.8 km / s
  Δvtot = 3.88 km / s

## Slide 5: Which Spacecraft can reach Moon?
Objective: To analyze performance need
The Space Shuttle – Fly me to the moon?
  When the Shuttle Orbital Maneuvering System (OMS) is turned on, it can cause a speed change of 0.6 m / s for every second that the engines are burning. How many seconds would the OMS have to remain on in order for the Space Shuttle to build up the necessary velocity change to reach the Moon?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule
The Δv to get to the moon is 3,880 m / s. The OMS can produce 0.6 m / s every second, so the total burn time would have to be T = 3,880 / 0.6 or about 6,467 s of continuous thrust.

## Slide 6: Which Spacecraft can reach Moon?
Objective: To analyze performance need
The Space Shuttle – Fly me to the moon?
  The OMS can produce a maximum Δ v of 1,000 m / s before consuming all of its 4,850 kg of fuel. How many kilograms of fuel will the OMS have to expend to get to the Moon?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule
We need a total Δv of 3,880 m / s, so 4,850 kg x (3,880 / 1,000) = 18,818 kg of fuel.

## Slide 7: Which Spacecraft can reach Moon?
Objective: To analyze performance need
The Space Shuttle – Fly me to the moon?
  Does the Space Shuttle have the payload capacity to carry enough extra fuel for this one-way trip?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule
The maximum cargo mass is 28,000 kg, the OMS fuel would require 18,818 / 28,000 = 0.67 times the maximum load of the Space Shuttle cargo bay, i.e. 67 % of the payload capability.

## Slide 8: Which Launch Site is the best?
Objective: To get good understanding of trajectories
Which launch site would you choose and why for:
  GTO mission
  ISS mission
  SSO mission
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 9: Which Launch Site is the best?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule
GTO
ISS
ISS
SSO

## Slide 10: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Design the propulsion subsystem for a LEO cargo return capsule
  Dry mass of 10 tons
  Mission duration of 6 months
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 11: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Design the propulsion subsystem for a LEO cargo return capsule
  To develop a vehicle, its associated infrastructure and operations, capable of delivering pressurized cargo to human outposts in LEO and returning cargo to Earth (basic configuration)
  To execute a demonstration mission to the ISS targeting a launch date before the end of 2029
  To ensure that the vehicle, its associated infrastructure and operations, are compatible with the evolutions to a crew transportation service to human outposts in LEO (evolution step 1) and to a cargo return service from Gateway in cis-lunar orbit without major modifications of the architecture (evolution step 2)
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 12: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Main requirements (L0 – Level 0):
  Maiden flight with demo to ISS before end 2029
  Upload 4 ton pressurized cargo to LEO
    Cargo density of 260 kg / m³
  Download 2 ton pressurized cargo
  Competitive price / kg on LEO market
    < 75 k€ / kg for pressurized cargo upload
    3.5 ton mission => 260 M€
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 13: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Main requirements (L0 – Level 0):
  Versatility / growth potential for evolution towards
    LEO crewed missions (a minimum crew size of 3, a docked mission duration of 210 days and an autonomous flight duration consistent with the phasing, rendezvous, and re-entry concepts, including contingencies)
    Download 2 ton cargo mission from Lunar Gateway
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 14: Which Propulsion System for LEO Capsule?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule
Launcher
separation
Holding
plane
Docking / Un-docking
Re-entry
Landing

## Slide 15: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system selection (we consider launch abort system as part of launch vehicle):
  Which propulsion technology might fit to LEO cargo return capsule?
    Electrical propulsion
      Electromagnetic acceleration (MPD thruster, pulsed plasma thruster, magnetic nozzle thruster)
      Electrostatic acceleration (gridded ion thruster, hall effect thruster, field emission EP, electrospray thruster)
      Electrothermal acceleration (resistojet thruster, arcjet thruster)
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 16: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system selection (we consider launch abort system as part of launch vehicle):
  Which propulsion technology might fit to LEO cargo return capsule?
    Thermal propulsion
      Nuclear thermal thruster
      Solar thermal thruster
      Cold gas thruster
    Chemical propulsion
      Gaseous
      Liquid
      Solid
      Hybrid
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 17: Which Propulsion System for LEO Capsule?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 18: Lecture # 2 Back-up
Δv and trajectories
Propulsion subsystem design for a LEO cargo return capsule

## Slide 19: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
    Electrical propulsion
      Electromagnetic acceleration (MPD thruster, pulsed plasma thruster, magnetic nozzle thruster)
      Electrostatic acceleration (gridded ion thruster, hall effect thruster, field emission EP, electrospray thruster)
      Electrothermal acceleration (resistojet thruster, arcjet thruster)
    Thermal propulsion
      Nuclear thermal thruster
      Solar thermal thruster
      Cold gas thruster
    Chemical propulsion
      Gaseous
      Liquid
      Solid
      Hybrid

## Slide 20: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 21: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Design the propulsion subsystem for a LEO cargo return capsule
  Dry mass of 10 tons
  Mission duration of 6 months
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 22: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
    Electrical propulsion
      Electromagnetic acceleration (MPD thruster, pulsed plasma thruster, magnetic nozzle thruster)
      Electrostatic acceleration (gridded ion thruster, hall effect thruster, field emission EP, electrospray thruster)
      Electrothermal acceleration (resistojet thruster, arcjet thruster)
    Thermal propulsion
      Nuclear thermal thruster
      Solar thermal thruster
      Cold gas thruster
    Chemical propulsion
      Gaseous
      Liquid
      Solid
      Hybrid

## Slide 23: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 24: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
    Propulsion technology trade

## Slide 25: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 26: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which performance is required for LEO cargo return capsule?
  Are the customer (L0) requirements sufficient?
    Delta v…
    Thrust…
    Isp…
    Delta v need is about 500 m/s for LEO cargo return capsule
    Thrust need differs between attitude control and delta v maneuvers
    Attitude control requires pulse mode firing with small MIB
    Delta v maneuver require steady state firing with sufficient thrust
    Thrust level of 20 N is good starting point for attitude control thrusters
    Thrust level of 200 N is reasonable for delta v thrusters (considering 4 thrusters running in parallel)
    Isp depends on propellant combination

## Slide 27: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 28: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which performance is required for LEO cargo return capsule?
    Isp…
    Isp depends on propellant combination
    Rocket CEA
    Propellant data from REFPROP (computer program developed by the National Institute of Standards and Technology (NIST). NIST database contains the thermophysical data of several fluids in the gas, liquid and supercritical state which are accessible through a Python request calling the REFPROP library)

## Slide 29: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 30: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which performance is required for LEO cargo return capsule?
    Isp…
    Isp depends on propellant combination
    Rocket CEA

## Slide 31: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 32: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
    Oxygen
    Nitrogen
    CO2 carbon dioxide
    Water

## Slide 33: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 34: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
    Electrolyser

## Slide 35: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 36: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
    Sabatier reactor

## Slide 37: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 38: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?

## Slide 39: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 40: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Any impact by evolution step 2? Docking to Lunar Gateway?
    Delta v need of 4 km / s

## Slide 41: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 42: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system selection:
  Which propulsion technology might fit to LEO cargo return capsule?
  Final selection?
So this was the easy part. Let’s continue with some more difficult topics…

## Slide 43: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 44: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system design:
  Budgets?
    Propellant budget
    Pressurant budget
    Mass budget
    Power budget
    Pressure budget
    Temperature budget

## Slide 45: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 46: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system design:
  Functional break-down?
    To provide axial thrust (delta v maneuver)
    To provide orbital control (attitude control maneuver)
    To load propellant
    To store propellant
    To feed propellant
    To monitor propulsion system (pressure, temperature, …)
    To operate valves
    To control temperature

## Slide 47: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 48: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system design:
  Functional matrices?
    Functions versus phases
    Functions versus products
Function | Ground phase | Ascent phase | Orbital phase | De-orbit phase
F1 Axial thrust |  |  | X | X
F2 Orbital control |  |  | X | X
Function | Pressure vessel | Tank | Valve | Thruster
F1 Axial thrust | X | X | X | X
F2 Orbital control | X | X | X | X

## Slide 49: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 50: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system design:
  Interfaces?
    Electrical interface
    Mechanical interface
    Thermal interface
    Structural interface
    Communication interface

## Slide 51: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 52: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system design:
  Requirements?
    L1 System
    L2 Subsystem
    L3 Equipment

## Slide 53: Which Propulsion System for LEO Capsule?
A
B
  C
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 54: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system design:
  Alert!
    Dry mass increase of 1 ton
    MBSE – Model Based System Engineering
    Any changes to propulsion system selection?

## Slide 55: SW 1: Spacecraft Subsystems I - Propulsion Exercise Propulsion system selection exercise: LEO cargo return capsule
Propulsion system design:
  Mayday!
    Did we consider RAMS / safety?
    Quality control?
    Configuration management?

## Slide 56: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Assumptions:
  Performance: 200 N bi-propellant thruster
  Oxidizer: HTP (98 % concentrated H2O2)
  Fuel: DMAZ (hypergolic with HTP with some add-ons)
  Epsilon: 100
  Chamber pressure: 10 bar

## Slide 57: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Main dimensions:

## Slide 58: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Rocket CEA:
  Input
    Chamber pressure (10 bar)
    Mixture ratio
    Nozzle area ratio so called epsilon (100)
    Chemical composition assumption
    Chemical reaction: Combustion frozen @ throat
    Propellant data from REFPROP (computer program developed by the National Institute of Standards and Technology (NIST). NIST database contains the thermophysical data of several fluids in the gas, liquid and supercritical state which are accessible through a Python request calling the REFPROP library)
  Output
    Thruster vacuum specific impulse Isp
    Chamber characteristic speed c*

## Slide 59: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Rocket CEA:
  Optimal mixture ratio for HTP_98 / DMAZ?
    MR = 3.0
    Isp = 320 s
    c* = 1687,75 m / s

## Slide 60: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster architecture:
  Cooling method?
    Radiative cooling
    Film cooling
    Regenerative cooling
    Vortex cooling
    Ablative cooling
    Capacitive cooling
    Radiative cooling or film cooling
    We choose film cooling (note: radiative cooling is always given) with showerhead ingestion considering 12 orifices in axial direction

## Slide 61: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster architecture:
  Cooling fluid and flow rate?
    Fuel is very often used as cooling fluid
    Selection depends on fluid heat capacity, mixture ratio, mass flow rate, density and oxidizer + fuel combination
    In our case we choose HTP as cooling fluid due to mixture ratio and hence high HTP mass flow rate compared to DMAZ
    As a starting flow rate we consider 30 % compared to nominal mass flow rate (note: This will reduce the thruster performance compared to CEA analysis results)

## Slide 62: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Mass flow rate?

## Slide 63: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Oxidizer + fuel + cooling mass flow rate?
-

## Slide 64: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Throat diameter?

## Slide 65: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Main dimensions:
  Throat length?
    Throat is considered as a cylinder, with the height equal to the diameter, which enables to provide the throat length (assumption acceptable for small thrusters)

## Slide 66: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Nozzle design?
    Baseline is to implement a bell-shape nozzle
    As first estimation, the length of the bell-shape nozzle is calculated as 80% of the length of a reference 15° conical nozzle (cf Rocket Propulsion Elements Cone- and Bell-Shaped Nozzles” paragraph)
    We can then derive the nozzle length L_noz as

## Slide 67: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Nozzle design?
    Nozzle diameter
    Nozzle length L_noz

## Slide 68: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Chamber dimension?
    Chamber is composed of a cylindrical part and a conical part to link the cylindrical part to the throat
    The cylindrical part diameter is defined with the following equation
    Current baseline contraction angle is 20° (initial assumption for small thruster)
    Length of the conical part L_con is defined as follows

## Slide 69: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Chamber dimension?
    Characteristic length L* / combustion efficiency
    Longer combustion chamber results in higher combustion efficiency (i.e. higher performance)

## Slide 70: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Chamber dimension?
    Contraction ratio
    For constant L*, high contraction ratio results in shorter combustion chamber length

## Slide 71: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Chamber dimension?
    Contraction ratio
    We choose 8

## Slide 72: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Chamber dimension?
    Characteristic length
    We choose L* = 0.8 m
    Combustion chamber cylindrical part length:

## Slide 73: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Chamber length?

## Slide 74: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Thruster length?

## Slide 75: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Injection method?
  Is partially depending on ignition type
  Ignition of propellants
    Hypergolic ignition
    Catalytic decomposition
    Thermal decomposition (e.g. hot gas, thermal wire, …)
    Spark plug
    Glow plug
    Laser ignitor
    Resonance acoustic ignition
    …
    Torch ignitor (Different propellant or same propellants with smaller amount)
    For HTP / DMAZ propellant combination hypergolic ignition is given

## Slide 76: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Injection method?
  Injection method for propellants
    Impingement
    Concentric / coaxial tube (with or without swirl)
    Splash plate
    Showerhead
    Pintle injector

## Slide 77: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Injection method?
    Impingement method w.r.t. hypergolic propellants as they are well studied
    Unlike or like impingement?
      Like impinging is first impinging of all fuel flows and all oxidizer flows and subsequently mixing of fuel and oxidizer
      Unlike impinging is direct impinging of fuel flows and oxidizer flows
      Unlike impingement
      2 on 1 unlike impingement for 200 N thruster

## Slide 78: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Injector design?
    To size the orifice diameter, a correlation for the orifice ratio which maximizes the mixing efficiency is commonly used
    This correlation calculates the product of the velocity-head ratio and diameter ratio of the two streams based on experimental data

## Slide 79: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Injector design?
    Following constraints + steps need to be considered:
      Constraint # 1: One of the constraints to consider when 3D printing elements is the maximum angle printable (above an angle of 45°, post-processing is required to manufacture the part)
      Input parameter: The mass flow rate is fixed to provide a 200 N thrust
      Orifice size: To increase the fuel orifice size and facilitate manufacturability, the pressure drop for the fuel and oxidizer orifices is fixed at 0.5 bars (smallest orifice size manufacturable is fixed at 0.4 mm diameter with post-processing to ensure a good surface finishing)
      For a triplet (2 on 1), the most uniform mixture ratio distribution is obtained when the product of the velocity-head ratio and diameter ratio of the two streams is equal to 1.6
      Therefore, the fuel orifices diameter is first estimated and based on this value, the oxidizer orifice size is calculated to optimize the velocity-head ratio product
      Injection angle: The injection angles are estimated considering a resultant momentum angle null

## Slide 80: SW 1: Spacecraft Subsystems I - Propulsion Exercise Equipment layout exercise: First design iteration of 200 N thruster
Thruster design:
  Injector design?
    Following constraints + steps need to be considered:
      Orifice length: The orifice length should have a value above 15 times the orifice diameter according to NASA
      Free stream length: For the hypergolic injector, the fuel Lfs ratio is fixed to 10 which imposes the oxidizer Lfs ratio

## Slide 81: SW 1: Spacecraft Subsystems I - Propulsion Exercise
Equipment layout exercise: First design iteration of 200 N thruster

## Slide 82: SW 1: Spacecraft Subsystems I - Propulsion Exercise
Equipment layout exercise: First design iteration of 200 N thruster
Ready for 3D printing (choosing good material) +
respecting post manufacturing inspection / cleaning

## Slide 83: What do we know on Teammates?
Objective: What do we know on Teammates
What would be the most audacious thing that you have every done? Parachute jump
What song could you sing? Never ask me to sing!
What is your favorite holiday destination? Bicycle trips in the Alpes
If you could interview anyone famous (dead or alive, real or fiction) who would that be? No interest
What person has influenced you the most? Apart from my parents it is Richard Nerurkar who initiated my interest in running
Space Propulsion ENG-510
L1 – Personalities & Icebreaker