## Slide 1: EPFL Space Center eSpace
Space Propulsion ENG-510

## Slide 2: Lecture # 3 Introduction & General Course Information
Brief information on your lecturer and the space propulsion course

## Slide 3: Project Outline
Exercise Description:
Exercise # 3 (due date on 23.3.2025): Performance Analysis
  1-pager with the performance analysis of your Water rocket including theoretical description of the equations involved
  Presentation of analysis results including graphs like altitude over time, speed over time, mass over time, pressure over time
  Description of payload separation system + performance
Evaluation on 25.3.2025
  To provide more details on the ground I/F (for some groups)
Space Propulsion ENG-510
L3 - Introduction

## Slide 4: Lecture # 3 Part # 3 Introduction in Propulsion Systems
Brief overview on all space propulsion systems

## Slide 5: What is the principle of Space Propulsion?
Space Propulsion:
Space propulsion or better in-space propulsion exclusively deals with propulsion systems used in the vacuum of space
(In-space propulsion should not be confused with space launch or atmospheric re-entry)
In that sense space or spacecraft propulsion is any method used to accelerate spacecraft / satellites by ejection of material
So the basic working principle in its simplest form, is a system that accelerates matter to provide a force of thrust that moves or rotates a vehicle
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 6: What is the principle of Space Propulsion?
Basic Relations:
Velocity change – Basic rocket equation (Tsiolkovsky rocket equation)
...Delta v - maximal change of velocity of the vehicle [m / s]
…Exhaust velocity [m / s]
...Mass change [kg]
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 7: What is the principle of Space Propulsion?
Basic Relations:
Specific impulse – Propulsion efficiency (the efficiency of propellant use (the amount of impulse produced per mass of propellant
…Specific impulse [s]
…Earth gravitational acceleration [m / s²]
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 8: What is the principle of Space Propulsion?
Basic Relations:
Thrust – Propulsion duration
...Momentum thrust magnitude [N]
Mass flow rate of the propellant [kg/s]
…Exhaust velocity [m/s]
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 9: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Space propulsion / in-space propulsion / towards space propulsion – Everything that accelerates a vehicle (launcher, rocket, satellite, orbital vehicle) by ejection of material but also…
Non-ejection systems that accelerates a vehicle like solar sails
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 10: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Space Propulsion ENG-510
L3 – Propulsion Systems
Space Propulsion
Material Ejection
Non-Material Ejection

## Slide 11: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Material and Acceleration:
  Material needs to be exhausted (which is already given by pressure difference between storage reservoir and space vacuum)
  Material needs to be accelerated as much as possible to increase efficiency
Space Propulsion ENG-510
L3 – Propulsion Systems
Mass
Acceleration
Impulse
Orifice

## Slide 12: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Propulsion systems are categorized in this course w.r.t. acceleration principle:
  Acceleration by thermal heating or cooling
  Acceleration by chemical reaction
  Acceleration by electrostatic fields or electromagnetic fields
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 13: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Thermal Propulsion Systems
  A thermal propulsion system is a system that ejects a propellant that is externally heated before being passed through a nozzle to produce thrust at a high medium velocity (as opposed to being internally heated by a combustion reaction as in a chemical propulsion system) or that is cooled down by expansion before being passed through a nozzle to produce at a small exhaust velocity
  Thermal rockets can theoretically give high performance, depending on the fuel used and design specifications
  Today the simple cold gas thruster is widely used for attitude control
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 14: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Thermal Propulsion Systems
  For a space propulsion system, the efficiency of propellant use (the amount of impulse produced per mass of propellant) is measured by the specific impulse which is proportional to the effective exhaust velocity
  For thermal propulsion systems, the specific impulse increases as the square root of the temperature, and inversely as the square root of the molecular mass of the exhaust
  In the simple case where a thermal source heats an ideal monatomic gas reaction mass, the maximum theoretical specific impulse is directly proportional to the thermal velocity of the heated gas
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 15: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Thermal Propulsion Systems
…Specific impulse [s]
…Exhaust velocity [m / s]
...Ejected mass [kg]
…Boltzmann constant [J / K]
...Temperature [K]
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 16: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Chemical Propulsion Systems
  Chemical propulsion systems obtain the energy needed to generate thrust by ‘internal’ chemical reactions to create a hot gas that is expanded (through a nozzle) to produce thrust with a medium exhaust velocity
  Many different propellant combinations are used to obtain these chemical reactions, including, for example, hydrazine, liquid oxygen, liquid hydrogen, nitrous oxide and hydrogen peroxide
  Propellants can be used as a monopropellant or in bi- respectively tri-propellant configurations
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 17: Which Propulsion Systems do we know?
Objective: To categorize different space propulsion systems
Electrical Propulsion Systems
  In contrast to chemical propulsion systems, electric propulsion systems use electrostatic or electromagnetic fields to accelerate a charged propellant
  The benefit of this method is that the acceleration of a charged propellant by electric fields can achieve very high exhaust velocities, up to 10 times greater than those of a chemical engine, producing steady thrust with far less fuel
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 18: Which Propulsion Systems do we know?
Objective: To categorize different (most relevant) space propulsion systems
Space Propulsion ENG-510
L3 – Propulsion Systems
Space Propulsion
Material Ejection
Non-Material Ejection
Thermal Propulsion Systems
Chemical Propulsion Systems
Electrical Propulsion Systems

## Slide 19: Which Propulsion Systems do we know?
Objective: To categorize different (most relevant) space propulsion systems
Space Propulsion ENG-510
L3 – Propulsion Systems
Space Propulsion
Material Ejection
Non-Material Ejection
Thermal Propulsion Systems
Chemical Propulsion Systems
Electrical Propulsion Systems

## Slide 20: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Thermal Propulsion Systems
  Cold gas propulsion systems
  Cold gas / liquid propulsion systems (e.g. Water rocket…)
  Solid powder / cold gas propulsion systems
  Cryogenic boil-off propulsion systems
  Liquefied gas propulsion systems
  Steam (hot Water vapor) propulsion systems
  Electrothermal propulsion systems
  Solar thermal propulsion systems
  Nuclear thermal propulsion systems
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 21: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Thermal Propulsion Systems – Group 1 – Acceleration principle by expansion leading to medium cool-down
  Cold gas propulsion systems
  Cold gas / liquid propulsion systems (e.g. Water rocket…)
  Solid powder / cold gas propulsion systems
  Cryogenic boil-off propulsion systems
  Liquefied gas propulsion systems
  Steam (hot Water vapor) propulsion systems
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 22: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Thermal Propulsion Systems – Group 2 – Acceleration principle by medium heating with electric power (+ expansion leading to medium cool-down)
  Electrothermal propulsion systems
  Thermal Propulsion Systems – Group 3 by medium heating with other power means (+ expansion leading to medium cool-down)
  Solar thermal propulsion systems
  Nuclear thermal propulsion systems
  Laser thermal propulsion systems
  Microwave thermal propulsion systems
  Others…
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 23: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Space Propulsion ENG-510
L3 – Propulsion Systems
Cold gas propulsion systems
Acceleration by Expansion
Thermal Propulsion Systems
Acceleration by Electric Heat
Acceleration by other Power Heat
Cold gas / liquid propulsion systems
Solid powder / cold gas propulsion systems
Cryogenic boil-off propulsion systems
Liquefied gas propulsion systems
Steam (hot Water vapor) propulsion systems
Arcjet Electrothermal Thruster
Resistojet Electrothermal Thruster

## Slide 24: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Space Propulsion ENG-510
L3 – Propulsion Systems
Solar thermal propulsion systems
Acceleration by Expansion
Thermal Propulsion Systems
Acceleration by Electric Heat
Acceleration by other Power Heat
Nuclear thermal propulsion systems
Radioisotope thermal propulsion systems
Laser thermal propulsion systems
Microwave thermal propulsion systems

## Slide 25: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
For group 2 and group 3 Thermal Propulsion Systems it is important to understand the power needed to increase especially the Isp to a higher value compared to a pure expansion acceleration principle
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 26: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Description of Steam (hot Water vapor) Propulsion Systems:
  A steam rocket (also known as a "hot water propulsion system") is a thermal propulsion system that uses water held in a pressure vessel at a high temperature, such that its saturated vapor pressure is significantly greater than ambient pressure
  The water is allowed to escape as steam through a rocket nozzle to produce thrust
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 27: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Description of Steam (hot Water vapor) Propulsion Systems:
  Water, while under pressure, is heated up to a high temperature (approx. 250 to 500 °C)
  As the hot water goes through the nozzle and the pressure reduces, the water flashes to steam pressing on the nozzle, and leaving at high speed
  The nozzle of hot water thermal propulsion systems must be able to withstand high pressure, high temperatures and the particularly corrosive nature of hot water
  The simplest design has a pressurized water tank where the water is heated
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 28: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 1
Characteristics of Steam (hot Water vapor) Propulsion Systems:
  High degree of reliability
  Very low exhaust velocity since the high latent heat of vaporization means that very little actual steam is produced and the exhaust consists mostly of water
  If high temperatures and pressures are used, then the tank is very heavy
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 29: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Acceleration by Electric Heat as for example in electrothermal thrusters (+ through expansion via a nozzle)
  Resistojets: fluid warm-up with an electric resistance
  Arcjets: fluid warm-up with an electric arc
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 30: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Space Propulsion ENG-510
L3 – Propulsion Systems
Acceleration by Expansion
Thermal Propulsion Systems
Acceleration by Electric Heat
Acceleration by other Power Heat
Arcjet Electrothermal Thruster (~ 8 km/s)
Resistojet Electrothermal Thruster (~ 2 km/s)

## Slide 31: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Electrothermal Thruster – Operations and Performance
  Thrust generated by heating and acceleration of propellant through a nozzle
  Hence specific impulse maximized for propellants with high specific heat and high temperature
  High specific heat => low molecular weight
  Low molecular weight gaseous propellants are more difficult to store (tank mass and volume scales approximately with inverse of molecular weight)
  Trade of propellant mass gains against tank mass penalty
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 32: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion
Space Propulsion ENG-510
L3 – Propulsion Systems
Acceleration by Expansion
Thermal Propulsion Systems
Acceleration by Electric Heat

## Slide 33: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
  Resistojets are electrothermal devices in which the propellant is heated by passing through a resistively heated chamber or over a resistively heated element before entering a downstream nozzle
  The increase in exhaust velocity is due to thermal heating of the propellant, which limits the Isp to rather low levels for an EP system (< 500 s)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 34: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
  Application: many
  Working fluid: hot gas
  Working fluid generation: resistive heating
  Acceleration: nozzle
  Exhaust velocity (typical): 1 – 5 km/s
  Power (typical): 10 W – 2 kW
  Temperatures: typically ~ 800 to 1500 K
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 35: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
  Principle:
    Electrical heaters instead of chemical combustion (no ionization)
  Propellants:
    Nearly all (Butane, Water, Xenon, Nitrogen, Hydrazine, Ammonia, Hydrogen)
  Typical Isp:
    50 s (Xe) to 300 (Hydrazine) @ 50 to 90 %
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 36: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
  Advantages
    Simpler design / configuration
  Disadvantages
    Performance efficiency is less compared to GIT (Gridded Ion Thruster)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 37: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 38: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 39: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
  EHT – Electrothermal hydrazine thrusters
  Heats the decomposition products of a monopropellant hydrazine thruster to boost the specific impulse
  Performance summary:
    Specific impulse 290 to 300 s
    150 to 800m N
    Specific power typically 1 to 2 W/mN
    Efficiencies apparently > 100 %; due to contribution from chemical energy released during decomposition
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 40: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Resistojet thrusters
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 41: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
  An arcjet is also an electrothermal thruster that heats the propellant by passing it though a high current arc in line with the nozzle feed system
  As there is an electric discharge involved in the propellant path, plasma effects are insignificant in the exhaust velocity because the propellant is weakly ionized
  The electrical discharge in the propellant flow adds energy to the propellant
  Use either an inert propellant, or are combined with a monopropellant hydrazine thruster
  Isp is therefore limited by the thermal heating to less than about 700 s for easily stored propellants
  1994: First Arcjet used for operation on TELSTAR 401 (Martin Marietta)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 42: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
  Application: many
  Working fluid: plasma
  Working fluid generation: arc discharge
  Acceleration: nozzle
  Exhaust velocity (typical): 5 – 10 km/s
  Power (typical): 1 – 2 kW
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 43: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
  Principle:
    Electric arc heats incoming gas up to several thousand degree (only little ionization is needed)
  Propellants:
    Lightweight (H2, He, N2H4, NH3)
    Not amused about oxygen (erosion) and carbon (deposition)
  Typical Isp:
    600 s (Hydrazine) @ 30 to 40 %
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 44: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
  Advantages:
    Technology requiring low power (9 kW/N)
  Drawbacks:
    Limited specific Impulse
    Erosion and Arc stability
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 45: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 46: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 47: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
  A
Space Propulsion ENG-510
L2 – Propulsion Systems
Deposition
Erosion

## Slide 48: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 2
Arcjet thrusters
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 49: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Acceleration by other power sources to heat propellant (+ through expansion via a nozzle)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 50: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Space Propulsion ENG-510
L3 – Propulsion Systems
Solar thermal propulsion systems
Acceleration by Expansion
Thermal Propulsion Systems
Acceleration by Electric Heat
Acceleration by other Power Heat
Nuclear thermal propulsion systems
Radioisotope thermal propulsion systems
Laser thermal propulsion systems
Microwave thermal propulsion systems

## Slide 51: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Description of solar thermal propulsion systems
  A solar thermal rocket is a spacecraft propulsion system that would make use of solar power to directly heat reaction mass (propellant like Hydrogen), and therefore would not require an electrical generator, like most other forms of solar-powered propulsion do
  The rocket would only have to carry the means of capturing solar energy, such as mirrors
  The heated propellant would be fed through a conventional rocket nozzle to produce thrust
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 52: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Description of solar thermal propulsion systems
  Its engine thrust would be directly related to the surface area of the solar collector and to the local intensity of the solar radiation
  In the shorter term, solar thermal propulsion has been proposed both for longer-life, lower-cost, more efficient use of the sun and more-flexible cryogenic upper stages
  Solar thermal propulsion is also a good candidate for use in reusable inter-orbital tugs, as it is a high-efficiency low-thrust system that can be re-fueled with relative ease
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 53: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Architecture of solar thermal propulsion systems
Space Propulsion ENG-510
L2 – Propulsion Systems
Tank
Valve
Exhaust
R
Regulator
Collector
Heating

## Slide 54: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Solar thermal propulsion systems
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 55: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Description of nuclear thermal propulsion systems
  A nuclear thermal rocket (NTR) is a type of thermal rocket where the heat from a nuclear reaction (nuclear fission), replaces the chemical energy of the propellants in a chemical propulsion system
  In an NTR, a working fluid (propellant), usually Liquid Hydrogen, is heated to a high temperature in a nuclear rocket and then expands through a rocket nozzle to create thrust
  The external nuclear heat source theoretically allows a higher effective exhaust velocity and is expected to double or triple payload capacity compared to chemical propellants that store energy internally
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 56: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Description of nuclear thermal propulsion systems
  NTRs have been proposed as a spacecraft propulsion technology, with the earliest ground tests occurring in 1955
  The USA maintained an NTR development program through 1973 when it was shut down to focus on Space Shuttle development
  Although more than ten reactors of varying power output have been built and tested, as of 2021, no nuclear thermal rocket has flown
  Further classification is the type of core: Solid, liquid or gas core
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 57: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  In a nuclear thermal rocket a working fluid, usually liquid hydrogen, is heated to a high temperature in a nuclear reactor, and then expands through a nozzle to create thrust
  The nuclear reactor's energy replaces the chemical energy of the reactive chemicals in a chemical propulsion system
  Due to the higher energy density of the nuclear fuel compared to chemical fuels, the resulting specific impulse of the engine is at least twice as good as chemical engines
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 58: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  A nuclear thermal propulsion system can be categorized by the type of reactor, ranging from a relatively simple solid reactor up to the much more difficult to construct but theoretically more efficient gas core reactor
  As with all thermal propulsion system designs, the specific impulse produced is proportional to the square root of the temperature to which the working fluid (reaction mass) is heated
  To extract maximum efficiency, the temperature must be as high as possible
  For a given design, the temperature that can be attained is typically determined by the materials chosen for reactor structures, the nuclear fuel, and the fuel cladding
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 59: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  Solid core nuclear reactor fuel
    Solid core nuclear reactors have been fueled by compounds of uranium that exist in solid phase under the conditions encountered and undergo nuclear fission to release energy
    Flight reactors must be lightweight and capable of tolerating extremely high temperatures, as the only coolant available is the working fluid/propellant
    A nuclear solid core engine is the simplest design to construct and is the concept used on all tested NTRs
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 60: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 61: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  NERVA solid core design (tested on ground)
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 62: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  Liquid core nuclear reactor fuel
    Liquid core nuclear engines are fueled by compounds of fissionable elements in liquid phase
    A liquid-core engine is proposed to operate at temperatures above the melting point of solid nuclear fuel and cladding
    The higher operating temperatures would be expected to deliver specific impulse performance on the order of 1300 to 1500 s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 63: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  Liquid core nuclear reactor fuel
    A liquid-core reactor would be extremely difficult to build with current technology
    One major issue is that the reaction time of the nuclear fuel is much longer than the heating time of the working fluid
    If the nuclear fuel and working fluid are not physically separated, this means that the fuel must be trapped inside the engine while the working fluid is allowed to easily exit through the nozzle
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 64: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  Gas core nuclear reactor fuel
    The final fission classification is the gas-core system
    This is a modification to the liquid-core design which uses rapid circulation of the fluid to create a torodial pocket of gaseous uranium fuel in the middle of the reactor, surrounded by hydrogen
    In this case, the fuel does not touch the reactor wall at all, so temperatures could reach several tens of thousands of degrees, which would allow specific impulses of 3000 to 5000 s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 65: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  Gas core nuclear reactor fuel
    In this basic design, the "open cycle", the losses of nuclear fuel would be difficult to control, which has led to studies of the "closed cycle" or where the gaseous nuclear fuel is contained in a super-high-temperature quartz container, over which the hydrogen flows
    The closed-cycle engine has much more in common with the solid-core design, but this time is limited by the critical temperature of quartz instead of the fuel and cladding
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 66: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  Gas core nuclear reactor fuel
Space Propulsion ENG-510
L2 – Propulsion Systems
Closed Cycle Gas Core
Open Cycle Gas Core

## Slide 67: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  NTER (Nuclear Thermal Electric Rocket) Concept from ESA
    Conductive heating of the hydrogen in the subsonic area
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 68: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  NTER (Nuclear Thermal Electric Rocket) Concept from ESA
    The cryogenic hydrogen is first pumped at high pressure, and then flows through a heat exchanger to be used as cold source for the Brayton cycle
    At the exit of the exchanger, the warm hydrogen can optionally provide some cooling to the throat area to protect the throat from excessive heating
    At this point the hydrogen enters the nuclear core at a temperature beyond 540K
    It is heated by the nuclear core up to an assumed temperature 2550K
    Then the hydrogen flows through the longitudinal channels of a turbo-inductor
    Its temperature is increased to 3250K by convection
    Finally, the hydrogen is exhausted through a nozzle to produce the thrust
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 69: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  NTER (Nuclear Thermal Electric Rocket) Concept from ESA
    Advantages: Testing on ground seems to be possible / safe
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 70: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Nuclear thermal propulsion systems
  NTER (Nuclear Thermal Electric Rocket) Concept from ESA
    Disadvantages: Very high engine mass
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 71: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Radioisotope thermal propulsion systems
  A variant is the radioisotope thermal propulsion system, in which the reaction mass is heated by a radioisotope heat source instead of a nuclear fission reactor
  A radioisotope rocket or radioisotope thermal rocket is a type of thermal propulsion system that uses the heat generated by the decay of radioactive elements to heat a working fluid, which is then exhausted through a rocket nozzle to produce thrust
  They are similar in nature to nuclear thermal propulsion systems, but are considerably simpler and often have no moving parts
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 72: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Radioisotope thermal propulsion systems
  The basic idea is a development of existing radioisotope thermoelectric generator, or RTG, systems, in which the heat generated by decaying nuclear fuel is used to generate power
  In the space propulsion the generator is removed, and the working fluid is instead used to produce thrust directly
  Temperatures of about 1500 to 2000 °C are possible in this system, allowing for specific impulses of about 700 to 800 s
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 73: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Radioisotope thermal propulsion systems
  However the amount of power generated by such systems is typically fairly low
  Whereas the full "active" reactor system in a nuclear thermal propulsion system can be expected to generate over a gigawatt, a radioisotope generator might get 5 kW
  Another drawback to the use of radioisotopes in rockets is an inability to change the operating power
  The radioisotope constantly generates heat that must be safely dissipated when it is not heating a propellant
  Reactors, on the other hand, can be throttled or shut down as desired
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 74: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Laser thermal propulsion systems
  The laser thermal propulsion system is a thermal propulsion system in which the propellant is heated by energy provided by an external laser beam
  The beam heats a solid heat exchanger, which in turn heats an inert liquid propellant, converting it to hot gas which is exhausted through a conventional nozzle
  The thermal energy source is a laser, which heats a working fluid in a heat exchanger
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 75: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Laser thermal propulsion systems
  Depending on the laser power, a laser thermal propulsion systems can have a thrust-to-weight ratio similar to chemical propulsion systems, while achieving a specific impulse similar to nuclear thermal propulsion systems
  There are two main approaches: off-board, where the laser source is external to the spacecraft, and onboard, where the laser is part of the spacecraft's propulsion system
  For ground-to-orbit launches, the laser source for such a rocket would be a permanent installation capable of high-frequency launches, while the rockets would only contain inert propellant
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 76: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Laser thermal propulsion systems
  N
  A laser thermal rocket is both a type of beam-powered propulsion and a thermal rocket. The thermal energy source is a laser, which heats a working fluid in a heat exchanger. The working fluid is then expanded through a nozzle to produce thrust. Depending on the laser power, a laser thermal rocket can have a thrust-to-weight ratio similar to chemical rockets, while achieving a specific impulse similar to nuclear thermal rockets.[7] For ground-to-orbit launches, the laser source for such a rocket would be a permanent installation capable of high-frequency launches, while the rockets could contain inert propellant
  There are two main approaches: off-board, where the laser source is external to the spacecraft, and onboard, where the laser is part of the spacecraft's propulsion system.
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 77: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Microwave thermal propulsion systems
  A microwave thermal propulsion system is similar to a laser thermal propulsion system, except that it is powered by a microwave source, for example a ground-based phased array
  Relative to lasers, the main advantage of using microwaves is that sources currently cost 1 to 3 orders of magnitude less per Watt
  The main disadvantage is that the microwave beam director needs to have a much larger diameter than a laser beam director due to beam diffraction effects
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 78: Which Thermal Propulsion Systems exist?
Objective: To develop the basics of thermal propulsion – Group 3
Microwave thermal propulsion systems
  In microwave thermal propulsion, an external microwave beam is used to heat a refractory heat exchanger to > 1500 K, heating a propellant such as hydrogen, methane, or ammonia
  This improves the propulsion system's specific impulse and thrust/weight ratio relative to conventional rocket propulsion
  For example, hydrogen can provide a specific impulse of 700–900 seconds and a thrust/weight ratio of 50-150
Space Propulsion ENG-510
L2 – Propulsion Systems

## Slide 79: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Space Propulsion ENG-510
L3 – Propulsion Systems
Space Propulsion
Material Ejection
Non-Material Ejection
Thermal Propulsion Systems
Chemical Propulsion Systems
Electrical Propulsion Systems

## Slide 80: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Space Propulsion ENG-510
L3 – Propulsion Systems
Chemical Propulsion Systems
Combustion
Detonation
Liquid propulsion systems
Rotation Detonation Engine
Pulse Detonation Engine
Gaseous propulsion systems
Gelled propulsion systems
Hybrid propulsion systems
Solid propulsion systems

## Slide 81: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Chemical Propulsion Systems
  Gaseous propulsion systems
  Liquid propulsion systems
  Gelled propulsion systems
  Solid propulsion systems
  Hybrid (liquid / solid) propulsion systems
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 82: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Chemical Propulsion Systems
  Gaseous propulsion systems
  Liquid propulsion systems
  Gelled propulsion systems
  Solid propulsion systems
  Hybrid (liquid / solid) propulsion systems
Space Propulsion ENG-510
L3 – Propulsion Systems
Propellant Phase in Tanks
Solid
Liquid
Gas
Chemical Reaction
No
Decomp
Combustion
Hydrazine (N2H4) HTP (H2O2) ADN
Monopropellant Thruster
LOx / LH2 – LOx / LCH4 – MON / MMH – HTP / Ethanol
HTP / IPA
Bipropellant Thruster
GOx / GCH4
Double base or composite
Bi-prop Thruster
Solid / Liquid
Hybrid Thruster Bi-prop
Gelled
Liquid Thruster

## Slide 83: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Chemical Propulsion Systems
Space Propulsion ENG-510
L3 – Propulsion Systems
Energy
Impulse
Chemical Energy by chemical reaction
Mass flow control by a nozzle throat
Kinetic Energy
Pressure + temperature increase

## Slide 84: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Chemical Propulsion Systems
Space Propulsion ENG-510
L3 – Propulsion Systems
Pressurization System

## Slide 85: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Chemical Propulsion Systems
  Propellant (reactant): O2, N2O4, H2O2, HNO3, NO2, H2, C𝑥H𝑦, N2H4, HNO3, NH4, NO2, …
  Propellant state: Cryogenic, green (non-toxic), storable (liquid in a room T), …
  Propellant phase (at storage or at injection…): Solid, liquid, gas
  Chemical reaction: Combustion, exothermic decomposition, …
  Pressure feeding method: Blow-down, regulator, Turbopump, …
  Cooling method: Regenerative cooling, ablative cooling, film cooling, radiative cooling, …
  Usage: Launch, upper stage, apogee kick, orbit insertion, etc
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 86
Propellant Phase in Tanks
Solid
Liquid
Gas
Chemical Reaction
No
Decomp
Combustion
GOx / GH2
Water Propulsion
The ultimate
green propellant
GOx / GCH4
NOx / Ethane
2-phase condition or supercritical condition

## Slide 87: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Characteristics of Gas / Gas Combustion Propulsion Systems:
  Gaseous propulsion systems with Water propulsion as the ultimate green propellant?
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 88: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Characteristics of Gas / Gas Combustion Propulsion Systems:
  High system complexity (combustion involved and Electrolyzer needed)
  Acceptable Δv
  Extremely safe operation
  No contamination from exhaust (combustion) gases
  Low thrust
  Fuel cell could be added for Energy storage
  Combination with ECLSS – Life Support System
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 89: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Architecture of Gas / Gas Combustion Propulsion Systems:
Space Propulsion ENG-510
L3 – Propulsion Systems
Water Tank
Valve
Exhaust
E
Electrolyzer
Valve
GOx Tank
GH2 Tank

## Slide 90: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Architecture of Gas / Gas Combustion Propulsion Systems:
  Propellant is stored as liquid
  Electrolyzer uses electrical energy as provided by S/C in order to generate GOx and GH2
  3 tanks are needed for Water propulsion system
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 91: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
REACH (no progress since a long time…): Registration, Evaluation and Authorization of Chemicals
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 92: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Chemical propulsion systems applications and green replacement candidates
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 93: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 94: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Is defined as propulsion with propellants that are produced in Space from water via an electrolyzer
  Is a semi electric propulsion where propellant generation (over a long time at low power) and usage (high thrust during a short period) is decoupled
  Water is stored at low pressure in a conventional tank; gases are generated in orbit
  Combined with a fuel cell it can even be used as a highly efficient battery
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 95: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Functional scheme:
Space Propulsion ENG-510
L3 – Propulsion Systems
Fully integrated System
for small satellites

## Slide 96: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Operational mode:
Space Propulsion ENG-510
L3 – Propulsion Systems
Gas Tanks (partly) empty
Gas Tanks full
Thruster Operation  Generation of Impulse
(Fuel cell operation  Generation of electric Power)
Electric Power  Charging of Gas Tanks
Next cycle
Start

## Slide 97: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Operation mode of the system is in cycles between gas generation and usage
  Functioning sequence of the subsystem:
    After the start the water feed is switched ON: water from the water tank is fed via low pressure into the electrolyzer
    GOX and GH2 are produced in the electrolyzer via electric power with a high pressure
    After production the propellants are stored in gas tanks and are ready for use (gas tanks full)
    The gases are used in the thrusters to generate thrust. Optional they can be used in a fuel cell to generate electric power
    When the gas tanks are empty the process starts again (back to step 1)
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 98: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Water tank size is driven by the total impulse requirement and a Thruster ISP of 320 s
  Gas tank size is driven by the required propellant mass per individual maneuver (cycle)
  Electrolyzer power is driven by the required propellant mass per individual maneuver (cycle) and the available / allowed charge time
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 99: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  System sizing parameter:
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 100: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion versus Conventional System
Example: Earth Care mission
  System Architecture
  4 x 5 N thrusters
  Total Propellant: 240 - 310 kg Hydrazine
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 101: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
  Mission Analysis
  Maximum impulse per sequence, derived from provided sample data: 5627 Ns
  2.6 kg Hydrazine, or 1.9 kg Water (based on Isp = 300 s)
  Amount needs to be available before next re-filling sequence could be started
  Derived Water Propulsion System Architecture
  GH2 – Tank: 52 ltr
  GO2 – Tank: 26 ltr
  Water Tank: 228 kg => 285 ltr Tank @ 5:1 Blow-down ratio
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 102: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
  Electrical Power Supply
  Theoretical possible (with satellite design changes): 350 W during sun, 150 W during Eclipse (Remark: Electrolyzer output not scalable, only on / off! Two cells required)
  Rough estimation for preliminary design: 200 W
  Orbit Data: 95 minutes total, 40 minutes in sun, 55 minutes in eclipse
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 103: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: Earth Care mission – Tank size
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 104: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: Earth Care mission – Charge time
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 105: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
  Example: Earth Care mission – Charge time versus available power
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 106: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
  Example: Earth Care mission – Gas tank volume versus impulse
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 107: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Test status:
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 108: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Test status:
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 109: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Example: Sierra Space
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 110: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  Example: Sierra Space
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 111: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  High performance (high Isp)
  Low cost, green propellant without any potential limitations in future
  Can be preloaded at manufacturer
  High gas pressure is only generated when electrical power is applied – safe
  If combined with fuel cell it can even be used as battery
  Existing COTS components can be used
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 112: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Water Propulsion
  But higher system complexity due to additional elements like electrolyzer or compressor
  Thruster requires high temperature combustion chamber material
  Usage only possible in cycle mode
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 113: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: NASA satellite with Water propulsion system
  A NASA CubeSat will launch into low-Earth orbit to demonstrate a new type of propulsion system
  Carrying a pint of liquid water as fuel, the system will split the water into hydrogen and oxygen in space and burn them in a tiny rocket engine for thrust
  Hydros hardware unit is a water-based propulsion system, sized for CubeSats
  The system uses electricity to produce gas propellants – hydrogen and oxygen – from liquid water and burns these gases in a rocket nozzle to generate thrust
  Hydros was developed by Tethers Unlimited
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 114: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Other Gaseous Propulsion Systems
  GOX / GCH4 (seems to be very interesting considering number of launch vehicles with LOX / LCH4 propellant
  NOx / Propylene self-pressurization propellants
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 115: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: TEC Nyx Moon capsule
  Nyx Moon capsule from The Exploration Company considers LOx / LCH4 thruster as main propulsion system
  Cryogenic liquid propellants will boil-off during the mission
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 116: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: TEC Nyx Moon capsule
  GOx / GCH4 generated during the mission could be used as attitude control system
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 117: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: Dawn Aerospace green bi-propellant propulsion system
  Self-pressurization propellants are considered
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 118: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Characteristics of Gas / Gas Combustion Propulsion Systems:
  B
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 119: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion :
  B
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 120: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: Dawn Aerospace green bi-propellant propulsion system
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 121: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: Dawn Aerospace green bi-propellant propulsion system
  Propellant tanks must support high pressure levels
  Long duration burns must be compatible with vaporization rate
  Potentially heaters are needed for propellant tanks in order to improve vaporization rate
  Gaseous feed to thruster must be ensured
  Cooling of thruster might be more difficult
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 122: Which Chemical Gaseous Propulsion Systems exist?
Objective: To develop the basics of chemical gaseous propulsion
Example: Dawn Aerospace green bi-propellant propulsion system
  But results in advantages linked to on-orbit refueling as well as sloshing limitation (in supercritical phase) important for de-orbiting kit
Space Propulsion ENG-510
L3 – Propulsion Systems

## Slide 123: Lecture # 3 Introduction & General Course Information
Brief information on your lecturer and the space propulsion course

## Slide 124: Potential Special Events
Proposals:
In May:
  Visit of EPFL rocket team test facility (e.g. on the Wednesday after the launch event, May 28)
In May:
  External lecturer with highlight lecture out of EPFL plasma center
  Topic: PhD on electric thrusters in VLEO + test possibilities in the plasma center
  Date: May 20
Space Propulsion ENG-510
L3 - Introduction

## Slide 125: Student Feedback
What are your expectations?
Feedback:
  From Monday 17 March until midnight Sunday 23 March, the teacher will have an opportunity to get feedback from students on your Bachelor, Master, CMS and MAN courses through the Indicative Student Feedback on Teaching
  Please use it!
Space Propulsion ENG-510
L3 - Introduction