## Slide 1: EPFL Space Center eSpace
Space Propulsion ENG-510

## Slide 2: Lecture # 3 Exercise
Propulsion subsystem design for a LEO cargo return capsule

## Slide 3: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Design the propulsion subsystem for a LEO cargo return capsule
  Dry mass of 10 tons
  Mission duration of 6 months
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 4: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Design the propulsion subsystem for a LEO cargo return capsule
  To develop a vehicle, its associated infrastructure and operations, capable of delivering pressurized cargo to human outposts in LEO and returning cargo to Earth (basic configuration)
  To execute a demonstration mission to the ISS targeting a launch date before the end of 2029
  To ensure that the vehicle, its associated infrastructure and operations, are compatible with the evolutions to a crew transportation service to human outposts in LEO (evolution step 1) and to a cargo return service from Gateway in cis-lunar orbit without major modifications of the architecture (evolution step 2)
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 5: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Main requirements (L0 – Level 0):
  Maiden flight with demo to ISS before end 2029
  Upload 4 ton pressurized cargo to LEO
    Cargo density of 260 kg / m³
  Download 2 ton pressurized cargo
  Competitive price / kg on LEO market
    < 75 k€ / kg for pressurized cargo upload
    3.5 ton mission => 260 M€
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 6: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Main requirements (L0 – Level 0):
  Versatility / growth potential for evolution towards
    LEO crewed missions (a minimum crew size of 3, a docked mission duration of 210 days and an autonomous flight duration consistent with the phasing, rendezvous, and re-entry concepts, including contingencies)
    Download 2 ton cargo mission from Lunar Gateway
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 7: Which Propulsion System for LEO Capsule?
Space Propulsion ENG-510
L3 – LEO Capsule
Launcher
separation
Holding
plane
Docking / Un-docking
Re-entry
Landing

## Slide 8: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system selection (we consider launch abort system as part of launch vehicle):
  Which propulsion technology might fit to LEO cargo return capsule?
    Electrical propulsion
      Electromagnetic acceleration (MPD thruster, pulsed plasma thruster, magnetic nozzle thruster)
      Electrostatic acceleration (gridded ion thruster, hall effect thruster, field emission EP, electrospray thruster)
      Electrothermal acceleration (resistojet thruster, arcjet thruster)
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 9: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system selection (we consider launch abort system as part of launch vehicle):
  Which propulsion technology might fit to LEO cargo return capsule?
    Thermal propulsion
      Nuclear thermal thruster
      Solar thermal thruster
      Cold gas thruster
    Chemical propulsion
      Gaseous
      Liquid
      Solid
      Hybrid
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 10: Which Propulsion System for LEO Capsule?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 11: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system selection (we consider launch abort system as part of launch vehicle):
  Which propulsion technology might fit to LEO cargo return capsule?
    Electrical propulsion
      Electromagnetic acceleration (MPD thruster, pulsed plasma thruster, magnetic nozzle thruster)
      Electrostatic acceleration (gridded ion thruster, hall effect thruster, field emission EP, electrospray thruster)
      Electrothermal acceleration (resistojet thruster, arcjet thruster)
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 12: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system selection (we consider launch abort system as part of launch vehicle):
  Which propulsion technology might fit to LEO cargo return capsule?
    Thermal propulsion
      Nuclear thermal thruster
      Solar thermal thruster
      Cold gas thruster
    Chemical propulsion
      Gaseous
      Liquid
      Solid
      Hybrid
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 13: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Design the propulsion subsystem for a LEO cargo return capsule
  Dry mass of 10 tons
  Mission duration of 6 months
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 14: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system selection (we consider launch abort system as part of launch vehicle):
  Which propulsion technology might fit to LEO cargo return capsule?
    Thermal propulsion
      Cold gas thruster
    Chemical propulsion
      Gaseous
      Liquid
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 15: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Which propulsion technology might fit to LEO cargo return capsule?
    Propulsion technology trade
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 16: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
B
  C
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 17: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Which performance is required for LEO cargo return capsule?
Are the customer (L0) requirements sufficient?
  Delta v…
  Thrust…
  Isp…
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 18: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Which performance is required for LEO cargo return capsule?
Are the customer (L0) requirements sufficient?
  Delta v need is about 500 m/s for LEO cargo return capsule
  Thrust need differs between attitude control and delta v maneuvers
  Attitude control requires pulse mode firing with small MIB
  Delta v maneuver require steady state firing with sufficient thrust
  Thrust level of 20 N is good starting point for attitude control thrusters
  Thrust level of 200 N is reasonable for delta v thrusters (considering 4 thrusters running in parallel)
  Isp depends on propellant combination
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 19: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Which performance is required for LEO cargo return capsule?
  Isp…
  Isp depends on propellant combination
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 20: Which Propulsion System for LEO Capsule?
Space Propulsion ENG-510
L2 – ∆v & LEO Capsule

## Slide 21: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Which performance is required for LEO cargo return capsule?
  Isp…
  Isp depends on propellant combination
  Rocket CEA
  Propellant data from REFPROP (computer program developed by the National Institute of Standards and Technology (NIST). NIST database contains the thermophysical data of several fluids in the gas, liquid and supercritical state which are accessible through a Python request calling the REFPROP library)
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 22: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 23: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Oxygen
  Nitrogen
  CO2 carbon dioxide
  Water
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 24: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Electrolyser
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 25: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Electrolyser
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 26: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Sabatier reactor
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 27: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Sabatier reactor
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 28: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Electrolyser + Sabatier Reactor
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 29: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 1? Crew of 3 on board?
  Electrolyser + Sabatier Reactor
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 30: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 2? Docking to Lunar Gateway?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 31: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Any impact by evolution step 2? Docking to Lunar Gateway?
  Delta v need of 4 km / s
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 32: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Final selection?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 33: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
  Which propulsion technology might fit to LEO cargo return capsule?
  Final selection?
So this was the easy part. Let’s continue with some more difficult topics…
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 34: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Budgets?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 35: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Budgets?
    Propellant budget
    Pressurant budget
    Mass budget
    Power budget
    Pressure budget
    Temperature budget
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 36: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Functional break-down?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 37: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Functional break-down?
    To provide axial thrust (delta v maneuver)
    To provide orbital control (attitude control maneuver)
    To load propellant
    To store propellant
    To feed propellant
    To monitor propulsion system (pressure, temperature, …)
    To operate valves
    To control temperature
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 38: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Functional matrices?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 39: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Functional matrices?
    Functions versus phases
    Functions versus products
Space Propulsion ENG-510
L3 – LEO Capsule
Function | Ground phase | Ascent phase | Orbital phase | De-orbit phase
F1 Axial thrust |  |  | X | X
F2 Orbital control |  |  | X | X
Function | Pressure vessel | Tank | Valve | Thruster
F1 Axial thrust | X | X | X | X
F2 Orbital control | X | X | X | X

## Slide 40: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Interfaces?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 41: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Interfaces?
    Electrical interface
    Mechanical interface
    Thermal interface
    Structural interface
    Communication interface
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 42: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Requirements?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 43: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Requirements?
    L1 System
    L2 Subsystem
    L3 Equipment
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 44: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Alert!
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 45: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Alert!
    Dry mass increase of 1 ton
    MBSE – Model Based System Engineering
    Any changes to propulsion system selection?
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 46: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Mayday!
Space Propulsion ENG-510
L3 – LEO Capsule

## Slide 47: Which Propulsion System for LEO Capsule?
Objective: To understand propulsion system selection process
Propulsion system design:
  Mayday!
    Did we consider RAMS / safety?
    Quality control?
    Configuration management?
Space Propulsion ENG-510
L3 – LEO Capsule