## Slide 1: EPFL Space Center eSpace
Space Propulsion ENG-510

## Slide 2: Lecture # 4 Introduction & General Course Information
Brief update on space propulsion course

## Slide 3: Oral Exam
Exercise Date:
Oral exam will take place on Wednesday, July 2 and Thursday, July 3 between 9 am and 5 pm
Excel spreadsheet with time slots will be uploaded next week on Moodle
Please book your timeslots starting from Tuesday, April 8
First in, first choice
Space Propulsion ENG-510
L4 - Introduction

## Slide 4: Special Lecture
Special Lecture:
Presentation on Electric Thrusters in VLEO + Test Facilities for Electric Thruster at EPFL will be given on Tuesday, May 27
Space Propulsion ENG-510
L4 - Introduction

## Slide 5: Test Facility Visit
ERT Test Facility Visit (including firing demonstration):
Test facility visit is proposed for Wednesday, May 28 starting between 9 to 10 am
Who is interested to join?
Agenda:
  Test facility tour
  Hot firing test (TBC)
Space Propulsion ENG-510
L4 - Introduction

## Slide 6: LOx/LH2 versus LOx/LCH4
Sustainability:
Which propellant combination is more sustainable?
  It is difficult to compare the two fuel propellants
  The pollution from Hydrogen mainly comes from the electricity used on ground to produce it
  During the combustion mainly Water vapor is released which is the first greenhouse gas
  For Methane the extraction and production is not that high compared to Hydrogen
  On flight it releases several particles and it is not known today how soot is developed in the plume
  And effects of emissions in the upper atmosphere are poorly known
Space Propulsion ENG-510
L4 - Introduction

## Slide 7: LOx/LH2 versus LOx/LCH4
Sustainability:
Which propellant combination is more sustainable?
  So potentially Methane as we lack knowledge on impact of sooth in upper atmosphere…
Space Propulsion ENG-510
L4 - Introduction

## Slide 8: Lecture # 4 Part # 3 Introduction in Propulsion Systems
Brief overview on all space propulsion systems

## Slide 9: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems
Space Propulsion
Material Ejection
Non-Material Ejection
Thermal Propulsion Systems
Chemical Propulsion Systems
Electrical Propulsion Systems

## Slide 10: Which Chemical Propulsion Systems exist?
Space Propulsion ENG-510
L4 – Propulsion Systems
Chemical Propulsion Systems
Combustion
Detonation
Liquid propulsion systems
Gaseous Propellant Detonation
Liquid Propellant Detonation
Gaseous propulsion systems
Gelled propulsion systems
Hybrid propulsion systems
Solid propulsion systems

## Slide 11: Which Chemical Propulsion Systems exist?
Objective: To develop the basics of chemical propulsion
Chemical Propulsion Systems
  Gaseous propulsion systems
  Liquid propulsion systems
  Gelled propulsion systems
  Solid propulsion systems
  Hybrid (liquid / solid) propulsion systems
Space Propulsion ENG-510
L4 – Propulsion Systems
Propellant Phase in Tanks
Solid
Liquid
Gas
Chemical Reaction
No
Decomp
Combustion
Hydrazine (N2H4) HTP (H2O2) ADN
Monopropellant Thruster
LOx / LH2 – LOx / LCH4 – MON / MMH – HTP / Ethanol
HTP / IPA
Bipropellant Thruster
GOx / GCH4
Double base or composite
Bi-prop Thruster
Solid / Liquid
Hybrid Thruster Bi-prop
Gelled
Liquid Thruster

## Slide 12: Which Chemical Propulsion Systems exist?
Space Propulsion ENG-510
L4 – Propulsion Systems
Chemical Propulsion Systems
Combustion
Detonation
Liquid propulsion systems
Rotation Detonation Engine
Pulse Detonation Engine
Gaseous propulsion systems
Gelled propulsion systems
Hybrid propulsion systems
Solid propulsion systems

## Slide 13: Which Chemical Propulsion Systems exist?
Space Propulsion ENG-510
L4 – Propulsion Systems
Chemical Propulsion Systems
Combustion
Detonation
Liquid propulsion systems
Rotation Detonation Engine
Pulse Detonation Engine
Mono-propellant
Bi-propellant
Tri-propellant

## Slide 14: Which Chemical Propulsion Systems exist?
Space Propulsion ENG-510
L4 – Propulsion Systems
Chemical Propulsion Systems
Combustion
Detonation
Liquid propulsion systems
Rotation Detonation Engine
Pulse Detonation Engine
Mono-propellant
Bi-propellant
Tri-propellant

## Slide 15: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of liquid combustion mono-propellant propulsion
Liquid propulsion systems
  Monopropellant, bi-propellant or tri-propellant
  Storable or cryogenic propellants
  Toxic or non-toxic (hazardous or green) propellants
  Hypergolic or non-hypergolic propellants
  Pressure-fed (self-pressurization, blow-down or regulated) or pump-fed propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 16: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid mono-propellant propulsion
Liquid propulsion systems
  kit
Space Propulsion ENG-510
L4 – Propulsion Systems
Propellant Phase in Tanks
Solid
Liquid
Gas
Chemical Reaction
No
Decomp
Combustion
Hydrazine (N2H4) / HTP (H2O2) / ADN / HAN / LMP
Monopropellant Thruster
HAN..Hydroxyl Ammonium Nitrate
ADN…Ammonium Di-Nitramide
LMP-103S…ADN + Methanol + Water + Ammonia

## Slide 17: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid mono-propellant propulsion
Liquid propulsion systems
  kit
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 18: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Architecture for liquid mono-propellant decomposition propulsion systems:
Space Propulsion ENG-510
L4 – Propulsion Systems
Tank
Valve
Exhaust
Regulator
Pressurant
Tank
Catalysator
R

## Slide 19: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: Pressure-regulated
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 20: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: Blow-down
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 21: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Mono-propellant propulsion systems (including redundancy)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 22: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Mono-propellant propulsion System
Space Propulsion ENG-510
L4 – Propulsion Systems
Bi-prop
Mono-prop

## Slide 23: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Mono-propellant propulsion System
Space Propulsion ENG-510
L4 – Propulsion Systems
Pressurization (blow-down)
Fuel
Oxidizer

## Slide 24: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Characteristics of a mono-propellant propulsion system
  Relatively simple, robust, cheap
  Toxic propellant (Hydrazine is very often used) but also more and more ‘green’
  Catalysator is needed for decomposition
  Blow-down mode is very often used (ratio of 4 to 1)
  Pressure range between 5.5 bar to 24.6 bar
  Isp is between 210 to 230 s (Exhaust velocity of 2.0 km / s to 2.3 km / s)
  Thrust between 1 N to 1 kN
  Modular set-up is possible using COTS (cost optimization)
  Temperature and heat exchange must be controlled
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 25: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Mono-propellant propulsion system thruster design
Space Propulsion ENG-510
L4 – Propulsion Systems
25

## Slide 26: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Mono-propellant propulsion System
Space Propulsion ENG-510
L4 – Propulsion Systems
26
Injection Tube
Throat
Thermal
Barrier
Catalyst
Heater
Valve
(not shown)
Injection Head
Decomposition
Chamber with
Catalyst

## Slide 27: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Mono propellant propulsion system
Space Propulsion ENG-510
L4 – Propulsion Systems
Canted Thruster
Scarved Thruster

## Slide 28: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Thruster design:
  Catalyst bed must be heated prior to firing
    Typically takes 45 minutes to reach temperature of ~ 250 °C
  Thruster can be fired cold (< 10 °C) however the degradation increases
    Typically a thruster will have been qualified to 10 to 15 cold starts as part of the life test (safe mode recovery)
    The thruster can also be started between 10 and 250 °C (pre-heat start) but number of starts will also be limited (~ 1000 starts)
    Once the thruster has performed one cold start, the temperature will be in the pre-heat range from the thrust reaction
  Catalyst is made from Alumina granules, with Iridium coating
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 29: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Thruster design:
  Catalyst is made from Alumina granules, with Iridium coating
  Catalyst bed is susceptible to:
    Catalyst poisoning –amines and silicates particularly
    High gas flow will damage the catalyst bed
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 30: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Functional principal for liquid mono-propellant decomposition propulsion systems:
  Exothermal decomposition of Hydrazine
  Hot gas is accelerated in the Nozzle and ejected
  Typical catalysator are S405 or KC12GA
  Reaction equation: 3N2H4 -> 4NH3 + N2 4NH3 -> 2N2 + 6H2
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 31: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Hydrazine (N2H4) Characteristics
  Hydrazine: colourless hygroscopic liquid, oily, flammable,
  Stable chemical, can be stored for long periods of time without loss of purity
  Boiling point = 113.5 °C, Freezing point = 2 °C
  Density ~ 1008 kg/m³ at 20 °C
  Fumes in air with vapours which are 4 % heavier than air
  Fishy Ammonia-like odour detectable at a mean of 3.7 ppm
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 32: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Hydrazine is a hazardous chemical!
  Air vapour mixture can be highly flammable
  Can cause fire on contact with rust
  Protective clothing and breathing apparatus must be worn
  Can detonate if subjected to physical shock (rapid adiabatic compression e.g. during priming)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 33: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 34: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  HTP – High Test Peroxide (H2O2 – Hydrogen Peroxide concentration > 85 %)
  ADN
  HAN
  LMP-103S
  In principle very similar to Hydrazine [N2H4] but potentially some specific features like decomposition, catalyst composition, heating, …
  Catalyst lifetime…
  Density Isp…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 35: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Energetic ionic liquids
    By definition, an ionic liquid is a salt with a melting point below 100 °C used in the liquid state
    Ionic liquid mono propellants are usually mixtures of an oxidizer salt, a fuel and water
    The most studied oxidizer salts for propellant applications are HNF (Hydraziniumnitroformate), HAN (Hydroxylammoniumnitrates) and ADN (Ammoniumdinitramide)
    Two ADN formulations LMP-103S and FLP-106, have received particular attention in Europe
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 36: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Energetic ionic liquids
    LMP-103S has been selected by the Swedish company ECAPS
    A successful in-space demonstration was achieved on the PRISMA mission, using 1 N thrusters and the monopropellant LMP-103S
    Since then the HPGP technology based on LMP-103S now provides a low-hazardous and flight-proven, performance enhancer for small and secondary satellites
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 37: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Energetic ionic liquids
    An important HAN formulation is the monopropellant AF- M315E respectively ASCENT (Advanced Spacecraft Energetic Non-Toxic Propellant)
    The ASCENT propellant is used on the NASA cube sat mission which failed to go into orbit around the moon earlier 2023 when debris blocked propellant lines for the spacecraft’s thrusters
    Otherwise it could be stated that the propellant has performed a successful in-orbit demonstration as it is suspected that foreign object debris somewhere in the propulsion system caused the thruster problems
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 38: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Nitrous oxide
    Another promising class of Green Propellants are the so called nitrous oxide fuel blends
    Those fuel blends consist of nitrous oxide mixed with different hydrocarbons (e.g. C2H2, C2H4, or C2H6)
    To obtain the propellant, the single components are pressurized, cooled (down to about 220K) and mixed
    Characteristic for the blends are the high vapor pressures, which could enable self-pressurization of the whole propulsion system
    One the one hand the high reactivity of the mixture offers the opportunity of a simple ignition system (e.g. a spark plug)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 39: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Nitrous oxide
    On the other hand, the whole propulsion system needs a proper flashback arrestor to avoid flame propagation into the tank during all possible operation modes
    Another challenging aspect is the high combustion temperature of those premixed propellants
    A reliable cooling system must be established to handle combustion temperatures up to 3500 K
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 40: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Nitrous oxide
    A significant advantage of the nitrous oxide fuel blends is their high Isp
    Depending on the mixture composition, an increase of 100 s compared to hydrazine is possible
    Furthermore only minor health hazards arise, dealing with those propellant mixtures
    So cheaper and easier handling seems to be possible
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 41: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Nitrous oxide
    But…
    Three people have been killed and numerous persons injured by a prior explosion involving (nitrous oxide) in the motor design of Virgin Galactic space ship
    A report by the California Division of Occupational Safety and Health said the 2007 blast occurred three seconds after the start of a cold-flow test of nitrous oxide
    The engine was not firing during the test at the Mojave Air and Space Port
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 42: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Hydrogen Peroxide
    Hydrogen peroxide is a third group of green propellants currently under investigation
    Typically the concentration for H2O2 used as a rocket propellant is in between 80 to 90 %
    Those concentrations are needed to achieve an Isp of about 150 s as a mono-propellant, which is quite low compared to hydrazine
    Characteristic for hydrogen peroxide is its decomposition to O2 and H2O with time
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 43: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Hydrogen Peroxide
    Due to its reactivity, compatible materials have to be selected carefully
    Advantages of H2O2 are its benign effect on environment and the low health hazards
    Furthermore a catalytic decomposition is possible and the combustion temperature is significant lower than that of other green propellant candidates
    The explosive hazards coming along with the use of hydrogen peroxide need to be more thoroughly investigated
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 44: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 45: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: Benchmark Space Systems Ocelot thruster using HTP
  HTP (High Test Peroxide with concentration of more than 85 % H2O2) provides interesting performance
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 46: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: TU Delft thruster using HTP
  HTP (High Test Peroxide) could also be ignited by thermal decomposition and not only exothermic decomposition (e.g. thermal wire)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 47: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: TU Delft thruster using HTP
  HTP (High Test Peroxide) could also be ignited by thermal decomposition and not only exothermic decomposition (e.g. thermal wire)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 48: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: Benchmark Space Systems Ocelot thruster using HTP
  But HTP decomposes over time…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 49: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: Benchmark Space Systems Ocelot thruster using HTP
  But HTP decomposes over time…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 50: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Example: Benchmark Space Systems Ocelot thruster using HTP
  HTP was used a lot at the beginning of the space race
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 51: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
A
  B
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 52: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Green Hydrazine
    Blend of Hydrazine with other liquids to 100- to 1000-fold reduced vapor pressure compared to neat hydrazine
    Such propellants present a previously-unexplored path to realize the same benefits offered by current high-TRL green ionic liquid propellants while preserving the favorably low operating temperatures and preheat power requirements of heritage monopropellant technologies
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 53: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
‘Greener’ propellant…
  Green Hydrazine
    Specifically, green hydrazine-based propellants:
      Can be fired in conventional, low-cost nickel-based super-alloy thrusters
      Deliver specific impulse equal to hydrazine and 25-35% greater density-specific impulse
      Do not require higher catalyst bed preheat temperatures than hydrazine
      Remain liquid below -50ºC, potentially obviating the need for feed system heating
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 54: Which Liquid Mono-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical liquid combustion mono-propellant propulsion
Summary
  Monopropellant liquid propulsion systems provide interesting performance for small spacecraft and limited Δv need
  Monopropellant systems are getting once again popular by the use of greener propellant
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 55: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid propulsion systems
  Monopropellant, bi-propellant or tri-propellant
  Storable or cryogenic propellants
  Toxic or non-toxic (hazardous or green) propellants
  Hypergolic or non-hypergolic propellants
  Pressure-fed (self-pressurization, blow-down or regulated) or pump-fed propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 56: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
A little bit of history…
  The idea of liquid rocket as understood in the modern context first appears in the book The Exploration of Cosmic Space by Means of Reaction Devices, by the Russian school teacher Konstantin Tsiolkovsky
  This seminal treatise on astronautics was published in May 1903, but was not distributed outside Russia until years later, and Russian scientists paid little attention to it
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 57: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
A little bit of history…continued
  Pedro Paulet wrote a letter to El Comercio in Lima in 1927, claiming he had experimented with a liquid rocket engine while he was a student in Paris three decades earlier
  Historians of early rocketry experiments, among them Max Valier, Willy Ley and John D. Clark, have given differing amounts of credence to Paulet's report
  Valier applauded Paulet's liquid-propelled rocket design in the Verein für Raumschiffahrt Die Rakete, saying the engine had "amazing power" and that his plans were necessary for future rocket development
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 58: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
A little bit of history…continued
  Wernher von Braun would later describe Paulet as "the pioneer of the liquid fuel propulsion motor" and stated that "Paulet helped man reach the Moon "
  The first flight of a liquid-propellant rocket took place on March 16, 1926 at Auburn, Massachusetts, when American professor Dr. Robert H. Goddard launched a vehicle using liquid oxygen and gasoline as propellants
  The rocket rose just 41 feet during a 2.5-second flight that ended in a cabbage field, but it was an important demonstration that rockets utilizing liquid propulsion were possible
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 59: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
A
  B
Space Propulsion ENG-510
L4 – Propulsion Systems
Propellant Phase in Tanks
Solid
Liquid
Gas
Chemical Reaction
No
Decomp
Combustion
LOx / LH2 – LOx / LCH4 – MON / MMH – HTP / Ethanol
HTP / IPA
Bipropellant Thruster

## Slide 60: Which Liquid Bi-propellant Propulsion Systems exist?
Space Propulsion ENG-510
L4 – Propulsion Systems
Pressurization System
Storable or cryogenic
Toxic or non-toxic
Hypergol or not
Cooling concept?
Pressure-fed or pump-fed

## Slide 61: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems
Tank
Valve
Exhaust
Regulator
Pressurant
Tank
Combustion
Valve
Regulator
Pressurant
Tank
R
R
PDE
Propulsion Drive Electronics

## Slide 62: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Characteristics (advantages) of a Bi-propellant Propulsion System
  Highest achievable specific impulse for chemical rocket propulsion
  Controllability (on / off control, restart ability, throttable, pulse mode firing which results in important engine parameter for reaction control thruster – minimum impulse bit)
  Easy adaptation to launcher or S/C architecture
  Possibility of realistic ground testing and pre-launch check-out
  Enable component redundancy to virtually any level
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 63: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Example: Orion-ESM Propulsion System
  Human-rated
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 64: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Example: A5 Upper Stage EPS Propulsion System
  Commercial launch vehicle
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 65: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Architecture for Liquid Bi-propellant Combustion Propulsion Systems :
  Liquid propellant must be stored in separate tanks (e.g. cylindrical tanks, spherical tanks, torus tanks, spherical + conical tanks, …)
  It allows to operate all Equipment below the regulator at lower pressure and therefore has lower strength requirements
  It allows to operate the thruster at constant inlet pressure until the storage tank pressure drops below the regulator pressure and therefore ensures consistent level of thrust
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 66: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 67: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Characteristics (disadvantages) of a Bi-propellant Propulsion System
  Lower density than solid propellants
  Higher parts count than other chemical systems
  High complexity
  Concerns on leakage
  Concerns on combustion stability
  Difficult to control flow
  Need mixture ratio control
  Need special design for zero-g ignition
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 68: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Characteristics (advantages) of a Bi-propellant Propulsion System
  Highest achievable specific impulse for chemical rocket propulsion
  Controllability (on / off control, restart ability, throttable, pulse mode firing which results in important engine parameter for reaction control thruster – minimum impulse bit)
  Easy adaptation to launcher or S/C architecture
  Possibility of realistic ground testing and pre-launch check-out
  Enable component redundancy to virtually any level
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 69: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Additional classification of liquid bi-prop systems:
  Cryogenic or storable propellants (higher performance but also need for thermal insulation)
  Hypergolic or non-hypergolic (dedicated ignitor needed versus risk of hard start)
  Toxic or non-toxic (similar to mono-propellant…)
  Pressure-fed or pump-fed (pressure-fed similar to mono-prop versus higher performance by pump-fed)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 70: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 71: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Toxic or non-toxic (similar to mono-propellant…)
  Conventional Bipropellant are:
    Fuel: Monomethyl Hydrazine MMH
    Oxidiser: (Di)Nitrogen Tetroxide NTO
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 72: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Toxic or non-toxic (similar to mono-propellant…)
  Mono-methyl Hydrazine, MMH (CH3NHNH2) Characteristics:
    Mono methyl hydrazine is a clear, water-white, hydroscopic, toxic
    Stable chemical, can be stored for long periods of time
    MMH is not sensitive to shock or friction and is more stable than hydrazine under conditions of mild heating
    MMH is very reactive and will undergo a wide variety of reactions with both organic and inorganic compounds.
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 73: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Toxic or non-toxic (similar to mono-propellant…)
  Nitrogen Tetroxide (N2O4) Characteristics:
    Nitrogen tetroxide, also known as dinitrogen tetroxide, is a red/brown liquid
    Highly reactive, very toxic oxidiser which is thermally stable and insensitive to mechanical shock and impact
    Non-flammable but will support combustion and react hypergolically with high energy fuels
    Boiling point = 21°C at atmospheric pressure
    Freezing point = -13 °C (MON-3)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 74: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Toxic or non-toxic (similar to mono-propellant…)
  Nitrogen Tetroxide (N2O4) Characteristics:
    Density ~ 1.44 kg / litre at 20 °C (MON-3)
    Irritating, unpleasant odour, similar to bad eggs
    Nitrogen Tetroxide is a hazardous chemical!
    Air / vapour mixtures can be flammable
    Will not burn by itself, but will support combustion of other chemicals
    Protective clothing and breathing apparatus must be worn whilst handling
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 75: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Toxic or non-toxic (similar to mono-propellant…)
  Mixed Oxides of Nitrogen, MON (today in propulsion applications, Nitrogen Tetroxide is mixed with Nitric Oxide gas, NO) (not to be confused with Nitrous Oxide or Nitric Acid)
  When NO is in solution the resultant chemical mixture is called Mixed Oxides of Nitrogen or MON
    Written as MON-i, where i indicates the percentage NO (volume)
    1 % NO content = MON-1 –most used with UDMH fuel
    3 % NO content = MON-3 –most used with N2H4 and MMH
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 76: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Toxic or non-toxic (similar to mono-propellant…)
  NO addition slightly decreases oxidation potential, and makes it more expensive
  Corrosiveness is decreased however, particularly in contact with titanium alloys
  Addition of NO turns the NTO from red / brown to clear green!
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 77: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Architecture for Liquid Bi-propellant Combustion Propulsion Systems:
  Propellant feeding cold be performed as pressure-fed or pump-fed system
  Pressure-fed is either self-pressurized or with inert gas support
  Pressure-fed with inert gas could be either in blow-down modus or pressure-regulated
  Pump-fed could be performed with turbopump or e-pump
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 78: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure-fed system is feeding liquid propellant to the Combustion Chamber by large pressure difference (>> 20 bar in propellant tank versus vacuum in combustion chamber)
  Blow-down system
  High pressure (gaseous) storage system in pressurant vessels
  Low pressure (solid powder) storage on ground ignited in orbit
  Self-pressurization
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 79: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure-fed cycle
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 80: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure-fed system
  The pressure-fed engine / propulsion system is a class of rocket engine designs
  A separate gas supply, usually Helium or Nitrogen pressurizes the propellant tanks to force fuel and oxidizer to the combustion chamber
  To maintain adequate flow, the tank pressures must exceed the combustion chamber pressure
  Pressure fed engines have simple plumbing and have no need for complex and occasionally unreliable turbopumps
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 81: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure-fed system
  A typical startup procedure begins with opening a valve, often a one-shot pyrotechnic device, to allow the pressurizing gas to flow through check valves into the propellant tanks
  Then the propellant valves in the engine itself are opened
  If the fuel and oxidizer are hypergolic, they burn on contact; non-hypergolic fuels require an igniter
  Multiple burns can be conducted by merely opening and closing the propellant valves as needed, if the pressurization system also has activating valves
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 82: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure-fed system
  They can be operated electrically, or by gas pressure controlled by smaller electrically operated valves.
  Care must be taken, especially during long burns, to avoid excessive cooling of the pressurizing gas due to adiabatic expansion
  Cold gas could freeze a propellant, decrease tank pressures or damage components not designed for low temperatures
  Pressure-fed engines have practical limits on propellant pressure, which in turn limits combustion chamber pressure
  High pressure propellant tanks require thicker walls leading to higher mass
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 83: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Blow-down pressure-fed system
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 84: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Self-pressurized pressure-fed system
  Self-pressurized pressure-fed system leads to higher propellant tank structural mass
  But not dedicated pressurization system is needed
  Vaporization need limits use for long duration burns
  Example: Gate Space with NOx / Ethane
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 85: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Self-pressurized pressure-fed system
  Hydrogen Peroxide / Fuel (Octane, Ethanol, …)
    Effect of self decomposition
    Compatibility aspects
  Nitrous Oxide / Ethane
    Self-pressurization
    High tank pressure, tank mass
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 86: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure regulated pressure-fed system
  Pressure-fed regulated system requiring pressure regulator (Reducing the input pressure of a fluid by passive mechanism)
  Pressure-fed regulated system results in constant propellant tank pressure = constant flow rate = constant reaction = constant thrust
  Only gas tank needs high-pressure
  But chamber pressure < O/F tank pressure ≪ gas tank pressure
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 87: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure regulated pressure-fed system
  Mechanical pressure regulator
    The mechanical pressure regulator controls the flow of gas into the propellant tanks
    The PR will convert a range of high pressures into a constant low pressure (within limits)
    The pressure regulator will work automatically based on the inlet pressure
    Most types are series redundant (if the primary valve fails, the outlet pressure will rise until the secondary seat takes over)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 88: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure regulated pressure-fed system
  Mechanical pressure regulator
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 89: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure regulated pressure-fed system
  Electro-mechanical pressure regulator
  Bang-bang regulation with solenoid valves
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 90: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure regulated pressure-fed system
  Electro-mechanical pressure regulator
  Bang-bang regulation with solenoid valves
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 91: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure regulated pressure-fed system
  Ball valve…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 92: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed system:
  Pump-fed system is feeding high pressure to the Combustion Chamber resulting in low tank pressure = light weight tank
  Today turbo-pumps are mainly used but also more and more electro-pumps are considered
  Turbo-pumps are technically very difficult equipment
  Electro-pumps require lot of power (i.e. batteries, mass, …)
  Note: Cryogenic propellant require a very low tank pressure
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 93: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Turbo-pumps architecture
  Gas generator cycle
  Combustion tap-off cycle
  Expander-bleed cycle (single or dual expander cycle)
  Full expander cycle
  Staged combustion cycle (fuel-rich, Ox-rich, full flow)
Electro-pumps architecture
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 94: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Turbo-pumps architecture
Space Propulsion ENG-510
L4 – Propulsion Systems
Engine Cycle | Open Cycle (Dump Gas) | Closed Loop (Re-use Gas)
Burner | Gas Generator Combustion Tap-off | Staged Combustion
Regenerative cooling | Expander-bleed | Full expander

## Slide 95: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems
Gas Generator Cycle
Gas-generator rocket cycle - Some of the fuel and oxidizer is burned separately to power the pumps and then discarded
Most gas-generator engines use the fuel for nozzle cooling
Burner dedicated for the turbine

## Slide 96: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed gas-generator cycle:
  The gas-generator cycle is a power cycle of a pumped liquid bi-propellant engine
  Part of the unburned propellant is burned in a gas generator (or pre-burner) and the resulting hot gas is used to power the propellant pumps before being exhausted overboard and lost
  Because of this loss, this type of engine is termed open cycle
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 97: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems
Combustion Tap-off Cycle
Combustion tap-off cycle - Diagram of the open-cycle combustion tap-off rocket cycle
A small portion of exhaust from the combustion chamber is tapped off to power the turbine(s)

## Slide 98: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed combustion tap-off cycle:
  The combustion tap-off cycle is a power cycle of a bi-propellant engine
  The cycle takes a small portion of hot exhaust gas from the combustion chamber and routes it through the turbo-pump turbines to pump fuel before being exhausted (similar to the gas generator cycle)
  Since fuel is exhausted, the tap-off cycle is considered an open-cycle engine. The cycle is comparable to a gas-generator cycle engine with turbines driven by main combustion chamber exhaust rather than a separate gas generator or pre-burner
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 99: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed combustion tap-off cycle:
  Example: Blue Origin BE-3 engine
  The cycle is simple with only one combustion chamber and a less stressful engine shutdown process
  However, engine startup is more complicated and due to the hot gas fed from the main combustion chamber into the turbopumps, the turbine must be built to withstand higher-than-normal temperatures
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 100: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems
Expander-bleed Cycle - Expander open cycle
(Also named coolant tap-off)
Bleed a part of expanded (coolant) gas
Expander-bleed Cycle

## Slide 101: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed expander-bleed cycle:
  The expander-bleed cycle is a modification of the traditional expander cycle
  In the bleed (or open) cycle, instead of routing all of the heated propellant through the turbine and sending it back to be combusted, only a small portion of the heated propellant is used to drive the turbine and is then vented overboard without going through the combustion chamber
  The other portion is injected into the combustion chamber
  Bleeding off the turbine exhaust allows for a higher turbopump efficiency by decreasing back-pressure and maximizing the pressure drop through the turbine
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 102: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed expander-bleed cycle:
  Compared with a standard expander cycle, this allows higher engine thrust at the cost of efficiency by dumping the turbine exhaust
  Example: Mitsubishi LE-5A engine was the world's first expander bleed cycle engine to be put into operational service
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 103: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed dual expander cycle:
  In a similar way that the staged combustion cycle can be implemented separately on the oxidizer and fuel on the full flow cycle, the expander cycle can be implemented on two separate paths as the dual expander cycle
  The use of hot gases of the same chemistry as the liquid for the turbine and pump side of the turbopumps eliminates the need for purges and some failure modes
  Additionally, when the density of the fuel and oxidizer is significantly different, as it is in the LH2 / LOx case, the optimal turbopump speeds differ so much that they need a gearbox between the fuel and oxidizer pumps
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 104: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed dual expander cycle:
  The use of dual expander cycle, with separate turbines, eliminates this failure-prone piece of equipment (i.e. gear box)
  Dual expander cycle can be implemented by either using separated sections on the regenerative cooling system for the fuel and the oxidizer, or by using a single fluid for cooling and a heat exchanger to boil the second fluid
  In the first case, for example, you could use the fuel to cool the combustion chamber, and the oxidizer to cool the nozzle extension
  In the second case, you could use the fuel to cool the whole engine and a heat exchanger to boil the oxidizer
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 105: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems
Full Expander Cycle
Expander rocket engine (closed cycle) - Heat from the nozzle and combustion chamber powers the fuel and oxidizer pump
Use of expanded (coolant) gas

## Slide 106: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed full expander cycle:
  The full expander cycle is a power cycle of a bi-propellant engine
  In this cycle, the fuel is used to cool the engine's combustion chamber, picking up heat and changing phase
  The now heated and gaseous fuel then powers the turbine that drives the engine's fuel and oxidizer pumps before being injected into the combustion chamber and burned
  Because of the necessary phase change, the expander cycle is thrust limited by the square-cube law
  When a bell-shaped nozzle is scaled, the nozzle surface area with which to heat the fuel increases as the square of the radius, but the volume of fuel to be heated increases as the cube of the radius
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 107: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed full expander cycle:
  So, beyond approximately 300 kN of thrust, there is no longer enough nozzle area to heat enough fuel to drive the turbines and hence the fuel pumps
  Higher thrust levels can be achieved using a bypass expander cycle where a portion of the fuel bypasses the turbine and or thrust chamber cooling passages and goes directly to the main chamber injector
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 108: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed full expander cycle:
  All expander cycle engines need to use cryogenic propellant such as liquid Hydrogen, liquid Methane or liquid Propane that easily reaches its boiling point
  Some expander cycle engines may use a gas generator of some kind to start the turbine and run the engine until the heat input from the thrust chamber and nozzle skirt increases as the chamber pressure builds up
  An example of an expander cycle engine is the Vinci engine for the Ariane 6 launch vehicle
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 109: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems
Pre-burner system with 2 chambers
Staged Combustion Cycle – Fuel Rich

## Slide 110: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed staged combustion cycle:
  The staged combustion cycle (sometimes known as topping cycle, pre-burner cycle, or closed cycle) is a power cycle of a bi-propellant engine
  In the staged combustion cycle, propellant flows through multiple combustion chambers and is thus combusted in stages
  The main advantage relative to other rocket engine power cycles is the high fuel efficiency measured through the specific impulse, while its main disadvantage is its complexity
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 111: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed staged combustion cycle:
  Typically, propellant flows through two kinds of combustion chambers: the first called pre-burner and the second called main combustion chamber
  In the pre-burner, a small portion of propellant, usually fuel-rich, is partly combusted, and the increasing volume flow is used to drive the turbo-pumps that feed the engine with propellant
  The gas impulse, is then injected into the main combustion chamber and combusted completely with the other propellant to produce thrust
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 112: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed staged combustion cycle:
  The main advantage is fuel efficiency due to all of the propellant flowing to the main combustion chamber, which also allows for higher thrust
  The staged combustion cycle is sometimes referred to as closed cycle, as opposed to the gas generator cycle or open cycle where a portion of propellant never reaches the main combustion chamber, here the full flow passes the main combustion chamber
  The disadvantage is its complexity, partly a result of the pre-burner exhaust of hot and highly pressurized gas which, particularly when oxidizer-rich, produces extremely harsh conditions for turbines and plumbing
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 113: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed staged combustion cycle:
  Several variants of the staged combustion cycle exist
  Pre-burners that burn a small portion of oxidizer with a full flow of fuel are called fuel-rich, while pre-burners that burn a small portion of fuel with a full flow of oxidizer are called oxidizer-rich
  When both oxidizer-rich and fuel-rich pre-burners are used on a single engine, the cycle is called full-flow staged combustion.
  Staged combustion designs can be either single-shaft or twin-shaft.
  In the single-shaft design, one set of pre-burner and turbine drives both propellant turbo-pumps
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 114: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed staged combustion cycle:
  In the twin-shaft design, the two propellant turbopumps are driven by separate turbines, which are in turn driven by the outflow of either one or separate pre-burners
  Relative to a single-shaft design, the twin-shaft design requires an additional turbine (and possibly another pre-burner) but allows for individual control of the two turbo-pumps
  In addition to the propellant turbopumps, staged combustion engines often require smaller boost pumps to prevent both pre-burner back-flow and turbo-pump cavitation
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 115: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems
Pre-burner system with 2 chambers
Stage Combustion Cycle – Full Flow

## Slide 116: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed full flow staged combustion cycle:
  Full-flow staged combustion (FFSC) is a twin-shaft staged combustion cycle that uses both oxidizer-rich and fuel-rich pre-burners
  The cycle allows full flow of both propellants through the turbines
  The fuel turbo-pump is driven by the fuel-rich pre-burner, and the oxidizer turbo-pump is driven by the oxidizer-rich pre-burner
  Benefits of the full-flow staged combustion cycle include turbines that run cooler and at lower pressure, due to increased mass flow, leading to a longer engine life and higher reliability
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 117: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed full flow staged combustion cycle:
  Further, the full-flow cycle eliminates the need for an inter-propellant turbine seal normally required to separate oxidizer-rich gas from the fuel turbopump or fuel-rich gas from the oxidizer turbo-pump, thus improving reliability
  Since the use of both fuel and oxidizer pre-burners results in full gasification of each propellant before entering the main combustion chamber, faster chemical reactions are given in the combustion chamber, allowing a smaller combustion chamber
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 118: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pump-fed full flow staged combustion cycle:
  This in turn makes it feasible to increase the chamber pressure, which increases efficiency
  Potential disadvantages of the full-flow staged combustion cycle include increased engineering complexity of two pre-burners, relative to a single-shaft staged combustion cycle, as well as an increased parts count
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 119: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 120: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
But one could also use an electric pump…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 121: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems
Electric-pump Cycle
Electric-feed rocket cycle – The oxidizer and fuel are fed to the pump which increases the pressure before injecting it into the combustion chamber. The pumps are actuated by an electric motor powered by batteries. An inverter converts the batteries' DC electricity to the AC needed by the motor. The fuel is also circulated around the outside of the combustion chamber and nozzle to prevent it from overheating

## Slide 122: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Electric pump-fed system:
  The electric pump-fed engine is a bi-propellant engine cycle in which the fuel pumps are electrically powered, and so all of the input propellant is directly burned in the main combustion chamber, and none is diverted to drive the pumps
  This differs from traditional engine cycles, in which the pumps are driven by a portion of the input propellants.
  An electric cycle engine uses electric pumps to pressurize the propellants from a low-pressure fuel tank to high-pressure combustion chamber level
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 123: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Electric pump-fed system:
  The pumps are powered by an electric motor with electricity from a battery bank
  Example: Rutherford engine from the Electron launch vehicle from Rocketlab
  In comparison to turbo-pumped rocket cycles such, an electric cycle engine has potentially worse performance due to the added mass of the batteries but may have lower development and manufacturing costs due its mechanical simplicity, its lack of high temperature turbomachinery, and its easier controllability
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 124: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Electric pump-fed system:
  Example: Huracan engine from The Exploration Company
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 125: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure Vessels Types (including vessels for pressurant gas storage but also propellant storage)
  Type I – Full metal: Cylinder is made entirely from metal
  Type II – Hoop wrap: Metal cylinder, reinforced by a belt-like hoop wrap with fibre-reinforced resin
  Type III – Fully wrapped, over metal liner: Diagonally wrapped fibres form the load bearing shell on the cylindrical section and at the bottom and shoulder around the metal neck. The metal liner is thin and provides the gas tight barrier
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 126: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure Vessels Types (including vessels for pressurant gas storage but also propellant storage)
  Type IV – Fully wrapped, over non-metal liner: A lightweight thermoplastic liner provides the gas tight barrier, and the mandrel to wrap fibers and resin matrix around. Only the neck which carries the neck thread and its anchor to the liner is made of metal, which may be lightweight Aluminum or sturdy stainless steel
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 127: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure Vessels Types (including vessels for pressurant gas storage but also propellant storage)
  Type V - Compared to Type I, II and III tanks using metal, and Type IV tanks using a plastic liner, Type V pressure vessels offer the lightest weight, featuring a fully composite construction reinforced primarily with carbon fiber but without a liner. However, because the liner serves as a barrier to prevent gases and cryogenic liquids from permeating into the composite laminate at high pressures building liner less tanks that can perform reliably for potentially thousands of pressurization cycles is no easy feature
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 128: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure Vessels Types (including vessels for pressurant gas storage but also propellant storage)
  Polar mounted or equatorial mounted
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 129: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure Vessels Types
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 130: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Pressure Vessels Considerations
  Propellant / pressurant leakage
  Leak before burst - Leak before burst describes a pressure vessel designed such that a crack in the vessel will grow through the wall, allowing the contained fluid to escape and reducing the pressure, prior to growing so large as to cause fracture at the operating pressure
  Liquid propellant control
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 131: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Positive Expulsion Device – Bladder, Diaphragm (metallic or plastic)
  Surface Tension Device – Capillary forces
  Piston Device – Pressure force
  Pre-acceleration + Collector – Acceleration forces
  Damping – Baffles
  Zero-sloshing Tank – De-orbitation for small spacecraft
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 132: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control:
    Example: Stage separation
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 133: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control:
    Example: Stage separation
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 134: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Positive Expulsion Device – Plastic diaphragm
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 135: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Positive Expulsion Device – Metallic diaphragm
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 136: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Positive Expulsion Device – Bladder
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 137: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Surface Tension Device – Capillary forces
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 138: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Piston Device – Pressure force
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 139: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Pre-acceleration + Collector (Sponge) – Acceleration forces
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 140: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
a
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 141: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 142: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Damping (Sloshing, Vortex) – Baffles
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 143: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Liquid Propellant Control
  Zero-sloshing Tank – De-orbitation for small spacecraft
  Potentially Piston…
  Or N2O in supercritical state…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 144: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Functions
  Fill & Drain
  Isolation
  Regulation
  Flow control
  Throttling
  …
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 145: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Pyro Valves (N/O – normally open – or N/C – normally closed)
  SMA Valves (Shape Memory Alloy)
  Check Valves
  Monostable Valves (Solenoid valves) – Flow Control Valves
  Bistable Valves (Latch valves)
  Pneumatic Valves
  Electric Valves
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 146: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Ball Valves
  Fill & Drain Valves
  Burst Disk + Relief Valve
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 147: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Pyro Valves (N/O – normally open – or N/C – normally closed): Redundancy
    PVs are a one shot deal
    Explosive charges are fired to open the valve (normally closed type) or to close the valve (normally open type
    PVs are used to permanently change the flow paths within the propulsion system
    Better leakage rate than latch or solenoid valves
    Cost effective
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 148: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Pyro Valves (N/O – normally open – or N/C – normally closed): Redundancy
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 149: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  SMA Valves (Shape Memory Alloy): Low shock but duration for temperature increase
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 150: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Check Valves: Never tight + oscillations
    Non return valves prevent the mixing of oxidiser and fuel vapour in the pipes
    No electronic parts
    Valves allow the flow of gas in one direction only
    Valves can exert a high pressure drop in the system (especially when series redundant)
    Good reliability
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 151: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Check Valves: Never tight + oscillations
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 152: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types:
  Monostable Valves (Solenoid valves): Pressure assisted or not + force balance (also in dynamic case) + heating
    Solenoid valve is a monostable valve
    “Normally closed” version will only remain open whilst powered, where after they return to closed position
    “Normally open” versions are also available
    As with the latch valve, they are used to control propellant flow around the system
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 153: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types:
  Monostable Valves (Solenoid valves):
Space Propulsion ENG-510
L4 – Propulsion Systems
In-line SV

## Slide 154: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Bistable Valves (Latch valves): Force balance (also in dynamic case) + power need
    Latch valve is a bistable valve
    The position open/closed is controlled by a short electrical pulse on demand
    Most examples contain an internal position indicator to determine valve position
    The function of the valve is to control propellant (sometimes gas) flow around the propulsion system
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 155: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Bistable Valves (Latch valves): Force balance (also in dynamic case) + power need
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 156: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Test Ports, Fill and Drain Valves or Fill and Vent Valves (FDV, FVV or TP)
    The name determines the function, but all are fundamentally the same valve
    They are used on ground to enable fluids to be put into the system, or to perform tests on ground
    The valves are operated using a counterpart called a ground half coupling
    Often called Mechanical Valves, Service Valves or Flight Half Couplings
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 157: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Test Ports, Fill and Drain Valves or Fill and Vent Valves (FDV, FVV or TP)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 158: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Burst Disk & Relief Valves:
    Pressure relief valve will be set to a pre-determined “cracking pressure”
    If the pressure gets too high within the system the relief valve vents gas to prevent over pressurisation (particularly tanks)
    Burst discs work in the same way, but once opened, they cannot be closed
    They are not particularly desirable as the reliability of the system can be impaired –analytical design solutions are better
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 159: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  Burst Disk & Relief Valves:
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 160: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Valve Types
  And everything can be a little bit smaller…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 161: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Other propulsion equipment
  Transducer (Pressure, Temperature, Flow rate, Position indication, Acceleration)
  Filter (Liquid and Gaseous)
  Heater
  Heat exchanger
  Electrolyzer
  Sabatier Reactor
  Compressor
  …
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 162: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems
Pressure Transducer
He - Filter
Pressure Transducer High Accuracy
Propellant Filter

## Slide 163: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Other propulsion equipment
  Transducer (Pressure, Temperature, Flow rate, Position indication, Acceleration)
    Pressure transducers convert physical pressure into an equivalent electrical signal
    PTs are typically powered continuously through life
    PTs are used to monitor pressure which is used to determine
    Correct function of the system (Propellant gauging calculations, Thruster performance)
    The PTs come in various low and high pressure ranges and are calibrated during supplier testing
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 164: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Other propulsion equipment
  Transducer (Pressure, Temperature, Flow rate, Position indication, Acceleration)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 165: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Other propulsion equipment
  Filter (Liquid and Gaseous)
    Filters are used to filter particulate from gas or propellant to protect downstream components
    The propulsion systems are precision cleaned during assembly, however residual particulate and debris created from pyro valves can damage valves
    Filters will exert a pressure drop at high flow rates, which must be taken into account
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 166: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Other propulsion equipment
  Filter (Liquid and Gaseous)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 167: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
And thruster for sure…
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 168: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thruster definitions:
  Steady State
    Refers to the configuration where the thruster valves are fully open
    Continuous thrust is produced (provided conditions remain stable)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 169: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thruster definitions:
  Pulse Mode
    At the same pressure, a net lower thrust can be produced by cycling the valve producing a series of impulsive pulses for more accurate positioning
    The Impulse bit is the equivalent thrust which can be produced for a given pulse
    Minimum Impulse bit is the smallest possible amount of thrust which can be produced by a thruster for given operating conditions
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 170: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thruster definitions:
  Pulse Mode
    Duty cycle
  Transient Phases
    Thrust rise time
    Thrust decay time
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 171: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant engines
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 172: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Injection method for propellants (e.g. spin, showerhead, …)
  Cooling of engine
  Trimming of engine
  Ignition of propellants
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 173: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Trimming / calibration of engine
      Orifice (passive)
      Throttling valve / injector (active)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 174: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Cooling of engine (Combustion Chamber, Throat, Nozzle Extension)
    Radiative cooling
    Capacitive cooling (Phase change material)
    Film cooling
    Vortex cooling
    Regenerative cooling
    Ablative cooling
    Transpiration cooling
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 175: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Cooling of engine (Combustion Chamber, Throat, Nozzle Extension)
    Film cooling
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 176: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Cooling of engine (Combustion Chamber, Throat, Nozzle Extension)
    Regenerative cooling
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 177: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Cooling of engine (Combustion Chamber, Throat, Nozzle Extension)
    Vortex cooling
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 178: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Cooling of engine (Combustion Chamber, Throat, Nozzle Extension)
    Vortex cooling
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 179: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Injection method for propellants (e.g. spin, showerhead, …)
    Impingement
    Showerhead
    Concentric tube (with or without swirl)
    Splash plate
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 180: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Injection method for propellants (e.g. spin, showerhead, …)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 181: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Ignition of propellants
    Hypergolic ignition
    Catalytic decomposition
    Thermal decomposition
    …
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 182: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Bi-propellant thrusters / engines
  Ignition of propellants
    Spark plug
    Glow plug
    Laser ignitor
    Resonance acoustic ignition
    Thermal wire
    …
    Torch ignitor (Different propellant or same propellants with smaller amount)
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 183: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Dual Mode Propulsion
  Dual Mode systems combine elements of monopropellant and bipropellant systems
  Dual mode propulsion system can have a high thrust bipropellant engine and small precise monopropellant engines
  Or resistojets or arcjets may be used instead of catalytic hydrazine thrusters
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 184: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Dual Mode Propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 185: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Dual Mode Propulsion
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 186: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Dual Mode Propulsion
  Example: Bepi Colombo
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 187: Which Liquid Bi-propellant Propulsion Systems exist?
Objective: To develop the basics of chemical L/L combustion bi-propellant propulsion
Mixed Mode Propulsion
  Mixed Mode propulsion refers to the use of different propellant types with one thruster:
    Cold gas, mono-prop or bi-prop operation of a thruster
    Small flow (igniter flow) or full flow
Space Propulsion ENG-510
L4 – Propulsion Systems

## Slide 188: Back-up
Brief overview on all space propulsion systems