## Slide 1: EPFL Space Center eSpace
Space Propulsion ENG-510

## Slide 2: Lecture # 7 Electrical Propulsion Systems
Brief overview on all space propulsion systems

## Slide 3: Which Electrical Propulsion Systems exist?
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 4: Which Electrical Propulsion Systems exist?
Electrical Propulsion Systems:
Space Propulsion ENG-510
L7 – Propulsion Systems
Space Propulsion
Material Ejection
Non-Material Ejection
Thermal Propulsion Systems
Chemical Propulsion Systems
Electrical Propulsion Systems

## Slide 5
Space Propulsion ENG-510
L7 – Propulsion Systems
Electrical Propulsion Systems
Electrostatic
Electromagnetic
Helicon Thruster
Magnetic Nozzle
Pulsed Plasma Thruster
Electrothermal
Thermal Propulsion Systems
ResistojetThruster
Arcjet Thruster
MPD Thruster

## Slide 6: Which Electrical Propulsion Systems exist?
  Electrical Propulsion Systems:
Basics
  Electrothermal (or part of Thermal Propulsion Systems…)
    Power heats propellant
    Expansion through a nozzle (same as for a chemical thruster)
  Electrostatic
    Propellant is ionized
    Accelerated using electrostatic fields
  Electromagnetic
    Propellant is ionized
    Accelerated by interaction of discharge current with magnetic field (JxB Lorentz force)
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 7: Which Electrical Propulsion Systems exist?
  Electric Propulsion Systems:
B
  C
    D
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 8
Space Propulsion ENG-510
L7 – Propulsion Systems
Electrical Propulsion Systems
Electrostatic
Electromagnetic
Helicon Thruster
Magnetic Nozzle
Pulsed Plasma Thruster
Electrothermal
Thermal Propulsion Systems
ResistojetThruster
Arcjet Thruster
MPD Thruster

## Slide 9: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetoplasmadynamic Thruster
  MPD thrusters are electromagnetic devices that use a very high current arc to ionize a significant fraction of the propellant and then electromagnetic forces (Lorentz J x B forces) in the plasma discharge to accelerate the charged propellant
  Since both the current and the magnetic field are usually generated by the plasma discharge, MPD thrusters tend to operate at very high powers in order to generate sufficient force for high specific impulse operation and thereby also generate high thrust compared to the other EP systems
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 10: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetoplasmadynamic Thruster
  There are two main types of MPD thrusters, applied-field and self-field
  Applied-field thrusters have magnetic rings surrounding the exhaust chamber to produce the magnetic field, while self-field thrusters have a cathode extending through the middle of the chamber
  Applied fields are necessary at lower power levels, where self-field configurations are too weak
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 11: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetoplasmadynamic Thruster
  In theory, MPD thrusters could produce extremely high specific impulses (Isp) with an exhaust velocity of up to and beyond 110000 m/s, triple the value of current xenon-based ion thrusters, and about 25 times better than liquid rockets
  MPD technology also has the potential for thrust levels of up to 200 newtons (N), by far the highest for any form of electric propulsion
  MPD thruster technology has been explored academically
  One important problem is that power requirements on the order of hundreds of kilowatts are required for optimum performance
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 12: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetoplasmadynamic Thruster
  Application: only a pulsed demonstration up to now
  Working fluid: plasma
  Working fluid generation: arc discharge
  Acceleration: electromagnetic, 100 V
  Exhaust velocity (typical): ~ 110 km/s
  Power (typical): > 100 kW
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 13: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetoplasmadynamic Thruster
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 14
Space Propulsion ENG-510
L7 – Propulsion Systems
Electrical Propulsion Systems
Electrostatic
Electromagnetic
Helicon Thruster
Magnetic Nozzle
Pulsed Plasma Thruster
Electrothermal
Thermal Propulsion Systems
ResistojetThruster
Arcjet Thruster
MPD Thruster

## Slide 15: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Pulsed Plasma Thruster
  A PPT is an electromagnetic thruster that utilizes a pulsed discharge to ionize a fraction of a solid propellant ablated into a plasma arc and electromagnetic effects in the pulse to accelerate the ions to high exit velocity
  The pulse repetition rate is used to determine the thrust level
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 16: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Pulsed Plasma Thruster
  Application: several demonstrations also in orbit (e.g. PETRUS from TU Stuttgart)
  Working fluid: plasma
  Working fluid generation: pulsed arc discharge
  Acceleration: electromagnetic / electrothermal, 1-3 kV
  Exhaust velocity (typical): 5-20 km/s
  Power (typical): 10 W
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 17: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Pulsed Plasma Thruster
  PTs are very robust due to their inherently simple design (relative to other electric spacecraft propulsion techniques)
  PPTs benefit from reduced fuel consumption compared to traditional chemical rockets as well as high specific impulse improving performance
  But, due to energy losses caused by late time ablation and rapid conductive heat transfer from the propellant to the rest of the spacecraft, propulsive efficiency (kinetic energy of exhaust / total energy used) is very low compared to other forms of electric propulsion, at around just 10%
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 18: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Pulsed Plasma Thruster
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 19
Space Propulsion ENG-510
L7 – Propulsion Systems
Electrical Propulsion Systems
Electrostatic
Electromagnetic
Helicon Thruster
Magnetic Nozzle
Pulsed Plasma Thruster
Electrothermal
Thermal Propulsion Systems
ResistojetThruster
Arcjet Thruster
MPD Thruster

## Slide 20: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Helicon Thruster
  Wait for special lecture…
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 21
Space Propulsion ENG-510
L7 – Propulsion Systems
Electrical Propulsion Systems
Electrostatic
Electromagnetic
Helicon Thruster
Magnetic Nozzle
Pulsed Plasma Thruster
Electrothermal
Thermal Propulsion Systems
ResistojetThruster
Arcjet Thruster
MPD Thruster

## Slide 22: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetic Nozzle Thruster
  A magnetic nozzle is a convergent-divergent magnetic field that guides, expands and accelerates a plasma jet into vacuum
  The magnetic field in a magnetic nozzle plays a similar role to the convergent-divergent solid walls in a Laval nozzle, wherein a hot neutral gas is expanded first sub sonically and then supersonically to increase the thrust
  A magnetic nozzle converts the internal energy of the plasma into directed kinetic energy due to interaction of the applied magnetic field with the electric charges
  The main advantage of a magnetic nozzle over a solid one is that it can operate contactless, i.e. avoiding the material contact with the hot plasma
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 23: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetic Nozzle Thruster
  Additional advantages include the capability of modifying the strength and geometry of the applied magnetic field in-flight, allowing the nozzle to adapt to different propulsive requirements and space missions
  Magnetic nozzles are the fundamental acceleration stage of several next-generation plasma thrusters like the Helicon plasma thruster, the VASIMR Variable Specific Impulse Magnetoplasma Rocket and the applied-field magnetoplasma-dynamic thruster
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 24: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetic Nozzle Thruster
  The performance of a magnetic nozzle, in terms of its specific impulse, generated thrust and overall efficiency depends on the plasma thruster to which it is connected
  The magnetic nozzle should be regarded as a thrust augmentation device, whose role is to convert plasma thermal energy into directed kinetic energy
  Therefore, thrust and specific impulse are strongly dependent on the electron temperature of the plasma inside the plasma source
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 25: Which Electrical Propulsion Systems exist?
  Electromagnetic Propulsion Systems:
  Magnetic Nozzle Thruster
Space Propulsion ENG-510
L7 – Propulsion Systems

## Slide 26: Non-material Ejection Propulsion Systems
Brief overview on non-material ejection space propulsion systems

## Slide 27: Which Non-material Ejection Propulsion Systems exist?
Non-material Ejection Propulsion Systems:
Space Propulsion ENG-510
L7 – Non-material Ejection
Space Propulsion
Material Ejection
Non-Material Ejection
Thermal Propulsion Systems
Chemical Propulsion Systems
Electrical Propulsion Systems

## Slide 28: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Classical space propulsion systems are today limited as delta v is linked to propellant mass
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 29: Which Non-material Ejection Propulsion Systems exist?
Non-material Ejection Propulsion Systems:
Space Propulsion ENG-510
L7 – Non-material Ejection
Space Propulsion
Material Ejection
Non-Material Ejection
Catapult launch
Solar Sail
Beam power
Tether

## Slide 30: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
Rocket advancements
  High energy chemical fuels
  Nuclear rockets
  Propulsion by annihilating antimatter
  Magnetic thrust chambers
  Air-augmented rockets (e.g. ramjet, scramjet)
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 31: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Non-rocket advancements
  Solar power / solar sail
  Catapult launch (e.g. spin launch, canon or slider)
  Tether propulsion systems
  External beamed power (e.g. Laser)
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 32: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Solar power / solar sail
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 33: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Solar power / solar sail
  Solar sails use the pressure of sunlight for propulsion, angling toward or away from the Sun so that photons bounce off the reflective sail to push a spacecraft
  This eliminates heavy propulsion systems and could enable longer duration and lower-cost missions
  Although mass is reduced, solar sails have been limited by the material and structure of the booms, which act much like a sailboat’s mast
  But NASA is about to change the sailing game for the future.
  A next-generation solar sail technology – known as the Advanced Composite Solar Sail System – was launched aboard Rocket Lab’s Electron rocket
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 34: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Solar power / solar sail
  The technology could advance future space travel and expand our understanding of our Sun and solar system
  The Advanced Composite Solar Sail System demonstration uses a twelve-unit (12U) CubeSat built by NanoAvionics to test a new composite boom made from flexible polymer and carbon fiber materials that are stiffer and lighter than previous boom designs
  The mission’s primary objective is to successfully demonstrate new boom deployment, but once deployed, the team also hopes to prove the sail’s performance
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 35: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Solar power / solar sail
  Like a sailboat turning to capture the wind, the solar sail can adjust its orbit by angling its sail
  After evaluating the boom deployment, the mission will test a series of maneuvers to change the spacecraft’s orbit and gather data for potential future missions with even larger sails
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 36: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Catapult launch (e.g. spin launch, canon or slider)
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 37: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Catapult launch (e.g. spin launch, canon or slider)
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 38: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Catapult launch (e.g. spin launch, canon or slider)
  Space gun
    In Project HARP, a 1960s joint United States and Canada defence project, a 410 mm gun was used to fire a 180 kg projectile at 3,600 m / s (12,960 km / h), reaching an apogee of 180 km, hence performing a suborbital spaceflight
    However, a space gun has never been successfully used to launch an object into orbit or out of Earth's gravitational pull
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 39: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Catapult launch (e.g. spin launch, canon or slider)
  Space gun
    In Project HARP, a 1960s joint United States and Canada defence project, a 410 mm gun was used to fire a 180 kg projectile at 3,600 m / s (12,960 km / h), reaching an apogee of 180 km, hence performing a suborbital spaceflight
    However, a space gun has never been successfully used to launch an object into orbit or out of Earth's gravitational pull
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 40: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Catapult launch (e.g. spin launch, canon or slider)
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 41: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Tether propulsion systems (i.e. plasma brake)
  Plasma brake does not use any propellant, instead it utilizes the interaction of ionospheric plasma and a charged micro-tether to generate Coulomb drag
  This is similar to atmospheric drag-based devices, but unlike them, micro-tether is safe to other spacecraft and the Coulomb drag is orders of magnitude stronger than atmospheric drag
  This difference in deaccelerating forces is even larger as the orbital altitude increases
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 42: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  Tether propulsion systems (i.e. plasma brake)
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 43: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  External beamed power (e.g. Laser)
  NASA Innovative Advanced Concepts (NIAC) proposal: Pellet-beam concept
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 44: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  External beamed power (e.g. Laser)
  The pellet-beam concept requires two spacecraft – one that sets off for interstellar space, and one that goes into orbit around Earth
  The spacecraft orbiting Earth would shoot a beam of tiny microscopic particles at the interstellar spacecraft
  Those particles would be heated up by lasers, causing part of them to melt into plasma that accelerates the pellets further, a process known as laser ablation
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 45: Which Non-material Ejection Propulsion Systems exist?
  Non-material Ejection Propulsion Systems:
  External beamed power (e.g. Laser)
  Those pellets could reach 120 km / s and either hit the sail of the interstellar spacecraft or repel a magnet within it, helping to propel the spacecraft to huge speeds that would let it whizz out of our heliosphere – the bubble of the solar wind around our Solar System
  The NIAC proposal examines a new propulsion architecture for fast transit of heavy (1 ton and more) payloads across the Solar System and to the interstellar medium
Space Propulsion ENG-510
L7 – Non-material Ejection

## Slide 46: Future Propulsion Systems
Brief overview on future space propulsion systems

## Slide 47: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 48: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Innovative Propulsion, by definition, shall:
  Bring significant positive benefit in terms of mass, performance, cost and flexibility
  Be at low TRL yet enough (> TRL 2) to be engineered and demonstrated in a medium term
  Enable new missions or applications
  Facilitate the creation of new markets
  Enhance reliability and competitiveness
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 49: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
The objectives of the IP–CCI are:
  To identify and support the strategic interest of ESA member states, industry and academia
  To stimulate the propulsion ecosystem of the ESA member states
  To increase the technology readiness, implement IOV / IOD missions, foster the research, development and testing capabilities and demonstrate the applications and services
  To provide an increased visibility of innovative propulsion activities for space
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 50: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 1 - High Efficiency Atmospheric-Breathing Electric Propulsion
  Atmospheric-breathing electric propulsion systems are defined by their capability to generate thrust using as propellant the gases of the atmosphere, which are collected by an intake installed on the same platform
  They are capable of operating with variable atmospheric gas mixtures and densities, and resilient to long term operation in a challenging environment
  This topic targets innovative electric propulsion systems with high thrust-to-power and high-specific-impulse capability
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 51: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 2 - Advanced Airbreathing Propulsion
  Generating lift by means of atmospheric flight while ingesting the atmospheric oxidizer into the airbreathing engine results into an overall lighter flight vehicle: there is no need to carry the oxidizer and the related storage system on board and the high aerodynamic efficiency L/D > 1 lowers further the required thrust with respect to classical non-lifting vehicles
  The main applications are to first stages of launchers, replacing the booster function and potentially performing some of the duty of subsequent stages, or suborbital point-to-point transports
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 52: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 2 - Advanced Airbreathing Propulsion
  Owing to a wide flight regime, potentially from Mach 0 to about 12, the vehicle and its propulsion must perform in an ample operational range
  This challenges the design of the propulsion system, which may incorporate variable geometry elements to enlarge the operational regime of the:
    Air intake and isolator
    Compressor: ram- or turbo based
    Combustor and injectors
    Nozzle and thrust vectoring
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 53: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 2 - Advanced Airbreathing Propulsion
  As an alternative to the multi-mode variable cycle engine, an engine integrating different propulsion elements can also be considered, e.g. a turbine- or rocket- based combined cycle engine and a (sc)ramjet which provides the required operational range
  In either case of a variable cycle engine or a combination of propulsion systems, the following design aspects have a critical impact in the overall performance of the vehicle:
    The transition between modes of operation, e.g. turbo to ramjet or ram to scramjet
    The overall integration of the propulsion system in the vehicle
    The combined aerothermal and aerodynamic loads throughout the mission
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 54: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 2 - Advanced Airbreathing Propulsion
  In either case of a variable cycle engine or a combination of propulsion systems, the following design aspects have a critical impact in the overall performance of the vehicle:
    The overall thrust-to-drag (aero-propulsive) balance to assure net thrust and acceleration
    The various combustion regimes
    The internal flow path design from an aero-thermo-mechanical-structural point of view
    The design and integration of the variable geometry components, e.g. intakes, throats and nozzles, by translation, deflection or morphing of the structural elements
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 55: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 2 - Advanced Airbreathing Propulsion
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 56: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 3 - Rotating and Pulse Detonation Propulsion
  Detonative propulsion engines exhibit superior performance in terms of specific impulse than conventional liquid, hybrid or solid rocket engines
  In addition, the pressure gain combustion offers the advantage of lowering the required injection pressure, thus potentially benefiting from an overall reduction in system mass
  There are two approaches to realize detonative combustion in a propulsive system: pulse detonation and rotating detonation
  Both concepts have the potential of simplifying and reducing the weight of the current propulsion systems
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 57: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 3 - Rotating and Pulse Detonation Propulsion
  Although the research on detonative combustion started more than half a century ago, the needs of more affordable and efficient propulsion system justify this breakthrough
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 58: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 3 - Rotating and Pulse Detonation Propulsion
  RTE (Rotating Detonation Engine)
    A rotating detonation engine (RDE) uses a form of pressure gain combustion, where one or more detonations continuously travel around an annular channel
    Computational simulations and experimental results have shown that the RDE has potential in transport and other applications
    In a detonative combustion, the flame front expands at supersonic speed
    It is theoretically more efficient than conventional deflagrative combustion by as much as 25% which would provide major fuel savings
    Disadvantages include instability and noise
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 59: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 3 - Rotating and Pulse Detonation Propulsion
  RTE (Rotating Detonation Engine)
    The basic concept of an RDE is a detonation wave that travels around a circular channel (annulus)
    Fuel and oxidizer are injected into the channel, normally through small holes or slits
    A detonation is initiated in the fuel / oxidizer mixture by some form of igniter
    After the engine is started, the detonations are self-sustaining
    One detonation ignites the fuel / oxidizer mixture, which releases the energy necessary to sustain the detonation
    The combustion products expand out of the channel and are pushed out of the channel by the incoming fuel and oxidizer
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 60: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 3 - Rotating and Pulse Detonation Propulsion
  RTE (Rotating Detonation Engine)
    Although the RDE's design is similar to the pulse detonation engine (PDE), the RDE is superior because the waves cycle around the chamber, while the PDE requires the chambers to be purged after each pulse
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 61: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 3 - Rotating and Pulse Detonation Propulsion
  PTE (Pulse Detonation Engine)
    A pulse detonation engine (PDE) is a type of propulsion system that uses detonation waves to combust the fuel and oxidizer mixture
    The engine is pulsed because the mixture must be renewed in the combustion chamber between each detonation wave and the next
    Theoretically, a PDE can operate from subsonic up to a hypersonic flight speed of roughly Mach 5
    Key issues for further development include fast and efficient mixing of the fuel and oxidizer, the prevention of autoignition, and integration with an inlet and nozzle
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 62: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 4 - Water Propulsion
  Water propulsion systems are currently being developed for various applications
  In the search for non-toxic, non-carcinogenic and in general non-hazardous replacements of hydrazine, water is the ultimate green propellant
  While the specific impulse can be better than that of other monopropellants, the main advantage is the removal of hazards, such as toxicity and adiabatic decomposition of hydrazine
  The water is not toxic nor carcinogenic and therefore handling is by definition as safe as, or even safer, than that of any other conceivable green propellant
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 63: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 4 - Water Propulsion
  The main advantages of water propulsion are thus on the one hand the safe storability of the propellant in form of the stable reaction product, water
  Water is however also a substance which can be found, in solid state, in various places in the solar system (comets, lunar poles, Martian soil, etc.)
  The concept of water propulsion is therefore, beyond the immediate applications as hydrazine replacement in LEO satellites, potentially very useful in future exploration missions, employing a simple form of In-Situ Resource Utilization (ISRU), with only limited propellant processing equipment required
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 64: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 4 - Water Propulsion
  Several different types of water propulsion exist, with possibly the most common current application being Water-Resistojets (WR)
  This type of thermo-electric propulsion uses the water itself as propellant
  In contrast Water Electrolysis Propulsion (WEP) employs an electrolyser to generate the actual propellants oxygen and hydrogen from the stored water
  The two gases are then used to operate conventional chemical propulsion thrusters
  Other concepts, like water electrolysis Hall Effect Thrusters (HET) using oxygen and hydrogen for electric propulsion, are also currently under development
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 65: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 5 - Long Term Storability and Operation of Hydrogen Peroxide
  Hydrogen peroxide was developed as a propellant for missiles in the 1940s and 1950s until it was replaced by higher performing combinations of propellants, such as hydrazine in the case of satellites, or cryogenically stored liquid hydrogen / liquid oxygen for launchers
  Since the 1990s, hydrogen peroxide development for thrusters (in particular small thrusters in the 5N class) has enjoyed a renaissance of activity, as the desire for non-toxic propellants for spacecraft has increased
  Pure hydrogen peroxide will naturally decompose into water (steam) and oxygen given the right catalyst
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 66: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 5 - Long Term Storability and Operation of Hydrogen Peroxide
  Stabilizers are added to the hydrogen peroxide to facilitate the storage and allow the safe use as propellant, thus reducing the purity
  These additives have the undesirable effect of reducing the propulsive efficiency, hence their use needs to be minimized wherever possible
  In launch vehicle and other short-term applications, a cumulative increase of pressure can be vented overboard to prevent over pressurization of the storage tanks
  Nonetheless, this is not desirable, or even nor possible in some cases, for multi-year mission satellites
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 67: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 5 - Long Term Storability and Operation of Hydrogen Peroxide
  on satellites, such as titanium alloys and some stainless steels, facilitate the decomposition of hydrogen peroxide and therefore are not suitable in their current form for the long-term storage of hydrogen peroxide-based propellants
  In order to use hydrogen peroxide for long term applications, alternative materials for components and / or alternative stabilizing additives need to be used
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 68: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 5 - Long Term Storability and Operation of Hydrogen Peroxide
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 69: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 6 - Innovative Aerodynamic Surfaces
  The topic of innovative aerodynamic surfaces comprises ailerons, elevons, flaps, rudders, or panels that modify the aerodynamic characteristics of a vehicle and produce lift and drag forces
  Several categories of aerodynamic surfaces are envisaged, subdivided between primary surfaces and complementary surfaces
  Primary surfaces are ailerons, elevators, and rudders
  Ailerons are mounted on the trailing edge of the flying vehicle and move in opposite directions
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 70: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 6 - Innovative Aerodynamic Surfaces
  Elevators are a moveable part of the horizontal stabilizers, hinged to the back of the tail of the flying vehicle
  Rudders are mounted on the trailing edge of the vertical stabilizer, part of the empennage
  Complementary surfaces are spoilers, flaps, slats, and airbrakes
  Spoilers are used to disrupt the airflow and reduce the lift whereas flaps and slats are used to increase the lift of the flying vehicle. Airbrakes are used to increase drag
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 71: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 6 - Innovative Aerodynamic Surfaces
  This topic focus on the conception, architecture design, technical analysis, development, and operations of Innovative Aerodynamic Surfaces as propulsive mean for a flight vehicle
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 72: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 6 - Innovative Aerodynamic Surfaces
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 73: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 7 - Long-term In-space Cryogenic Propulsion and ISRU Propellants
  The higher performance of cryogenic propellants and the ubiquity of their precursor availability in the solar system means that they are perfectly suited for in situ resource utilization (ISRU) and in-orbit re-fueling
  Many lunar and Martian missions in particular hope to exploit these propellant options
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 74: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 7 - Long-term In-space Cryogenic Propulsion and ISRU Propellants
  These mission concepts include:
    Martian and Lunar transit stages
    Propulsive Landers
    Space Tugs
    Re-fueling stations
  Such systems must withstand thermal environments for transfers to Mars / Moon and back, including long duration transfers up to 6 months and dwell time of ~12-24 months
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 75: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 7 - Long-term In-space Cryogenic Propulsion and ISRU Propellants
  Current cryogenic approaches are limited to the much shorter-lived applications for launch vehicles
  The requirements for the in-space applications for these propellants will require a significant overhaul of both our understanding of cryogenic propellant management and the product catalogue that has been evolved to exploit them
  The scale of these engines will be similar to, or smaller than existing upper stage engines (~ 100 kN)
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 76: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 7 - Long-term In-space Cryogenic Propulsion and ISRU Propellants
  However, they will have additional challenging requirements: large number or restarts/reusability, deep ability to throttle, and clustering of engines for higher thrusts (in applications such as landers and large transfer stages)
  To realize a long-term cryogenic propulsion system several key technologies and operational concepts need to be addressed including: low / zero boil off technologies, cryo-fluid handling and management, thermal management of temperature distribution within the tanks and zero / low consumption chill down in preparation for engine operation
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 77: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 8 - Space Tethers
  Space tethers are long, strong, charged cables which can be used for propulsive maneuvers in space thanks to their interaction with charged particles present in the high layers of the atmosphere and in the solar wind
  Their working principle allows for propellant-less orbital transfers or de-orbiting satellites at the end of their life
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 78: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 9 - Beamed Energy Propulsion
  A variety of different concepts for space transportation systems with Beamed Energy Propulsion (BEP) engines were proposed in past studies by several different authors
  They can be roughly grouped in the following categories:
    Plasma: The incoming beamed energy is focused by a mirror system. In the focal point on-board propellant or ambient air is converted into plasma
    The ejected plasma propels the vehicle by momentum exchange
    Laser ablative propulsion, where the target spacecraft or space debris is ablated to create an impulse, also falls in this category
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 79: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 9 - Beamed Energy Propulsion
  They can be roughly grouped in the following categories:
    Thermal: A heat exchanger in the vehicle is heated by beamed energy
    The heat is transferred to on-board propellant, which is ejected in a classical convergent-divergent nozzle
    A special form of thermal beamed energy propulsion is the solar thermal propulsion stage, where the beam source is the sun
    Sail: The beamed energy is reflected by a sail
    The resulting radiation pressure exacts a force on the vehicle
    The Solar Sail is a specific concept of this category, using the pressure of the solar light for propellant less propulsion
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 80: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 9 - Beamed Energy Propulsion
  They can be roughly grouped in the following categories:
    Climber: The climber type is a vehicle for a space elevator type transportation system
    The climber will convert beamed energy into mechanical energy used for climbing the tether to the orbital destination station
  While the Sail is a feasible approach for in-space applications only, the Climber is a radically different concept and difficult to compare with other propulsion systems
  And now the pellet beam…out of NASA Innovative Advanced Concepts (NIAC)
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 81: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 9 - Beamed Energy Propulsion
  They can be roughly grouped in the following categories:
    Pellet beam:
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 82: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 9 - Beamed Energy Propulsion
  They can be roughly grouped in the following categories:
    Pellet beam: The pellet-beam concept requires two spacecraft – one that sets off for interstellar space, and one that goes into orbit around Earth
    The spacecraft orbiting Earth would shoot a beam of tiny microscopic particles at the interstellar spacecraft
    Those particles would be heated up by lasers, causing part of them to melt into plasma that accelerates the pellets further, a process known as laser ablation
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 83: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 9 - Beamed Energy Propulsion
  They can be roughly grouped in the following categories:
    Those pellets could reach 120 km / s and either hit the sail of the interstellar spacecraft or repel a magnet within it, helping to propel the spacecraft to huge speeds that would let it whizz out of our heliosphere – the bubble of the solar wind around our Solar System
    The NIAC proposal examines a new propulsion architecture for fast transit of heavy (1 ton and more) payloads across the Solar System and to the interstellar medium
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 84: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 10 - Nuclear Electric Propulsion
  Space nuclear electric propulsion (NEP) is a technology that utilizes nuclear reactions to generate electricity and propel spacecraft using electric propulsion (EP) thrusters
  The idea of using nuclear energy for space propulsion dates back to the 1950s, with the development of nuclear thermal rockets or nuclear power reactors by the US and the Soviet Union
  Since then, various countries and organizations have conducted research and development in NEP as it could revolutionize space exploration by enabling faster and more efficient travel through space
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 85: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 10 - Nuclear Electric Propulsion
  Potential applications of NEP include Earth-Moon space tugs, manned missions to Mars, deep space exploration, asteroid mining, or even satellite servicing and maintenance
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 86: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 11 - Nuclear Thermal Propulsion
  In the 1960s and 1970s extensive research on nuclear propulsion was performed by the United States of America and the Soviet Union
  Due to financial constraints and a shift in focus, this research did ultimately not lead to operational systems
  Meanwhile a lot of progress has been made, not only in reactor technology, but also in material science
  Future exploration and science missions with large payload mass and at the same time high delta v demand, can often not be fulfilled by either the available high specific impulse electric propulsion or the available high thrust chemical propulsion
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 87: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 11 - Nuclear Thermal Propulsion
  Already in the early stages of space exploration it became clear that nuclear propulsion and power are key enabling technologies for an extended human presence on moon or Mars
  Recently NASA and DARPA announced the plans for a nuclear thermal propulsion demonstrator (DRACO) to be launched within fiscal year 2027
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 88: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 12 - Metallic Propellant for Chemical Propulsion
  The potential use of metals can be exploited not only as a fuel for space vehicles but also as a motivating and promising technology for future “settlement plans” on the Moon and Mars
  The prominent features of metal fuel technology are:
    It offers a completely CO2-free way to produce heat and/or electrical power and to store energy for deferred uses
    It is a safe commodity for trading large energy stocks across the world, thanks to its intrinsically high energy density value
    It relies on existing infrastructures, does not require large investments for new power plants, and does limit to the bare minimum its environmental footprint
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 89: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 12 - Metallic Propellant for Chemical Propulsion
  The prominent features of metal fuel technology are:
    It is based on a large and practically unlimited resource of fuel food stock and on a fully reversible way to recycle the combustion products in an environmentally friendly manner
  The main goal of this technology is to zero the CO2 emissions in the production and recycling processes, as well as in storing and trading energy reserves and assets
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 90: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 12 - Metallic Propellant for Chemical Propulsion
  The prospective propellants are:
    Magnesium powder: With the compromise of specific impulse, ignition condition, combustion rate and sufficiency, powdered magnesium is considered as most promising fuel adopted for Mars or Moon Mission based on ISRU
    This has huge challenges in terms of feeding powder to a chamber for combustion
    Nonetheless, it could be interesting from an in-situ resource utilization perspective in that, if the ISRU processes can convert, for example, lunar regolith metal oxides to metal (e.g. magnesium) and oxygen, these can be used as propellants or an energy source and would be 100% locally sourced
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 91: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 12 - Metallic Propellant for Chemical Propulsion
  The prospective propellants are:
    Magnesium powder: Besides, huge abundance of magnesium oxide mineral in Martian regolith has been discovered, which makes the production of magnesium powder on Mars to be possible in the future
    Aluminum powder: In energetic applications, such as propellants, pyrotechnics and explosives, aluminum is widely used because of its high combustion enthalpy, easy availability, low toxicity and good stability
    Aluminum, whether powders or flakes, is used to increase the energy and raise the flame temperature in rocket propellants
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 92: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 12 - Metallic Propellant for Chemical Propulsion
  The prospective propellants are:
    Hydrogen: Physicists Wigner and Hungtinton predicted that hydrogen could turn into an electricity-conducting solid metal at the right temperature and pressure
    Metastable metallic hydrogen would be a very light-weight, low volume, powerful rocket propellant
    Indeed, for comparison, liquid (molecular) hydrogen-oxygen used in modern rockets performs with an Isp of ~460 s whereas metallic hydrogen has a theoretical Isp of 1700 s
    Nonetheless, producing the pressure required to reach that state is extremely complex
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 93: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 12 - Metallic Propellant for Chemical Propulsion
  The prospective propellants are:
    Hydrogen: Currently, several laboratories across the world are working with a Diamand Anvil Cell, in which two opposing diamonds with flattened tips squeeze a thin rhenium gasket
    Although there are some promising results, this technology is not mature for industrial production of metallic hydrogen
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 94: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 13 - Advanced High Altitude Platform Systems (aHAPS)
  High-Altitude Platform Systems or High-Altitude Pseudo-Satellites are flying vehicles able to fly and/or hover at high altitudes above 20 km in the Earth atmosphere
  They can operate as Very Low Earth Observation (VLEO) flight vehicles and are considered as pseudo- or atmospheric-satellites
  Their main applications are telecommunications, weather monitoring, and surveillance, similarly to LEO satellites
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 95: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 13 - Advanced High Altitude Platform Systems (aHAPS)
  Another significant application, distinguishing them from conventional LEO satellites, is using them as carrier vehicles for air-launched rockets, making use of the high altitude the flight vehicle can reach
  These systems can be in the form of airships, balloons, and airplanes
  This topic will evolve around the Flight Vehicle Engineering of such systems, specifically on the advanced propulsion and enhanced aerothermodynamics, making them more efficient while increasing their versatility and performance
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 96: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 13 - Advanced High Altitude Platform Systems (aHAPS)
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 97: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 14 - Innovative Propulsion on Non-Terrestrial Bodies
  Non-Terrestrial bodies come either with or without an atmosphere where propulsive systems and units would relate to landers or observation vehicles (e.g. drones…)
  In absence of an atmosphere, one would rather need rocket engines to translate a craft both horizontally and vertically
  In the presence of an atmosphere, one can exploit it to generate lift or to hover by means of aerodynes and aerostats
  Within the class of aerodynes, one can distinguish between rotorcraft or fixed-wing planes
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 98: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 14 - Innovative Propulsion on Non-Terrestrial Bodies
  In both cases, lift is generated by fluid-dynamic forces which carry the weight whereas the propulsion system generates the thrust to compensate for the drag and provide the acceleration
  For aerostats, e.g. balloons, dirigibles…, lift is generated by buoyancy, while lateral translation is generated by wind (drag) or a propulsion unit
  This propulsive unit can either make use of the atmosphere by means of e.g. an electrical driven fan, an oxidizer breathing engine, a fuel breathing engine... or fall back to a rocket engine not relying on the atmosphere
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 99: Which Future Propulsion Systems are developed?
  ESA Innovative Propulsion – Cross Cutting Initiative:
Topic # 14 - Innovative Propulsion on Non-Terrestrial Bodies
  Finally, among these different propulsion innovations, one should assess what power sources feed the engine, namely electrical (photovoltaic or nuclear), chemical (mono- or bi-propellant), ‘fluid’-breathing (using the species in the atmosphere), where the chemical propellant might be coming from an ISRU plant
Space Propulsion ENG-510
L7 – Future Propulsion Systems

## Slide 100: Lecture # 7 Summary
Brief synthesis on space propulsion course

## Slide 101: Which Summary of Lecture is given?
  Summary:
Basic idea of space propulsion course is to give (nearly) complete overview on all propulsion systems related to space (from lift-off on ground to deep-space exploration)
This idea is in principle achieved by intense discussion on thermal, chemical and electrical propulsion systems as well as non-material ejection propulsion systems and future propulsion systems
More detailed information needs to be collected by yourself!
Space Propulsion ENG-510
L7 – Summary

## Slide 102: EPFL Space Center eSpace
Space Propulsion ENG-510
The End

## Slide 103: Lecture # 7 Introduction & General Course Information
Brief update on space propulsion course

## Slide 104: Launch Event
Launch Schedule:
Tuesday, May 27
Between 9 am and noon
All groups shall be present during the complete event (constraints w.r.t. exams will be for sure considered)
Weather is out of control
It is highlighted that booster / core stage fixation shall be strengthened
Space Propulsion ENG-510
L7 - Introduction

## Slide 105: Oral Exam
Schedule:
Wednesday, July 2 and Thursday, July 3
Excel table is uploaded on Moodle
Please fill out table
Space Propulsion ENG-510
L7 - Introduction

## Slide 106: Oral Exam
Use Case Example:
A propulsion system shall be designed for a GEO (Geostationary Earth Orbit) satellite
  Spacecraft mass is 6 tons
  Spacecraft lifetime is 10 years
  Propulsion system shall ensure attitude control of the spacecraft over the complete lifetime
  Main trade-off criterions for the propulsion system are simplicity (simple architecture), robustness (mature technology) and price (small number of components)
  Main performance requirements are thrust [1 N], thrust duration [10.000 s], total impulse [10.000 Ns] and MIB (Minimum Impulse Bit) [0.1 Ns]
Space Propulsion ENG-510
L7 - Introduction

## Slide 107: Oral Exam
Use Case Example:
Which propulsion systems could be considered?
Which propulsion system do you propose?
How do you justify your selection (advantages, disadvantages of the different propulsion systems)?
Can you explain different methods to ignite an engine?
Space Propulsion ENG-510
L7 - Introduction

## Slide 108: Oral Exam
Use Case Example:
Can you explain following graph …?
Space Propulsion ENG-510
L7 - Introduction
Delta v [km / s]
0
5
10
15
0
20
MR [-]
1
10
100
ve = 2 km / s
ve = 4 km / s
ve = 10 km / s
ve = 30 km / s

## Slide 109: Oral Exam
Use Case Example:
You have 5 minutes for preparation of your answers
Afterwards Q & A will be performed
Space Propulsion ENG-510
L7 - Introduction

## Slide 110: Oral Exam
Use Case Example:
Wednesday, July 2
Space Propulsion ENG-510
L7 - Introduction
02.07.2025 | 
8:00 - 8:30 | Tania Rosset
8:30 - 9:00 | Antoine Marchand
9:00 - 9:30 | Michaël Fuser
9:30 - 10:00 | Sven Profichet
10:00 - 10:30 | Mike Michel Bauer
10:30 - 11:00 | João von Haehling
11:00 - 11:30 | William Martin
11:30 - 12:00 | Alexis RUPRECHT
Break | 
13:00 - 13:30 | Thibault Bardet
13:30 - 14:00 | Guillaume Keusch
14:00 - 14:30 | Patrick Alexis Zvezdin
14:30 - 15:00 | Alexandre Aires Viegas
15:00 - 15:30 | Florian Kurz
15:30 - 16:00 | maximilien Rochat
16:00 - 16:30 | Pierre-Sylvain Rosset
16:30 - 17:00 | Ramon Heeb
17:00 - 17:30 | Alfonso Monna
17:30 - 18:00 | 

## Slide 111: Oral Exam
Use Case Example:
Thursday, July 3
Space Propulsion ENG-510
L7 - Introduction
03.07.2025 | 
8:00 - 8:30 | 
8:30 - 9:00 | 
9:00 - 9:30 | 
9:30 - 10:00 | Maxime Bugnion
10:00 - 10:30 | Melani Cvetkovska
10:30 - 11:00 | Loris Hegg
11:00 - 11:30 | Tom Rathjens
11:30 - 12:00 | Bron Ward
Break | 
13:00 - 13:30 | Jehan Corcelle
13:30 - 14:00 | Oscar Foubert
14:00 - 14:30 | Sameh Lahouar
14:30 - 15:00 | Marcel Zelent
15:00 - 15:30 | Maximilian Bonvin
15:30 - 16:00 | Ryan Svoboda
16:00 - 16:30 | Aliénor Perruchio
16:30 - 17:00 | 
17:00 - 17:30 | 

## Slide 112: Feedback
Feedback:
Tool is running
Please provide feedback
Number of ECTS points was checked and is considered as fair following EPFL regulations
New lecture going more in propulsion details is in preparation
Space Propulsion ENG-510
L6 - Introduction

## Slide 113: Future Evolution
Potential additional lecture (first ideas):
Detailed equipment design
3d printing of parts
Testing
Final verification together with New Space Company
Space Propulsion ENG-510
L6 - Introduction

## Slide 114: Test Facility Visit
ERT Test Facility Visit (including firing demonstration):
Test facility visit is proposed for Wednesday, May 28 with departure at 9 am
No interest?
Space Propulsion ENG-510
L6 - Introduction

## Slide 115: The End
Thank you!
All the best!
Do not hesitate to reach out to me!
Space Propulsion ENG-510
L6 - Introduction

## Slide 116: EPFL Space Center eSpace
Space Propulsion ENG-510
The Real End