## Slide 1: ENV 501 / GR A3 30 Exercise session 3: Handwritten MFA + Jupyter Notebook MFA
Teaching assistant:
Jair Campfens jair.campfens@epfl.ch
Fall 2024

## Slide 2
The production of photovoltaic cells can be represented in a simplified manner depicting only the two main processes; silicon wafer production and photocell production. The flow data for each of the processes are as follows:
Wafer production (for 1kg silicon wafers) | 
Input | 
Silicon [kg] | 1
Energy [MJ] | 420
Output | 
Silicon wafers [kg] | 1
Photocell production (for 1m2 photovoltaic cells) | 
Input | 
Energy [MJ] | 13.6
Glass [kg] | 10
Silicon wafers [kg] | 1.6
Output | 
Photovoltaic cells [m2] | 1
Perform a system analysis: establish the system diagram and derive the balance equations.
Develop the output equations considering each of the inputs, and calculate the amount of energy, silicon and glass needed to produce 1 m2 of PV cells.
Exercise — Photovoltaic cell production

## Slide 3
Exercise — Photovoltaic cell production

## Slide 4
InputE1∙k1 + InputSi∙k2 = Output1∙k3
Exercise — Photovoltaic cell production
Input=
Output
}
Material or energy unit
k material and/or energy ratio

## Slide 5
InputE1∙k1 + InputSi∙k2 = Output1∙k3
Output1∙k3 + InputE2∙k4 + InputG∙k5 = Output2∙k6
Exercise — Photovoltaic cell production
Input=
Output
}
Material or energy unit
k material and/or energy ratio

## Slide 6
InputE1∙k1 + InputSi∙k2 = Output1∙k3
Output1∙k3 + InputE2∙k4 + InputG∙k5 = Output2∙k6
InputE1∙k1 + InputSi∙k2 + InputE2∙k4 + InputG∙k5 = Output2∙k6
Exercise — Photovoltaic cell production

## Slide 7
The production of photovoltaic cells can be represented in a simplified manner depicting only the two main processes; silicon wafer production and photocell production. The flow data for each of the processes are as follows:
Wafer production (for 1kg silicon wafers) | 
Input | 
Silicon [kg] | 1
Energy [MJ] | 420
Output | 
Silicon wafers [kg] | 1
Photocell production (for 1m2 photovoltaic cells) | 
Input | 
Energy [MJ] | 13.6
Glass [kg] | 10
Silicon wafers [kg] | 1.6
Output | 
Photovoltaic cells [m2] | 1
Perform a system analysis: establish the system diagram and derive the balance equations.
Develop the output equations considering each of the inputs, and calculate the amount of energy, silicon and glass needed to produce 1 m2 of PV cells.
Exercise — Photovoltaic cell production

## Slide 8
x kg Si-wafers = k2∙x kg Si + k1∙x MJ energy
  x kg Si-wafers = 1∙x kg Si + 420∙x MJ energy
y m2 PV cells = k3∙y Si-wafers + k5∙y kg glass + k4∙y MJ energy
  y m2 PV cells = 1.6∙y Si-wafers + 10∙y kg glass + 13.6∙y MJ energy
Exercise — Photovoltaic cell production

## Slide 9
Therefore, to produce 1 m2 of PV cells, we need 1.6∙1 kg Si, 10∙1 kg glass, and (420∙1.6 + 13.6∙1) MJ energy.
→ 1.6 kg Si, 10 kg glass, and 685.6 MJ energy is required.
Exercise — Photovoltaic cell production