## Slide 1: ENV 501 / GR A3 30 MFA Software – Tutorial STAN
Teaching assistant:
Jair Campfens jair.campfens@epfl.ch
Fall 2024

## Slide 2: Software for MFA
Tools for mapping and calculating mass balance systems
  STAN (STofflussANalysen) by TU Wien, Institut für Wassergüte, Ressourcenmanagement und Abfallwirtschaft
    Free software available at: http://www.stan2web.net/downloads/stan
  Umberto
Others
  Matlab (Toolbox Simulink)
  Mathematica
  R

## Slide 3: What is STAN?
subSTance flow ANalysis
  Free software for material flow analysis (based on Austrian standard ÖNorm S 2096; MFA − application in waste management)
  Available in EN or DE
You can use STAN to:
  Build graphical models with predefined components (processes, flows, system boundaries etc.)
  Enter or import known data (mass flows, stocks, transfer coefficients etc.) for different layers and periods
  Produce Sankey-style diagrams
  Consider data uncertainty and error propagation
(Source: www.stan2web.net, 2019)

## Slide 4
Shapes Window
Drawing area (DA)
Properties Window
Menu toolbars

## Slide 5: To get started…
File management
  Open new document [Ctrl + N]
  Open existing document [Ctrl + O]
  Save document (.zmfa file) [Ctrl + S]
Use the STAN web platform can for file exchange between users:
  Login to STAN portal directly from program
  Possibility to Load/Save/Delete/Modify STAN files via portal

## Slide 6: Inserting a process
Click on in the Shapes window
Click to drop at desired position
Processes can be resized/moved in the DA, and assigned values and renamed/modified in the Properties window
P

## Slide 7: Inserting a flow between processes
Click on in the Shapes window
Click to drop at Process 1 and drag to Process 2
Flows can be assigned values and renamed/modified in the Properties window

## Slide 8: Inserting import/export flows
Click on or in the Shapes window
Click to drop in DA and drag to the relevant process
Import and export flows can be assigned values and renamed/modified in the Properties window
I
E

## Slide 9: Defining the system boundary
Click on in the Shapes window
Click to drop in DA and drag over the relevant processes and flows
System boundary will be refreshed automatically with the change in stocks and the sum of imp/exp when data values are defined

## Slide 10: Properties window
Defines values for flows, stocks, transfer coefficients and other details

## Slide 11: Other important elements
Layers
  Layers can be used to organise different types of goods/substances
  To create a new layer: Edit > Layers and Periods > Layers
  Choose a substance/material from the list
    Additional substances can be added to the predefined list: Edit > Define Material

## Slide 12: Other important elements
Periods
  Periods can be defined to perform analysis over multiple time periods
  To edit period information: Edit > Layers and Periods > Periods
  Modify the parameters as desired
Default period for new projects is the current year
If multiple periods are considered, they must have the same duration and be consecutive

## Slide 13: Other important elements
Units can be selected, defined, and modified via Edit > Define Units

## Slide 14: Data Import & Export
Edit > Data Explorer [Ctrl + D]
To edit data, edit mode must be switched on
  Data can be entered for processes, flows, transfer coefficients etc.
  Data can be copied to/from clipboard
  Data can be imported from and exported to Excel

## Slide 15: Calculation
Calculation procedures in STAN can include:
  data reconciliation
  computation of unknown quantities
  calculation of uncertainties
Before calculation, consider:
  Layer & Period selection
    Edit > Layers and Periods
  Processes to exclude from balancing
  Display of coarse (mass) balance of processes within process icons
    Extras > Options > Processes & Flows

## Slide 16: Calculation
To perform simple calculation, press F5 or click in the Data Input toolbar
Additional calculation options (calculation method, trace level) can also be defined if necessary
  Edit > Calculation dialog

## Slide 17: Export system diagram
File > Export Diagram
  Select graphical options
  Copy to clipboard or export as file