## Slide 1: Buckingham-PI theorem
Dimensional analysis
Fracture of materials

## Slide 2: Statement
"If there is a physically meaningful equation involving a certain number n physical variables, then the original equation can be rewritten in terms of a set of p = n − k dimensionless parameters π1, π2, ..., πp constructed from the original variables, where k is the number of physical dimensions involved."

## Slide 3: Why is it useful ?
Find laws and equations based on physical variables
Get a better intuition of the important parameters of a system
Form precise laws from experiments (or theories)
NB: here π is not 3.1415 …. BUT a dimensionless parameter !

## Slide 4: Steps of the theorem
Determine the N important system parameters (physical variables) for what we want to find
Build the matrix of the physical variables/dimensions and find its rank K
Determine the number of dimensionless groups p = N – K
  N is the number of physical variables (speed, density, pressure...)
  K is the number of physical dimensions (kg, m, s...) -> Always take base units for conveniance !
Build the p dimensionless groups
Find the equation for the physical parameter you are interested in !
  If there is only one group, only one experiment will be necessary to find a numerical value of the dimensionless parameter π
  If there is multiple group, multiple experiments will be necessary to find the link between them.

## Slide 5: Exemple
We aim to find a relationship for the time t it takes for an object initially at rest to fall a certain distance h, under the influence of gravity g. (We neglect friction)
Step 1 :
  What are the physical variables ?
  What are their physical dimensions ?
  t = [s]
  h = [m]
  g = [a] = [m/s²]
  N = 3

## Slide 6: Example
Step 2 : build the matrix with :
  Physical variables in columns
  Physical dimensions in row
 | t | g | h
s | 1 | -2 | 0
m | 0 | 1 | 1
This is a matrix of rank K = 2 !
Step 3 : Determine the number of dimensionless parameters p
  P = N – K = 3 – 2 = 1

## Slide 7: Example
Step 4 : Chose and build the p dimensionless parameters
  We need only 1 : since we want to find t at the end, let's take it as a basis ! (we could also search h for a given t …)
  We need to balance t with the other N-P physical variables to make π dimensionless
  For easier resolution, let's replace the physical variables with their dimensions
  We can solve this independently for each dimension !
    second, T : 0 = 1 + 2a
    meter, L : 0 = -a - b
    a = -1/2
    b = 1/2

## Slide 8: Example
Step 5 : let's find the relation for t !
  If you know t, g and h, how many experiments will you need to do to determine the numerical value of π ?
  After one experiment, we find π² = 2 !
  By isolating t, we find :
  Which is the same relation we would find by resolving kinetics with acceleration = g and initial speed = 0 !

## Slide 9
What if there is more than one dimensionless parameter ? (p > 1)
You need to make more experiments, varying the value of the physical variables to find this relation :
In our case, if there was more than one dimensionless parameter (for example, adding air drag/resistance), we would need to solve by experiments :
Be careful the relation f could be non-trivial ! (For example, the Reynold's number is a dimensionless parameter, influencing other equations through this f in complex ways !)

## Slide 10: Any question ?
Exercices 1, 2 and 4 will be about Buckingham-Pi
Exercice 3 will be about wave propagation