## Slide 1
Bioimaging with holotomography microscopy
MSE-471. Biomaterials (pour MX)
Practical work sessions.

## Slide 2: Objectives
1. Understand Instrumentation and workflow
- Self-study of PPT material and YouTube videos (EP1,2,3 on moodle);
- the working principle and advantages of Nanolive compared to traditional imaging
2. Sample preparation and image acquisition (In class)
Exposure to how sample preparation is performed, including multi-channel imaging
Video demonstration ( Nanolive imaging demo in LAB）
3. Data analysis and interpretation (In lab)
- Experience in processing and analyzing holotomography data using Nanolive software, including 3D visualization of subcellular structures
- Exercises (image processing, coloring/staining)

## Slide 3
Logistics
 | Group 3 | Group 4
08:15-08:45 | Objective 2 | Objective 2
08:50-09:20 | Objective 3 (in lab) | Objective 1
09:20-09:50 | Objective 1 | Objective 3 (in lab)
Reflective questions:
1. How does Nanolive work?
2. In what circumstances would you use Nanolive rather than others?
3. Do you prefer to use this technique to image the cells in your gel and why/why not?

## Slide 4
1
Light microscopy
Bright field
Fluorescence microscopy
BRIGHT FIELD:
Imaging in accordance to light absorption, scattering and deflection by the sample.
Most cells are thin and transparent!
BUT
Phase contrast
Light microscopy in cell biology. Techniques.

## Slide 5
2
Light microscopy
Light microscopy in cell biology. Techniques.
Annular ring
Phase plate
Phase contrast: Enhancement by phase shift.

## Slide 6
3
Light microscopy
Light microscopy in cell biology. Techniques.
FLUORESCENCE MICROSCOPY:
Use of fluorophores 
Intercalating dyes, immunofluorescence (primary and secondary antibodies)…
- Photobleaching issues.
- Out-of-plane fluorescence.

## Slide 7
4
Light microscopy
Light microscopy in cell biology. Techniques.
Confocal microscopy: only records light from the focal plane of the sample

## Slide 8
5
Light microscopy
Light microscopy in cell biology. Techniques.
Certain limitations of fluorescence microscopy:
Long imaging time
Rigorous sample preparation
Potential toxicity of exogenous dyes
Limited to qualitative analysis
Holotomography microscopy

## Slide 9
6
Holotomography
Holotomography microscopy.
HOLOGRAPHY
TOMOGRAPHY
+
2D quantitative phase imaging
3D refractive index distribution reconstruction

## Slide 10
7
Holotomography
Holotomography microscopy.
HOLOGRAPHY. A hologram is a photographic recording of a light field.

## Slide 11
8
Holotomography
Holotomography microscopy.
Possible quantitative analysis
HOLOGRAPHY. A hologram is a photographic recording of a light field.

## Slide 12
9
Holotomography
Holotomography microscopy.
Attenuation
TOMOGRAPHY. Imaging by sections (rotation) + reconstruction.

## Slide 13
10
Holotomography
Holotomography microscopy.
General advantages:
Labelling process not required.
Non-invasive: Elimination of phototoxicity and no bleaching.
Enables quantitative analysis.
Allows for refractive index-based digital staining.
Ultra-fast imaging speed (1.7s/tomograph)  Real-time.

## Slide 14
11
Nanolive 3D Cell Explorer
Holotomography microscopy.
Nanolive 3D Cell Explorer:

## Slide 15
12
Nanolive 3D Cell Explorer
Holotomography microscopy.
Nanolive 3D Cell Explorer:
Self-adjusting optics (compatibility with different supports, dynamic adaptation).
Top-stage incubator to maintain physiological cell environment.
Fluorescence microscopy compatibility.