## Slide 1: Transverse Dynamics :: Equation of Motion and Solutions
Laboratory for Particle Accelerator Physics, EPFL

## Slide 2: Introduction Linear Dynamics
accelerator = series of elements for beam guiding (bending, focusing) and acceleration; often arranged in a closed loop (ring)
guiding fields must ensure long term (h) stability of circulating particles
questions to be answered:
How to ensure bound motion of a particle beam?
What are conditions for stability?
Amplitude and frequency of particle oscillations?
Statistical beam properties like beam width and angular spread?
How to design magnet lattices (arrangements of dipoles and quads in a line)?
What is the impact of field errors in bending and focusing magnets?

## Slide 3: References and Accessible Reading Material
available on the internet:
P. Schmüser & J. Rossbach, Basic course on accelerator optics:
https://cds.cern.ch/record/247501/files/p17.pdf
F.Tecker, Longitudinal Dynamics:
https://arxiv.org/pdf/1601.04901.pdf
Book, H.Wiedemann, Particle Accelerators, download pdf
https://link.springer.com/book/10.1007%2F978-3-319-18317-6
M. Sands, Physics of Electron Storage Rings: An Introduction.
https://digital.library.unt.edu/ark:/67531/metadc865991/
CERN Accelerator School (CAS) proceedings homepage (huge!)
http://cas.web.cern.ch/cas/CAS_Proceedings.html
CERN Accelerator School on Medical Applications:
https://cds.cern.ch/record/2271793/files/33-8-PB.pdf
books, papers:
M.Conte and W.McKay, An Introduction to the Physics of Particle Accelerators, World Scientific, 2008
S.Peggs, T.Satogata, Introduction to Accelerator Dynamics, Cambridge University Press, 2017
A. Wolski, Beam Dynamics in high energy particle accelerators, Imperial College Press, 2014
A. W. Chao, M. Tigner, Handbook of Accelerator Physics and Engineering, World Scientific 1999
E. D. Courant and H. S. Snyder, Annals of Physics: 3, 1-48 (1958)

## Slide 4: Make Particles Circulate
Main Dipoles
Main Dipoles
Main Dipoles
Main Dipoles

## Slide 5: Focusing the Particles
Main Dipoles
Main Dipoles
Main Dipoles
Quadrupoles

## Slide 6: Bending Magnet - SLS dipole
magnetic rigidity:

## Slide 7: Quadrupole Magnet - Focusing Element

## Slide 8: Quadrupole Lens
Focusing in one plane
Defocusing in the other plane
S
N
N
S
Focusing
Defocusing

## Slide 9
Next: Equation of Motion
suited coordinate system
linearizing forces and deriving differential equation

## Slide 10: Curvilinear Coordinate System
aim: derive a set of equations that describe the motion of a single particle wrt. a curved coordinate system around the reference orbit of a beam, ( x, y )
particle coordinate:
see also: Frenet-Serret coordinates, e.g. Wiedemann chap 4.3

## Slide 11: Deriving the Equation of Motion (see Appendix)
starting with general equation of motion:
the effect of the curved coordinate system, i.e. the moving unit vectors ex, es must be included in the calculation
dipole and quadrupole field
field gradient
varying sign convention !
k – value [m-2]
orbit curvature
curved coordinates
k - value
off momentum term
derivative w.r.t. path-length s, not time t
Notes: describe deviation from nominal orbit, x,y
start from equation of motion, consider only linear fields and introduce path length as independent variable instead of time
field parametrized as vertical dipole field plus quadrupole fields; dipole 1/rho, quad k

## Slide 12: Equation of Motion
DE is valid for drift spaces, Quadrupoles (k≠0), combined function magnets (k≠0, 1/≠0) and for off-momentum particles (p≠0, first order)
we discuss solutions of different cases of this equations in single accelerator magnets, depending on K(s), (s), p
see also Wiedemann sec. 1.5.8
generalised form:

## Slide 13: geometric meaning of coefficients
= curvature
1/ [m-1]
K = amplitude dependent curvature K[m-2]
inside quadrupole field

## Slide 14: Summary on Approximations used
small displacements (paraxial optics)
only dipole and quadrupole magnets (linear field changes)
design orbit lies in a plane (flat accelerator)
no coupling between motion in hor. and vert. plane (upright magnets)
small momentum deviations (quasi monochromatic beam)
in general: no quadratic or higher order terms (linear beam optics)
linear parametrization of magnetic field:

## Slide 15
Next: Solving the Equation of Motion using Matrices
matrix approach using principal trajectories
drift space, focusing and defocusing quadrupole

## Slide 16: Piecewise solution of trajectory equation in terms of principal trajectories
Dispersion Trajectory
(= particular solution of eq.)
Sinelike Trajectory
Cosinelike Trajectory
C(s), S(s) are independent solutions of the homogeneous equation:
see also Wiedemann sec. 5.5

## Slide 17: Formulation as Transport Matrix
proof:
 det = 1 initially, and it does not change as motion proceeds

## Slide 18: Piecewise Solution of Equation
general form of equation similar to harmonic oscillator with three cases: K=0, K<0, K>0
s
C
K(s)
K is piecewise constant, in a ring it repeats at least after one turn (s=C)

## Slide 19: Drift Space
particle moves straight
1.) K=0: Drift Space
L

## Slide 20: Focusing Quadrupole
2.) K > 0: Focusing Quadrupole
thin lens approximation:
f
x

## Slide 21: Defocusing Quadrupole
3.) K < 0: Defocusing Quadrupole
thin lens approximation for defocusing quad:
f
x

## Slide 22: Special Case: Weak Focusing
 one oscillation per turn as expected for „weak focusing“
reference orbit
particle orbit

## Slide 23: Dispersion Trajectory
is solution of equation:
is constructed from homogeneous solutions C(s), S(s):
proof: by insertion in above DE and by using CS´- C´S=1.
compare components of particle trajectory:

## Slide 24: Dispersion Trajectory in combined function magnet (Dipole & Quadrupole)
for K > 0
for K < 0
for K = 0
 Dispersion is generated by bending fields
 Dispersion oscillates in Quadrupoles like particle trajectories

## Slide 25: Quadrupole Doublet
concatenation of particle transport through a series of elements:
l
 Mdoublet is always focusing
(M = transport matrix 2x2)
[thin lens approximation]

## Slide 26: 3x3 transport matrix for off-momentum particles
can be re-formulated as a single matrix multiplication:
this formulation is convenient when computing the dispersion function

## Slide 27: Matrix Notation
… is one approach to describe particle trajectories in accelerators – for each element a matrix for linear computation can be defined.
The matrix can be extended to all six dimensions of phase space:
x, x’, y, y’, s, 
path length
energy deviation =E/E0
The matrix notation can be generalised to higher order dependencies. For example a tensor of rank 3 holds coefficients Tijk for a quadratic map of particle coordinates.
In this case R contains 36 parameters, some of which have practical importance for example in coupling horizontal and vertical motion.

## Slide 28
Next: Stability and Twiss Matrix
Eigenvalues and Stability
Twiss Matrix Decomposition

## Slide 29: Stability Criterion
for stable oscillation in a ring these coordinates must stay finite for n  ∞:
to assess stability use decomposition of M in Eigenvectors:
then:
thus it is sufficient analysing the Eigenvalues to assess stability of linear motion
n must be bounded for n   ( = complex number in general)
M = transport matrix of entire ring

## Slide 30: Stability Criterion :: Matrix & EV Properties
transfer matrix M has properties that can be used:
from that follows:
this can be extended to 4dim matrices (coupled horizontal + vertical)
bounded for
with  = real number
Im
Re
stable = EVs on unit circle

## Slide 31: Stability Criterion – the Trace of M
motion is stable if |Tr M|<2, which also means that  is real
see also Schmüser/Rossbach, and sect. 4.1, Wiedemann chap. 10.1.2
2x2 matrix: characteristic polynomial
quadratic equation for eigenvalues 
solution: values 1, 2
Computation of eigenvalues via characteristic polynomial:

## Slide 32: Summary Matrix Treatment
equation of motion is piecewise solved for constant K(s)
x, x’ are propagated by concatenated multiplication with 2x2 matrices
defocusing and focusing quadrupoles are combined in overall focusing doublets
linear motion in a ring is stable if |Tr M|<2
det M = 1 (also: M symplectic)
s
C
K(s)
pattern repeats

## Slide 33
Next: Analytical Solution
Hills equation
Beta function
phase space ellipse
include momentum offset
tune Qx, Qy

## Slide 34: Solution of Hill´s equation
First used by an astronomer George Hill in his studies of the motion of celestial bodies, a motion under the influence of periodically changing forces
1838 -- 1914

## Slide 35: Hill: Solution for periodic K
the beta function [m] is a scaling factor for the amplitude of orbit oscillations, and their local wavelength
A, 0 are constants of motion
weak quads
strong quads
- well known Betafunction of accelerators
variables are not related to relativistic factors
(sorry for the historic nomenclature)

## Slide 36: Comparison to Classical Harmonic Oscillator
amplitude is fixed:
phase grows linear with time:
conserved (energy):

## Slide 37: Hill Equation (pseudo harmonic equation)
amplitude varies:
phase increases monotonically but growth rate varies as 1/ :
conserved (action J):
Twiss
Parameters:

## Slide 38: Computing the Beta Function in three ways
1.) from the transport matrix of a closed ring
2.) by solving a DE for  (DE without proof)
3.) by using a transport matrix for Twiss parameters (C,S principal trajectories)

## Slide 39: Computing the transport matrix from Twiss Parameters
transport matrix s=s0 s1 (arbitrary section):
0, 0 at s0
,  at s1
 = phase advance between s0, s1

## Slide 40: The one turn matrix Mrev
special case: choose symmetry point  = 0
transport matrix for one revolution, “One Turn Matrix”
same location:  = 0
 = 2Q phase advance for complete turn, Q = “Tune” of accelerator

## Slide 41: Twiss Matrix
this expression has similar properties as
it holds:

## Slide 42: Beta Function in a Drift
β* = min
s

in a field free region  follows a quadratic function
the coefficients are related to the TWISS parameters
at min we have a waist

## Slide 43: Adding Dispersion
where D(s) is a solution of:
note:
D(s) = dispersion function as lattice solution – not exactly the same as
the previously introduced dispersion trajectory for single elements
(s) = used in some literature instead dispersion function D(s)
outside bending magnets D behaves like particle trajectories

## Slide 44: Phase Space Ellipse
1
4
2
3
x’
x
J = particle action (oscillation amplitude)
observing the coordinates of a particle at one location in a ring for consecutive turns
x, x’ describe an ellipse in phase space when  is varied
example φ= Q×2  0.37×2 phase advance per turn
see also Schmüser/Rossbach sect. 4.3/4.4, Wiedemann chap. 8.1.2

## Slide 45: Courant-Snyder Invariant
E.D. Courant and H.S. Snyder, Theory of the Alternating Synchrotron, Annals of Physics 3 (1958) 1
x’
x
at one location this phase space ellipse is sampled by a particle with action J
when moving along the magnet lattice, the ellipse is changing size, but it stays an ellipse
the area of the ellipse is invariant (Courant-Snyder Invariant) and equals 2 × action.
the unit is [mrad], or often [mmmrad]
this constant of motion refers to a single particle, emittance is a statistical property

## Slide 46: Courant-Snyder Invariant
E.D. Courant and H.S. Snyder, Theory of the Alternating Synchrotron, Annals of Physics 3 (1958) 1
x’
x
at one location this phase space ellipse is sampled by a particle with action J
when moving along the magnet lattice, the ellipse is changing size, but it stays an ellipse
the area of the ellipse is invariant (Courant-Snyder Invariant) and equals 2 × action.
the unit is [mrad], or often [mmmrad]
this constant of motion refers to a single particle, emittance is a statistical property

## Slide 47: Courant-Snyder Invariant
E.D. Courant and H.S. Snyder, Theory of the Alternating Synchrotron, Annals of Physics 3 (1958) 1
x’
x
at one location this phase space ellipse is sampled by a particle with action J
when moving along the magnet lattice, the ellipse is changing size, but it stays an ellipse
the area of the ellipse is invariant (Courant-Snyder Invariant) and equals 2 × action.
the unit is [mrad], or often [mmmrad]
this constant of motion refers to a single particle, emittance is a statistical property

## Slide 48: Courant-Snyder Invariant
E.D. Courant and H.S. Snyder, Theory of the Alternating Synchrotron, Annals of Physics 3 (1958) 1
x’
x
at one location this phase space ellipse is sampled by a particle with action J
when moving along the magnet lattice, the ellipse is changing size, but it stays an ellipse
the area of the ellipse is invariant (Courant-Snyder Invariant) and equals 2 × action.
the unit is [mrad], or often [mmmrad]
this constant of motion refers to a single particle, emittance is a statistical property

## Slide 49: Action vs. Emittance
x
single particles are associated with a particular ellipse
when observing a beam with a wire scanner a (projected) rms width x is measured; one ellipse corresponds to x
emittance  is the average value of action J
 more on emittance next lesson

## Slide 50: What beam will fit into the machine?
y
y’
-h/2
h/d
-h/d
h/2
h
d
Electron
Trajectories
Matched beam emittance
Unmatched beam emittance
Example: Acceptance of a lengthy aperture restriction (limits amplitude and angle)
F. Sannibale
`

## Slide 51: Admittance of an accelerator
admittance = the largest ellipse that can be accepted
  at any point along the accelerator
  units = phase space area [mmmrad]
  if the available half-aperture is d(s) there is at some s a minimum of
  so in general:
  Special case: uniform aperture d(s) = d the minimum occurs at bmax

## Slide 52: The Betatron Frequency Q (tune of accelerator)
Tune = Number of Betatron Oscillations per Turn (remember Q1 for purely weak focusing)
the choice of tune is important to avoid resonances
Both integer and fractional part are important
for machine design
around ring

## Slide 53: Resonance Plot
[R.Steinhagen, CERN]
LHC working point
condition for resonance:
order of resonance:
Qx

## Slide 54: Tunes and Orbit in LHC
Example Measured Beam Spectrum:
LHC Revolution Frequency: 11.3kHz
peak position: 3.5kHz = 0.31×11.3kHz
Example Orbit Oscillations:
LHC Tunes:
Qx = 62.31
Qy = 60.32
relevant for stability: non-integer part

## Slide 55: Smooth Approximation
simplify:
can be used to estimate important parameters:
note: Q  R, i.e. proportional to size
compare cyclotron: Q  , independent of size!

## Slide 56: Normalized Coordinates
in normalized coordinates the particle describes a circle in phase space
x‘
xn‘
x
xn
unit of normalized coordinates:
 this re-scaling of coordinates is related to the Floquet theorem (see appendix)

## Slide 57
Next: Summary of this Lesson

## Slide 58: Summary Linear Beam Dynamics I
1) Matrix Treatment
varies with s
off-momentum part
2) Analytical Treatment

## Slide 59: Summary Beam Dynamics - I
tune = number of oscillations per turn:
x’
x
phase space area is preserved
single particle vs. emittance

## Slide 61: Appendix, Derivation: Equation of Motion I
used here:
starting with general equation of motion:
comment: the main purpose here is to correctly treat the effect of the curved coordinate system, i.e. the moving unit vectors ex, es

## Slide 62: Derivation: Equation of Motion II
right side of equation, the force:
use:
assumptions:
no Bs
Bx(y=0) = 0
result: two equations hor/vert from x,y components:
in literature g has varying sign conventions
Wiedemann, Table 6.2: g=+dBy/dx
Schmüser/Hillert: g= -dBy/dx

## Slide 63: Derivation: Equation of Motion III
introduce path length s as independent variable:
use:

## Slide 64: Derivation: Equation of Motion IV
use:

## Slide 65: Floquet Theorem :: related to normalized coordinates
has two solutions in the form:
with:
for accelerators we note:
[envelope functions]
see also Schmüser/Rossbach sect. 4.2, Wiedemann chap. 10.2.1

## Slide 66: Applying Floquet to transport matrix
transport matrix M can be factorized in an „oscillatory“ and an „envelope“ part; oscillatory part describes a circle in normalised coordinates
then for k turns in accelerator (M = one turn matrix):
with: