## Slide 1: mesoscopic and nanoscale physcis
nanometer scale
atoms
molecules & clusters
electron mean free path
bulk materials
Length scale
meso
micro
macro
mesoscopic physics deals with the physics of small objects consisting of a collection of atoms
Laboratory of Quantum Physics: Topology and Correlations
Quantum transport in Mesoscopic systems
(PHYS-462)
Mitali Banerjee (LQP)
Ref: Supriyo Dutta/ H.S.J. van der Zant (TU Delft)

## Slide 4
x

## Slide 12: Quantum Dots
vertical dot
metal grain
metallic SET
nanotube
self assembled
MBE grown
lateral

## Slide 13: lateral vs. vertical
an electrical engineers point of view

## Slide 14: Lateral Dots: Formed in GaAs/AlGaAs 2DEG
Electrons travel in sub-surface layer:
CONTACT GATE CONTACT
Only lowes sub-band occupied at low T
+
+++
+++ + + + +
Surface
doping layer
Al0.3Ga0.7As
GaAs
Fermi energy
Negative voltage on gates depletes underlying electrons & defines dot cavity
GaAs
I (pA)

## Slide 15: gate defined dots
point contacts
A
B
C
1
2
3
A,B,C : control quantum point contacts transmission to reservoirs
1,2,3: control confinement potential / energy levels only
X control dot-internal tunneling rate
A
B
C 1
X 2

## Slide 16: Quantum Point Contact Leads
-0.7
-0.6
-0.5
2
-0.3
0
-0.4
-0.2
-0.1
VNOSE (V)
-0.6
-0.4 -0.2
VQPC1 (V)
0.0
4
6
8
8
6
4
2
0
2
g (e /h)
300
200
100
0
-100
-200
-300
Nose (mV)
-200
0
QPC2 (mV)
200
Not all QPCs are perfect:
6
4
2
0
2
g (e /h)
150
50
100
VG (mV)
0
VNOSE
VQPC1
1 µm
I
slide from A. Huibers, Thesis (1999)

## Slide 17: Open vs. Closed
Open Dot
Closed Dot
2
Vgate set to allow ≥ 2e /h conductance
through each point contact
Dot is well-connected to reservoirs
Transport measurements exhibit CF and Weak Localization
Vgate set to require tunnelling across point contacts
Dot is isolated from reservoirs, contains discrete energy levels
Transport measurements exhibit Coulomb Blockade
point contacts

## Slide 18: Coulomb Blockade in Closed Dots
c dot
Finite energy E =e2/C is needed to
add an additional electron to the dot. When kT<<Ec charging blocks conduction in valleys.
0.15
0.10
0.05
0.00
-200
-198 -196
V (mV)
-194
g (e2/h)
N
N+1
N+2 . . .
V
1 μm2
Coulomb blockade peaks:
resonant transport through dot levels

## Slide 19: Electrostatic Energy
apply voltages
what is potential on dot? voltage divider...
can use Vg to shift dot energy!!

## Slide 20: Charging Energy
capacitance of dot to world = C
energy stored in capacitor
charging energy
can range from
~0 to many meV
Classical Effect, NOT quantum

## Slide 21
Confinement Energy
harmonic potential
μeV to meV
complicated potential
x
average level spacing
E
quantum mechanical effect!!

## Slide 22: Capacitor Model
total dot energy
offset charge

## Slide 23: Constant Interaction Model
: interaction of electron k with rest
constant inteaction: model ϕk with CΣ
total dot energy

## Slide 24: Chemical Potential / Addition Energy
μ=0: change N current flows
addition energy
energy to add one more electron
constant interaction model:

## Slide 25: Quantum Coulomb Blockade
0.20
0.15
0.10
0.05
0.00
-250
-200
-150
V (mV)
-100
-50
0
For kT < Δ, each peak describes tunnelling into a single eigenstate. Wavefunction amplitude fluctuations lead to peak height fluctuations.
g (e2/h)
V
B=0 mT B=20 mT
kT ~ 3μeV
Δ ~ 10μeV Ec ~ 200μeV
slide from J. Folk (2002)

## Slide 26: Coulomb Diamonds
200nm
VSD
I
kT ~ 1.5μeV
Δ ~ 1000μeV Ec ~ 2000μeV
differential conductance: peaks when current through dot is changing

## Slide 27: Coulomb Diamonds
-eVSD
200nm
VSD
I
peaks in g appear when dot level aligned with either source or drain chemical potential

## Slide 28: Coulomb Diamonds, Sequential Tunneling Transport
electrons tunnel on / off dot one by one
(charging energy)
electrons do not change energy when tunneling
dot energy unchanged

## Slide 29: Coulomb Diamonds
two slopes, each associated with its respective dot-lead capacitance
Eadd

## Slide 30: Excited State Spectroscopy: Sequential Transport
2ES
1ES GS
-eVSD
2ES
1ES GS
-eVSD
2ES
1ES GS
-eVSD
only one excess electron can be on dot (charging energy)
A
B C
A
B
C
lab to investigate quantum levels in device!!
quantum confinement energies
internal excitations (spin)

## Slide 31: Cotunneling Transport
-eVSD
Δ
VSD
>Δ
elastic cotunneling (blue circle)
before tunneling
after
dot energy
unchanged
dot now in excited state
inelastic cotunneling
(white lines)
dot energy changes only possible for VSD>Δ
before tunneling
-eVSD
Δ
higher order process:
two electrons tunnel and change energy
after

## Slide 32: Temperature Regimes
no charging effects, no Coulomb blockade
classical Coulomb blockade (metallic CB)
temperature broadened
transport through several quantum dot energy levels
peak conductance idependent of T FWHM ~ 4.35kT
Γ = ΓL + ΓR
escape broadening (tunneling rates)

## Slide 33: Temperature Regimes
quantum Coulomb blockade temperature broadened regime resonant tunneling
transport through only one dot level
peak conductance 1/T FWHM ~ 3.5kT
quantum Coulomb blockade lifetime broadened regime transport through only one dot level
peak conductance e2/h indep. of T FWHM ~ Γ

## Slide 34: Temperature Dependence: Theory
Δ= 0.01 e2/C
kT / e2C
a 0.075
b 0.15
c 0.3
d 0.4
e 1
f 2
van Houten, Beenakker & Staring, NATO ASI Series

## Slide 35: Temperature Dependence: Experiment
Foxman et al., PRB50, 14193 (1994)
crossover 3.5 to 4.3kT peak width peak g
1/T dependence: quantum regime T independent: cassical regime
3.5 kT
4.4 kT
inverse peak height
peak width

## Slide 36: Line Shapes: Experiments
Foxman et al., PRB47, 10020 (1993)
T-broadened
lifetime broadened

## Slide 37: Charge Switching / Telegraph Noise
Elzermann, 2003